## Slide 1: Welcome!
We will begin in a few minutes.
Please be sure to sign the registration form to receive credit for attending today’s learning event.
Notes: Do
Meet and greet participants as they arrive. Start learning names, make them feel comfortable and settled in the training environment.
Make sure your opening has PUNCH:
Promotes interest and enthusiasm for the session
Understands participants’ needs
Notes ground rules and administrative/housekeeping needs
Clarifies expectations
Helps everyone get to know each other
State your expectations around participation: Make it known and expected that you will be encouraging and inviting participation.
Tips to facilitate connections:
Thank participants for their contribution (ideally with their name)
Praise participation (especially the first person to speak)
Express confidence in the participants
Restate what someone said earlier (“As John mentioned earlier….”)
Encourage participants to share what others were saying in their small groups (without naming names)
Invite someone you heard speaking in a small group to share with the entire group
Encourage the group to respond to an individual’s comment/question
Physical Room / Training Venue Setup:
If using a table arrangement, consider grouping 4 to 6 students at each station. This will help encourage conversation and discussion during activities.
Get people standing at regular intervals during your training session. Research shows that people learn up to 15% more when standing up!

## Slide 2: Boring and Notching in Wood-Frame Construction
Simpson Strong-Tie® Training
Presenter Name | Title

## Slide 3: Credit Information
AIA Member Information
This course is registered with AIA CES for continuing professional education. As such, it does not include content that may be deemed or construed to be an approval or endorsement by the AIA of any material of construction or any method or manner of handling, using, distributing, or dealing in any material or product. Upon completion of this course, Credit(s) earned will be reported to AIA CES for AIA members who pass the course and have entered their AIA member number on their Simpson profile page. A link to the Certificate of Completion will be available upon completion of this course. Only AIA LU/HSW will be reported.
This course offers 1 LU/HSW credit.
AIA Course Number: AIA-BNWC0117
Notes: Presenter Information
NOTE: Please be sure each attendee LEGIBLY signs the event sign-in sheet.
Say
All questions concerning proprietary products will be addressed after the conclusion of the AIA portion of the presentation. The meeting format is 50 minutes of content, followed by 10 minutes of Q & A.
Do
Explain the credits awarded for:
AIA: 1LU/HSW credit.
IACET: 0.1 (Equivalent to 1 hour) CEU credits.
Review the submission process for audiences requiring either AIA LU/HSW (health, safety and welfare) credits or CEU credits:
For those seeking AIA HSW credit, there is no test required. AIA members must be sure to provide their AIA member number on the sign-in sheet. Please make sure name, email and AIA member number are clearly printed so Simpson can report credits to the AIA on their behalf.
For those seeking IACET credit, they must take and pass the test. They must self-report CEU credits to their certifying organization or agency.

## Slide 4: Credit Information, cont.
IACET Accreditation Information
Simpson Strong-Tie® has been accredited as an Authorized Provider by the International Association for Continuing Education and Training (IACET), 7918 Jones Branch Drive, Suite 300, McLean, VA 22102; (703) 506-3275. In obtaining this approval, Simpson Strong-Tie® has demonstrated that it complies with the ANSI/IACET Standard which is recognized internationally as a standard of good practice. As a result of their Authorized Provider accreditation status, Simpson Strong-Tie® is authorized to offer IACET CEUs for its programs that qualify under the ANSI/IACET Standard.
This course offers 0.1 CEU (1 hour of credit).
Notes: Review the submission process for audiences requiring IACET CEU credits.
For those seeking IACET credit, they must take and pass the online test. They must self-report CEU credits to their certifying organization or agency.
Explain the credits awarded: IACET: 0.1 (Equivalent to 1 hour) CEUs.

## Slide 5: Credit Information, cont.
ICC Member Information
This course has been approved by the International Code Council (ICC) for continuing professional education. For learners that complete this course, it is your responsibility to self-report your credits to the ICC. Please retain your Completion Certificate for your records.
Be sure that your ICC ID number is provided on the sign-in sheet or in your Simpson profile in order to have it displayed on your certificate.
This course offers 0.1 CEU (1 hour of credit).
ICC Course Number: 13899
Notes: Review the submission process for audiences requiring ICC CEU credits.
For those seeking ICC credit, there is no test required. ICC members must provide their ICC ID number on the sign-in sheet or in their Simpson profile in order to have it displayed on their certificate. It is the responsibility of the participant to self-report their credits to the ICC. Ask them to retain their Completion Certificate for their records.
Explain the credits awarded: ICC: 0.1 (Equivalent to 1 hour) CEUs.

## Slide 6: AIA and CEU Credit Offerings
Visit
strongtie.com/workshops
for more information
Notes: Do
Explain that we have additional PK topics available that offer HSW credits for AIA members.
Explain that we have a library of online courses available in our Simpson Student Center that also offer AIA HSW credits. They can access our online courses at strongtie.com/workshops.

## Slide 7: Course Description
Boring and Notching in Wood-Frame Construction
This course was created to help familiarize building inspectors, contractors and specifiers with code-compliant protection and structural repair techniques for utility penetrations in structural wood members using the International Residential Code and International Building Code.
Course Contents
Introduction / Learning Objectives
Lesson 1: Plumbing and Mechanical
Lesson 2: Heating, Ventilation and Air Conditioning (HVAC)
Lesson 3: Electrical Wiring
Wrap Up / Questions
Notes: Do
Review the course description and course contents.

## Slide 8: Learning Objectives
Upon completion of this seminar, you will be able to:
Plumbing and Mechanical
Identify the size and location of allowable penetrations in wood members for plumbing and mechanical utilities in accordance with the IRC and IBC
Summarize the required repairs of notched or bored wood members that have exceeded the limitations for plumbing and mechanical applications
Summarize the required protections for piping in notched or bored wood members that have exceeded the limitations for plumbing and mechanical applications
Notes: Do
Review the learning objectives for the course.
Inform students that the assessment questions will be based on these learning objectives. Slides that may contain information relevant to the test have an orange graduation cap located in the bottom-left corner.

## Slide 9: Learning Objectives (cont.)
Upon completion of this seminar, you will be able to:
Heating, Ventilation and Air Conditioning
Identify the size and location of allowable penetrations in wood members for heating, ventilation and air conditioning in accordance with the IRC and IBC
Summarize the required repairs of cut or notched wood members that have exceeded the limitations for heating, ventilation and air conditioning applications
Notes: Do
Continue to review the learning objectives for the course.

## Slide 10: Learning Objectives (cont.)
Upon completion of this seminar, you will be able to:
Electrical Wiring
Identify the size and location of allowable penetrations in wood members for electrical wiring in accordance with the IRC and NEC
Summarize the required protections for wiring in bored wood members that have exceeded the limitations for electrical applications
Notes: Do
Continue to review the learning objectives for the course.

## Slide 11: A Word About Building Codes
All of the major building codes feature regulations on the size and/or location of penetrations in wood members for plumbing, HVAC and electrical components.
In many cases, in order to comply with the code, hardware is required to:
Restore strength to wood members
Protect utilities within the wall
Notes: All of the major building codes feature regulations on the size and/or location of penetrations in wood members for plumbing, HVAC and electrical components. In many cases, in order to comply with the code, hardware is required to restore strength to wood members and protect utilities within the wall.
This course is intended to illustrate the penetrations that are allowed under the various codes with and without repair or protection. Manufacturers offer a range of products to help meet these code requirements.
The information in this course is a summary of the requirements from the 2012, 2015 and 2018 International Residential Code (IRC), International Building Code (IBC), International Plumbing Code (IPC), International Mechanical Code (IMC), Uniform Plumbing Code (UPC), and the 2011, 2014 and 2017 National Electrical Code (NEC).

## Slide 12: PLUMBING AND MECHANICAL
After completing this lesson, you will be able to:
Identify the size and location of allowable penetrations in wood members for plumbing and mechanical utilities in accordance with the IRC and IBC
Summarize the required repairs of notched or bored wood members that have exceeded the limitations for plumbing and mechanical applications
Summarize the required protections for piping in notched or bored wood members that have exceeded the limitations for plumbing and mechanical applications
Notes: Do
Review the lesson title and objective.

## Slide 13: In This Lesson…
This lesson is separated into two parts:
Top and Bottom Plates
for Plumbing and Mechanical
Studs
for Plumbing and Mechanical
1
2
Part
Part
Notes: Say
This lesson is separated into two parts. Part 1 will discuss repair and protection requirements for top and bottom plates, while Part 2 will focus on requirements for studs.

## Slide 14: Introduction to Top and Bottom Plates for Plumbing and Mechanical
Top and Bottom Plates
for Plumbing and Mechanical
1
Part
When installing plumbing throughout a wood structure, the building codes address two requirements regarding top, bottom and sill plates:
The reinforcement of members where material has been removed
The protection of piping within walls
When structural repair is required
Required structural repairs
When protection of piping is required
Required protection of piping
Notes: Say
When installing plumbing throughout a wood structure, the building codes address two requirements regarding top, bottom and sill plates:
The reinforcement of members where material has been removed, and
The protection of piping within walls.

## Slide 15: Structural Repair is Required When…
Plumbing and Mechanical — Top and Bottom Plates
International Residential Code
50% of the top plate is removed in an exterior wall or interior load-bearing wall for piping or ductwork.
2012-2018 IRC R602.6.1
International Building Code
Any cut, notch or hole is removed from top or bottom plates for plumbing, heating or other pipes.
2012 IBC 2308.9.8, 2015-2018 IBC 2308.5.8
Notes: Say
In the International Residential Code, or IRC, structural repair is required when a cut, notch or hole that is more than 50% of the top-plate width is removed in an exterior wall, or interior load-bearing wall for piping.
In the International Building Code, or IBC, structural repair is required when any cut, notch or hole is removed from the top or bottom plates for plumbing, heating or other pipes. This means no bored holes or notches are allowed without structural repair.
Note
This slide contains information found in the post-course knowledge assessment.
Referencing the IRC: Structural repair is required when a hole, cut or notch that is more than _______________ of the top plate width is removed in an exterior wall, or interior load-bearing wall for piping.
25%
40%
50%
60%

## Slide 16: Structural Repair is Required When… (cont.)
Plumbing and Mechanical — Top and Bottom Plates
International Residential Code
International Building Code
Max. hole diameter or notch without repair or protection:
1¾" for 2x4
2¾" for 2x6
And notch or bore is at least 1½" (1" UPC) from the edge of plate.
No bored holes or notches are allowed without structural repair.
Page 4
Notes: Say
The maximum hole or notch depth allowed is 1-3/4" for a 2x4 and 2-3/4" for a 2x6, when designing with the IRC.
No cuts, notches or holes for plumbing or other pipes are allowed in the top or bottom plates without a structural repair strap when designing with the IBC.
Do
Have students refer to page 4 of the participant handout. There is information on this slide that may help fill in the blanks.

## Slide 17: Required Structural Repairs…
Plumbing and Mechanical — Top and Bottom Plates
International Residential Code
Galvanized, 16-gauge 1½"-wide metal tie.
Fastened across the top plate with (8) 10d x 1½" nails on each side.
Tie must extend at least 6" past the opening.
2012-2018 IRC R602.6.1
International Building Code
Galvanized, 16-gauge 1½"-wide metal tie.
Fastened across each plate (top and bottom) with (6) 16d nails on each side of each plate.
2012 IBC 2308.9.8, 2015-2018 IBC 2308.5.8
Page 5
Notes: Say
Both the IRC and IBC require structural repair to be a galvanized, 16-gauge metal tie that is at least 1-1/2" wide.
However, the IRC requires a repair strap on the upper-top plate only, while the IBC requires a repair strap on both top plates and the bottom plate.
In the IRC, the tie must be fastened with eight 10d nails, having a minimum length of 1-1/2", at each side of the opening. 16d nails are also acceptable. In the IBC, each tie must be fastened with six 16d nails at each side of the opening.
Do
Have students refer to page 5 of the participant handout. There is information on this slide that may help fill in the blanks.
Note
This slide contains information found in the post-course knowledge assessment.
Referencing the IBC: Structural repair for each plate is a 16-gauge, galvanized metal tie that is at least 1-1/2" wide. What is the minimum amount of nails required to be fastened on each side of the opening of each plate?
4 nails on each side of the opening of each plate
6 nails on each side of the opening of each plate
8 nails on each side of the opening of each plate
12 nails on each side of the opening of each plate

## Slide 18: Protection of Piping Within the Wall is Required When…
Plumbing and Mechanical — Top and Bottom Plates
International Residential Code
Piping is closer than 1½" or 1¼" to the edge of the plate, depending on the installation application.
2012 IRC M1308.2, 2015-2018 IRC M1308.2.1
2012-2018 IRC P2603.2.1
2012-2018 IRC M1502.5
2012 IRC G2439.5.3, 2015-2018 IRC G2439.6
International Building Code
Piping is closer than 1½" to the edge of the plate (1" UPC).
2012-2018 IPC 305.6
2012-2018 IMC 305.5
2012-2018 UPC 312.9
Notes: Say
In the IRC, protection of piping is required when piping other than cast iron or galvanized steel is closer than 1-1/2" to the edge of the plate for the installation of general mechanical systems (per IRC M1308.2). For general plumbing or clothes dryer exhausts, protection of piping is required for holes or notches closer than 1-1/4“ to the edge of the plate (per IRC P2603.2.1, M1502.5, and G2439.6).
The IBC refers to the International Plumbing Code, or IPC, for the protection requirements of piping within walls. The IPC states that protection of piping is required when piping other than cast iron or galvanized steel is closer than 1-1/2" to the edge of the plate.
For jurisdictions that use the Uniform Plumbing Code, or UPC, protection is required for plastic and copper piping closer than 1" to the edge of the plate.

## Slide 19: Required Protection…
Plumbing and Mechanical — Top and Bottom Plates
International Residential Code
16-gauge steel protective plate that covers the area notched/bored.
Extends 2" above the sole plates or below top plates.
2012-2018 IRC P2603.2.1
2012-2018 IRC M1502.5
2012 IRC G2439.5.3, 2015-2018 IRC G2439.6
International Building Code
16-gauge steel protective plate (UPC: 18-gauge) that covers the area notched/bored.
Extends 2" above the sole plates or below top plates (UPC: 1½").
2012-2018 IPC 305.6
2012-2018 IMC 305.5
2012-2018 UPC 312.9
Page 5
Notes: Say
Required protection, referencing the IRC, is a 16-gauge steel protective plate that covers the side of the plate and extends 2" above the sole plates and below top plates.
The IBC, again, refers to the IPC, which also states that required protection is a 16-gauge steel protective plate that covers the side of the plate and extends 2" above the sole plates and below top plates.
For jurisdictions that use the UPC, it allows an 18-gauge steel protective plate that extends 1-1/2" above the sole plates and below the top plates.
Do
Have students refer to page 5 of the participant handout. There is information on this slide that may help fill in the blanks.

## Slide 20: Required Protection… (cont.)
Plumbing and Mechanical — Top and Bottom Plates
Electrical Nail Stops do not satisfy code requirements (IRC or IBC) for plumbing or mechanical applications
Is this 2" above the sole plate or below the top plates?
Does it meet the code requirement for lateral load transfer, when required?
Notes: Say
Electrical nail stops do not satisfy the code requirements of either the IRC or IBC for plumbing or mechanical applications because they do not provide protection 2" above or below the plates, nor do they meet the code requirements for lateral load transfer (when required).

## Slide 21: Required Protection… (cont.)
Plumbing and Mechanical — Top and Bottom Plates
Protective Shield Plates where structural repair is not required (IRC only)
Load-bearing or non-load-bearing bottom/sole/sill plate
Non-load-bearing wall, top plates
Notes: Say
Not all applications will require both structural repair and protection of piping when designing with the IRC. For example, the top plates of non-load-bearing walls and the sole plates of load-bearing walls may not require a repair strap per the IRC. However, protection of the piping within the wall may still be required if the piping is closer than an inch and a half from the edge of the wood.
In these situations, a protective shield plate is a suitable product for plumbing and mechanical applications that require protection only. Proper protective plates are created with 16-gauge steel and extend two inches above sole plates or two inches below top plates.

## Slide 22: Required Protection… (cont.)
Plumbing and Mechanical — Top and Bottom Plates
Protective Shield Plates — Galvanized Steel Required?
16-gauge steel protective plate, 0.062" or 0.0575" thick. Galvanized not specifically required. Ask your local building official.
Notes: Say
Galvanized steel may not be required for protective plates, but it is recommended. The codes require a shield plate to be either 0.062" or 0.0575" thick depending on the section of the code referenced. However, the code does not specifically state for the plate to be galvanized. Uncoated 16-gauge steel is 0.06" thick, which satisfies the minimum requirement of 0.0575". However, other sections of the code specify 0.062" as the minimum thickness. This would require the 16-gauge steel to be galvanized. Ask your local building official what they will allow.
Do
Point out photo and note that uncoated steel may rust.
Discuss US Standard Steel Gauge Equivalents in Nominal Dimensions chart. It is possible for a plate to be 16-gauge, uncoated steel and still meet the 0.0575“ requirement.

## Slide 23: Summary of IRC Requirements
Plumbing and Mechanical — Top and Bottom Plates
IRC Code References
Repair top plates and protect piping (load-bearing wall)
R602.6.1, M1308.2, P2603.2.1
Protect piping (non-load-bearing wall)
M1308.2, P2603.2.1
Repair top plates
R602.6.1
Load Bearing — Top
When more than 50% of plate width is removed, structural repair is required. When piping closer than 1½", protection plate that extends 2" below / above member is required.
Non-Load Bearing — Top or Bottom
Protection needed when piping closer than 1½".
Notes: Say
Let’s quickly recap the IRC code requirements for notching and boring into plates for plumbing and mechanical applications.
When more than 50% of the top-plate width is removed, structural repair is required. A suitable repair product would be a galvanized, 16-gauge metal tie that is at least 1-1/2" wide. This tie must be fastened with eight 10d nails, having a minimum length of 1-1/2", at each side of the opening. 16d nails are also acceptable. The tie must extend 6" past the opening.
To protect the piping in a non-load-bearing wall, a suitable product would be a 16-gauge steel protection plate that extends 2" above the sole plates or 2" below the top plates.
What are our options if a top plate needs structural repair and the piping within the wall needs protection? [See next slide]

## Slide 24: Summary of IRC Requirements (cont.)
Plumbing and Mechanical — Top and Bottom Plates
Repair and Protect Plate
Meets the IRC code requirements for both “Protection Against Physical Damage” and “Lateral Load Transfer.”
Required on load-bearing walls for top plates only.
Note the eight nail holes to meet the nailing requirements.
Notes: Say
To repair the top plates and protect the piping within a load-bearing wall, a dual-purpose repair-and-protect plate is a suitable product. These will meet the IRC code requirements for both “protection against physical damage” and “lateral load transfer.”
The plate must be made from galvanized, 16-gauge steel and must be fastened with a minimum of eight 10d nails, having a minimum length of 1-1/2", at each side of the opening. 16d nails are also acceptable. The plate must also extend 2" below the framing member.
In the product picture shown on the slide, the notch width is limited to 4-5/8" to meet the IRC requirement: “The metal tie must extend at least 6" past the opening.”
Note
This slide contains information found in the post-course knowledge assessment.
Referencing the IRC: The protective shield plate shown in the image meets the IRC code requirements for:
Protection against physical damage
Lateral load transfer
Both protection against physical damage and lateral load transfer
Neither protection against physical damage or lateral load transfer

## Slide 25: Summary of IBC Requirements
Plumbing and Mechanical — Top and Bottom Plates
IBC Code References
Repair top plates and bottom plates
2012 IBC 2308.9.8, 2015-2018 IBC 2308.5.8
Protect piping
2012-2018 IPC 305.6
2012-2018 IMC 305.5
2012-2018 UPC 312.9
Top and Bottom Plate Repair / Protection – Piping closer than 1½" to edge of plate.
Top and Bottom Plate Repair – Piping further than 1½" to edge of plate.
Cannot Attach Protection Plate to Sole – Use 2x wood blocking.
Top and Bottom Plate Repair / Protection – Piping closer than 1½" to edge of plate and most or all of plate width removed.
Notes: Say
Next we’ll recap the IBC code requirements for notching and boring into plates for plumbing and mechanical applications.
Structural repair is required when any wood is removed from the plates in the form of a cut, notch or hole. To repair the top and bottom plates, a 16-gauge, galvanized metal tie that is at least 1-1/2" wide is required on each plate. Each tie must be fastened with six 16d nails on each side of the opening.
Protection of piping is required when piping other than cast iron or galvanized steel is closer than 1-1/2" to the edge of the plate. To protect the piping within the wall, a suitable product would be a 16-gauge, steel protective plate that extends 2" above the sole plates or below the top plates. For jurisdictions using the UPC, an 18-gauge steel protective plate that extends 1-1/2" above the sole plates or below the top plates would be acceptable.
Let’s review a few scenarios:
Do
Discuss scenarios shown on slide.
Top and Bottom Plate Repair/Protection – Piping closer than 1-1/2" to edge of plate. Wherever the soles/plates are cut, a galvanized structural repair tie that is 16 gauge x 1-1/2" wide is required on each sole/plate and shall be fastened with (6) 16d nails on each side of the cut (per the IBC). If piping is closer than 1-1/2" to the edge of the lumber, a protection plate is required that extends 2" above/below the framing member (per the IPC, IMC). When plastic and copper piping penetrates framing members to within 1" of the edge, a steel nail plate not less than 18 gauge, that extends 1-1/2" beyond the pipe or tubing on each side, is required (per the UPC).
Top and Bottom Plate Repair – Piping further than 1-1/2" (1" UPC) to edge of plate. Wherever the soles/plates are cut, a galvanized structural repair tie that is 16 gauge x 1-1/2" wide is required on each sole/plate and is to be fastened with (6) 16d nails on each side of the cut (IBC).
Cannot Attach Protection Plate to Sole – Where a protection plate cannot attach to a sole plate, 2x wood blocking should be added on either side of notch/hole to accept prongs.
Top and Bottom Plate Repair/Protection – Piping is closer than 1-1/2" to edge of plate and most or all of plate width removed. Whenever both the compressive and tensile capacities of the plates are compromised, a compression-tension strap provides capacities for an engineered solution while also meeting prescriptive requirements.

## Slide 26: Summary of IBC Requirements (cont.)
Plumbing and Mechanical — Top and Bottom Plates
Both Parts are Required to Repair and Protect
IBC requires six nails in each plate (both plates for a double top plate).
2-in-1 repair / protect products do not contain the required amount of nail holes.
Notes: Say
It is important to note that to meet the IBC code requirements for “protection against physical damage” and “lateral load transfer,” two separate products are necessary: a repair strap and a protective plate.
Each top plate requires six nails on each side of the cut or notch; a total of 24 nails when repairing a double top plate. The previously discussed 2-in-1 repair/protect plates will not meet IBC code because they contain only 16 nail holes.
A galvanized, 16-gauge protection plate that extends two inches below the top plates may be used to protect the piping within the wall. To repair the plates, a 16-gauge metal tie on each plate fastened with six nails on each side of the cut or notch may be used.
Note
This slide contains information found in the post-course knowledge assessment.
Referencing the IBC: To meet the IBC code requirements for protection against physical damage and lateral load transfer, both the protection plate and metal ties are required (see photo to the right).
True
False

## Slide 27: Introduction to Studs for Plumbing and Mechanical
Studs
for Plumbing and Mechanical
2
Part
When installing plumbing throughout a wood structure, the building codes address two requirements regarding studs:
The reinforcement of members where material has been removed
The protection of piping within walls
When structural repair is required
Required structural repairs
When protection of piping is required
Required protection of piping
Notes: Say
When installing plumbing throughout a wood structure, the building codes address two requirements regarding studs:
The reinforcement of members where material has been removed, and
The protection of piping within walls.

## Slide 28: Structural Repair Is Required When…
Plumbing and Mechanical — Studs
International Residential Code and International Building Code + IPC/IMC/UPC
Notching: Structural repair is required when a stud is notched to a depth greater than 25% of the width in bearing walls, or 40% in non-bearing partitions.
IRC R602.6, 2012 IBC 2308.9.10, 2015-2018 IBC 2308.5.9, IMC 302.3.2, IPC 307.2, 2012-2018 UPC 312.11
Non-load- bearing stud 40% notch allowed
Bearing stud 25% notch allowed
Page 6
Notes: Say
The requirements between the IRC and IBC are the same for determining when structural repair is required for notching or boring into studs.
When notching a stud for piping or mechanical applications, structural repair is required to restore strength when a stud is notched to a depth greater than 25% of the width in bearing walls, or 40% in non-bearing partitions.
Do
Have students refer to page 6 of the participant handout. There is information on this slide that may help fill in the blanks.

## Slide 29: Structural Repair Is Required When… (cont.)
Plumbing and Mechanical — Studs
International Residential Code and International Building Code + IPC/IMC/UPC
Boring: Structural repair is required when a hole is bored to a diameter exceeding 40% of the stud width in bearing walls, or 60% in non-bearing partitions.
Double stud: 40–60% allowed
No holes closer than 5/8" from edge
No holes located at same section as notch
Single load-bearing stud, 40% bored hole allowed
Double stud, 60% bored hole allowed
IRC R602.6, 2012 IBC 2308.9.11, 2015-2018 IBC 2308.5.10, IMC 302.3.3, IPC 307.2, 2012-2018 UPC 312.11
Page 6
Notes: Say
When boring a hole through a stud for piping or mechanical applications, structural repair is required to restore strength when a hole is bored to a diameter exceeding 40% of the stud width in bearing walls, or 60% in non-bearing partitions.
One exception, however, is that a hole may be drilled between 40–60% of the stud diameter in bearing walls if the bored stud is doubled and not more than two successive doubled studs are bored.
In no case shall the edge of a bored hole be closer than 5/8" from the edge of the stud. Bored holes shall not be located at the same section of the stud as a cut or notch.

## Slide 30: Structural Repair Is Required When… (cont.)
Plumbing and Mechanical — Studs
International Residential Code and International Building Code + IPC/IMC/UPC
Stud Size (in.) | Application | Max. Hole Diameter (in.) | Max. Notch Depth (in.)
2x4 | Interior / Non-bearing | 2-1/8 | 1-3/8
 | Exterior / Bearing | 1-3/8 | 7/8
2x6 | Interior / Non-bearing | 3-1/4 | 2-3/16
 | Exterior / Bearing | 2-3/16 | 1-3/8
Max. Bored Hole Diameter / Notch Depth
Page 7
?
?
Notes: Say
It can be difficult to measure the size of a hole or notch in a wood member using percentages. The table shown on the slide displays the maximum bored-hole diameters and notch depths for 2x4 and 2x6 studs in bearing and non-bearing applications.
Do
Have students refer to page 7 of the participant handout and attempt the exercise with their neighbors. What is the maximum allowable hole diameter for a load-bearing 2x4? What is the maximum allowable notch depth for a non-load-bearing 2x6?
After a few minutes, review the correct answers by clicking the mouse for a reveal animation.
Note
This slide contains information found in the post-course knowledge assessment.
What is the correct value missing in the table below? (Maximum hole diameter for a load-bearing 2x4)
1-1/4 in.
1-3/8 in.
2 in.
2-3/16 in.

## Slide 31: Required Structural Repairs…
Plumbing and Mechanical — Studs
International Residential Code
If maximum hole / notch specifications are exceeded, a suitable stud shoe, approved by building official, must be installed.
Stud shoes should be load-rated and code-listed.
2012-2018 IRC R602.6
International Building Code
Responsibility of Designer to provide an engineered solution (e.g., stud shoes).
Stud shoes should be load-rated and code-listed.
2012 IBC 2308.4, 2015-2018 IBC 2308.8
Page 6
Notes: Say
Code-listed and load-rated stud shoes meet the requirements of both the IRC and IBC for repairing studs with notches or bored holes that exceed the limits. The IRC explicitly permits the use of approved stud shoes where they are installed in accordance with the manufacturer’s recommendations. The IBC allows a designed solution in accordance with accepted engineering practice, such as an approved stud shoe.
Do
Have students refer to page 6 of the participant handout. There is information on this slide that may help fill in the blanks.

## Slide 32: Required Structural Repairs… (cont.)
Plumbing and Mechanical — Studs
Types of Stud Shoes
Available for many stud sizes, but no one has a load-rated, code-listed stud shoe for 4-2x’s.
Compression Only
Installs with nails
Stud Sizes: 2x, 3x, 2-2x, 3-2x
Compression and Tension
Installs with structural screws
Stud Sizes: 2x, 2-2x, 3-2x, 4x
Notes: Say
There are two types of load-rated and code-listed stud shoes available. The first is designed for compression loads only and is installed with nails on 2x, 3x, 2-2x, and 3-2x studs. The second is designed for both compression and tension loads, and is installed with structural screws on 2x, 2-2x, 3-2x and 4x studs.

## Slide 33: Required Structural Repairs… (cont.)
Plumbing and Mechanical — Studs
Which is the correct product for a 3-2x stud on a load-bearing wall?
PICTURE A
PICTURE B
Notes: Ask
Which is the correct stud shoe product for a 3-2x stud on a load-bearing wall?
Do
Click to start animation (correct/incorrect visual).
Say
That’s right, Picture B is correct! A stud shoe for a 3-2x stud needs to be load-rated and code-listed for both tension and compression on a load-bearing wall. The incorrect solution in Picture A is not load-rated or code-listed, nor can it handle tension loads.
Note
This slide contains information found in the post-course knowledge assessment.
Which picture shows the correct stud shoe product for a 3-2x stud on a load-bearing wall?
Picture A
Picture B

## Slide 34: Required Structural Repairs… (cont.)
Plumbing and Mechanical — Studs
Approved Stud Shoes
Many stud shoes do not have a load rating or code listing!
What is an “approved stud shoe” based on without a load rating and an appropriate ICC-ES or IAPMO-UES code report?
Notes: Say
Be careful, as many stud shoes do not have a load rating or code listing. What is an “approved stud shoe” based on without a load rating and an appropriate ICC-ES or IAPMO-UES code report?
---
ICC – International Code Council
IAPMO – International Association of Plumbing and Mechanical Officials

## Slide 35: Protection of Piping Within the Wall Is Required When…
Plumbing and Mechanical — Studs
International Residential Code
Piping is closer than 1½" or 1¼" to the edge of the framing member, depending on the installation application.
2012 IRC M1308.2, 2015-2018 IRC M1308.2.2
2012-2018 IRC P2603.2.1
International Building Code
Piping is closer than 1½" to the edge of the framing member (1" UPC).
2012-2018 IPC 305.6
2012-2018 IMC 305.5
2012-2018 UPC 312.9
Allowable penetration limitations for studs are the same as they are for top and bottom plates.
Notes: Say
The allowable penetration limitations for studs are the same as they are for the top and bottom plates.
In the IRC, protection of piping is required when piping other than cast iron or galvanized steel is closer than 1-1/2" to the edge of the framing member for the installation of general mechanical systems (per IRC M1308.2). For general plumbing installations, protection of piping is required for holes or notches closer than 1-1/4" to the edge of the framing member (per IRC P2603.2.1).
The IBC refers to the International Plumbing Code, or IPC, for the protection requirements of piping within walls. The IPC states that protection of piping is required when piping other than cast iron or galvanized steel is closer than 1-1/2" to the edge of the framing member.
For jurisdictions that use the Uniform Plumbing Code, or UPC, protection is required for plastic and copper piping closer than 1" to the edge of the framing member.

## Slide 36: Required Protection…
Plumbing and Mechanical — Studs
International Residential Code
16-gauge steel protective plate.
Covers the area notched/bored.
2012-2018 IRC P2603.2.1
2012 IRC M1308.2, 2015-2018 IRC M1308.2.2
International Building Code
16-gauge steel protective plate (UPC: 18-gauge).
Covers the area notched/bored.
2012-2018 IPC 305.6
2012-2018 IMC 305.5
2012-2018 UPC 312.9
A 16-gauge steel nail stop is a suitable product to protect the stud
Page 6
Notes: Say
For the IRC, required protection is a 16-gauge steel protective plate that covers the area of the pipe where the member is notched or bored.
The IBC, again, refers to the IPC, which also states that required protection is a 16-gauge steel protective plate that covers the area of the pipe where the member is notched or bored.
For jurisdictions that use the UPC, an 18-gauge steel protective plate is allowed.
A 16-gauge steel nail stop is a suitable product to protect the stud.
Do
Have students refer to page 6 of the participant handout. There is information on this slide that may help fill in the blanks.

## Slide 37: Summary of IRC and IBC Requirements
Plumbing and Mechanical — Studs
IRC Code References
Repair stud and protect piping
R602.6, M1308.2, P2603.2.1
Protect piping
M1308.2, P2603.2.1
IBC/IPC/IMC/UPC Code References
Repair stud
2012 IBC 2308.9.10, 2015-2018 IBC 2308.5.9
2012 IBC 2308.9.11, 2015-2018 IBC 2308.5.10
2012 IBC 2308.4, 2015-2018 IBC 2308.8
Protect piping
IPC 305.6, IMC 305.5, UPC 312.9
Stud Repair
When notching / boring exceeds guidelines, a suitable stud shoe should be installed.
Stud Protection
When piping closer than 1½", protection plate is required (nail stop).
Notes: Say
Let’s quickly recap the code requirements for notching and boring into studs for plumbing and mechanical applications.
To repair the studs and protect the piping within a wall, a code-listed and load-tested 16-gauge steel stud shoe is a suitable product.
To protect the piping in a wall, a suitable product would be a 16-gauge steel protection plate, such as a nail stop, that covers the area of the pipe where the member is notched or bored.
A combination of a stud shoe and nail stop may be required for large bored holes to protect both sides of the stud.

## Slide 38: Summary of IRC and IBC Requirements (cont.)
Plumbing and Mechanical — Studs
Repair and Protect Stud
Combining Stud Shoes with Nail Stops
Because the pipe is within 1½" to the edge of the stud, the stud shoe protects one side and a nail stop is required to protect the other side.
Notes: Say
A combination of a nail stop and a stud shoe should be used to repair and protect the stud.
Because the pipe is within 1-1/2" to the edge of the stud, the stud shoe protects one side and a nail stop is required to protect the other side.

## Slide 39: Lesson One Complete
Now that you’ve completed this lesson, you should be able to:
Identify the size and location of allowable penetrations in wood members for plumbing and mechanical utilities in accordance with the IRC and IBC
Summarize the required repairs of notched or bored wood members that have exceeded the limitations for plumbing and mechanical applications
Summarize the required protections for piping in notched or bored wood members that have exceeded the limitations for plumbing and mechanical applications
Notes: Do
Review the lesson objective summary.

## Slide 40: HEATING, VENTILATION AND AIR CONDITIONING
After completing this lesson, you will be able to:
Identify the size and location of allowable penetrations in wood members for heating, ventilation and air conditioning in accordance with the IRC and IBC
Summarize the required repairs of cut or notched wood members that have exceeded the limitations for heating, ventilation and air conditioning applications
Notes: Do
Review the lesson title and objective.

## Slide 41: Introduction to Top and Bottom Plates for HVAC
HVAC
Structural Repair of Plates
When installing HVAC throughout a wood structure, the building codes address the reinforcement of top and bottom plates where material has been removed to allow the passage of ductwork.
When structural repair is required
Required structural repairs
Notes: Say
When installing heating, ventilation and air conditioning throughout a wood structure, the building codes address the reinforcement of top and bottom plates where material has been removed to allow the passage of ductwork.

## Slide 42: Structural Repair Is Required When…
HVAC — Structural Repair of Plates
International Residential Code
50% of the top plate is removed in an exterior wall or interior load-bearing wall for piping or ductwork.
2012-2018 IRC R602.6.1
International Building Code
Any cut, notch or hole is removed from top or bottom plates for ductwork.
2012 IBC 2308.9.8, 2015-2018 IBC 2308.5.8
Notes: Say
When designing with the IRC, structural repair is required when a cut, notch or hole that is more than 50% of the top-plate width is removed in an exterior wall, or interior load-bearing wall for ductwork.
When designing with the IBC, no cuts or notches for heating, ventilation or air conditioning are allowed in the top or bottom plates without structural repair.
The maximum notch depth allowed is 1-3/4" for a 2x4 and 2-3/4" for a 2x6 when designing with the IRC.
No cuts or notches for heating, ventilation or air conditioning are allowed in the top or bottom plates without a structural repair strap when designing with the IBC.
Note
This slide contains information found in the post-course knowledge assessment.
Referencing the IBC: No cuts or notches are allowed for ductwork without structural repair to the top and bottom plates.
True
False

## Slide 43: Structural Repair Is Required When… (cont.)
HVAC — Structural Repair of Plates
International Residential Code
International Building Code
Max. hole diameter or notch without repair or protection:
1¾" for 2x4
2¾" for 2x6
And notch or bore is at least 1½" (1" UPC) from the edge of plate.
No bored holes or notches are allowed without structural repair.
Page 8
Notes: Say
The maximum hole or notch depth allowed is 1-3/4" for a 2x4 and 2-3/4" for a 2x6, when designing with the IRC.
No cuts, notches or holes for plumbing or other pipes are allowed in the top or bottom plates without structural repair when designing with the IBC.
Do
Have students refer to page 8 of the participant handout. There is information on this slide that may help fill in the blanks.

## Slide 44: Required Repairs…
HVAC — Structural Repair of Plates
International Residential Code
Top Plate Repair – 1 Bay (Load Bearing)
Galvanized, 16-gauge 1½"-wide metal tie on top plate.
(8) 10d x 1½" nails at each side of opening.
Tie extends 6" past opening.
Top Plate Repair – 2 Bays (Load Bearing)
Difficult to find long 1½" tie.
Solution: use 3"-wide tie.
3"-wide tie provides equivalent tension capacity.
No Repairs Necessary (Non-Load Bearing)
R602.6.1: limitations only apply to load bearing walls.
R602.3.2: wood walls shall be capped with double top plate.
Ask your local building official.
IRC R602.6.1, IRC R602.3.2
Page 9
Notes: Say
The top-plate repair solutions using the IRC for load-bearing HVAC applications differ depending on whether it is a single bay or side-by-side ductwork.
Repair for a single bay with duct work is a galvanized, 16-gauge metal tie that is at least 1-1/2" wide on one or more top plate. This tie must be fastened with eight 10d nails, with a minimum length of 1-1/2", at each side of the opening. 16d nails may also be used. The tie must extend 6" past the opening.
For side-by-side ductwork, it may prove difficult to find a 1-1/2“-wide strap with the necessary length to extend 6" past the openings. One solution is to use a 3"-wide tie (with all other requirements remaining the same). In this application, a 3"-wide strap provides equivalent tension capacity.
There may not be limitations or repairs required for non-load bearing walls. Section R602.6.1 states that the limitations only apply to exterior or load-bearing walls. However, Section R602.3.2 states that wood stud walls shall be capped with a double top plate. Notches that require total removal of material would not have a capped top plate. Ask your local building official what they will allow for interior non-load-bearing walls.
Do
Have students refer to page 9 of the participant handout. There is information on this slide that may help fill in the blanks.
Note
This slide contains information found in the post-course knowledge assessment.
Referencing the IRC: When repairing a plate that has been cut for ductwork, the repair strap must extend at least __________ past the opening.
3 inches
6 inches
9 inches
12 inches

## Slide 45: Required Repairs… (cont.)
HVAC — Structural Repair of Plates
International Residential Code
When is a strap not required?
When the entire side of the wall with the notch or cut is covered by WSP sheathing.
Most of the time, side of wall with notch or cut is on the inside of a load-bearing exterior wall and covered by drywall.
In this typical application, a strap would be required.
IRC R602.6.1
Notes: Say
A strap or metal tie is not required on the top plates of a load-bearing wall when the entire side of the wall with the notch or cut is covered by wood structural panel sheathing. Most of the time, however, the side of the wall with the notch or cut is on the inside of a load-bearing exterior wall and covered by drywall. Therefore, in this typical application, a strap would be required.

## Slide 46: Required Repairs… (cont.)
HVAC — Structural Repair of Plates
International Building Code
Top and Bottom Plate Repair – 1 Bay
Galvanized, 16-gauge 1½"-wide metal tie on both top plates and the bottom plate.
(6) 16d nails at each side of opening.
Top and Bottom Plate Repair – 2 Bays
Difficult to find long 1½"-wide tie.
Solution: use 3"-wide tie.
3"-wide tie provides equivalent tension capacity.
2012 IBC 2308.9.8, 2015-2018 IBC 2308.5.8
Page 10
Notes: Say
The top- and bottom-plate repair solutions using the IBC for HVAC applications also differ depending on whether they are for a single bay or side-by-side ductwork.
Repair for a single bay with ductwork is a galvanized, 16-gauge metal tie that is at least 1-1/2" wide on both top plates and the bottom plate. Each tie must be fastened with six 16d nails on each side of the opening and the tie must extend 6" past the opening.
For side-by-side ductwork, it may prove difficult to find a 1-1/2" wide strap with the necessary length to extend 6" past the openings. One solution is to use a 3"-wide tie (with all other requirements remaining the same). In this application, a 3"-wide strap provides equivalent tension capacity.
Do
Have students refer to page ten of the participant handout. There is information on this slide that may help fill in the blanks.

## Slide 47: Required Repairs… (cont.)
HVAC — Structural Repair of Plates
International Residential Code and International Building Code
When the entire top plate is removed for ductwork in a load-bearing wall, a galvanized, 16-gauge metal tie should be installed on both sides of the cut plate.
TOP PLATE
TOP PLATE
DUCT
16-GAUGE METAL TIE
16-GAUGE METAL TIE
Overhead View of Top Plates
Notes: Say
Regardless whether the wood-framed structure is designed with the IRC or IBC, a galvanized, 16-gauge metal tie should be installed on both sides of the cut plate when the entire top plate is removed for ductwork in a load-bearing wall.

## Slide 48: Summary of IRC Requirements
HVAC — Top and Bottom Plates
IRC Code References
Repair top plates
R602.6.1, R602.3.2
Galvanized, 16-gauge metal tie, 1½" wide
HVAC chase in exterior or load-bearing wall
Galvanized, 16-gauge metal tie, 1½" wide (3" wide preferred)
HVAC chase (2) adjacent stud bays
Notes: Say
Let’s quickly recap the IRC code requirements for repairing the top plates for heating, ventilation and air conditioning applications.
To repair the top plate of load-bearing wall with ductwork, a suitable product would be a galvanized, 16-gauge metal tie fastened with eight 10d nails, having a minimum length of 1-1/2", at each side of the opening. 16d nails are also acceptable. The tie shall be a minimum of 1-1/2" wide. For a side-by-side application, a 3"-wide tie provides equivalent tension capacity.
When the entire top plate is removed for ductwork in a load-bearing wall, a galvanized, 16-gauge metal tie should be installed on both sides of the cut plate.
Interior, non-load-bearing walls may not require structural repair. Ask your local building official for clarification.

## Slide 49: Summary of IBC Requirements
HVAC — Structural Repair of Plates
IBC Code References
Repair top and bottom plates
2012 2308.9.8, 2015-2018 2308.5.8
Galvanized, 16-gauge 1½"-wide metal tie on each top plate and the bottom plate
Galvanized, 16-gauge 1½"-wide (3" wide preferred) metal tie on the top plates and bottom plate
Notes: Say
Next we’ll recap the IBC code requirements for repairing the top and bottom plates for heating, ventilation and air conditioning applications.
To repair the top and bottom plates, a 16-gauge, galvanized metal tie that is at least 1-1/2“ wide is required on each plate. This tie must be fastened with six 16d nails at each side of the cut.
For side-by-side applications that have ducts in two consecutive bays, it is recommended to use a 3"-wide strap. It may be difficult to locate a 1-1/2“-wide strap that has the required length to extend across both bays.

## Slide 50: Lesson Two Complete
Now that you’ve completed this lesson, you should be able to:
Identify the size and location of allowable penetrations in wood members for heating, ventilation and air conditioning in accordance with the IRC and IBC
Summarize the required repairs of cut or notched wood members that have exceeded the limitations for heating, ventilation and air conditioning applications
Notes: Do
Review the lesson objective summary.

## Slide 51: ELECTRICAL WIRING
After completing this lesson, you will be able to:
Identify the size and location of allowable penetrations in wood members for electrical wiring in accordance with the IRC and NEC
Summarize the required protections for wiring in bored wood members that have exceeded the limitations for electrical applications
Notes: Do
Review the lesson title and objective.

## Slide 52: Introduction to Top Plates, Bottom Plates and Studs for Electrical Wiring
Electrical Wiring
Top Plates, Bottom Plates and Studs
When installing electrical wiring throughout a wood structure, the building codes require protection of wiring to prevent damage.
When protection of wiring is required
Required protection of wiring
Notes: Say
When installing electrical wiring throughout a wood structure, the building codes require protection of wiring to prevent damage.

## Slide 53: Protection of Wiring Within the Wall Is Required When…
Electrical Wiring — Protection of Wiring Within Plates and Studs
International Residential Code
A hole is closer than 1¼" to the edge of a wood member.
IRC Table E3802.1
International Building Code
Bored holes in joists, rafters or wood members are closer than 1¼" from the edge of the wood.
2011-2017 NEC 300.4
Bored holes closer than 1¼" to the edge of a wood member require protection
Notes: Say
In the IRC, protection of electrical wiring is required when a hole is closer than 1-1/4" to the edge of a wood member.
The IBC refers to the National Electric Code, or NEC, for the protection requirements of electrical wiring within walls. The NEC states that protection of wiring is required where bored holes in joists, rafters or wood members are closer than 1-1/4" from the edge of the wood.
Note
This slide contains information found in the post-course knowledge assessment.
Protection of wiring within a wall is required when bored holes in joists, rafters or wood members are closer than __________ from the edge of the wood.
1-1/4 inches
1-1/2 inches
1-3/4 inches
2 inches

## Slide 54: Protection of Wiring Within the Wall Is Required When… (cont.)
Electrical Wiring — Protection of Wiring Within Plates and Studs
Allowable under code with no repair / protection required:
Maximum hole diameter in studs and plates to maintain 1¼" distance:
2x4 = 1"
2x6 = 3"
Page 11
Notes: Say
A 2x4 stud or plate may have a maximum hole diameter of 1" to maintain the 1-1/4" distance.
A 2x6 stud or plate may have a 3" hole to maintain the 1-1/4" distance.
Do
Have students refer to page eleven of the participant handout. There is information on this slide that may help fill in the blanks.

## Slide 55: Required Protection…
Electrical Wiring — Protection of Wiring Within Plates and Studs
International Residential Code
Required protection of electrical wiring is a 0.0625" steel plate (approximately 16 gauge) that covers the area of the wiring.
IRC Table E3802.1
International Building Code
Required protection is a 1/16" protective steel plate (approximately 16 gauge) that covers the area of the wiring.
IBC 2701.1, NEC 300.4
Protection shall be a 0.0625" steel plate that covers the area of the wiring (a nail stop is a suitable product)
Notes: Say
Required protection, referencing the IRC, is a 0.0625" steel protective plate that covers the area of the wiring.
The IBC, again, refers to the NEC, which also states that required protection is a 1/16" steel protective plate that covers the area of the wiring. 1/16" is equal to 0.0625", and both are approximately 16 gauge.
When a hole containing electrical wiring is closer than 1-1/4" from the edge of a wood member (due to diameter or placement), a protective plate is required. A 16-gauge steel nail stop meets the requirements of the IRC and NEC.
Note
This slide contains information found in the post-course knowledge assessment.
A 16-gauge steel nail stop provides adequate protection for electrical wiring within a wood member.
True
False

## Slide 56: Summary of IRC and IBC Requirements
Electrical Wiring — Protection of Wiring Within Plates and Studs
IRC Code References
Repair top plates, bottom plates and studs
IRC Table E3802.1
IBC/NEC Code References
Protect wiring within wall
NEC 300.4
When a hole is closer than 1¼" from the edge of a wood member (due to diameter or placement), a protective plate is required.
Page 11
Notes: Say
Let’s quickly recap the IRC, IBC and NEC code requirements for boring into plates or studs for electrical applications.
To protect the wiring within the wall, a suitable product would be a 16-gauge steel protection plate that covers the area of the wiring, such as a nail stop. This method of protection meets the minimum requirements of the IRC, IBC and NEC.
Do
Have students refer to page eleven of the participant handout. There is information on this slide that may help fill in the blanks.

## Slide 57: Lesson Three Complete
Now that you’ve completed this lesson, you should be able to:
Identify the size and location of allowable penetrations in wood members for electrical wiring in accordance with the IRC and NEC
Summarize the required protections for wiring in bored wood members that have exceeded the limitations for electrical applications
Notes: Do
Review the lesson objective summary.

## Slide 58: COURSE COMPLETION
Questions?

## Slide 59: Course Completion
Simpson Strong-Tie
This concludes the American Institute of Architects Continuing Education Systems course
For a library of Simpson Strong-Tie AIA CES courses,
visit strongtie.com/workshops
Notes: Do
Draw the meeting to a close. Hand out literature and business cards.
Say
If you have ongoing projects that you would be interested in reviewing together, please let me know.

## Slide 60: Next Steps!
AIA: For those seeking AIA LU/HSW: You will receive an email with a link allowing access to print your Certificate. Congratulations, you will have earned 1 LU/HSW credit. If your AIA member number has been inserted into your profile, Simpson Strong-Tie will report your credits on your behalf to the AIA. No test is required in order to receive HSW credits.
IACET: For those seeking IACET CEUs: You will receive an email with a link allowing access to print your Certificate of Attendance and instructions directing you to the Simpson Student Center to take the exam before credits can be awarded. Once the exam is taken and passed, you will have earned 0.1 CEUs (1 hour of credit). You can then access your Certificate of Completion from the Course Content tab. You must self-report your credits to your certifying organization or agency.
If you have questions or need assistance, please contact training@strongtie.com.
Notes: Presenter Notes:
Review the email and notification process as outlined in this slide.
AIA LUs:
For those that want AIA HSW credit, be sure to provide your AIA number on the sign-in sheet and Simpson will report your credits to the AIA on your behalf.
No test is required for AIA credit.
CEUs:
For those seeking CEUs, watch for an email with instructions to access the online test. After you have passed the test, you may access your Certification of Completion from the course content tab.
You must self-report your credits to your certifying organization or agency.

## Slide 61: Next Steps!
ICC: For those seeking ICC CEUs: You will receive an email with a link allowing access to print your Certificate. Congratulations, you will have earned 0.1 ICC CEU (1 hour of credit). Please make sure your ICC member number has been inserted into your profile. It is your responsibility to self-report your credits to the ICC. Please retain your Completion Certificate for your records.
IACET: For those seeking IACET CEUs: You will receive an email with a link allowing access to print your Certificate of Attendance and instructions directing you to the Simpson Student Center to take the exam before credits can be awarded. Once the exam is taken and passed, you will have earned 0.1 CEUs (1 hour of credit). You can then access your Certificate of Completion from the Course Content tab. You must self-report your credits to your certifying organization or agency.
If you have questions or need assistance, please contact training@strongtie.com.
Notes: Presenter Notes:
Review the email and notification process as outlined in this slide.
Watch for an email directing you to the Student Center to print your certificate.
No test is required for ICC credit. You must self-report your credits to ICC.
For those seeking general IACET CEUs after you have passed the online test, you may access your Certification of Completion from the course content tab. You must self-report your credits to your certifying organization or agency.