## Slide 1
PLEASE READ
Dear Instructor,
This presentation is available in both AIA and ICC versions.
For AIA: Right click and un-hide slides 5 and 47
For ICC: Right click and un-hide slides 6 and 48
Slide 2 is an optional slide

## Slide 2: Welcome!
We will begin in a few minutes.
Please be sure to sign the registration form to receive credit for attending today’s learning event.
Notes: Do
Meet and greet participants as they arrive. Start learning names, make them feel comfortable and settled in the training environment.
Make sure your opening has PUNCH:
Promotes interest and enthusiasm for the session
Understands participants’ needs
Notes ground rules and administrative/housekeeping needs
Clarifies expectations
Helps everyone get to know each other
State your expectations around participation: Make it known and expected that you will be encouraging and inviting participation.
Tips to facilitate connections:
Thank participants for their contribution (ideally with their name)
Praise participation (especially the first person to speak)
Express confidence in the participants
Restate what someone said earlier (“As John mentioned earlier….”)
Encourage participants to share what others were saying in their small groups (without naming names)
Invite someone you heard speaking in a small group to share with the entire group
Encourage the group to respond to an individual’s comment/question
Physical Room / Training Venue Setup:
If using a table arrangement, consider grouping 4 to 6 students at each station. This will help encourage conversation and discussion during activities.
Get people standing at regular intervals during your training session. Research shows that people learn up to 15% more when standing up!

## Slide 3: Cracking the Concrete Anchor Codes
AIA Provider: 50119826
The Latest Industry Standards for the Design of Post-installed Anchor Products
AIA Course Number: AIA-CCAC2014
www.strongtie.com
Notes: Do
Be sure to mention the AIA provider and course number for those requiring AIA credit. Ask the attendees to write down this information for reference. For AIA members, we will submit this information for them.

## Slide 4: Credit Information
IACET Accreditation Information
Simpson Strong-Tie® has been accredited as an Authorized Provider by the International Association for Continuing Education and Training (IACET). As a result of their Authorized Provider accreditation status, Simpson Strong-Tie® is authorized to offer IACET CEUs for its programs that qualify under the ANSI/IACET Standard.
This course offers 0.1 CEU (1 hour of credit).
Notes: Review the submission process for audiences requiring IACET CEU credits.
For those seeking IACET credit, they must take and pass the online test. They must self-report CEU credits to their certifying organization or agency.
Explain the credits awarded: IACET: 0.1 (Equivalent to 1 hour) CEUs.

## Slide 5: Credit Information
AIA Member Information
This course is registered with AIA CES for continuing professional education. As such, it does not include content that may be deemed or construed to be an approval or endorsement by the AIA of any material of construction or any method or manner of handling, using, distributing, or dealing in any material or product. Upon completion of this course, Credit(s) earned will be reported to AIA CES for AIA members who pass the course and have entered their AIA member number on their Simpson profile page. A link to the Certificate of Completion will be available upon completion of this course. Only AIA LU/HSW will be reported.
This course offers 1 LU/HSW credit.
AIA Course Number: AIA-CCAC2014
Notes: Presenter Information
NOTE: Please be sure each attendee LEGIBLY signs the event sign-in sheet.
Say
All questions concerning proprietary products will be addressed after the conclusion of the AIA portion of the presentation. The meeting format is 50 minutes of content, followed by 10 minutes of Q & A.
Do
Explain the credits awarded for:
AIA: 1LU/HSW credit.
IACET: 0.1 (Equivalent to 1 hour) CEU credits.
Review the submission process for audiences requiring either AIA LU/HSW (health, safety and welfare) credits or CEU credits:
For those seeking AIA HSW credit, there is no test required. AIA members must be sure to provide their AIA member number on the sign-in sheet. Please make sure name, email and AIA member number are clearly printed so Simpson can report credits to the AIA on their behalf.
For those seeking IACET credit, they must take and pass the test. They must self-report CEU credits to their certifying organization or agency.

## Slide 6: Credit Information, cont.
ICC Member Information
This course has been approved by the International Code Council (ICC) for continuing professional education. For learners that complete this course, it is your responsibility to self-report your credits to the ICC. Please retain your Completion Certificate for your records.
Be sure that your ICC ID number is provided on the sign-in sheet or in your Simpson profile in order to have it displayed on your certificate.
This course offers 0.1 CEU (1 hour of credit).
ICC Course Number: 178
Notes: Review the submission process for audiences requiring ICC CEU credits.
For those seeking ICC credit, there is no test required. ICC members must provide their ICC ID number on the sign-in sheet or in their Simpson profile in order to have it displayed on their certificate. It is the responsibility of the participant to self-report their credits to the ICC. Ask them to retain their Completion Certificate for their records.
Explain the credits awarded: ICC: 0.1 (Equivalent to 1 hour) CEUs.

## Slide 7: Additional Credit Offerings
Visit
strongtie.com/workshops
for more information
Course Name | CEUs | AIA | ICC
Introduction to Deck Design | 0.1 | ✔ | ✔
Introduction to Wind Design and the Wood Frame Construction Manual | 0.1 | ✔ | ✔
Shear Walls and Lateral Bracing in Light Frame Construction | 0.1 | ✔ | ✔
Understanding Restraint Rod Systems | 0.1 | ✔ | ✔
Cracking the Concrete Anchor Codes | 0.1 | ✔ | ✔
Concrete Deterioration | 0.1 | ✔ | ✔
Moment Frame Design | 0.1 | ✔ | ✔
Introduction to Wind Code Provisions and Meteorological Concepts | 0.1 | ✔ | ✔
Wind Design in Accordance with ASCE 7-10 | 0.1 | ✔ | ✔
Wood Framed Seismic Design 1: Code Provisions, Design Parameters | 0.1 | ✔ | ✔
Notes: Do
Explain that we have additional PK topics available that offer credit for ICC members and HSW credits for AIA members.
Explain that we have a library of online courses available in our Simpson Student Center that also offer ICC and AIA HSW credits. They can access our online courses at strongtie.com/workshops.

## Slide 8: Course Description
This course provides a thorough overview of the latest industry standards related to the design of post-installed anchor products for anchoring into concrete and masonry base materials.
In addition to an overview, this course provides a more detailed discussion on specific code sections and standards related to the latest requirements for the proper design and specification of code compliant products.
Cracking the Concrete Anchor Codes:
Notes: Speakers Notes:
Briefly review the course description without reading it verbatim.

## Slide 9: Learning Objectives
Upon completion of this seminar, you should be able to:
Provide an overview of the latest industry standards for designing:
  Anchoring into masonry
  Anchoring into concrete
Describe latest test standards for anchor products
Explain the significance of research reports for anchoring products
Understand the importance of specifying anchor products that meet the latest industry standards
Notes: Say
The intent is that attendees walk away from this class with a thorough understanding of the standard of practice for anchoring into masonry and concrete such that they will be able to provide an overview of them.
In addition, emphasis will be placed on understanding the important test standards for anchor products.
Lastly, attendees should be able to explain the significance of product research reports and the value & credibility they add to a construction pro
Do
Review the learning objectives for the course.
Inform students that the assessment questions will be based on these learning objectives. Slides that may contain information relevant to the test have an orange graduation cap located in the bottom-left corner.
duct.

## Slide 10: Agenda
Standard of practice for Anchoring into Concrete
L
1
L
2
L
3
Standard of practice for Anchoring into Masonry
Define the standard of practice for anchor design
Building code
Referenced standards
Research reports and/or Tests
Notes: Say:
The purpose of this presentation is to summarize the latest standards in the industry as they relate to designing anchors.
Throughout this class we will define what we mean by “standard of practice” by first looking at what the building code has to say and working our way through referenced standards along with research reports and test criteria.
Then we will focus on the standard of practice as it relates specifically to designing anchors into masonry and then designing anchors into concrete.
What we will see throughout the presentation is that the standard of practice is often dependent upon both the base material being anchored into as well as the type of anchor product being designed.
To accompany and summarize this presentation we have provided a several page handout.

## Slide 11: Why is All This Important?
Notes: Say
This slide illustrates the importance of educating people about the latest standards in the industry.
These articles emphasize the importance of actually designing to, not just knowing about, the latest industry standards.
These pictures represent failures that have occurred in recent years where the failure 1.) tragically led to someone’s death, and 2.) was in some way a result of a connection-related issue.
In the case of the Bid Dig project, it not only involved a connection-related issue but it was specifically a post-installed anchor (adhesive anchor) related issue.
It is this very project failure that led to many of the changes we will discuss later on related to adhesive anchor products.

## Slide 12: Establishing the Standard of Practice
L
1
Notes: Say
We will start by discussing what we mean when we say Standard of Practice and will look at how it is established.

## Slide 13: Standard of Practice
Establishing the Standard of Practice with:
Building codes
Referenced Standards
Research reports
Test data
Standard of Practice Definition:
A consensus that industry has determined how a certain process should be performed.
Notes: Notes:
Although there is no one set definition of Standard of Practice, as it relates to anchor design perhaps it is best defined as…
When establishing the standard of practice we will first look at what the building code has to say, then move onto its referenced standards for additional information and then onto the concept of using research reports and test data to justify designing/using a product on a job.
While we will focus on anchor design, this same process could be used for many other building products.
Animations:
Standard of Practice Definition on slide at start.
Click 1+ imaged of referenced material and accompanying text.

## Slide 14: Building Code
Starting point
May or may not contain provisions for anchor products
If not, look at “Referenced Standards” in Chapter 35
Notes: Sometimes the building code will contain provisions for anchor products directly in the body of the code.
If not, sometimes the code’s referenced standards will address how to design, test and qualify the anchor product.
Chapter 35 of the IBC contains a list of various referenced standards. However, even these referenced standards sometimes don’t address all types of post-installed anchor products.

## Slide 15: Alternative Methods
Notes: When the building code, or its referenced standards, doesn’t provide any specific provisions for a building product it is often considered an “alternate material.”
Section 104.11 of the IBC addresses the use of “alternate materials” on a project.
It essentially says that the building official has the authority to approve the use of alternate materials so long as they meet the intent of the code.
To assist the building official in the approval process, the concept of a research report is mentioned as a means to provide supporting data.
The research reports are to be from an “approved source.”
While this could vary from jurisdiction to jurisdiction, most building officials consider agencies such as ICC-ES and IAPMO UES to be “approved sources.”
In the event a research report is unavailable, and/or where preferred otherwise by a building official, there is a section in 104.11 that says that the building official can ask for testing of an alternate material at no expense to them.
Given the 2 options, most building officials would prefer a research report as opposed to taking on the additional liability of approving test methods for specialty building products.
Quiz Note
This slide features information that will be found on the post-training knowledge assessment:
True or false: Section 104.11 of the International Building Code (IBC2003 or IBC2006), titled “Alternate Materials,” says that it is up to the building official to determine if an alternate material (one that is not prescribed by the building code) is considered “approved.”
True
False

## Slide 16: Research Reports
Industry established criteria to evaluate products against
Products independently tested and evaluated against criteria
Research report issued showing Conditions of Use
Reports made available to public free of charge
Notes: Animations:
Images and first text on screen at start.
Click 1 = “Products…” text
Click 2 = “Research…” text
Click 3 = “Reports…” text
Notes:
In addition, it is important to understand the process that one must go through to obtain a research report for a building product.
First, an Acceptance Criteria (ICC-ES ACs) or Evaluation Criteria (IAPMO UES ECs) is established by the industry. Typically this involves academia, manufacturers, building officials and engineers coming to an agreement on the minimum set of standards that a product should be evaluated against in order to be qualified as code compliant in the report.
Then the product must be independently sampled and tested to that criteria.
There are often many optional tests with the criteria. So if a product either didn’t pass or wasn’t tested to that optional test then the research report will not recognize that product for whatever condition that test was qualifying it for.
That is why the research report is a very important document as it will contain the code recognized Conditions of Use for the product.
Research reports are then posted to the code report agencies website and are often made available from the product manufacturer’s website as well.
The biggest value of the code report is that it provides a summary of independent tests the product has been evaluated for and the corresponding ‘Conditions of Use’ it is considered recognized for.

## Slide 17: Anchoring into Masonry
L
2
Notes: Moving on with the show….
We will start by discussing the standard of practice for designing anchors into masonry.

## Slide 18: Anchoring into Masonry
What does the Building Code say?
IBC Chapter 21 – Masonry…
What does the Referenced Standard (ACI 530) say?
ACI 530 contains two chapters that address anchoring into masonry
Chapter 2 – Allowable Stress Design (ASD)
Chapter 3 – Strength Design (SD)
Contains nothing about anchoring into masonry
ACI 530
Notes: Animations:
At start: Question and image of building code on slide.
Click 1= text “Contains nothing about anchoring into masonry”
Click 2= arrow and ACI 530 text and image with second question comes on.
Notes
So to start, let’s take a look at what the building code has to say about anchoring into masonry.
IBC Chapter 21 is titled Masonry.
However, there are no provisions within IBC Chapter 21 that pertain specifically to anchoring into masonry.
IBC makes several references to ACI 530/TMS402/TMS602 (ACI 530).
ACI 530 contains 2 chapters that contain provisions for anchoring into masonry
  Chapter 2 contains information when designing using Allowable Stress Design (ASD)
  Chapter 3 contains information when designing using Strength Design (SD)
Quiz Note
This slide features information that will be found on the post-training knowledge assessment:
SD is an acronym that stands for the phrase:
Stress Design
Strength Design
State Design

## Slide 19: ACI 530: Chapter 2
Section 2.1.4.1:
Contains test design requirements for “anchor bolts solidly grouted in masonry”
  If not designed per 2.1.4.2, design by test is permitted
  Testing shall be done in accordance with ASTM E488
  Allowable loads < 20% of average tested strength
    Safety Factor = 5.0
Notes: Referring to Chapter 2, Section 2.1.4.1 contains test design requirements for “anchors solidly grouted in masonry”
It says that if anchors are not designed per Section 2.1.4.2 then the anchor design is permitted to be based on testing.
The tests shall be done in accordance with ASTM E488 with the exception of a minimum of 5 tests are required instead of only 3.
The “allowable load” of the anchor for design purposes shall not exceed 20% of the average tested strength.
So in other words, this section established that a Safety Factor of 5.0 shall be used when anchoring into “solidly grouted” masonry.

## Slide 20: ACI 530: Chapter 2
Section 2.1.4.2:
Contains design information for plate, headed, and bent-bar anchors”
  Equations for tension and shear
  Calculate “allowable” loads for anchors
Sets precedence for alternate materials
  ASTM E488 testing
  Allowable loads using Safety factor = 5.0
Notes: Notes:
Section 2.1.4.2 contains “design” information for certain anchor types such as those that are ‘cast-in-place’ or grouted solidly into masonry.
For these anchor types, there are equations available to calculate the allowable tension and shear loads.
Although there are no provisions within ACI 530 specific to post-installed anchor products, this section sets the precedence for: 1.) designing anchors based on testing, and 2.) using a Safety Factor of 5.0 when using an alowable stress design approach for anchoring into masonry.

## Slide 21: What does the Research Report and/or Tests say?
Established ACs for masonry anchoring
  AC01 – mechanical expansion anchors
  AC58 – adhesive anchors in CMU
  AC60 – adhesive anchors in URM
  AC70 – power-driven fasteners into CMU
  AC106 – mechanical screw anchors
ACs consider things ASTM doesn’t, such as:
  Serviceability (deflection)
  Special inspection
  Reliability (installation)
  Quality (manufacturing)
Notes: Animations:
On start = “Establishing ACs” text, following bullets, and both images on screen.
Click 1= “ACs consider things…”
Notes:
Since there are no specific provisions for “post-installed anchors into masonry” in either IBC or its referenced standards, let’s look what Research Reports have to say.
There are several Acceptance Criteria for anchor products installed into masonry.
What’s important to note here is that the Acceptance Criteria is often dependent upon the anchor type (expansion, vs. screw anchors, vs. adhesive anchor) as well as dependent upon the type of masonry (grout-filled CMU vs. URM).
In addition, these Acceptance Criteria often consider things that ASTM E488 doesn’t. Things such as:
  Serviceability – deflection limits during testing
  Special Inspection procedures
  Reliability of anchor installation
  Quality of manufacturing process (audits)
These additional things are what differentiates a product with a research report vs. a product with only published test data.

## Slide 22: How to Design Using Anchor Load Tables in CMU
Determine capacity (“allowable load”) for individual anchor
Apply reduction factors for edge distance
Apply reduction factors for anchor spacing
❶
❷
❸
Notes: Notes:
When a research report is issued for an anchor product into masonry, it should contain tables showing the allowable load (tension and shear) for the product depending on where in the wall it is installed (such as top of wall, face if wall, end of wall, etc.).
In some cases, factors are provided to adjust (reduce) the published anchor capacity for nearby edges and nearby spaced anchors.
Depending on other variables, there can sometimes be additional adjustment factors required (such as for in-service temperature, etc.).

## Slide 23: In Summary:
There are no provisions in the building code specific to post-installed anchors
There are no provisions in the referenced standards specific to post-installed anchors
Research reports contain provisions specific to post-installed anchor products
Anchor design is based on Allowable Stress Design approach
Notes: Notes:
So in summary, the current standard of practice for post-installed anchors into masonry is:
  To test the anchor to the most thorough test and evaluation criteria which can be found in an ICC-ES Acceptance Criteria (dependent on anchor type and type of masonry).
  To design the anchor using an “allowable stress design” approach where
    allowable loads include a minimum Safety Factor of 5.0 (not 4.0 like was traditionally done in concrete anchor design)
    Loads are reduced for nearby edges and anchors using published factors
Animations:
First check mark and text on screen at start.
Click 1 = second check mark and text
Click 2 = third check mark and text
Click 3 = fourth check mark and text

## Slide 24: Look for Products with Evaluation Reports for Anchoring into Masonry
Adhesive Anchors
Screw Anchors
Expansion Anchors
Powder-Actuated Pins & Gas-Actuated Pins
Notes: Notes:
Without going into a detail of any product and their features and benefits, some manufacturers offer products that have a research report recognized for anchoring into masonry are shown on this slide.
In addition to summarizing the products code report qualified for masonry anchoring, what’s also important to note on this slide is that the products that appear here may or may not also have code report recognition for anchoring into concrete that we will talk about next.
Always contact the manufacturer’s representative for product specific questions and assistance properly designing with anchor products.

## Slide 25: Look for Products with Evaluation Reports for Anchoring into Masonry
PAT and GAS pin offerings
Titen HD
AT-XP
SET-XP
ET-HP
Strong Bolt 2
Wedge-All
Adhesive Anchors
Screw Anchors
Expansion Anchors
Powder-Actuated Pins & Gas-Actuated Pins
Notes: Notes:
Without going into a lot of detail of each of these products and their features and benefits, the Simpson Strong-Tie products that have a research report recognized for anchoring into masonry are shown on this slide.
In addition to summarizing the Simpson Strong-Tie products code report qualified for masonry anchoring, what’s also important to note on this slide is that the products that appear here may or may not also have code report recognition for anchoring into concrete that we will talk about next.
Always contact the manufacturer’s representative for product specific questions and assistance properly designing with anchor products.

## Slide 26: Anchoring into Concrete
L
3
Notes: Now moving onto anchoring into concrete…

## Slide 27: What does the Building Code say?
IBC Chapter 19 – Concrete
Section 1908 and 1909 contain information specific to anchorage
Notes: Notes:
First we will start by looking at what the building code has to say…
In Chapter 19 we find two sections of the building code related to anchorage to concrete.
Section 1908 covers anchorage using an Allowable Stress Design approach.
The key things to note about this section is that it is said to not apply:
  To anchors installed in hardened concrete (aka, a post-installed anchor), or
  Where load combinations include earthquake loads effects
If either of these exists, then Section 1908 refers the reader to Section 1909
Section 1909 covers anchorage using a Strength Design (SD) approach.
The key things to note about this section is that:
  Certain types of post-installed anchors are addressed in this section,
  Reference is made to ACI 318 Appendix D for the design of anchors covered within the scope of Appendix D, and
  Anchors that are not within the scope of Appendix D shall be designed using Strength Design in accordance with an approved procedure.
As an aside, there are a few other modifications IBC makes to ACI 318 Appendix D in Section 1905. However, many of the modifications in Section 1905 have since been identified as “in conflict” with the 2011 edition of ACI 318 which is referenced by IBC 2012. These identified issues have already been proposed and approved to be included in the IBC 2015. Refer to S.K. Ghosh
**Be sure to discuss the differences between Ultimate Strength Design (USD) and Allowable Stress Design (ASD). USD method is a relatively newer design method based on a more statistical and probabilistic approach than the ASD method.
Quiz Note
This slide features information that will be found on the post-training knowledge assessment:
True or false: With respect to anchor design, the Ultimate Strength Design (USD) method is a relatively newer design method based on a more statistical and probabilistic approach than the Allowable Stress Design (ASD) method.
True
False

## Slide 28: ASD vs. SD
Rn = x – k s (for each failure mode)
Frequency (%)
Ultimate Load (lb.)
Allowable Stress Design (ASD)
Rallow = x / FS
x
Frequency (%)
Ultimate Load (lb.)
x
= dependent on test performance
k = dependent on number of tests
fRn
Rn
ks
fRn
Strength Design (SD)

## Slide 29: ASD vs. SD
≤
≤
Allowable Stress Design (ASD)
Strength Design (SD)
Anchor testing is significantly different (Strength Design is much more complex)
Strength Design considers fluctuation in tests (Allowable Stress Design doesn’t)
Cannot compare anchor capacities to one another (apples & oranges)
Interaction check (demand/capacity) is more of an apples-to-apples comparison
Take-Aways:
Allowable Capacity
S.F
Estimated
Loads (D,L,W,E)

Load
Factors
(1.2,1.6,..)
Charac-
teristic
Capacity
*
Average
Ultimate
Load
(from
Testing)
Design
Strength
Factored
Design
Load
Average
Ultimate
Load
Service
Loads (D+L+…)
Notes: Notes:
This slide is to illustrate the differences between Allowable Stress Design and Strength Design as it relates to post-installed anchor design and testing
The key things to take away from this slide are that:
  Although the Average Ultimate Load is shown as the same grey bar on both SD and ASD, the time, effort and requirements are much more demanding under the SD compared to ASD
  The standard deviation directly affects the anchor’s capacity in SD (not the case in ASD)
  The design of an anchor under SD is more involved and time consuming than ASD
    The approach outlined in the SD method must be performed for each failure mode (typically 7), whereas in ASD the designer performs the approach one time for tension and one time for shear.
  It is very difficult to compared the ASD to SD method due to the many differences between the 2 approaches.

## Slide 30: What does the Referenced Standard (ACI 318 Appendix D) say?
Scope of Appendix D: Applications
Connections between structural elements
Safety-related attachments to concrete
Cast-in-Place Anchors
Post-Installed Anchors
This includes expansion, undercut anchors, and (as of 2011) adhesive anchors.
    Note:
Notes: Notes:
Since IBC references ACI 318 Appendix D, let’s take a look at what it has to say about anchoring into concrete.
Appendix D covers certain anchor applications and certain anchor types.
The applications covered within its scope are
  Connections between structural elements, and
  Safety-related attachments to concrete
The anchor types covered within its scope are
  Cast-in-place anchors
  Post-installed anchors such as:
    Expansion and undercut anchors, and
    Adhesive anchors (2011 edition)
It is worth noting that not every application or every anchor type s covered under Appendix D (such as screw type anchors or powder actuated fasteners). We will come back to this a little later.

## Slide 31: ACI 318 Appendix D
Provides a strength design method for concrete anchoring
Identifies potential anchor failure modes
Provides equations to calculate capacity for each failure mode
Notes: Notes:
To summarize what Appendix D is from a big picture perspective…
  It is a strength design method for designing anchorage into concrete
  It identifies possible failure modes that an anchor might experience if it is acted upon by a tension or shear load.
  It provides equations for one to calculate what capacity is associated with those failure modes.
Animations:
Image of code, first check mark, and text on screen at start.
Click 1 = second check mark and text
Click 2 = third check mark and text

## Slide 32: ACI 318-11 Appendix D Failure Modes & Design Equations
Equations calculate capacity for different TENSION failure modes
Steel Failure
Concrete Breakout
Pullout
Side-face Blowout
Adhesive Bond
Notes: Notes:
This slide it to quickly summarize the failure modes considered by Appendix D
Quiz Note
This slide features information that will be found on the post-training knowledge assessment:
Appendix D gives equations for anchor failure modes. Which of the following is not a tension failure mode for a post-installed anchor?
Steel
Concrete breakout
Pryout

## Slide 33: ACI 318-11 Appendix D Failure Modes & Design Equations
Equations calculate capacity for different SHEAR failure modes
Steel Failure
Concrete Pryout
Concrete Breakout
Notes: Notes:
This slide it to quickly summarize the failure modes considered by Appendix D
Quiz Note
This slide features information that will be found on the post-training knowledge assessment:
Appendix D gives equations for anchor failure modes. Which of the following is not a tension failure mode for a post-installed anchor?
Steel
Concrete breakout
Pryout

## Slide 34: ACI 318 Appendix D
Requires post-installed anchors be tested & qualified per ACI 355 standard
  ACI 355.2 for expansion and undercut anchors
  ACI 355.4 for adhesive anchors
Allows design of anchorage in both uncracked and cracked concrete conditions
Allows design for many different anchor types/configurations by use of equations
  No more tables for reduction factors (edge/spacing)
Notes: Animations:
First check mark and text on screen at start.
Click 1 = second check mark and text
Click 2 = third check mark and text
Notes:
Appendix D requires post-installed anchors to be tested to a new test standard developed by ACI 355.
ACI 355.2 is the standard for mechanical expansion and undercut type anchors
ACI 355.4 is the standard for adhesive anchors
These ACI 355 standards address anchor performance in uncracked as well as cracked concrete conditions.
Based on all of the testing, manufacturers can provide normalized design data for one to design their anchor using the equations of App D. The normalized data allows the data to be used for a number of different conditions (edge, spacing, eccentric loading, etc).
Quiz Note
This slide features information that will be found on the post-training knowledge assessment:
True or false: One of the many tests included in ACI355.2 is a way to test post-installed expansion anchors for cracked concrete.
True
False

## Slide 35: What is “Cracked Concrete”?
Code (ACI 318 and ACI 355) permits up to 0.015” crack width
  Reinforcement controls cracking but does not prevent it
ACI 355 contains tests to evaluate what happens when an anchor is located in the presence of crack
Concrete structures can experience cracking under service loads.
Notes: Notes:
This slide is to make sure everyone understands what is meant by the words “cracked concrete” as discussed within Appendix D.
Even if one designs a concrete structure in accordance with ACI 318, it is still permitted to crack.
According to ACI 318 and ACI 355, the permissible crack widths in a structure can be up to 20/1000ths of an inch. (0.020”)
The ACI 355 test standards (355.2 and 355.4) consider this crack width and measures an anchor’s ability to perform when a crack of this size migrates through the installed anchor location.
Therefore if an anchor were used in an area of the structure where cracking were expected, the codes address this situation and allow one to design and specify and with an anchor product that has been proven to work through testing.

## Slide 36: ACI 355 Test Standard: Table 4.2
Reference tests
Performance under ideal conditions
Service tests
Establishes performance under expected service conditions
Reliability tests
Established reliability under adverse installation conditions
ACI 355 tests are much more extensive!
Notes: Notes:
The tests of ACI 355 are divided into 3 main categories:
  Reference tests
  Service tests
  Reliability tests
The main thing to take away from this slide is that the tests of ACI 355 are far more in-depth and complex than what anchors have been tested to in the past.
The ACI 355 tests measure not only the anchor’s peak load achieved when loaded but it also considers many adverse installation conditions and in-service conditions that were not addressed in previous test standards. Many anchor products that pass the “old” test standard do not perform well and are not able to be qualified under the ACI 355 standard.
Animations:
Boxes with text and graph on slide at start.
Click 1 = “ACI 355 tests are much more extensive” text box appear.

## Slide 37: What does the Research Report say?
Established Acceptance Criteria for concrete anchors
  AC193 – Mechanical Anchors
  AC308 – Adhesive Anchors
AC may include things ACI 355 doesn’t
  Inspections
  Quality (manufacturing)
Notes: Notes:
So we just learned that the building code’s referenced standard (ACI 318) does contain provisions for many post-installed anchor types for anchoring into concrete.
And ACI 318 Appendix D references and requires post-installed anchors be tested and qualified under ACI 355.
In this regard, these products might no longer be considered “alternate materials” per IBC Section 104.11 and accordingly a research report may not be perceived as a requirement.
However, ACI 318 and ACI 355 make several references to a product’s evaluation report. For this reason and others, it is still commonplace for post-installed anchor products covered within the scope of the codes to obtain research reports showing code compliance.
The research report still adds value in that it is an independent recognition of the product’s compliance to the latest standards in the industry.
The most current Acceptance Criteria for anchoring into concrete are:
  ICC-ES AC193 for mechanical anchors
  ICC-ES AC308 for adhesive anchors
These Acceptance Criteria sometime contain additional, more stringent, standards than ACI 355 does. Things like special inspection requirements as well as manufacturing quality requirements.

## Slide 38: Table Comparison
Allowable Stress Design (ASD) Tables
Strength Design (SD) Tables
Chord Deformation (excluding slip)
Panel Deformation & Nail Slip
Chord Splice Slip
Designers will now have to look at several different numbers in order to calculate the anchor’s capacity
    Note:
Notes: Notes:
Without going into too much detail, by taking a quick look at the old & new tables, you can see some of the differences
The first thing you notice is the size of the information.
On the left would be an example of an old ASD Table.
And on the right is an example of a new USD Table.
As shown here, for 3 embedments of a single ½” diameter anchor, there is a lot more information presented in the new table vs. the old table.
Designers will no longer be able to turn to the catalog and pick one number for the anchor’s tension capacity and one for shear, plug into the interaction equation and be done.
Instead they will have to look at several different numbers in order to calculate the anchor’s capacity.
In addition, under the new method there will no longer be any spacing and edge distance Load Reduction Factors as was published when designing under the Allowable Stress Design method.

## Slide 39: How to Design Using Anchor Tables in Concrete
Refer to Appendix D equation for each failure mode
Reference ACI 355 product testing to plug into equations where appropriate
Notes: Notes:
The designer must use the anchor product published performance data in combination with the ACI 318 Appendix D equations in order to complete the design.

## Slide 40: In Summary
Provisions are in the building code specific to some post-installed anchor types
Provisions are in the referenced standards specific to some post-installed anchor types
  Establish design and test requirements
Research reports still exist
  Shows independent recognition of product as code compliant
Anchor design is based on Strength Design approach
Notes: Notes:
So in summary, the current standard of practice for post-installed anchors into concrete is:

## Slide 41: Look for Products with Evaluation Reports for Anchoring into Masonry
Adhesive Anchors
Screw Anchors
Expansion Anchors
Powder-Actuated Pins & Gas-Actuated Pins
Notes: Notes:
Without going into detail of each of these products and their features and benefits, some examples of products that have a research report recognized for anchoring into concrete are shown on this slide.
In addition to summarizing the products code report qualified for masonry anchoring, what’s also important to note on this slide is that the products that appear here may or may not also have code report recognition for anchoring into masonry that was shown on a previous slide.
Always contact the manufacturer’s representative for product specific questions and assistance properly designing with anchor products.

## Slide 42: Look for Products with Evaluation Reports for Anchoring into Masonry
Adhesive Anchors
Screw Anchors
Expansion Anchors
Powder-Actuated Pins & Gas-Actuated Pins
AT-XP
SET-XP
ET-HP
Strong Bolt 2
Wedge-All
Titen HD
PAT and GAS pin offerings
Notes: Notes:
Without going into a lot of detail of each of these products and their features and benefits, the Simpson Strong-Tie products that have a research report recognized for anchoring into concrete are shown on this slide.
In addition to summarizing the Simpson Strong-Tie products code report qualified for masonry anchoring, what’s also important to note on this slide is that the products that appear here may or may not also have code report recognition for anchoring into masonry that was shown on a previous slide.
Always contact the manufacturer’s representative for product specific questions and assistance properly designing with anchor products.

## Slide 43: Properly Specifying Post-Installed Anchor Products
Notes: Although this might seem overwhelming from how you’re currently designing and specifying adhesive anchors, we might be able to help you start specifying products to meet these newer codes.

## Slide 44: Suggested General Note for Code Compliant Anchors
Refer to handout:
Addresses all post-installed anchor types (not just adhesive anchors)
Addresses anchoring into many different base material types (not just concrete)
Allows post-installed anchors to be used only when specified on the plans or when/where the contractor gets approvals from the EOR
Requires the contractor to contact the manufacturer’s rep for initial installation training
Lists all the latest test criteria required in order for an anchor to be considered for use on the job
Classifies and “approves” anchor products based on anchor types and base material
Encourages one product be used as the design basis for the job and allows contractor to submit alternate products so long as they submit documentation showing that submitted product meets the design basis product
Notes: Notes:
This note is very useful in that it:
Addresses all post-installed anchor types
Addresses anchoring into many different base material types
Allows post-installed anchors to be used only when specified on the plans or when/where the contractor gets approvals from the EOR
Requires the contractor to contact the manufacturer’s rep for initial installation training
Lists all the latest test criteria required in order for an anchor to be considered for use on the job
Classifies and “approves” anchor products based on anchor types and base material
Encourages one product to be listed as the design basis for the job and allows contractor to submit alternate products so long as they submit documentation showing that submitted product meets the design basis product.

## Slide 45: Any Questions?

## Slide 46: Course Completion
Simpson Strong-Tie
This concludes the continuing education course.
For a library of Simpson Strong-Tie courses,
visit strongtie.com/workshops
Notes: Do
Draw the meeting to a close. Hand out literature and business cards.
Say
If you have ongoing projects that you would be interested in reviewing together, please let me know.

## Slide 47: Next Steps!
AIA: For those seeking AIA LU/HSW: You will receive an email with a link allowing access to print your Certificate. Congratulations, you will have earned 1 LU/HSW credit. If your AIA member number has been inserted into your profile, Simpson Strong-Tie will report your credits on your behalf to the AIA. No test is required in order to receive HSW credits.
IACET: For those seeking IACET CEUs: You will receive an email with a link allowing access to print your Certificate of Attendance and instructions directing you to the Simpson Student Center to take the exam before credits can be awarded. Once the exam is taken and passed, you will have earned 0.1 CEUs (1 hour of credit). You can then access your Certificate of Completion from the Course Content tab. You must self-report your credits to your certifying organization or agency.
If you have questions or need assistance, please contact training@strongtie.com.
Notes: Notes:
(Review the email and notification process as outlined in this slide).
Watch for an email directing you to the Student Center to print your certificate.
No test is required for AIA credit.
For those seeking CEUs after you have passed the test, you may access your Certification of Completion from the course content tab.
For those that want AIA HSW credit, be sure to provide your AIA number on the sign-in sheet and Simpson will report your credits to the AIA on your behalf.
For those seeking IACET credit, after taking and passing the test, you must self-report your credits to your certifying organization or agency.

## Slide 48: Next Steps!
ICC: For those seeking ICC CEUs: You will receive an email with a link allowing access to print your Certificate. Congratulations, you will have earned 0.1 ICC CEU (1 hour of credit). Please make sure your ICC member number has been inserted into your profile. It is your responsibility to self-report your credits to the ICC. Please retain your Completion Certificate for your records.
IACET: For those seeking IACET CEUs: You will receive an email with a link allowing access to print your Certificate of Attendance and instructions directing you to the Simpson Student Center to take the exam before credits can be awarded. Once the exam is taken and passed, you will have earned 0.1 CEUs (1 hour of credit). You can then access your Certificate of Completion from the Course Content tab. You must self-report your credits to your certifying organization or agency.
If you have questions or need assistance, please contact training@strongtie.com.
Notes: Presenter Notes:
Review the email and notification process as outlined in this slide.
Watch for an email directing you to the Student Center to print your certificate.
No test is required for ICC credit. You must self-report your credits to ICC.
For those seeking general IACET CEUs after you have passed the online test, you may access your Certification of Completion from the course content tab. You must self-report your credits to your certifying organization or agency.