## Slide 1
PLEASE READ
Dear Instructor,
This presentation is available in both AIA and ICC versions.
For AIA: Right click and un-hide slides 5 and 62
For ICC: Right click and un-hide slides 6 and 63
Slide 2 is an optional slide

## Slide 2: Welcome!
We will begin in a few minutes.
Please be sure to sign the registration form to receive credit for attending today’s learning event.
Notes: Do
Meet and greet participants as they arrive. Start learning names, make them feel comfortable and settled in the training environment.
Be sure to pass out handouts – participants will need them to reference the code
Additional Presenting Tips:
Make sure your opening has PUNCH:
Promotes interest and enthusiasm for the session
Understands participants’ needs
Notes ground rules and administrative/housekeeping needs, for example will there be a break?
Clarifies expectations
Help everyone get to know each other
State your expectations around participation: Make it known and expected that you will be encouraging and inviting participation.
Tips to facilitate connections:
Thank participants for their contribution (ideally with their name)
Praise participation (especially the first person to speak)
Express confidence in the participants
Restate what someone said earlier (“As John mentioned earlier….”)
If someone asks a question, ask a participant to answer: this engages the experts and invites conversation
Physical Room / Training Venue Setup:
If using a table arrangement, consider grouping 4 to 6 students at each station. This will help encourage conversation and discussion during activities.
Get people standing at regular intervals during your training session. Research shows that people learn up to 15% more when standing up!

## Slide 3
AIA Provider: 50119826 | AIA Course: AIA-CFR10118 | ICC Provider: 1025 | ICC Course: 15772
Instructor Name
Position / Title
Notes: Do
Be sure to mention the AIA provider and course number for those requiring AIA credit. Ask the attendees to write down this information for reference. For AIA members, we will submit this information for them.

## Slide 4: Credit Information
IACET Accreditation Information
Simpson Strong-Tie® has been accredited as an Authorized Provider by the International Association for Continuing Education and Training (IACET). As a result of their Authorized Provider accreditation status, Simpson Strong-Tie® is authorized to offer IACET CEUs for its programs that qualify under the ANSI/IACET Standard.
This course offers 0.1 CEU (1 hour of credit).
Notes: Review the submission process for audiences requiring IACET CEU credits.
For those seeking IACET credit, they must take and pass the online test. They must self-report CEU credits to their certifying organization or agency.
Explain the credits awarded: IACET: 0.1 (Equivalent to 1 hour) CEUs.

## Slide 5: Credit Information
AIA Member Information
This course is registered with AIA CES for continuing professional education. As such, it does not include content that may be deemed or construed to be an approval or endorsement by the AIA of any material of construction or any method or manner of handling, using, distributing, or dealing in any material or product. Upon completion of this course, Credit(s) earned will be reported to AIA CES for AIA members who pass the course and have entered their AIA member number on their Simpson profile page. A link to the Certificate of Completion will be available upon completion of this course. Only AIA LU/HSW will be reported.
This course offers 1 LU/HSW credit.
AIA Course Number: AIA-CFR10118
Notes: Presenter Information
NOTE: Please be sure each attendee LEGIBLY signs the event sign-in sheet.
Say
All questions concerning proprietary products will be addressed after the conclusion of the AIA portion of the presentation. The meeting format is 50 minutes of content, followed by 10 minutes of Q & A.
Do
Explain the credits awarded for:
AIA: 1LU/HSW credit.
IACET: 0.1 (Equivalent to 1 hour) CEU credits.
Review the submission process for audiences requiring either AIA LU/HSW (health, safety and welfare) credits or CEU credits:
For those seeking AIA HSW credit, there is no test required. AIA members must be sure to provide their AIA member number on the sign-in sheet. Please make sure name, email and AIA member number are clearly printed so Simpson can report credits to the AIA on their behalf.
For those seeking IACET credit, they must take and pass the test. They must self-report CEU credits to their certifying organization or agency.

## Slide 6: Credit Information, cont.
ICC Member Information
This course has been approved by the International Code Council (ICC) for continuing professional education. For learners that complete this course, it is your responsibility to self-report your credits to the ICC. Please retain your Completion Certificate for your records.
Be sure that your ICC ID number is provided on the sign-in sheet or in your Simpson profile in order to have it displayed on your certificate.
This course offers 0.1 CEU (1 hour of credit).
ICC Course Number: 15772
Notes: Review the submission process for audiences requiring ICC CEU credits.
For those seeking ICC credit, there is no test required. ICC members must provide their ICC ID number on the sign-in sheet or in their Simpson profile in order to have it displayed on their certificate. It is the responsibility of the participant to self-report their credits to the ICC. Ask them to retain their Completion Certificate for their records.
Explain the credits awarded: ICC: 0.1 (Equivalent to 1 hour) CEUs.

## Slide 7: Additional Credit Offerings
Visit
strongtie.com/workshops
for more information
Course Name | CEUs | AIA | ICC
Introduction to Deck Design | 0.1 | ✔ | ✔
Introduction to Wind Design and the Wood Frame Construction Manual | 0.1 | ✔ | ✔
Shear Walls and Lateral Bracing in Light Frame Construction | 0.1 | ✔ | ✔
Understanding Restraint Rod Systems | 0.1 | ✔ | ✔
Cracking the Concrete Anchor Codes | 0.1 | ✔ | ✔
Concrete Deterioration | 0.1 | ✔ | ✔
Moment Frame Design | 0.1 | ✔ | ✔
Introduction to Wind Code Provisions and Meteorological Concepts | 0.1 | ✔ | ✔
Wind Design in Accordance with ASCE 7-10 | 0.1 | ✔ | ✔
Wood Framed Seismic Design 1: Code Provisions, Design Parameters | 0.1 | ✔ | ✔
Notes: Do
Explain that we have additional PK topics available that offer credit for ICC members and HSW credits for AIA members.
Explain that we have a library of online courses available in our Simpson Student Center that also offer ICC and AIA HSW credits. They can access our online courses at strongtie.com/workshops.

## Slide 8: Course Description
Code Requirements for Conventionally Framed Roofs
We created this course to help familiarize Building Officials, Inspectors and Builders with code-compliant stick-framed roof systems using the 2015 IRC requirements.
Course Contents
Introduction / Learning Objectives
Roof Basics and Terminology
Code Requirements for Conventionally Framed Roofs
Questions and Wrap-up
Notes: Say:
Welcome to Code Requirements for Conventionally Framed Roofs. This is a technical course intended for Builders, Building Officials and Inspectors interested in code requirements for stick-framed roofs. This course reviews Chapter 8 of the International Residential Code (IRC) as it applies to conventionally framed roofing.
Note: After the accredited course is complete, there is a Stronger Roof Solutions PK available at the end of the deck.

## Slide 9: Learning Objectives
Upon completion of this seminar, you will be able to:
Identify correct application of IRC building codes for conventionally framed roof construction, also known as stick framing
Recognize the relationship between critical connections and there role in building a stable roof, such as the rafter/joist connection
Describe basics of conventional roof framing such as, hip and valley rafters, ridge boards and ridge beams and correct application of rafters, joists and other members
Notes: Do
Review the learning objectives for the course.
Inform students that the assessment questions will be based on these learning objectives. Slides that contain information relevant to the test have an orange graduation cap located in the bottom-left corner.

## Slide 10: IRC Chapter 8 Roof-Ceiling Construction
SECTION R802 Wood Roof Framing
  Grade mark, size, and identification
  Design and Construction
    Framing details
    Ceiling joist/rafter connections
    Ceiling joists lapping
  Fastening requirements
  Ceiling joist and rafter span
  Bearing
  Cutting & notching
  Lateral support
  Bridging
  Framing of openings
10. Wood Trusses
11. Roof Tie-Down
Notes: Say: The International Residential Code (IRC) and the International Building Code (IBC) define guidelines for building conventional light-frame wood structures without the need for engineering analysis of each component. This is known as prescriptive framing.
This course focuses on the IRC, Chapter 8, Section R802. The building codes address several requirements for Conventionally Framed Roof Construction. Today we’ll be focusing on the parts of the code that are required for conventionally framed roofs as relevant for Building Inspectors, Building Officials and Builders.
For more information on Conventional Light-Frame Construction please see Section 2308 in the IBC.

## Slide 11: Truss Assembly vs. Stick Framed Roof Construction
Stick-Frame Roof System
Work completed on site to prescriptive requirements
Space within the structure can be used for storage or living
Truss Roof System
Engineered building component designed for specific project
Quick Installation
Consistent quality control
Notes: Say: To start, let’s look at the two most common types of wood roof construction: Truss and Stick-Framed Systems.
Stick-Framed Systems consist of repetitive rafters and ceiling joists. Truss Roof Systems use prefabricated trusses placed at a prescribed spacing. Both approaches are widely used today. Stick framing has been around the longest - however, 4 out of 5 new homes built in the U.S. use truss construction.
Each type of roof construction has pros and cons. One main difference is that stick framing is done onsite, and trusses are made at a component manufacturer in a controlled environment. This means that stick framing has less lead time since trusses have to be ordered from the factory. However, since trusses are made at the factory they can be installed quickly and quality control is very consistent.
Our course focuses on stick framed construction.

## Slide 12: Hip and Valley Rafters
Valley and hip rafters are load bearing structural members.
Hip rafters are on the edge, which is called the “hip”
Valley rafters are located where two adjacent sloping surfaces of the roof meet
Notes: Say: One benefit of conventionally framed roofs is more flexibility of the roofline, this system allows for more complex framing.
Valley rafters follow the line of the valley where two perpendicular sides of the roof meet. Valley rafters are structural members, which need to be deeper than common rafters because they support a greater load and to provide full bearing for the rafter ends (jack rafters). **Note the large shaded area of the roof that the single valley rafter supports.
Hip rafters form the angles at the junction of inclined planes of the roof. Hip rafters attach to a ridge and the brace lands on a wall.
Do: Point out valley, hip and common rafters and area of load supported by valley rafter
Test Question
Valley Rafters are structural members that need to be deeper than common rafters are because they are load bearing and need to provide full bearing for the rafter ends.
True
False

## Slide 13: Ridge Board and Ridge Beams
Ridge Beam
Structural member: supports weight of rafters
Must be specifically designed for project
Ridge Board
Held up by rafters
Does not support weight of rafters, force is from the opposing rafters
Can be 1-by since non-structural
Notes: Say: At its most basic, a ridge board is held up by the rafters, and a ridge beam holds up the rafters.
The ridge beam is a structural member which supports the weight of the rafters. The beam needs to be specifically designed for the project.
The ridge board is a non-structural member where the rafters meet and are fastened to the board. The ridge board does not support the weight of the rafters, they are held up by the force of the opposing rafters. The board provides a nailing surface and can be a 1-by since it is non-structural.

## Slide 14: R802.2
The framing details required in Section R802 apply to roofs having a minimum slope of three units vertical in 12 units horizontal (25-percent slope) or greater. Roof-ceilings shall be designed and constructed in accordance with the provisions of this chapter and Figures R606.11(1), R606.11(2) and R606.11(3) or in accordance with AWC NDS. Components of roof-ceilings shall be fastened in accordance with Table R602.3(1).
1
Notes: Say: Here is the first code section. You can reference the code in the handout. Each section has a reference number so participants can easily follow. This code section is labeled as one and corresponds to the code section labeled as one in the handout.
Framing details apply to roofs with a minimum slope of 3:12
Mid-section focuses on concrete and masonry which we don’t focus on in this course.
Components of roof-ceilings will be fastened in accordance with Table R602.3.(1) which we will review later in the course

## Slide 15: Design and Construction
When roof slope is lower, ridge and rafters work like a joint, instead of a stable structure.
3:12
R802.2
Framing detail apply to roofs with a slope over 3:12
Roof with higher slopes create a more stable shape
Rafters on lower sloped roofs can not hold up the ridge, and the ridge acts like a joint
Notes: Say: The framing details to follow apply to roofs that have a slope over 3:12.
The reasons for this restriction are:
Roofs with higher rafter slopes and parallel joists are built to be a rigid triangle.
As the roof gets lower, the rafters no longer hold the ridge up; the ridge becomes more flexible like a joint. This changes the dynamics to make the lower slope not fit the prescriptive requirements.
Do: Discuss bullets one and two. On bullet three, CLICK to show joint action.

## Slide 16: Hanger Slope and Skew Calculator
Some manufacturers offer web tools to help determine the slope and skew.
Slope and skew calculator applications are useful tools for defining the direction and precise angles for framing members and connectors.
Notes: Say: Any general search will give you options for web tools that will help you determine the slope and skew.

## Slide 17: R802.3 Framing Details
Rafters shall be framed not more than 1½-inches offset from each other to ridge board or directly opposite from each other with a gusset plate as a tie.
Ridge board shall be not less than 1-inch nominal thickness and not less in depth than the cut end of the rafter.
2
Notes: Do: Point out as needed that the code is listed in the handout.
Rafters should be framed not more than 1 ½ inches offset
Ridge board shall not be less than 1 inch nominal thickness

## Slide 18: Framing Details: Ridge Board
R802.3
Ridge Board
Ridge board shall not be less in depth than the cut end of the rafter.
Rafters shall be framed not more than 1½" offset from each other
Ridge Board
Notes: Say: The ridge board is a non-structural member that keeps the opposite ends of the rafters in place. The rafters push against each other and keep the roof shape stable.
Ridge boards shouldn’t be less in depth than the end of the rafter.
Image on right shows the WRONG way. Rafters should not be more than 1 ½ inches offset. When the rafters are set too far apart it creates very weak construction.
Test Question
Roof systems are made with repetitive rafters and joists and should not be offset more than:
24 inches
18 inches
5 inches
1 ½ inches

## Slide 19: R802.3 Framing Details
At valleys and hips there shall be a valley or hip rafter not less than 2-inch nominal thickness and not less in depth than the cut end of the rafter.
Hip and valley rafters shall be supported at the ridge by a brace to a bearing partition or be designed to carry and distribute the specific load at that point.
Where the roof pitch is less 3:12 units horizontal structural members that support rafters and ceiling joists — such as ridge beams, hips and valleys — shall be designed as beams.
2
Notes: Say: The IRC requirements for hip and valley rafters are:
Valley and Hip rafters should be at least 2 inches thick
Hip and valley rafters should be supported by a brace to a bearing partition or be designed to carry a specific load at that point
If the roof is less than 3:12 all members that support rafters and ceiling joists should be designed as beams

## Slide 20: Framing Details: Valley and Hip Rafters
R802.3
Nominal thickness of 2 inches
Not less depth than the cut end of the rafters
Valley Rafter
Notes: Say: As opposed to “non-structural” ridge boards, valley rafters are structural members. As a structural member, they need to be deeper than rafters because they support more load and provide full bearing for the rafter tails. Note: here the valley is deeper than the cut-end of the jack rafter.

## Slide 21: Framing Details: Valley and Hip Rafters
R802.3
Hip and valley rafters are load bearing, structural members
Hip Jacks can benefit from additional support from manufactured components
Notes: Say: On the right a hip rafter is shown. Hip rafters are structural members as well, supporting smaller hip jack rafters. These installations can be difficult because the rafter is angled, because of this manufacturers provide sloped and skewed hanger connectors. Since the hip is supporting the hip jacks, consider additional support for hip jack connections.

## Slide 22: Framing Details: Valley and Hip Rafters
R802.3
Supported by a brace to a bearing partition or be designed to distribute load
Notes: Say: Hip and valley rafters should be supported by a brace to a bearing partition or be designed to carry a specific load at that point.
Hip rafters need to have braces at the upper ends, if this is not possible then an engineered connection is required to the supported ridge beam.
Connecting hip and valley rafters to ridge beams can be challenging. In some cases, attaching multiple members to the end of the ridge would require so many nails it could cause the ridge to split.

## Slide 23: Framing Details: Ridge Beam
R802.3
Where the roof pitch is less 3:12 structural members will be designed as beams.
Ridge Beam
Notes: Say: When the roof pitch is low, the rafters act as a simple span between the exterior wall and the ridge, so the rafter must be supported on both ends. The ridge beam is a structural member supporting the rafters.
What makes a ridge or rafter into a beam? Beams are thicker members and must designed for the project. They are structural members that carry loads and in this case transferring the loads to post or walls.

## Slide 24: R802.3.1 Ceiling Joists and Rafter Connections
Ceiling joists and rafters shall be nailed to each other in accordance with Table R802.5.1(9), and the rafter shall be nailed to the top wall plate in accordance with Table R602.3(1).
Ceiling joists shall be continuous or securely joined in accordance with Table R802.5.1(9) where they meet over interior partitions and are nailed to adjacent rafters to provide a continuous tie across the building when such joists are parallel to the rafters.
3
Notes: Say:
The IRC used to only require three nails from ceiling joist to rafters. But now that connection is a designed connection, listed in Table 802.5.1(9). In addition any laps and parallel ceiling joists that are fastened to the rafters are nailed with the same fastening. Other rafter-ceiling connections are listed in Table R602.3(1).

## Slide 25: Framing Details: Continuous Tie
R802.3.1
Ridge Board
Rafter
Joist
compression
tension
Notes: Say: Critical connections in the rafter system are the joist to rafter and joist to joist combination. These connections create a continuous tie.
The rafters and ceiling joists act as a rigid triangle — which is the most stable shape. This design withstands the rafter thrust that can happen when environmental or live loads are applied, such as people or snow.
Here’s what happens with rafter thrust.
Do: CLICK to show rafter thrust detail
Say: The rafters can push out from the walls and sag. To avoid this you need the tension tie created when the rafter/joist are properly fastened.

## Slide 26: Fastening Table R802.5.1(9)
Notes: Say: Newer requirements require a lot more nails to fasten joists to rafters and joist to joist lap connections. The connection between the rafter and joist is prescribed in Table R802.5.1(9)
Do: CLICK once – shading will highlight nailing
Say: In this example, a 7:12 roof slope with rafters spaced 24” o.c., with a 20 psf ground snow load (that is the minimum) will require nine 16d common nails for fastening the rafter to the joist.
There are a few challenges with this.
It’s a lot of nails
It requires 16d nails which are different from the other nail requirements to be used
Do: Ask how participants are handling this nailing requirements

## Slide 27: Fastening Table R602.3.1
Notes: Say: The joist rafter connection requirement includes:
No. 2 Table R602.3.1 nailing for joist to top plate
No. 4 Table: R802.5.1(9) table from previous slide specifies joist/rafter connection
No. 6 Table R602.3.1 nailing for rafter to top plate

## Slide 28: Rafter and Joist Fastening Connection
Table R602.3.1*
Three 10d nails rafter to plate
Two on one side, one on the other
Table R802.5.1(9)
Face nailing of Rafter to Joist
Using nine 16d nails
Table R602.3.1
Four 8d nails ceiling joist to top plate connection
*Footnote i
The toe nail on opposite side of rafters is not required when there is a parallel joist/rafter connection.
Notes: Say: This is what joist/rafter fastening requirement looks like for our parameters of:
7:12 pitch
36 ft span
Table 802.5.1.(9) requires nine 16d nails. Table R602.3.1 requires three nails from rafter to top plate. In addition, four nails are required for the ceiling joist to top plate connection.
Do: Click to show Footnote i., and removal of third nail.
Say: According to footnote i. the inside nail is not required when there is a parallel joist/rafter connection.

## Slide 29: What’s Wrong with this Picture?
Notes: Do: Ask class for opinion on image. Then CLICK to highlight offset rafters
Say: Do you see anything wrong with this construction? There can’t be a continuous tie because rafter and joists aren’t fastened together.
When rafters and joists are offset — we don’t make the joint/rafter connection.
As the roof doesn’t have a continuous tie, it is a less safe structure.

## Slide 30: Table R802.5.1(9) Footnotes
The following are exceptions to the nail requirements:
a. 40d box nails shall be permitted to be substituted for 16d common nails.
b. Nailing requirements shall be permitted to be reduced 25 percent if nails are clinched. (the pointed ends of nails are bent over)
c. Heel joint connections are not required when the ridge is supported by a load-bearing wall, header or ridge beam.
d. When intermediate support of the rafter is provided by vertical struts or purlins to a load bearing wall, the tabulated heel joint connection requirements shall be permitted to be reduced proportionally to the reduction in span.
e. Equivalent nailing patterns are required for ceiling joist to ceiling joist lap splices.
f. When rafter ties are substituted for ceiling joists, the heel joint connection requirement shall be taken as the tabulated heel joint connection requirement for two-thirds of the actual rafter-slope.
Notes: Say: If that nine nail requirement sounds bad, there is some good news. The good news is that footnotes allow from some reductions.
On the next slides we will focus on d, e and f.
Mention a.b.c. (optional)
Option to substitute 40d nails for 16d nails
Nails can be reduced by 25% if they are clinched
Heel joint connections are not required when the ridge is supported load-bearing wall, header or ridge beam

## Slide 31: Table R802.5.1(9) Footnote: d
Table R802.5.1(9)
Footnote d. allows for a reduction in the nailing
Intermediate support provided by purlins or vertical struts allows a reduction in span
Notes: Say: Purlins or vertical struts reduce the nailing on the rafter/joist and joist to joist lap connections, because it shortens the span value in the table. If you have a purlin at 10 ft. for a 24 ft. span, you can reduce the fastening to 14 ft.

## Slide 32: Ceiling Joists Lapped
Table R802.5.1(9)
Footnote e. lapped joists have the same nailing requirement as the rafter/joist connection.
R802.3.2
Where ceiling joists are
providing resistance to rafter thrust, lapped joists shall be nailed in accordance with R802.5.1(9).
Notes: Say: The joist-to-joist splice over walls also has to be fastened with the same requirements as the joist rafter connection. In our example that would be nine nails.
R802.3.2 states where ceiling joists are providing resistance to rafter thrust, lapped joists shall be nailed in accordance with R802.5.1(9)
Ceiling joists that are parallel to and attached to rafters require lap splices nailed per Table R802.5.1(9). Perpendicular joists that do not resist thrust can be nailed in accordance with R602.3.1.

## Slide 33: Table R802.5.1(9) Footnote: h
Table R802.5.1(9)
Footnote h. Tabulated heel joint connection requirements assume that ceiling joists or rafter ties are located at the bottom of the attic space. Where ceiling joists or rafters are located higher in the attic, heel joint connection requirements shall be increased as follows:
Rafter Tie
Notes: Say: This code requirement applies to the fastening on rafter ties. Rafter ties are installed in the lower thirds of the attic space when you do NOT have a tension tie along the base. This requirement is the joist and rafter connection listed in Table R802.5.1(9) multiplied by the factor above.
For example, 1/6 of the way up results in a requirement to increase that fastening by 1.2. If we apply this to our previous fastening requirement of nine nails the requirement would increase to eleven nails.
Rafter ties should not be confused with collar ties which are positioned in the upper third of the rafters.

## Slide 34: R802.3.1 Rafter Tie
Where ceiling joists are not connected to the rafters at the top wall plate, joists connected higher in the attic shall be installed as rafter ties, or rafter ties shall be installed to provide a continuous tie.
Rafter ties will not be less than 2 inches by 4 inches, installed in accordance with the connection requirements in Table R802.5.1(9), or equivalent capacities shall be provided.
3
Notes: Do: Continuing with R802.3.1 To meet the IRC code requirements:
When there are no joists at the top plate, joists are installed in the lower third of the rafter as rafter ties.
Rafter ties are in tension and provide a continuous tie
Rafter Ties will not be less than a 2 x 4 and installed with the connections requirements in Table R802.5.1(9)

## Slide 35: R802.3.1 Ceiling Joists and Rafter Connections
R802.3.1
Joists need to make a tension connection across beams when rafters and joist are parallel
Use straps and/or sheathing to create a continuous tie
Hangers alone do not provide a tie
Notes: Say: When joists do NOT span the entire length of a roof they do NOT create a continuous tie, unless they are fastened or connected together. Note: the joists are in tension. There has to be a tension connection across the beam — which means adding another method, such as straps over the top or sheathing, to transfer the tension across the beam. Hangers alone do not help provide a continuous tie because they are not rated for tension.

## Slide 36: R802.3.1 Rafter Tie
R802.3.1
Ceiling joist and rafter ties prevent walls from spreading under downward loads
Joists that are not installed at the plate level are Rafter Ties
Rafter Ties are used to transfer tension across ceiling
Notes: Say: When joists are not at top plate, rafter ties are used to transfer tension force across the ceiling. The joist may be the rafter tie when it is installed above the plate level.
Do: CLICK to show onsite photo
Test Question
Rafter ties are in_____________ when they are installed between rafters.
Compression
Tension
Reduction

## Slide 37: R802.3.1 Rafter Tie
R802.3.1
Rafters with perpendicular joists require a Rafter Tie
Spacing is now the same as rafters at a maximum of 24”
Rafter ties are located in the lower third of attic space
Rafter Ties
24
Notes: Say: Rafters with perpendicular joists require a rafter tie in order to resist thrust. Rafter ties are positioned across the joist. The code allows rafter ties to be raised up to 1/3 the total vertical height of the roof.
The older fastening table required spacing at 4 feet o.c.; now they need to be spaced 24 in. o.c., the same as the rafters are spaced. Rafter ties should not be less than 2 by 4.
Test Question
A joist located in the lower third of the attic is called a _________.
collar tie
rafter tie
hip rafter

## Slide 38: Continuous Tie Examples
Ties spaced > 48” o.c and not adequately connected to outlook
Lookout
Straps
R802.3.1
Lookout nailed to rafters
Metal straps connects lookouts to joists across floor
Notes: Say:
Even if the joists are perpendicular, you can still create a continuous tie. This image shows a lookout has been added. To create a continuous tie with this configuration you can use metal straps across joists. Nail straps will have equivalent nailing with Table R802.5.1(9)
Do: Point out the lookout, metal straps
CLICK to show photo of jobsite, Ties are spaced to far apart and not adequately connected to lookout.

## Slide 39: R802.3.1 Ridge Beam and Collar Ties
Where ceiling joists or rafter ties are not provided, the ridge formed by these rafters shall be supported by a wall or girder designed in accordance with accepted engineering practice.
Collar Ties or ridge straps to resist wind uplift shall be connected in the upper thirds of the attic space in accordance with Table R602.3.1.
Collar ties shall be not less than 1 inch by 4 inches, spaced not more that 4 feet o.c.
3
Notes: Do: To meet the IRC code requirements:
When there are no ceiling joists or rafter ties, the ridge must be supported by a wall or girder (ridge beam)
Collar ties or ridge straps to resist wind uplift are installed in the upper thirds in accordance with Table R602.3.1
Collar ties can not be less than 1 x 4 and spaced 4 feet o.c.

## Slide 40: R802.3.1 Ridge Beam
R802.3.1
When rafter or collar ties are not provided the ridge must be supported by an engineered wall or girder
Ridge beams are structural members
Notes: Say: To meet the IRC code requirements, when there are no ceiling joists or rafter ties, the rafters must be supported by a wall or girder, which is also called a ridge beam.
As we have discussed, there is a prescriptive code for roofs that are less than 3:12 that requires a ridge beam, also known as a girder. Ridge beams can be used for roofs with higher slopes - for example, in a cathedral ceiling. The ridge beam is a structural member supporting the rafters.
If there are no rafter or collar ties, then the ridge must be supported. This stops the top of the rafter from moving down protecting against thrust and allows the loads to be transferred down through the structure.

## Slide 41: R802.3.1 Collar Ties
R802.3.1
Collar ties or ridge straps to resist wind uplift shall be connected in the upper third of the attic space in accordance with Table R602.3(1). Collar ties shall be a minimum of 1-inch by 4-inch (nominal), spaced not more than 4 feet on center.0
Ridge Strap
Notes: Say: No longer just in high wind regions, all regions must use a collar tie or ridge strap to resist wind uplift. Joists and rafter ties are intended to keep the rafters from spreading. Collar ties, which are in the upper third, keep rafters from coming apart at the top. They do not provide a continuous tie.
Test Question
A collar tie is a joist that is placed anywhere in the attic area.
True
False

## Slide 42: Allowable Ceiling Joist Spans
4
Spans for ceiling joists shall be in accordance with Tables R802.4(1)
and R802.4(2).
Table R802.4(1) for uninhabitable attics without storage (Live Load = 10 psf)
Table R802.4(2) for uninhabitable attics with limited storage (Live Load = 20 psf)
For other grades and loading conditions refer to AF & PA Span Tables for Joists and Rafters.
Measure joist span horizontally from the (interior of) exterior wall.
Notes: Say: The IRC code for allowable ceiling joist spans has two tables, R802.4 (1) and R802.4(2). The tables determine the maximum unsupported horizontal distance that ceiling joists can span.
Joist are measured along the span of the joists, to the interior of the walls. For other grades, species and loading conditions refer to the American Wood Council Span Tables for Joists and Rafters.
Do: Click to show table
Say: R802.4 (1) and R802.4(2) are similar in the types of wood and sizes listed, but cover different allowable loads to allow for the weight of attic storage. Lumber is listed by species and grades. All lumber species have different material properties, for example southern pine is much stronger and stiffer than spruce. The maximum span will reflect this.

## Slide 43: Allowable Rafter Spans
5
Tables R802.5.1(1) to R802.5.1(8)
Roof LL=20 psf, ceiling not attached to rafters
Roof LL=20 psf, ceiling attached to rafters
Ground snow load = 30 psf, ceiling not attached to rafters
Ground snow load = 50 psf, ceiling not attached to rafters
Ground snow load = 30 psf, ceiling attached to rafters
Ground snow load = 50 psf, ceiling attached to rafters
Ground snow load = 70 psf, ceiling not attached to rafters
Ground snow load = 70 psf, ceiling attached to rafters
Measure rafter span from (interior of) exterior wall to ridge board. Check requirements in applicable table based on loads.
Notes:   Say: Select the size, span and spacing of rafters relative to the roof design from Tables R802.5.1(1) to R802.5.1(8)
Measure common rafter spans horizontally, beginning at the (interior of) exterior wall and ending at the ridge board. Measure jack rafter spans horizontally, beginning at the hip or valley rafter and ending at the ridge board. Do not measure rafter spans along the actual length of the rafter.

## Slide 44: Table R802.5.1(1) Footnote
The tabulated rafter spans assume that ceiling joists are located at the bottom of the attic space or that some other method …….such as rafter ties is provided at that location. Where ceiling joists or rafter ties are located higher in the attic space the rafter spans shall be multiplied by the following factors:
Notes: Say: Allowable rafter spans assume that ceiling joists are positioned at the bottom of the attic space. When the joist is moved up to be used as a rafter tie, extra bending force is put on the rafter. Because of this the code requires that the rafter span is reduced to account for the additional force created.
A rafter tie located 1/6 of the way up the attic space, will have a lesser span once the adjustment factor is applied.

## Slide 45: Crosstie Location
Weight on roof
Why do we adjust the rafter span when a joist is not at
the wall level and a rafter tie is used?
The bending force is caused by the weight on the roof plus the tension tie.
Tension Force
Tension Force
Notes: Say: Tension in the tie can cause the rafter to fail. The rafter span has to be adjusted to account for the load added to the downward and bending forces. If not, the bending force will cause shear stress resulting in tearing on the rafter.
Do: CLICK to show bending force
Say: The bending force is caused by the weight of the roof plus the tension tie.

## Slide 46: R802.5.1 Purlins
6
Installation of purlins to reduce the span of rafters is permitted as shown. Purlins shall be sized no less than the required size of the rafters that they support.
Purlins shall be continuous and shall be supported by 2-inch by 4-inch braces installed to bearing walls at a slope not less than 45 degrees from the horizontal. The braces shall be spaced not more than 4 feet on center and the unbraced length of braces shall not exceed 8 feet.
Notes: Say: Purlins can be used to reduce the clear span of rafters and provide extra support to the roof. As noted in the illustration at right, the purlins should not have less depth than the rafter. Purlins are continuous and supported by 2 by 4 braces installed at bearing walls.

## Slide 47: R802.5.1 Purlins
Purlins should not be less than the size of the rafter
Braces are 2-inches by 4-inches
Braces are installed to bearing walls at not less than 45 degrees
Braces are spaced not more than 4 feet o.c.
The unbraced length of the braces should not be more than 8 feet
Notes: Say: Braces should not be spaced more than four feet and the unbraced length of braces should not be more than 8 feet. Shown here is an example of installed purlins.
Do: CLICK Reveal braced purlins
Say: Studs under compression tend to buckle and lose load carrying capacity. The longer the “unbraced length,” the more likely this is to happen. Here we see that studs are nailed in a perpendicular lay-up to the braces to reduce or eliminate the unbraced length.

## Slide 48: R802.6 Bearing
The ends of each rafter or ceiling joist shall have not less than 1-1/2 inches of bearing on wood or metal and not less than 3 inches on masonry or concrete.
The bearing on masonry or concrete shall be direct, or a sill plate of 2-inch minimum nominal thickness shall be provided under the rafter or ceiling joist. The sill plate shall provide a minimum nominal bearing area of 48 square inches.
7
Notes: Do: To meet the IRC requirements the ends of rafters or ceiling joists shall not have less than 1 ½ of bearing on wood or metal and not less than 3 inches on masonry or concrete.

## Slide 49: Bearing
R802.6
Hangers are needed when there is less than 1-1/2” bearing on wood.
B ≥ 1½
Top Hanger
Bottom Hanger
Adjustable Hanger
Notes: Say: An engineered solution such as hangers, are needed when there is less than 1 ½ bearing on wood.
What do you think about this configuration? It looks pretty good, but there is a horizontal cut at the heel of the rafter. The connector won’t work if it is a sloped rafter without this cut.
Manufacturers provide hangers to address this sloped configuration, using these hangers is preferable. There are adjustable hangers, or custom-made sloped and skewed hangers made for a specific application.
Test Question
The end of each rafter or ceiling joist shall have not less than 3 inches of bearing on wood or metal.
True
False

## Slide 50: Cutting and Notching
8
Notches in solid lumber joists, rafters, blocking and beams shall not exceed one-sixth of the depth of the member, shall not be longer than one-third of the depth of the member and shall not be located in the middle one-third of the span.
Notches at the ends of the member shall not exceed one-fourth the depth of the member.
R802.7.1
The tension side of members four inches or greater in nominal thickness shall not be notched except at the ends of the members.
Notes: Say: For cutting and notching both where and what is cut is important.
Do: CLICK
There should be no notches in the middle of rafters and beams. There can be notches in the outer thirds, top or bottom if less than 1/6.
Do: CLICK
Notches at the very end should be less than ¼ of depth.
Do: CLICK
For a member that is four inches or greater in width, shall not be notched except at the ends. The tension side is the bottom edge.

## Slide 51: Cutting and Notching
8
Cutting and Notching
R802.7.1
The diameter of the holes bored or cut into members shall not exceed one-third the depth of the member.
Holes shall not be closer than 2 in. to the top or bottom of the member, or to any other hole located in the member. Where the member is also notched, the hole shall not be closer than 2 inches to the notch.
Notes: Say: For “cuts,” the diameter of holes bored or cut into members shall not exceed one third the depth of the member. Holes should be 2 inches away from top and bottom or from any other hole located in the member. If the member is already notched, the hole should not be closer than two inches to the notch.

## Slide 52: Lateral Support
9
Blocking to rafter or
ceiling joist per code
Fastening to Plate
Blocking or other lateral
support per code
R802.8
Roof framing members and ceiling joists having a depth-to-thickness ratio exceeding 5 to 1 based on nominal dimensions shall be provided with lateral support at points of bearing to prevent rotation
For roof rafters with ceiling joists attached per Table R602.3(1), the depth-thickness ratio for the total assembly shall be determined using the combined thickness of the rafter plus the attached ceiling joist.
Notes: Say: Lateral support is required to stop rafters from rolling over when the depth to thickness ratio exceeds 5 to 1.
An example of exceeding 5 to 1 would be 2 by 12 or greater. This isn’t a very common occurrence. If the rafters have the ceiling joists attached, the width of the ceiling joist is added. The ceiling joist is usually at least a 2-by, which would make our 2 by 12 example - now be 3 to 1 depth to thickness ratio. Illustrated here is blocking to a rafter for lateral support and fastening to plate.
Illustrated here is blocking to a rafter for lateral support and fastening to plate.

## Slide 53: Bridging
10
R802.8.1
Rafters and ceiling joists having a depth to-thickness ratio exceeding 6 to 1 based on nominal dimensions shall be supported laterally by solid blocking, diagonal bridging (wood or metal) or a continuous 1-inch by 3-inch wood strip nailed across the rafters or ceiling joists at intervals not exceeding 8 feet
Notes: Say: The code requires bridging only when the member ratio exceeds 6 to 1 — which would be a 2 by 14. Bridging is also not that common.
Bridging keeps the joists from rotating at location away from their supports under loads and losing the load carrying capacity. Blocking keeps rafters and joists from rolling at the supports.
Do: Note the three types of bridging, solid bridging, diagonal bridging or straps.

## Slide 54: Framing of Openings
11
RAFTER
RIDGE BOARD
DOUBLE TRIMMER RAFTER
DOUBLE HEADER
R802.9
When the header joist span exceeds 4 feet, the trimmer joists and the header joist shall be doubled
Approved hangers shall be used for the header joist to trimmer joist connections when the header joist span exceeds 6 feet.
Tail joists over 12 feet long shall be supported at the header by framing anchors or on ledger strips not less than 2 inches by 2 inches.
Header
Trimmer
Notes: Say: Similar to walls, when framing members are removed, framing around the outside has to be reinforced to carry the extra load, and headers must be installed to transfer the load to those trimmer joists. Shown here is a double header and double rafter.
Do: CLICK
Common case of a trayed ceiling where the framing of opening requirements would apply. Approved hangers are required for the header joist to trimmer joist. Shown here.
Do: CLICK
While the code is talking about openings in ceilings, it could be applied to other areas, like where these joists are headered off because of congestion in framing at that location.

## Slide 55: Roof Tie-Down
R802.11
Roof assemblies shall have uplift resistance in accordance with Sections R802.11.1.1 and R802.11.1.2.
Where the uplift force does not exceed 200 pounds, rafters and trusses spaced not more than 24 inches on center shall be permitted to be attached to their supporting wall assemblies in accordance with Table R602.3(1)
Where the basic wind speed does not exceed 115 mph, the wind exposure category is B, the roof pitch is 5:12 or greater, and the roof span is 32 feet or less, rafters and trusses spaced not more than 24 inches on center shall be permitted to be attached to their supporting wall assemblies in accordance with Table R602.3(1)
12
Notes: Say:
We’ll review R802.11.1.2 on the next slide, R802.11.1.1 refers to trusses and is not included.
In these two cases rafters or trusses can be attached per Table R602.3(1)
1) Uplift forces do NOT exceed 200 pounds, rafters and trusses spaced not more than 24 in. oc can be attached per Table R602.3(1)
2) Where all series of requirements are met:
Wind does not exceed 115mph
Wind Exposure is category B
Roof pitch is 5:12 or greater
Roof Span is 32 ft or less
Rafters and trusses spaced not more than 24 inches o.c.
When all of these are met it can be attached using 3 10b nails.

## Slide 56: Rafter Uplift Resistance
R802.11.1.2
Rafter uplift resistance. Individual rafters shall be attached to supporting wall assemblies by connections capable of resisting uplift forces as determined by
Table R802.11 or as determined by accepted engineering practice. Connections for beams used in a roof system shall be designed in accordance with accepted engineering practice.
13
Notes: Say: Vertical wind forces can create uplift forces that could lift a roof off a structure. When the uplift force exceeds 200 pounds as per previous slide then an enhanced rafter to wall connection is required. This can either be in accordance with the table R802.11 or an accepted engineering practice. A connector with the required load capacity is a great example of what can be used.

## Slide 57: Table R602.3.1
When uplift does not exceed 200 pounds rafters can be attached per Table R602.3.1
Notes: Say: Table R602.3(1) applies when the uplift force is less than 200 pounds.
The fastening requirement has been revised. This used to just cover the fastening of rafters, now it includes rafters or trusses. The requirement for a 175 lbs connector for trusses has been removed.
The fastening has changed from 2 toenails to 3 toenails, the connection has an increase of 50% in capacity!

## Slide 58: Table R802.11
When uplift is greater than 200 pounds, then a designed connection must be provided beyond the basic requirement for toenails
Table R802.11
Notes: Say:
This table gives the uplift for various situations. When uplift is greater than 200 pounds, then a designed connection must be provided beyond the basic requirement for toenails. The connector needs to have the capacity in the table or be designed in accordance with engineering practice.
This is a section of Table R802.11 showing required tie-down for roof framing. Remember that 200 pounds is the trigger. Here you can see where the 32’ roof span and >5:12 roof pitch comes from.
Test Question
When uplift is greater than ________, a design connection must be provided.
24 inches on center
115 mph
150 lbs
200 lbs

## Slide 59: Course Summary
We reviewed Chapter 8 of the IRC 2015 Code Requirements as it pertains to Conventionally Framed Roofs including: ceiling joist/rafter connections, ceiling joist lapping, fastening requirements, ceiling joist and rafter span, bearing, cutting & notching, framing of openings and tie-downs.
Code Requirements for Stick Framed Roofs
Conventionally framed roof-ceiling systems form a diaphragm that transfers lateral loads through the structure in a continuous load path. Rafters, ridge and joist form a continuous tie to support the roof against downward thrust.
Stick-frame roofs are a preferred method of building when flexibility in the roof shape or volume in the attic space is desirable. The code for conventionally framed roofs is based on historical performance and uses of prescriptive construction.
Notes: Review Summary

## Slide 60: Course Completion
Any Questions?

## Slide 61: Course Completion
Simpson Strong-Tie
This concludes the continuing education course.
For a library of Simpson Strong-Tie courses,
visit strongtie.com/workshops
Notes: Do
Draw the meeting to a close. Hand out literature and business cards.
Say
If you have ongoing projects that you would be interested in reviewing together, please let me know.

## Slide 62: Next Steps!
AIA: For those seeking AIA LU/HSW: You will receive an email with a link allowing access to print your Certificate. Congratulations, you will have earned 1 LU/HSW credit. If your AIA member number has been inserted into your profile, Simpson Strong-Tie will report your credits on your behalf to the AIA. No test is required in order to receive HSW credits.
IACET: For those seeking IACET CEUs: You will receive an email with a link allowing access to print your Certificate of Attendance and instructions directing you to the Simpson Student Center to take the exam before credits can be awarded. Once the exam is taken and passed, you will have earned 0.1 CEUs (1 hour of credit). You can then access your Certificate of Completion from the Course Content tab. You must self-report your credits to your certifying organization or agency.
If you have questions or need assistance, please contact training@strongtie.com.
Notes: Presenter Notes:
Review the email and notification process as outlined in this slide.
AIA LUs:
For those that want AIA HSW credit, be sure to provide your AIA number on the sign-in sheet and Simpson will report your credits to the AIA on your behalf.
No test is required for AIA credit.
CEUs:
For those seeking CEUs, watch for an email with instructions to access the online test. After you have passed the test, you may access your Certification of Completion from the course content tab.
You must self-report your credits to your certifying organization or agency.

## Slide 63: Next Steps!
ICC: For those seeking ICC CEUs: You will receive an email with a link allowing access to print your Certificate. Congratulations, you will have earned 0.1 ICC CEU (1 hour of credit). Please make sure your ICC member number has been inserted into your profile. It is your responsibility to self-report your credits to the ICC. Please retain your Completion Certificate for your records.
IACET: For those seeking IACET CEUs: You will receive an email with a link allowing access to print your Certificate of Attendance and instructions directing you to the Simpson Student Center to take the exam before credits can be awarded. Once the exam is taken and passed, you will have earned 0.1 CEUs (1 hour of credit). You can then access your Certificate of Completion from the Course Content tab. You must self-report your credits to your certifying organization or agency.
If you have questions or need assistance, please contact training@strongtie.com.
Notes: Presenter Notes:
Review the email and notification process as outlined in this slide.
Watch for an email directing you to the Student Center to print your certificate.
No test is required for ICC credit. You must self-report your credits to ICC.
For those seeking general IACET CEUs after you have passed the online test, you may access your Certification of Completion from the course content tab. You must self-report your credits to your certifying organization or agency.

## Slide 64: Credit Information, cont.
CLICK this link to open your
Attendance Certificate
Notes: Unhide – show if you have attendees interested in CEU credits.
Say
Within two days of attending the event, you should receive an Attendance Confirmation email from training@strongtie.com. This email will give instructions how to take the test and earn IACET credits for the workshop.
You will also be able to download your attendance certificate directly or access your class record in the Learning Center to retrieve your certificate and any other available resources.

## Slide 65: Access the Test for CEUs
In order to earn credits,
you will need to pass the test.
Click the Your Workshop link.
Notes: Unhide – show if you have attendees interested in CEU credits.
Say
Clicking the “Your Workshop” link in Step 1 will take you directly to the attended event.

## Slide 66: Stronger Roof Solutions
Stronger Roof Solutions
Simplify complicated connections.
Design and build a cost-effective and resilient stick-frame roof using our:
  LSSJ adjustable jack hangers
  HHRC hip-ridge connectors
  LRU rafter hangers.
Quick and simple installation makes it easy to meet code and pass inspection.
Notes: Do: After finishing class and directing class to accreditation and testing – Introduce this PK portion.
Why was the strong roof solution created?
To save time while building a stick-frame roof, while still building a strong roof that is resilient in download and uplift conditions.
The building code calls out for 1½" of direct bearing under joists .
Benefits
We are the only manufacturer to offer all of the key products for building a strong stick-frame roof — namely, LSSJ (and LSSU), HHRC and LRU connectors.
Key features
These three key connectors form an easy-to-understand system that allows builders to adopt correct building methods without having to adopt complex new procedures.
These three connectors not only strengthen stick-frame roofs, but are a cost-effective solution that can save builders time and help them avoid mistakes and eliminate inspection issues.

## Slide 67: LSSJ Hanger
LSSJ Hanger
Ideal for attaching jack rafters to hip members.
Quick and intuitive installation, resulting in lower labor costs.
The versatile, hinged seat is easily field-adjustable to typical rafter slopes, with a maximum slope of 12:12.
Notes: Say: The first part in our three parts Strong Roof Solution is the LSSJ Hanger.
Ideal for attaching jack rafters to hip members
Adjustable for ease of installation
Can be installed after the two members are in place

## Slide 68: HHRC Hip-Ridge Connector
HHRC
A heavy, field slope-able connector that attaches hip and roof beams to the end of a ridge beam
Installs with Strong-Drive® SD Connector screws (included with each connector)
Notes: Say: Part two is the HHRC Hanger
This is for where multiple beams meet
Heavy and slope-able
Installs with screws (included with connector)
Good for when multiple beams meet.

## Slide 69: LRU Rafter Hanger
LRU
Economic alternative for applications requiring a sloped hanger for rafter-to-ridge connections.
Unique design enables installation before or after the rafter is in place.
Field-adjustable seat helps improve job efficiency by eliminating mismatched angles in the field and lead times associated with special orders.
Notes: The LRUZ offers an economic alternative for those applications requiring a sloped hanger for rafter-to-ridge connections. Used with solid sawn rafters, the LRUZ’s unique design enables the hanger to be installed either before or after the rafter is in place. The field-adjustable seat helps improve job efficiency by eliminating mismatched angles in the field and lead times associated with special orders. The LRUZ offers comparable or better load capacity to other rafter hangers at a reduced cost while using fewer fasteners.
Note: the image shown here shows a ridge that is less than the depth of the rafters. Is this a code violation or is it covered by using an engineered solution?

## Slide 70: Additional Products
MSTI Strap
Ridge Strap
H2.5A
SDWC
Notes: Additional Products include:
H2.5A which provides a positive connection between rafter and wall to resist wind, uplift and seismic forces.
MSTI Strap designed to transfer tension loads in a wide variety of applications
SDWC Screw: If it is appropriate for your region structural screws for the joist to top plate connection can be considered, check with an engineering resource for equivalencies.