## Slide 1
AIA Course AIA-ROD10113
AIA Provider 50119826
Restraint Rod Systems
SHEAR WALL OVERTURNING VS. WIND UPLIFT
AND HOW TO DESIGN THEM PROPERLY
Notes: Meet and greet participants as they arrive. Start learning names, make them feel comfortable and settled in the training environment.
Make sure your opening has PUNCH:
Promotes interest and enthusiasm for the session
Understands participants’ needs
Notes ground rules and administrative/housekeeping needs
Clarifies expectations
Helps everyone get to know each other
State your expectations around participation: Make it known and expected that you will be encouraging and inviting participation.
Tips to facilitate connections:
Thank participants for their contribution (ideally with their name)
Praise participation (especially the first person to speak)
Express confidence in the participants
Restate what someone said earlier (“As John mentioned earlier….”)
Encourage participants to share what others were saying in their small groups (without naming names)
Invite someone you heard speaking in a small group to share with the entire group
Encourage the group to respond to an individual’s comment/question
Physical Room / Training Venue Setup:
If using a table arrangement, consider grouping 4 to 6 students at each station. This will help encourage conversation and discussion during activities.
Get people standing at regular intervals during your training session. Research shows that people learn up to 15% more when standing up!

## Slide 2: Credit Information
Understanding Restraint Rod Systems | Introduction
IACET Accreditation Information
Simpson Strong-Tie® has been accredited as an Authorized Provider by the International Association for Continuing Education and Training (IACET). As a result of their Authorized Provider accreditation status, Simpson Strong-Tie® is authorized to offer IACET CEUs for its programs that qualify under the ANSI/IACET Standard.
This course offers 0.1 CEU (1 hour of credit).
Notes: Do
Review the submission process for audiences requiring IACET CEU credits.
For those seeking IACET credit, they must take and pass the online test. They must self-report CEU credits to their certifying organization or agency.
Explain the credits awarded: IACET: 0.1 (Equivalent to 1 hour) CEUs.

## Slide 3: Credit Information
Understanding Restraint Rod Systems | Introduction
AIA Member Information
This course is registered with AIA CES for continuing professional education. As such, it does not include content that may be deemed or construed to be an approval or endorsement by the AIA of any material of construction or any method or manner of handling, using, distributing, or dealing in any material or product. Upon completion of this course, Credit(s) earned will be reported to AIA CES for AIA members who pass the course and have entered their AIA member number on their Simpson profile page. A link to the Certificate of Completion will be available upon completion of this course. Only AIA LU/HSW will be reported.
This course offers 1 LU/HSW credit.
AIA Course Number: AIA-ROD10113
Notes: Do
Please be sure each attendee LEGIBLY signs the event sign-in sheet.
Say
All questions concerning proprietary products will be addressed after the conclusion of the AIA portion of the presentation. The meeting format is 50 minutes of content, followed by 10 minutes of Q & A.
Do
Explain the credits awarded for:
AIA: 1LU/HSW credit
IACET: 0.1 (Equivalent to 1 hour) CEU credits
Review the submission process for audiences requiring either AIA LU/HSW (health, safety and welfare) credits or CEU credits:
For those seeking AIA HSW credit, there is no test required. AIA members must be sure to provide their AIA member number on the sign-in sheet. Please make sure name, email and AIA member number are clearly printed so Simpson can report credits to the AIA on their behalf.
For those seeking IACET credit, they must take and pass the test. They must self-report CEU credits to their certifying organization or agency.

## Slide 4: Credit Information
Understanding Restraint Rod Systems | Introduction
ICC Member Information
This course has been approved by the International Code Council (ICC) for continuing professional education. For learners that complete this course, it is your responsibility to self-report your credits to the ICC. Please retain your Completion Certificate for your records.
Be sure that your ICC ID number is provided on the sign-in sheet or in your Simpson profile in order to have it displayed on your certificate.
This course offers 0.1 CEU (1 hour of credit).
ICC Course Number: 183
Notes: Do
Review the submission process for audiences requiring ICC CEU credits.
For those seeking ICC credit, there is no test required. ICC members must provide their ICC ID number on the sign-in sheet or in their Simpson profile in order to have it displayed on their certificate. It is the responsibility of the participant to self-report their credits to the ICC. Ask them to retain their Completion Certificate for their records.
Explain the credits awarded: ICC: 0.1 (Equivalent to 1 hour) CEUs.

## Slide 5: Course Description
Understanding Restraint Rod Systems | Introduction
This is a technical course intended primarily for Structural Engineers and Designers interested in rod system design.
This course reviews two different types of restraint rod systems: one designed to resist shear wall overturning and the other to resist wind uplift.
Topics included in the course are design practices, testing, and the use of AC391 for designing continuous rod tie-down runs and continuous rod tie-down systems used to resist wind uplift.
Notes: Do
Review the course description.

## Slide 6: Agenda
Understanding Restraint Rod Systems | Introduction
❶ | Shear Wall Overturning vs. Wind Uplift Forces
❷ | Wind Uplift Restraint Rod Systems
❸ | Restraint Rod Systems for Shear Wall Overturning
❹ | Designing and Specifying Shear Wall Overturning Restraint Rod Systems
Notes: Do
Review agenda.

## Slide 7: Learning Objectives
Understanding Restraint Rod Systems | Introduction
Upon completion of this seminar, you will be able to:
Explain and contrast the differences between wind uplift and shear wall overturning restraint rod systems
Account for AC391 acceptance criteria in restraint rod system design
Evaluate performance differences between all-floors-tied-off and skipped floor shear wall overturning restraint rod systems
Evaluate 3 different design specification methods and select an appropriate method for any project
Notes: Do
Review the learning objectives.
ASK AUDIENCE:
“Is there anything you would like to add to this list if we have time today?”
DO: (Write down these additional learning objectives for review at the end of the presentation.)
“What type of design challenges have you had in the past with designing restraint rod systems?”
“How were you able to overcome these challenges?”
“How have manufacturer’s been able to help you in the past?”
“What else would you like to see manufacturer’s do to assist you as a engineer or designer?”
DO: Write down audiences answers to the above questions..
SAY: “Let’s see how many of these we can address today.”

## Slide 8: Restraint Rod Systems
Understanding Restraint Rod Systems | A Brief History of Restraint Rod Systems
A Brief History
Over 20 year history in the marketplace
Address both uplift and overturning restraint
Evolved from early system of connectors (metal ties, brackets or screws) to today’s system of rods and couplers
Shrinkage compensation devices introduced in 1998
Notes: Do
Briefly review bullet points of history to introduce the topic and some of the issues regarding design of systems- issues that you will address during the presentation.
Below is dialogue you may choose to incorporate into your “History lesson”.
Say
Rod tie-down systems have been used by the wood light-framed construction industry to resist shear wall overturning in lieu of traditional straps and holdowns for many years now. The design components of shear wall overturning rod systems are included in various codes and guidelines (NDS, ASTM, AISC Steel Construction Manual, ACI, and IBC).
For the past decade, rod tie-down systems have also been used to resist wind uplift forces. Yet codes and standards have not provided detailed guidance for design of these systems. Designers, consequently, have been forced to rely entirely on engineering judgment to create this load path.
This lack of guidance sometimes led to rod-restraint spacing based on rod tension and bearing plate capacities alone. This design neglects the wood components of the system and may lead to rods spaced too far apart, compromising the continuous load path, causing building damage and creating life-safety issues.

## Slide 9: Restraint Rod Systems
Understanding Restraint Rod Systems | A Brief History of Restraint Rod Systems
A Brief History
Engineering judgment was the early design guidance
Today-uplift systems: guided by ICC Acceptance criteria AC391 and AC316 (shrinkage compensation devices)
Today-overturning systems:
Designed by EOR with manufacturer’s input
Guided by code reports and guidelines (NDS, ASTM, AISC Steel Const. Manual, ACI, and IBC)
Notes: Do
Briefly review bullet points of history to introduce the topic and some of the issues regarding design of systems- issues that you will address during the presentation.
Below is dialogue you may choose to incorporate into your “History lesson”.
Say
Rod tie-down systems have been used by the wood light-framed construction industry to resist shear wall overturning in lieu of traditional straps and holdowns for many years now. The design components of shear wall overturning rod systems are included in various codes and guidelines (NDS, ASTM, AISC Steel Construction Manual, ACI, and IBC).
For the past decade, rod tie-down systems have also been used to resist wind uplift forces. Yet codes and standards have not provided detailed guidance for design of these systems. Designers, consequently, have been forced to rely entirely on engineering judgment to create this load path.
This lack of guidance sometimes led to rod-restraint spacing based on rod tension and bearing plate capacities alone. This design neglects the wood components of the system and may lead to rods spaced too far apart, compromising the continuous load path, causing building damage and creating life-safety issues.

## Slide 10: Shear Wall Overturning vs. Wind Uplift Forces
Understanding Restraint Rod Systems | Shear Wall Overturning vs. Wind Uplift Forces

## Slide 11: Overturning vs. Uplift Forces
Understanding Restraint Rod Systems | Shear Wall Overturning vs. Wind Uplift Forces
Overturning (Lateral)
When a building weight cannot stabilize a structure under a lateral force, it causes the structure to rotate off its foundation.
Uplift (Vertical)
As wind flows over the roof the wind creates a strong lifting effect, much like that of air flowing over an airplane wing.
Different Forces = Different Systems
Notes: Do
Explain two types of forces that restraint rod systems resist.

## Slide 12: Two Different Types of Restraint Rod Systems
Key Differences
Rod location
Load direction
Framing Requirements
Load path
Shrinkage/ compression location
Understanding Restraint Rod Systems | Shear Wall Overturning vs. Wind Uplift Forces
Shear Wall Overturning
Wind Uplift
Notes: Do
Use laser pointer to point to and highlight key differences.

## Slide 13: Key Differences
OC spacing at bearing walls
Understanding Restraint Rod Systems | Shear Wall Overturning vs. Wind Uplift Forces
Wind Uplift
Shear Wall Overturning
Rod Location
Shear wall ends
Roof level only (typically)
Applied Load
Each level
Roof level only
Restraints
Each level
Diaphragm / truss (rafter) / plate / bearing plate / rod
Load Path
Diaphragm / blocking / sole plate / sheathing / compression stud / bearing plate / rod
Occurs at a single location
Shrinkage and Compresison
Shear wall ends
Notes: Do
Explain the functional differences of each component in each system:
Rod location:
Overturning: Rod runs at ends of shear walls
Uplift: Rod runs at on-center spacing along all load bearing walls with uplift
Applied load location:
Overturning: Loads applied at each level
Uplift: Load applied at roof level only (typically)
Restraint location:
Overturning: Restraints (bearing plates) at each level resist incremental forces while rod resists cumulative forces.
Uplift: Restraint (bearing plate) at roof level only
Load path:
Overturning: Lateral force transfers from diaphragms to blocking or rim boards, to top plates, to wall sheathing, to end studs, to bearing plate, to rod,…load path is repeated at each level creating cumulative overturning until force is transferred to the foundation.
Uplift: Force transfers from roof diaphragm, to truss/rafter, to top plate, to bearing plate, to rod. Coupler nuts connect rods that transfer force to the foundation.
Shrinkage and compression location:
Overturning: Segmented per floor
Uplift: All dead load compression and shrinkage deflection occurs at a single location
Presenter Note
This slide features information that will be found on the post-training knowledge assessment:
In shear wall overturning restraint rod systems, loads are applied:
At roof and floor levels
At the roof level only
At the anchorage only
None of the above

## Slide 14: Wind Uplift Restraint Rod Systems
Understanding Restraint Rod Systems | Wind Uplift Restraint Rod Systems
Notes: Design and Industry Practices, Building Codes, Research Reports, and Acceptance Criteria for Wind Uplift Restraint Rod Systems

## Slide 15: Design Guidance for Wind Systems
Understanding Restraint Rod Systems | Wind Uplift Restraint Rod Systems
Is there a prescriptive design guide for wind uplift restraint rod systems?
Currently, there is no code referenced standard for continuous rod tie-down systems.
So, where can building designers turn to when designing these wind uplift restraint systems?
Manufacturers?
Engineering Judgment?
Acceptance Criteria alone?
Notes: Ask
What problems has a lack of a code-referenced standard caused or COULD cause when designing restraint rod systems?
Some possible answers you want to “fish” for:
-Substitution of product that does not meet quality standards or can’t be verified may fail in a wind or seismic event.
-A design that does not address the wood structural system and will fail under actual wind or seismic conditions.
-Variation in “engineer’s judgment” leads to variation in design. What is adequate to one may not be adequate to another.
-Other?

## Slide 16: What Have Manufacturers Provided Up Until Now?
Understanding Restraint Rod Systems | Wind Uplift Restraint Rod Systems
Evaluation Reports, issued prior to any Acceptance Criteria being developed for rod systems.
Newer Evaluation Reports include a new “design” section requiring the designer to evaluate top plate bending, deflection, and other wood component performance.
Caveat Emptor… trust but verify….
Be sure your manufacturer has evaluated the performance of the wood system, not just the rod system.
Notes: Say
Some language you may want to incorporate into your discussion.
Old Evaluation Reports were given to some manufacturers, but it is important to note that these reports were provided prior to any Acceptance Criteria being developed for rod systems. BUT, if you go look at these Legacy Reports now they include a new “Design” section that tells the Designer that they have to look at top plate bending, deflection, etc. Still, some manufactures continue to gloss over this and provide misleading information on their websites/catalogs.

## Slide 17: There is Some Additional Help
Understanding Restraint Rod Systems | Wind Uplift Restraint Rod Systems
In June 2010, ICC-ES passed and made effective Acceptance Criteria 391 for continuous rod tie-down systems for uplift.
This standard establishes the minimum levels of performance to meet the code’s intent.
Notes: Do
Discuss the difference between a code report and a code referenced standard in terms of design guidance.

## Slide 18: ICC-ES AC391: CRTR and CRTS
Understanding Restraint Rod Systems | Wind Uplift Restraint Rod Systems
ICC-ES AC391 establishes guidelines for the evaluation of either:
  The steel components comprising continuous rod tie-down runs (CRTR) only.
  The entire continuous rod tie-down systems (CRTS), which includes CRTR and the light-framed wood structure used to resist wind uplift.
Continuous Rod Tie-Down System (CRTS)
[includes CRTR]
Continuous Rod Tie-Down Run (CRTR)
Notes: Do
Describe the differences between CRTR and CRTS.
Presenter Note
This slide features information that will be found on the post-training knowledge assessment:
AC391 is used to evaluate Continuous Rod Tie-down Runs (CRTR) and Continuous Rod Tie-down Systems (CRTS) for resisting roof wind uplift in:
Concrete and masonry construction
Wood light-framed construction
Cold-formed steel framing
All of the above
Which of the following types of reports obtained by manufacturers require a Designer to calculate top-plate rotation, wood shrinkage, and define all wood detailing requirements?
Continuous Rod Tie-down Systems (CRTS)
Continuous Rod Tie-down Runs (CRTR)
Both of the above
None of the above

## Slide 19: Specific Design Requirements of AC391
Understanding Restraint Rod Systems | Wind Uplift Restraint Rod Systems
Section 1.2
Limited to resisting roof wind uplift in wood light-framed construction.
Excluded from AC391
Shear wall overturning systems or use in cold-formed steel framing.
Notes: Do
Note the limitation in AC391 to exclude overturning systems.
Presenter Note
This slide features information that will be found on the post-training knowledge assessment:
AC391 is used to evaluate Continuous Rod Tie-down Runs (CRTR) and Continuous Rod Tie-down Systems (CRTS) for resisting roof wind uplift in:
Concrete and masonry construction
Wood light-framed construction
Cold-formed steel framing
All of the above
Which of the following types of reports obtained by manufacturers require a Designer to calculate top-plate rotation, wood shrinkage, and define all wood detailing requirements?
Continuous Rod Tie-down Systems (CRTS)
Continuous Rod Tie-down Runs (CRTR)
Both of the above
None of the above

## Slide 20: What’s Not in the Code?
Understanding Restraint Rod Systems | Wind Uplift Restraint Rod Systems
The building code does not define the requirements for the wood structural system the rod system is installed within, such as:
Deflection limit for top plate flat bending
Top plate rotation
Rod elongation
Wood plate crushing
Wood shrinkage
Bearing plates
Anchorage capacity
AC391 does establish guidelines for evaluation of the wood frame system the rod system must perform in.
Notes: Do
Review the components of the wood frame structural system addressed by AC 391.
Ask
Why would it be important to address these components of the wood frame system?
Presenter Note
This slide features information that will be found on the post-training knowledge assessment:
AC391 is used to evaluate Continuous Rod Tie-down Runs (CRTR) and Continuous Rod Tie-down Systems (CRTS) for resisting roof wind uplift in:
Concrete and masonry construction
Wood light-framed construction
Cold-formed steel framing
All of the above
Which of the following types of reports obtained by manufacturers require a Designer to calculate top-plate rotation, wood shrinkage, and define all wood detailing requirements?
Continuous Rod Tie-down Systems (CRTS)
Continuous Rod Tie-down Runs (CRTR)
Both of the above
None of the above

## Slide 21: Design Guidance for Wind Systems
Understanding Restraint Rod Systems | Wind Uplift Restraint Rod Systems
Some manufacturers define the wind uplift restraint rod components (CRTR), but leave the “system” components (CRTS) design to the engineer.
Who is responsible for the design of the wood structural system…
CRTR
CRTS
Notes: Do
Discuss the responsibility and liability of the EOR or designer related to designing the wood frame structural system, not just the rod system.
Some similarities: Installing concrete tiles on a roof designed to support 3 tab shingles. The shingles may perform, but what if the supporting structure can’t hold up the roof?
Installing Michelin tires on a car with bad “tie-rods”. The tires will perform, but what if the tie-rods fail?

## Slide 22: Restraint Rod Systems for Shear Wall Overturning
Understanding Restraint Rod Systems | Restraint Rod Systems for Shear Wall Overturning

## Slide 23: Overturning Restraint Rod System – System Load Path
Understanding Restraint Rod Systems | Restraint Rod Systems for Shear Wall Overturning
How do forces enter, travel through, and exit the shear wall overturning restraint system?
Notes: Do
Click to start the animation.

## Slide 24: Overturning Restraint Rod System – System Load Path
Understanding Restraint Rod Systems | Restraint Rod Systems for Shear Wall Overturning
Lateral forces are applied to shear walls.
Notes: Do
Click to continue the animation.

## Slide 25: Overturning Restraint Rod System – System Load Path
Understanding Restraint Rod Systems | Restraint Rod Systems for Shear Wall Overturning
Sheathing fasteners transfer loads into posts, creating upward compression on wood plates and blocking as overturning forces occur.
Overturning forces are incremental, per floor.
Notes: Do
Click to continue the animation.

## Slide 26: Overturning Restraint Rod System – System Load Path
Understanding Restraint Rod Systems | Restraint Rod Systems for Shear Wall Overturning
Posts (at each level) transfer compression forces to wood members, causing bearing and bending on steel plates.
Notes: Do
Click to continue the animation.

## Slide 27: Overturning Restraint Rod System – System Load Path
Understanding Restraint Rod Systems | Restraint Rod Systems for Shear Wall Overturning
Rods transfer cumulative overturning forces, translated into tension forces, down level to level.
Notes: Do
Click to continue the animation.

## Slide 28: Overturning Restraint Rod System – System Load Path
Understanding Restraint Rod Systems | Restraint Rod Systems for Shear Wall Overturning
Anchorage transfers cumulative overturning forces into foundation.
Notes: Do
Click to continue the animation.

## Slide 29: Overturning Restraint Rod System – System Load Path
Understanding Restraint Rod Systems | Restraint Rod Systems for Shear Wall Overturning
This side of the structure is in TENSION.
This side of the structure is in COMPRESSION, where the forces are transferred down to the foundation by the wood members.
Notes: Do
Click to continue the animation.

## Slide 30: Overturning Restraint Rod System
Understanding Restraint Rod Systems | Restraint Rod Systems for Shear Wall Overturning
The uplift load is delivered to posts through sheathing fasteners.
Posts then deliver uplift load directly to the bearing plate.
Compression posts are close together to minimize top plate bending.
Spacing limited to control top plate bending.
Notes: Do
Explain how load is delivered to rods in an overturning system. Explain why compression post are close together [limiting top plate bending.

## Slide 31: Skipped-Floor System
Understanding Restraint Rod Systems | Restraint Rod Systems for Shear Wall Overturning
Three-story skipped-floor example:
Second- and third-floor restraints are not provided (skipped).
Single bearing plate at the top level is the sole point of restraint.
Skipped
Skipped
Notes: Do
Explain the concept of a “skipped-floor” system and the resulting accumulation of load at the roof top plate.

## Slide 32: All-Floors-Tied-Off System
Understanding Restraint Rod Systems | Restraint Rod Systems for Shear Wall Overturning
All-floors-tied-off example:
Each floor is restrained with a bearing plate and nut.
Loads are evenly distributed through the system at each floor.
Notes: Do
Explain the concept of an “all-floors-tied-off” system and the resulting distribution of load at each floor level.

## Slide 33: Skipped-Floor vs. All Floors Tied Off
Understanding Restraint Rod Systems | Restraint Rod Systems for Shear Wall Overturning
A single point of restraint for multiple levels
Overturning restraint provided at each level
Skipped-Floor System
All-Floors-Tied-Off System
Point
of Restraint
Points
of Restraint
Why are skipped-floor systems not recommended?
Notes: Ask
“What are the design advantages of an all-floors-tied-off system and why would you recommend it over a skipped-floor system?”
(The next few slides will highlight the pros/cons of each.)

## Slide 34: Cost Complications
Understanding Restraint Rod Systems | Restraint Rod Systems for Shear Wall Overturning
Skipped Floor
Overturning forces transfer up the building until a restraint is reached..
Elements at restrained point must resist uplift forces for non-restrained stories below.
RESULT: Increased lumber, threaded rod, and bearing plate sizes.
Tied-off
Incremental uplift at each level is transferred directly into the tiedown system at that level, reducing lumber/rod/plate sizes.
2- 2x4
6- 2x4
4- 2x4
6- 2x4
6- 2x4
6- 2x4
Skipped
Tied-off
Notes: Do
(Highlight the “con’s” of a skipped floor system and the resulting effects from the slide.)
(Highlight the “pro’s” of a tied-off systems and resulting cost savings due to reduced lumber/rod/plate sizes.)
(Some language you may want to incorporate in your discussion of this slide)
“Everyone thinks they are saving money by skipping floors because you don’t need bearing plates and nuts (and take-ups devices) at each level, but really you ADD COST b/c your compression studs and rod have to be the same size at each level of your structure. Tying off at each level makes the rods discontinuous, but this allows for reducing the rod and compression post sizes.”
Presenter Note
This slide features information that will be found on the post-training knowledge assessment:
All of the following are results of using a skipped-floor system for shear wall overturning rod systems, EXCEPT:
Lack of system redundancy
Increased overall cost
Increased construction stability
Increased drift

## Slide 35: Rod Elongation
Understanding Restraint Rod Systems | Restraint Rod Systems for Shear Wall Overturning
Skipped system: elongation accumulates at the base, damaging shear fastening, weakening system.
Rod elongation accumulates
at base
Divided
Tied-off system: elongation distributed between floors, lessening impact.
Notes: Talking Points
“In a skipped system, deflection has to be the same at the bottom as it is at the top because there is no other place for it to be restrained (consistent rod elongation).”
“In a ‘tied-off’ system- rod elongation is distributed between floors at each ‘tie-off’ point, lessening the impact.”
Presenter Note
This slide features information that will be found on the post-training knowledge assessment:
All of the following are results of using a skipped-floor system for shear wall overturning rod systems, EXCEPT:
Lack of system redundancy
Increased overall cost
Increased construction stability
Increased drift

## Slide 36: Design Example: Skipped Floor System
Understanding Restraint Rod Systems | Restraint Rod Systems for Shear Wall Overturning
F2=10k
T2=27k
C2=13+10=23k
F1=13k
T1=27k
C1=13k
F3=4k
T3=27k
C3=13+10+4=27k
13.5 k
27 k
13.5 k
27 k
23 k
13 k
Post axial load-uplift side
Detail A
Notes: (This slide provides an opportunity to walk the audience through a skipped floor system)
(A laser pointer will be helpful here.)
(Review the 3 floor section drawing on the right, highlighting the accumulation of uplift forces at upper floor due to the skipped floor system. Upper floors are required to resist uplift forces from floors below leading to larger posts, plates, rod sizes and therefore increased costs.
(Review Detail A, noting the accumulation of uplift forces that must be transferred through the third floor steel bearing plate into the top plate in a skipped floor system.)
Talking points:
Note the load path direction is bottom to top to bottom… inefficient
Overturning loads transferred to posts through boundary nailing, travel upward through compression until finding ONE point of restraint. One fails, all fails.
Ask audience “Where is that one point of restraint in a skipped floor system? From an earlier slide (slide 35) recall the possible effect to the building if a wind or seismic event were to occur before the rod system was installed- collapse.”
Entire system restrained at upper top plate by large steel bearing plate.
Load transfer from bearing plate to nut to rod.
Top floor tension force a result of all the lower posts transferring loads upward to top floor before coming back down. Posts in lower floors carry that force up in compression. Therefore, posts in top floor must resists uplift force from bottom floor. RESULT IS OVERSIZED POSTS AT MID AND UPPER FLOOR- NOT COST EFFECTIVE.
Section Drawing (on far right) notes:
  F1, F2 and F3 are inter-story uplift forces.
  T1, T2 and T3 are rod tension loads
  C1, C2 and C3 are the post compression loads due to uplift forces.
  Example does not include gravity loads.

## Slide 37: Testing Tells No Lies: Tyrell Gilb Lab Test 3 Story Skipped-Floor
Understanding Restraint Rod Systems | Restraint Rod Systems for Shear Wall Overturning
Notes: Do
Play video. Be sure to point the location of the stud and sheathing failure prior to starting the video.

## Slide 38: Design Example: All-Floors Tied-Off System
Understanding Restraint Rod Systems | Restraint Rod Systems for Shear Wall Overturning
Detail C
2 k
4 k
4 k
27 k
13 k
14 k
2 k
10 k
13 k
F3=4k
T3=4k
C3=4k
F2=10k
T2=10+4=14k
C2=10k
F1=13k
T1=13+10+4=27k
C1=13k
Uplift forces
Post axial load-uplift side
Detail B
Notes: (This slide provides an opportunity to walk the audience through the advantages of an all-floors-tied-off system vs. a skipped floor system.)
(A laser pointer will be helpful here.)
(Review the 3 floor section drawing on the right, highlighting the lack of accumulation of uplift forces at upper floors due to all floor tie offs. Upper floors are no longer required to resist uplift forces from floors below leading to smaller posts, plates, rod sizes and therefore decreased costs.
(Review Detail B, noting the reduction in loads that must be restrained/transferred into the top plate vs. the skipped floor system [4k vs. 27 kips] )
(Review Detail C, noting reduction in rod tension loads [T value] vs. skipped floor system [14 vs. 27 kips])
(Review Detail C, note reduction in compression loads [C value] vs. skipped floor system [10 vs. 23 kips])
Talking points:
Load path: overturning loads transfer to posts through boundary nailing and travel upward through floor system until finding a point of restraint AT EACH STORY=EFFICIENT.
Floor system or roof top plates resist uplift only from floor below. Posts are in compression due to uplift from inter-story loads.
Floor system or roof top plates held down by bearing plate on sole plate or roof top plate AT EACH FLOOR.
Bearing plates transfer EACH FLOOR’S load to nut then rod.
Posts on top floor resist uplift force only from floor below. Be sure to discuss that posts and rods can decrease in size on upper floors. RESULT IS COST SAVINGS DUE TO SMALLER POST SIZES ON MID AND UPPER FLOORS.
Detail B: Steel bearing plate is designed for bending and perp-to-grain load of 4 kips on top plates.
Detail B: Posts are designed for buckling load and perp-to-grain bearing load on top plates of 2 kips each.
Detail C: Incremental Bearing at each floor allows “tie-off” to occur.
Section Drawing (on far right) notes:
  F1, F2 and F3 are inter-story uplift forces.
  T1, T2 and T3 are rod tension loads
  C1, C2 and C3 are the post compression loads due to uplift forces.
  Example does not include gravity loads.
Presenter Note
This slide features information that will be found on the post-training knowledge assessment:
In an all-floors-tied-off system to resist overturning, posts and rods can decrease in size:
On upper floors
On the bottom floor
On every floor
They cannot decrease in size

## Slide 39: Testing Tells No Lies: Tyrell Gilb Lab Test 3 Story All-Tied-Off
Understanding Restraint Rod Systems | Restraint Rod Systems for Shear Wall Overturning

## Slide 40: Construction Stability
Understanding Restraint Rod Systems | Restraint Rod Systems for Shear Wall Overturning
Skipped-floor system:
Unstable until all floors are complete. Susceptible to mid-construction collapse in seismic or high wind event.
Tied-off system:
Restraint installed as each level complete, minimizing risk.
Notes: Say
Skipping floors may also lead to construction stability issues as the full lateral capacity of a shear wall is not achieved until overturning is restrained. If the contractor is using a system where you can tie off at each floor this could be installed as each level is completed – whereas in a skipped for system to have to wait until the entire structure is complete.
Presenter Note
This slide features information that will be found on the post-training knowledge assessment:
All of the following are results of using a skipped-floor system for shear wall overturning rod systems, EXCEPT:
Lack of system redundancy
Increased overall cost
Increased construction stability
Increased drift

## Slide 41: Frequency of Restraints
Understanding Restraint Rod Systems | Restraint Rod Systems for Shear Wall Overturning
When no redundancy ….. One fails, all fail.
Redundancy
No Redundancy
Notes: Do
Comment on the importance of redundancy in design.
Presenter Note
This slide features information that will be found on the post-training knowledge assessment:
All of the following are results of using a skipped-floor system for shear wall overturning rod systems, EXCEPT:
Lack of system redundancy
Increased overall cost
Increased construction stability
Increased drift

## Slide 42: All-Floors-Tied-Off
Understanding Restraint Rod Systems | Restraint Rod Systems for Shear Wall Overturning
Accommodates shrinkage at each floor independently
Greater system redundancy and is consistent with typical design load path
Lower overall cost
Reduced drift
Forces in the elements get smaller as they move up the structure
Notes: Do
(Highlight the design advantages of an all-tied-off-system as indicated on the slide.)
Accommodates shrinkage at each floor independently:
Individual rods are connected at each floor by a coupler take-up device
Greater system redundancy and is consistent with typical design load path:
Restraint provided at all floors. Lower levels are not dependent on restraint of floors above
Reduced drift:
Tying off at each floor does not allow the effect of rod elongation to accumulate at lower floors. Lower compression forces reduce crushing.
Lower overall cost:
Post and rods can decrease in size on upper floors
Forces in the elements get smaller as they move up the structure:
Bearing plate restraints provided at all floors. As a result, tension loads are smaller on upper floors
Presenter Note
This slide features information that will be found on the post-training knowledge assessment:
All of the following are results of using a skipped-floor system for shear wall overturning rod systems, EXCEPT:
Lack of system redundancy
Increased overall cost
Increased construction stability
Increased drift

## Slide 43: Skipped-Floor vs. All Floors Tied-Off Summary
Understanding Restraint Rod Systems | Restraint Rod Systems for Shear Wall Overturning
Notes: Do
(Briefly compare the 2 systems)
Presenter Note
This slide features information that will be found on the post-training knowledge assessment:
All of the following are results of using a skipped-floor system for shear wall overturning rod systems, EXCEPT:
Lack of system redundancy
Increased overall cost
Increased construction stability
Increased drift

## Slide 44: What is in the Building Code for Overturning Systems?
Understanding Restraint Rod Systems | Restraint Rod Systems for Shear Wall Overturning
All parts of an overturning restraint rod except the optional take-up devices.
Part of System | Defined By
Top-plate capacity | NDS Supp. Tables 4A & 4B
Steel bearing plates/nuts | ASTM A36 – bearing stress of the plate in bending. AISC Steel Construction Manual Table 7-20 for heavy hex nut sizes
Steel rod capacity | AISC Steel Construction manual, 13th Ed.
Coupler nuts | ACI 318 – 21.13.3 Mechanical reinforcement
Take-Up Devices | (Not defined by code – see ICC-ES AC316)
Anchorage | ACI 318 – Appendix D
Shear wall drift | Section 4.1.3 of the AWC Special Design Provisions for Wind and Seismic.
Notes: Say
The only part of an overturning rod system not in the code are the optional take-up devices.
Top-plate bearing pressure capacity defined by NDS Supp. Tables 4A & 4B
Steel bearing plates conform to ASTM A36 – allowable bearing stress of the plate in bending dependent on plate geometry: section modulus used with uniform pressure on cantilever moment to find steel bearing pressure capacity (see AISC Steel Construction Manual Table 7-20 for heavy hex nut sizes) – compare to wood bearing capacity
Steel rod capacity defined by AISC Steel Construction Manual, 13th Ed., Equations D2-1 (yielding) & D2-2 (rupture) conforming to ASTM standards A307, A449, or A193 Grade B7
Coupler nuts per ACI 318 – 21.13.3 Mechanical reinforcement
Take-up devices not defined by code – see ICC-ES AC316
Anchorage defined in ACI 318 – Appendix D
Code defined SW drift limitations will control OT rod system deflections or limit system performance – IBC-06 section 2305.3.1 & 2305.3.2
Presenter Note
This slide features information that will be found on the post-training knowledge assessment:
The only part of a shear wall overturning restraint rod system NOT in the code are the:
Steel bearing plates
Threaded rod
Shear wall drift
Take-up devices

## Slide 45: Designing and Specifying Shear Wall Overturning Restraint Rod Systems
Understanding Restraint Rod Systems | Designing and Specifying Shear Wall Overturning Restraint Rod Systems

## Slide 46: Manufacturer Solutions
Understanding Restraint Rod Systems | Designing and Specifying Shear Wall Overturning Restraint Rod Systems
Solutions should address overturning as well as shrinkage that occurs at each level of a multi-story structure.
Shrinkage compensation (take-up) devices are one way to address shrinkage.
Manufacturers differentiate themselves with design services or product and installation enhancements such as color-coded rod ends and bearing plates.
Notes: Do
Discuss the components of a complete system and how manufacturer’s try to differentiate themselves:
Based on offering a complete system, customer support, drawing and design services.
Based on lowest cost, which may not include a complete system or verifiable quality in the components.

## Slide 47: Specification Methods
Understanding Restraint Rod Systems | Designing and Specifying Shear Wall Overturning Restraint Rod Systems
Design Professional Responsibilities
Determine project loading and performance requirements.
Determine best solution to meet requirements (overturning restraint rod vs. conventional holdowns and strapping.
Stipulate (specify) these requirements on the design documents.
Review proposed solutions and shop drawings for conformance to specs and design intent.
Notes: Ask
With a show of hands, who would consider this a complete list?
Does this represent the design process your firm follows?
If not, what would you add or subtract from this list?

## Slide 48: Specification Methods
Understanding Restraint Rod Systems | Designing and Specifying Shear Wall Overturning Restraint Rod Systems
Design Review Checklist for Overturning Restraint Rod Systems
Run type design vs. structural requirements
Rod manufacturer component capacity check
  Rods/steel strength and mill certs
  Bearing plate size and capacity
  Shrinkage compensation devices for compression and tension
    AC 316 compliance
Movement/shrinkage check including maximum rod elongation and maximum deflection per floor
Tension rod location check
Drawing and calculation review
Notes: Do
Comment to audience that a larger checklist is on page 33 of F-L-SRS18 (Strong-Rod Systems Seismic and Wind Restraint Systems Guide) if those have been handed out.

## Slide 49: Specification Methods
Understanding Restraint Rod Systems | Designing and Specifying Shear Wall Overturning Restraint Rod Systems
Design Considerations
Areas of concern????
Performance of the wood structural system, not just the rod system
Cost-based decisions that effect product quality
  Product substitution…Grade stamps and mill certifications please?
Deferred submittal…..Friend of Foe?
Notes: Ask
Who analyzes the performance of the wood structure that the rod system must perform in? Such as: wood deflection limits, shear stress, top plate splice locations, top plate rotation, etc.
How far does the EOR’s responsibility and liability extend in the area of product quality and performance of the system?
Who is responsible if a manufacturer or sub-contractor proposes or substitutes lower cost rod that hasn’t been tested and has no mill certification?
How much control is lost over the specification process when manufacturer’s assume most of the design responsibility, or a contractor selects a product based on cost and not system reliability and whether product performance is verifiable as in the case of non-tested, non-certified steel?

## Slide 50: Specification Methods
Understanding Restraint Rod Systems | Designing and Specifying Shear Wall Overturning Restraint Rod Systems
Specification methods for overturning restraint rod systems
Send loads to manufacturers who optimize the runs.
  Software analysis
  Engineering calculations
Provide loads and generic specifications on drawings, then submit to manufacturer for optimization.
Specify catalog runs from a product catalog.
  Manufacturer can optimize runs during design review process
  Installation drawings and calculations typically provided for EOR review.

## Slide 51: Conclusion
Understanding Restraint Rod Systems | Conclusion

## Slide 52: Course Summary
Understanding Restraint Rod Systems | Conclusion
There are two types of restraint rod systems; one for wind uplift and one for shear wall overturning.
Significant performance differences exist between overturning skipped-floor systems, and all-floors-tied-off systems.
Testing rod systems for uplift has shown that by not accounting for the wood structure in designs, system performance is compromised.
For overturning systems, manufacturer’s have a number of ways to assist the EOR in the design and selection of the system.
Notes: Note: Each bullet comes on screen with a mouse click to allow the presenter time to ask the questions below
Review contents of seminar
Two types of restraint rod systems.
ASK AUDIENCE: “The next time your are designing a restraint rod system, what are the different design considerations you will need to make between these two systems?” (answers are given for uplift, then overturning systems)
Rod location: U= at oc spacings along bearing walls. O=at shear wall ends.
Applied load location: U= Typically at roof level only. O=at each level
Restraints: U=Typically at roof level. O=At each level
Shrinkage: U=At single location. O=Segmented per floor
Differences between overturning skipped floor and all-tied-off systems.
ASK AUDIENCE: “Please answer the following questions and tell me if these factors are cost or performance related? Why?”
“Which system typically has larger post sizes in the upper floors, skipped or tied-off? Why?” A=skipped.
“Which system has increased drift?” A=skipped
“Which system has shrinkage compensation per floor?” A=tied-off.
“Which system has more redundancy?” A=tied-off.
“Which system has more construction stability?” A=tied-off.
3.System performance is compromised when the wood structure is ignored.
ASK AUDIENCE:
“What parts of the wood structure should be accounted for in rod system design?”
Answer=top plate deflection, to plate rotation, top plate splice requirements, top plate crushing at bearing plate, shrinkage.
4. …regarding manufacture involvement in the design process…
ASK AUDIENCE:
“What are 3 ways to enlist the services of a manufacturer in the overturning rod design process?”
Answer= a. Send loads to manufacturer to optimize runs through software analysis and engineering calculations. (see sample output in participant’s guide)
b. Provide loads and generic specs on drawings, then submit to manufacturer for optimization.
c. Specify catalog runs on specifications and manufacturer will optimize during the design review process.

## Slide 53: Course Completion
Understanding Restraint Rod Systems | Conclusion
Simpson Strong-Tie
This concludes the continuing education course.
For a library of Simpson Strong-Tie courses,
visit strongtie.com/workshops.
Notes: Do
Draw the meeting to a close. Hand out literature and business cards.
Say
If you have ongoing projects that you would be interested in reviewing together, please let me know.

## Slide 54: Next Steps
Understanding Restraint Rod Systems | Conclusion
AIA: For those seeking AIA LU/HSW: You will receive an email with a link allowing access to print your Certificate. Congratulations, you will have earned 1 LU/HSW credit. If your AIA member number has been inserted into your profile, Simpson Strong-Tie will report your credits on your behalf to the AIA. No test is required in order to receive HSW credits.
IACET: For those seeking IACET CEUs: You will receive an email with a link allowing access to print your Certificate of Attendance and instructions directing you to the Simpson Student Center to take the exam before credits can be awarded. Once the exam is taken and passed, you will have earned 0.1 CEUs (1 hour of credit). You can then access your Certificate of Completion from the Course Content tab. You must self-report your credits to your certifying organization or agency.
If you have questions or need assistance, please contact training@strongtie.com.
Notes: Presenter Notes:
Review the email and notification process as outlined in this slide.
AIA LUs:
For those that want AIA HSW credit, be sure to provide your AIA number on the sign-in sheet and Simpson will report your credits to the AIA on your behalf.
No test is required for AIA credit.
CEUs:
For those seeking CEUs, watch for an email with instructions to access the online test. After you have passed the test, you may access your Certification of Completion from the course content tab.
You must self-report your credits to your certifying organization or agency.

## Slide 55: Next Steps
Understanding Restraint Rod Systems | Conclusion
ICC: For those seeking ICC CEUs: You will receive an email with a link allowing access to print your Certificate. Congratulations, you will have earned 0.1 ICC CEU (1 hour of credit). Please make sure your ICC member number has been inserted into your profile. It is your responsibility to self-report your credits to the ICC. Please retain your Completion Certificate for your records.
IACET: For those seeking IACET CEUs: You will receive an email with a link allowing access to print your Certificate of Attendance and instructions directing you to the Simpson Student Center to take the exam before credits can be awarded. Once the exam is taken and passed, you will have earned 0.1 CEUs (1 hour of credit). You can then access your Certificate of Completion from the Course Content tab. You must self-report your credits to your certifying organization or agency.
If you have questions or need assistance, please contact training@strongtie.com.
Notes: Presenter Notes:
Review the email and notification process as outlined in this slide.
Watch for an email directing you to the Student Center to print your certificate.
No test is required for ICC credit. You must self-report your credits to ICC.
For those seeking general IACET CEUs after you have passed the online test, you may access your Certification of Completion from the course content tab. You must self-report your credits to your certifying organization or agency.