## Slide 1
PLEASE READ
Dear Instructor,
This presentation is available in both AIA and ICC versions.
For AIA: Right click and un-hide slides 5 and 73
For ICC: Right click and un-hide slides 6 and 74
Slide 2 is an optional slide

## Slide 2: Welcome!
We will begin in a few minutes.
Please be sure to sign the registration form to receive credit for attending today’s learning event.
Notes: Do
Meet and greet participants as they arrive. Start learning names, make them feel comfortable and settled in the training environment.
Make sure your opening has PUNCH:
Promotes interest and enthusiasm for the session
Understands participants’ needs
Notes ground rules and administrative/housekeeping needs
Clarifies expectations
Helps everyone get to know each other
State your expectations around participation: Make it known and expected that you will be encouraging and inviting participation.
Tips to facilitate connections:
Thank participants for their contribution (ideally with their name)
Praise participation (especially the first person to speak)
Express confidence in the participants
Restate what someone said earlier (“As John mentioned earlier….”)
Encourage participants to share what others were saying in their small groups (without naming names)
Invite someone you heard speaking in a small group to share with the entire group
Encourage the group to respond to an individual’s comment/question
Physical Room / Training Venue Setup:
If using a table arrangement, consider grouping 4 to 6 students at each station. This will help encourage conversation and discussion during activities.
Get people standing at regular intervals during your training session. Research shows that people learn up to 15% more when standing up!

## Slide 3
AIA Provider: 50119826 | AIA Course: AIA-SDPWS116 | ICC Provider: 1025 | ICC Course: 8302
Instructor Name
Title / Role
Notes: Do
Be sure to mention the AIA provider and course number for those requiring AIA credit. Ask the attendees to write down this information for reference. For AIA members, we will submit this information for them.

## Slide 4: Credit Information
IACET Accreditation Information
Simpson Strong-Tie® has been accredited as an Authorized Provider by the International Association for Continuing Education and Training (IACET). As a result of their Authorized Provider accreditation status, Simpson Strong-Tie® is authorized to offer IACET CEUs for its programs that qualify under the ANSI/IACET Standard.
This course offers 0.1 CEU (1 hour of credit).
Notes: Review the submission process for audiences requiring IACET CEU credits.
For those seeking IACET credit, they must take and pass the online test. They must self-report CEU credits to their certifying organization or agency.
Explain the credits awarded: IACET: 0.1 (Equivalent to 1 hour) CEUs.

## Slide 5: Credit Information
AIA Member Information
This course is registered with AIA CES for continuing professional education. As such, it does not include content that may be deemed or construed to be an approval or endorsement by the AIA of any material of construction or any method or manner of handling, using, distributing, or dealing in any material or product. Upon completion of this course, Credit(s) earned will be reported to AIA CES for AIA members who pass the course and have entered their AIA member number on their Simpson profile page. A link to the Certificate of Completion will be available upon completion of this course. Only AIA LU/HSW will be reported.
This course offers 1 LU/HSW credit.
AIA Course Number: AIA-SDPWS116
Notes: Presenter Information
NOTE: Please be sure each attendee LEGIBLY signs the event sign-in sheet.
Say
All questions concerning proprietary products will be addressed after the conclusion of the AIA portion of the presentation. The meeting format is 50 minutes of content, followed by 10 minutes of Q & A.
Do
Explain the credits awarded for:
AIA: 1LU/HSW credit.
IACET: 0.1 (Equivalent to 1 hour) CEU credits.
Review the submission process for audiences requiring either AIA LU/HSW (health, safety and welfare) credits or CEU credits:
For those seeking AIA HSW credit, there is no test required. AIA members must be sure to provide their AIA member number on the sign-in sheet. Please make sure name, email and AIA member number are clearly printed so Simpson can report credits to the AIA on their behalf.
For those seeking IACET credit, they must take and pass the test. They must self-report CEU credits to their certifying organization or agency.

## Slide 6: Credit Information, cont.
ICC Member Information
This course has been approved by the International Code Council (ICC) for continuing professional education. For learners that complete this course, it is your responsibility to self-report your credits to the ICC. Please retain your Completion Certificate for your records.
Be sure that your ICC ID number is provided on the sign-in sheet or in your Simpson profile in order to have it displayed on your certificate.
This course offers 0.1 CEU (1 hour of credit).
ICC Course Number: 8302
Notes: Review the submission process for audiences requiring ICC CEU credits.
For those seeking ICC credit, there is no test required. ICC members must provide their ICC ID number on the sign-in sheet or in their Simpson profile in order to have it displayed on their certificate. It is the responsibility of the participant to self-report their credits to the ICC. Ask them to retain their Completion Certificate for their records.
Explain the credits awarded: ICC: 0.1 (Equivalent to 1 hour) CEUs.

## Slide 7: Additional Credit Offerings
Visit
strongtie.com/workshops
for more information
Course Name | CEUs | AIA | ICC
Introduction to Deck Design | 0.1 | ✔ | ✔
Introduction to Wind Design and the Wood Frame Construction Manual | 0.1 | ✔ | ✔
Shear Walls and Lateral Bracing in Light Frame Construction | 0.1 | ✔ | ✔
Understanding Restraint Rod Systems | 0.1 | ✔ | ✔
Cracking the Concrete Anchor Codes | 0.1 | ✔ | ✔
Concrete Deterioration | 0.1 | ✔ | ✔
Moment Frame Design | 0.1 | ✔ | ✔
Introduction to Wind Code Provisions and Meteorological Concepts | 0.1 | ✔ | ✔
Wind Design in Accordance with ASCE 7-10 | 0.1 | ✔ | ✔
Wood Framed Seismic Design 1: Code Provisions, Design Parameters | 0.1 | ✔ | ✔
Notes: Do
Explain that we have additional PK topics available that offer credit for ICC members and HSW credits for AIA members.
Explain that we have a library of online courses available in our Simpson Student Center that also offer ICC and AIA HSW credits. They can access our online courses at strongtie.com/workshops.

## Slide 8: Course Description
Diaphragm Design with 2015 SDPWS
This course was created to help familiarize structural engineers, designers, and architects with code-compliant diaphragm design techniques using the SDPWS.
Course Contents
Introduction / Learning Objectives
Lesson 1: Lateral Loads in a Wood-Frame Structure
Lesson 2: Code and Standard Provisions
Lesson 3: Diaphragm Behavior and Analysis
Lesson 4: Distribution of Diaphragm Forces
Lesson 5: Blocked vs. Unblocked Diaphragms
Wrap Up / Questions
Notes: Do
Review the course description and course contents.

## Slide 9: Learning Objectives
Upon completion of this seminar, you will be able to:
Explain how lateral loads are transferred throughout a wood-frame structure
Identify the code and standard provisions related to the design of diaphragms
Determine when a diaphragm may be classified as rigid, flexible, or semi-rigid for analysis purposes
Explain how forces are distributed to different elements within the diaphragm
Describe the differences between blocked and unblocked diaphragms
Notes: Do
Review the learning objectives for the course.
Inform students that the assessment questions will be based on these learning objectives. Slides that may contain information relevant to the test have an orange graduation cap located in the bottom-left corner.

## Slide 10
Lateral Loads in a Wood-Frame Structure
After completing this lesson, you will be able to:
Explain how lateral loads are transferred throughout a wood-frame structure
L
1
Notes: Do
Review the lesson title and objective.

## Slide 11: Continuous Load Path
Continuous load path: system of connections and elements that tie the structure together from the roof to the foundation.
[
]
The main elements of a
wood-frame building that
transfer lateral loads are
diaphragms and shear walls
●●●
Secure roof
to upper story
Secure upper story to first floor
Secure first floor to cripple wall
Secure cripple wall to foundation
Notes: Say
When designing a building, a basic consideration is that each structural element must be designed to carry a load. These loads must be transferred through the structure’s elements and connections into the foundation.
The load path is this transfer of forces through the structure.
Lateral loads are forces applied to a building parallel to the ground.
The main elements of a wood-frame building that transfer lateral loads are shear walls and diaphragms.

## Slide 12: Load Path Requirements
Complete load path is not just a design philosophy—it is required by the building code.
IBC 1604.4 Analysis
IRC R301.1
Notes: Optional Slide
Say
Complete load path is not just a design philosophy—it is required by the building code.
International Building Code 1604.4 Analysis states:
Any system or method of construction to be used shall be based on a rational analysis in accordance with the well-established principles of mechanics. Such analysis shall result in a system that provides a complete load path capable of transferring loads from their point of origin to the load resisting elements.
International Residential Code R301.1 states:
The construction of buildings and structures in accordance with the provisions of this code shall result in a system that provides a complete load path that meets all requirements for the transfer of all loads from their point of origin through the load-resisting elements to the foundation.

## Slide 13: Main Types of Lateral Loads
Seismic Loads
Wind Loads
2
MAIN
lateral
loads
to consider
when designing
Notes: Say
Wind and seismic loads are the most common loads that shear walls are designed to carry.
Do
Review graphic.

## Slide 14: Wind Loads on a Structure
WIND
Notes: Say
Wind loads create pressure on a structure, causing lateral and vertical forces.
Do
Click for animation between steps.
Say
Wind flows over and around the structure.
Positive pressure is applied perpendicular to windward walls.
Positive or negative pressure is applied perpendicular to the windward roof surface depending on roof pitch and building dimensions.
Negative pressure is applied perpendicular to the leeward roof surface.
Negative wind loads are applied perpendicular to the leeward wall surface.
Do
Click to show lateral forces animation.
Say
The floor or roof diaphragm distributes these wind forces to the shear walls.
Do
Click to show resisting lateral force animation.
Say
The shear walls then transfer the wind forces down to the foundation.

## Slide 15: Seismic Loads on a Structure
Seismic forces can be:
Lateral
(side-to-side)
Vertical
(up-and-down)
Notes: Say
Earthquake forces differ from wind forces as they are generated from ground movement at the base of the structure and the structure’s own mass creates inertia forces that distribute throughout the structure. Earthquake forces can be both lateral (side-to-side) and vertical (up-and-down).

## Slide 16: Reactions to Lateral Loads
Racking
When lateral forces engage the side of a structure, the load may cause it to lean over (rack) to one side.
Sliding
Lateral forces exerted against the side of a structure can also cause it to slide off of its foundation.
Overturning
When the structure is anchored in place to limit racking or sliding, the lateral force of wind or seismic loading causes the structure to rotate or overturn.
Notes: OPTIONAL SLIDE – Not necessary since this is more focused on shear walls rather than diaphragms.
Say
Structures require lateral force-resisting systems in order to resist racking, sliding and overturning caused by wind or seismic forces.
When lateral (wind or seismic) forces engage the diaphragm of a structure, it’s easy to visualize the force pushing horizontally on the top of the shear wall. Sheathing then transfers the shear from the top of the wall to the bottom of the wall while holding the wall together to resist racking. If the bottom plate of the wall is anchored to the foundation to resist sliding; the far end of the wall will press down (compression force) and the near side of the wall will lift up (tension force) – this is overturning.

## Slide 17: Shear Loads Acting Through a Diaphragm
Compression Chord
Tension Chord
Shear Wall Below Floor
Shear Wall Below Floor
Exaggerated Deflected Shape of Diaphragm
Notes: Say
When subjected to wind loads, the walls push or pull the floor or roof system (diaphragm) in the direction of the wind.
The floor or roof diaphragm is supported by shear walls parallel to the load.

## Slide 18: Resisting Lateral Loads
1
Roof
Diaphragm-
to-Wall
2
Through Upper
Story Wall
3
Floor-to-
Floor
4
Through First
Story Wall
5
Wall-to-
Foundation
Notes: Say
Seismic and wind forces need to be resisted at various points along the load path from the roof to the foundation.
Roof Diaphragm-to-Wall: The diaphragm transfers shear load into the blocking via the boundary nailing (which is 6” o.c. max). The blocking transfers the shear load into the wall top plates via clips.
Through Upper Story Wall: Shear from the top plate to bottom plate is typically transferred via sheathing by fastening it to top and bottom plates. Overturning forces are typically transferred through stud compression and bearing as well as stud tension and holdown anchors.
Floor-to-Floor: The shear load from the roof level is transferred from the upper story sole plate to the rim joist via nails or plates. Shear load from the floor diaphragm is transferred from the floor sheathing to the rim board via the boundary nailing. The combined roof and floor shear load is typically transferred from the rim joist to the lower story wall top plate.
Through First Story Wall: Shear from the top plate to bottom plate is typically transferred via sheathing by fastening it to top and bottom plates. Overturning forces are typically transferred through stud compression and bearing as well as stud tension and holdown anchors.
Wall-to-Foundation: The shear wall uses sill bolts transfers the induced shear forces to the foundation. Additionally, mudsill anchors or post installed anchors can be used as alternatives to cast-in-place sill bolts.

## Slide 19: Diaphragm Definition
Diaphragm: a flat bracing system acting like a deep, thin beam, used to transfer loads to shear walls or frame. The term “diaphragm” is usually applied to roofs and floors.
[
]
2007 APA, The Engineered
Wood Association
Notes: Say
Diaphragms are the horizontal elements in the lateral force-resisting system. A diaphragm is a flat bracing system acting like a deep, thin beam, used to transfer loads to shear walls or frame. The term is usually applied to roofs and floors. (2007 APA, The Engineered Wood Association)
In comparison, a shear wall is basically a vertical, cantilevered diaphragm fixed at its base.

## Slide 20: Diaphragm Components
Diaphragms are made of
the following components
Chords
Collectors
Sheathing
:
w = lateral load (plf)
Notes: Say
Diaphragms are made up of the following components:
Chords – Boundary members that are perpendicular to the lateral load. They carry the axial force created by the moment (like flanges of a steel wide-flange beam).
Collectors (Drag Struts) – Boundary members that are parallel to the lateral load. They transmit horizontal diaphragm reactions to the shear walls below.
Do
Click to show other figure with loading in the longitudinal direction.
Say
Important to Note: The same structural members (i.e. wood top-plates) may be chords and struts depending on which direction the diaphragm is loaded (longitudinally or transversely).
Sheathing – Either lumber sheathing (like a residential deck) or wood structural panel sheathing (plywood or OSB) which is fastened to the structural members below to resist shear forces.
Quiz Note
This slide features information that will be found on the post-course knowledge assessment.
Match the term with the correct definition:
Chords :: Carry the axial force created by the moment (like flanges of a steel wide-flange beam) and are perpendicular to lateral load.
Collectors (Drag Struts) :: Boundary members that are parallel to the lateral load. They are designed to transmit horizontal diaphragm reactions to the shear walls.
Sheathing :: A layer of boards or other wood or fiber materials applied to the outer studs, joists, and rafters of a building to strengthen the structure.

## Slide 21: Diaphragm Design Considerations
The following should be considered for diaphragm design:
Diaphragm shear capacity
Chord design
Collector (strut) design
Diaphragm deflection
❶
❷
❸
❹
[
]
We’ll cover these
topics in the
upcoming lessons
Notes: Say
The following should be considered for diaphragm design:
Diaphragm shear capacity (depends on sheathing thickness, orientation, fastener size and pattern, and framing lumber type and dimensions).
Chord design (tension and compression capacity and member to member transfer – i.e. top plate splice design).
Collector (strut) design (struts designed to transfer drag force between shear walls).
Diaphragm deflection (this is important for rigid vs. flexible diaphragm analysis).
We’ll cover these topics in the upcoming lessons.
Quiz Note
This slide features information that will be found on the post-course knowledge assessment.
Diaphragm shear capacity depends on:
Sheathing thickness and orientation
Fastener size and pattern
Framing lumber type and dimensions
All of the above

## Slide 22: Lesson One Complete
Now that you’ve completed this lesson, you should be able to:
Explain how lateral loads are transferred throughout a wood-frame structure
Notes: Do
Review the lesson objective summary.

## Slide 23
Code and Standard Provisions
After completing this lesson, you will be able to:
Identify the code and standard provisions related to the design of diaphragms
L
2
Notes: Do
Review the lesson title and objective.

## Slide 24: Experiences with Diaphragm Design
Overcoming problems with diaphragm design:
Break into groups of 2 or 3
Find out who drove the furthest this morning
Within your group, take one minute per person to find out:
    What was the most problematic situation you’ve seen or experienced when designing a diaphragm for a wood-frame structure?
    How could this problem have been prevented?
Notes: Audience Interaction: 5 minutes.
Say
Before we begin our next lesson, I’d like to get some feedback on your experience designing diaphragms.
So here’s what I’d like to do: Turn to your neighbors and break up into groups of __________ (2 or 3 depending on the size of the audience). Then take one minute per person and answer the following questions.
Who drove the furthest to be here this morning?
What was the most problematic situation you’ve seen or experienced when designing a diaphragm for a wood-frame structure?
How could this problem have been prevented?
Pick one scenario from your group to discuss with the group.
The person who drove the furthest today will be the spokesperson.
Ask
Ok, raise your hand… Who has one they’d like to discuss?
Do
Call on one or two groups and ask what the problem was and how they solved it.
Ask
Did anyone with a similar problem solve it a different way?
Follow up: How did you / would you solve it?
Anyone else?
Do
Keep an eye on the clock and end the discussion after a couple minutes.
Say
It’s easy to see that diaphragm design can be challenging. Hopefully after today, you will be aware of some other options and some tools to assist in the process.
Do
Return to the presentation.

## Slide 25: IBC §2305 and SDPWS
SECTION 2305
GENERAL DESIGN REQUIREMENTS FOR LATERAL-FORCE-RESISTING SYSTEMS
2305.1 General. Structures using wood shear walls and dia-phragms to resist wind, seismic and other lateral loads shall be designed and constructed in accordance with the provisions of this section. Alternatively, compliance with the AF&PA SDPWS shall be permitted subject to the limitations therein and the limitations of this code.
IBC 06
IBC 09, 12 & 15
SECTION 2305
GENERAL DESIGN REQUIREMENTS FOR LATERAL-FORCE-RESISTING SYSTEMS
2305.1 General. Structures using wood shear walls or wood-frame diaphragms to resist wind, seismic and other lat-eral loads shall be designed and constructed in accordance with the AF&PA SDPWS and the applicable provisions of Sec-tions 2305, 2306 and 2307.
Notes: Say
Historically, the IBC contained provisions and design tables for nailed and stapled wood diaphragms and shear walls. Prior to the 2009 edition, you were permitted to use the SDPWS as an alternative to these provisions, but still had to comply with requirements in the IBC.
Do
Click to show images and information for “IBC 09, 12, and 15.”
Say
Since 2009, the IBC states that “Structures using wood-frame shear walls or wood-frame diaphragms to resist wind, seismic or other lateral loads shall be designed and constructed in accordance with AF&PA SDPWS…” When the 2012 IBC came out, it had removed all nailed diaphragm and shear wall tables since they were duplicates to the SDPWS tables (however, the stapled tables remained).

## Slide 26: IBC §2306 and SDPWS
http://www.awc.org/codesstandards.php
IBC 09, 12 & 15
SECTION 2306
ALLOWABLE STRESS DESIGN
2306.2 Wood-frame diaphragms. Wood-frame diaphragms shall be designed and constructed in accordance with AF&PA SDPWS. Where panels are fastened to framing members with staples, requirements and limitations of AF&PA SDPWS shall be met and the allowable shear values set forth in Table 2306.2(1) or 2306.2(2) shall be permitted. The allowable shear values in Tables 2306.2(1) and 2306.2(2) are permitted to be increased 40 percent for wind design.
Notes: Say
Section 2306.2 (Wood-frame Diaphragms) simply refers to the SDPWS now -- except for the references to stapled tables.
Do
Point out that all AWC documents are now available for free viewing/downloading from their website at www.awc.org/standards/sdpws.php.

## Slide 27: Continuous Load Path is Required
4.1.1 Design Requirements
The proportioning, design, and detailing of engi-neered wood systems, members, and connections in lateral force-resisting systems shall be in accordance with the reference documents in 2.1.2 and provisions in this chapter. A continuous load path, or paths, with ad-equate strength and stiffness shall be provided to trans-fer all forces from the point of application to the final point of resistance.
Notes: Say
In Section 4.1.1 of the 2015 SDPWS, it states: “A continuous load path, or paths, with adequate strength and stiffness shall be provided to transfer all forces from the point of application to the final point of resistance.”
Do
Be sure to reinforce that Section 4.1.1 mentions both strength and stiffness.

## Slide 28: Factoring Nominal Unit Shear Capacities
Nominal Capacities
ASD = Nominal / 2.0
LRFD = Nominal x 0.8
Diaphragm Tables
Table 4.2A: Wood-Frame Diaphragms, Blocked
Table 4.2B: Wood-Frame Diaphragms, Blocked, High Load
Table 4.2C: Wood-Frame Diaphragms, Unblocked
4.2.3 Unit Shear Capacities
Tabulated nominal unit shear capacities for seismic design are provided in Column A of Tables 4.2A, 4.2B, 4.2C, and 4.2D; and for wind design in Column B of Tables 4.2A, 4.2B, 4.2C, and 4.2D. The ASD allowable unit shear capacity shall be determined by dividing the tabulated nominal unit shear capacity, modified by ap-plicable footnotes, by the ASD reduction factor of 2.0. The LRFD factored unit resistance shall be determined by multiplying the tabulated nominal unit shear capacity, modified by applicable footnotes, by a resistance factor, φD, of 0.80. No further increases shall be permitted.
Notes: Say
Factoring nominal unit shear capacities to ASD or LRFD levels is a simple process covered briefly in Section 4.2.3 “Unit Shear Capacities.”
To convert the capacity to ASD, divide the nominal amount by 2.
To convert the capacity to LRFD, multiply the nominal amount by 0.8.
Tabulated nominal unit shear capacities for seismic and wind design can be found in Tables 4.2A, 4.2B, 4.2C and 4.2D (lumber, rarely used). Note that the diaphragm capacity is dependent upon direction of the continuous panel joints relative to the direction of load and direction of framing members, but is independent of panel orientation.
Do
Review terminology if necessary.
ASD = Allowable Stress Design. A method of proportioning structural members and their connections such that stresses do not exceed specified allowable stresses when the structure is subjected to appropriate load combinations (also called working stress design).
LRFD = Load and Resistance Factor Design. A method of proportioning structural members and their connections using load and resistance factors such that no applicable limit state is reached when the structure is subjected to appropriate load combinations.
Quiz Note
This slide features information that will be found on the post-course knowledge assessment.
Tabulated nominal unit shear capacities for high load blocked wood structural panel diaphragms are provided in:
SDPWS Section 4.3.1
IBC Section 2305.1.2.1
SDPWS Table 4.2B
ASCE 7 Table 6-2

## Slide 29: Tabulated Nominal Unit Shear Capacities
Notes: Say
Here we have Table 4.2A “Nominal Unit Shear Capacities for Blocked Wood-Frame Diaphragms” shown on the slide.
Let’s zoom in for a better look.
Do
Click for animation.
Say
The table relates nominal unit shear capacity with diaphragm sheathing thickness, nail size and spacing, and sheathing grade to help determine the appropriate design and construction of the diaphragm. These tabulated values help ensure that the capacity of your diaphragm design will exceed the demand shear.
In addition to nominal unit shear capacities, the table provides apparent shear stiffness values (Ga) for use in the deflection calculation (which we will discuss in a later slide).

## Slide 30: Tabulated Nominal Unit Shear Capacities, cont.
Remember, these are Nominal Values – for ASD, divide value by 2
Notes: Say
Please remember that these are nominal values. As we discussed previously, to convert to ASD levels, we will need to divide the nominal value by 2.
Do
Review example on page 7 of Participant Handout.

## Slide 31: Maximum Aspect Ratio
Diaphragm Sheathing Type | Max L/W Ratio
Wood structural panel, unblocked | 3:1
Wood structural panel, blocked | 4:1
Single-layer straight lumber sheathing | 2:1
Single-layer diagonal lumber sheathing | 3:1
Double-layer diagonal lumber sheathing | 4:1
Table 4.2.4 Maximum Diaphragm Aspect Ratios
Horizontal or Sloped Diaphragms
Notes: Say
AWC’s AF&PA 2015 SDPWS Table 4.2.4 gives diaphragm aspect ratio limits as follows:
Wood structural panel, unblocked: 3:1
Wood structural panel, blocked: 4:1
Single-layer straight lumber sheathing: 2:1
Single-layer diagonal lumber sheathing: 3:1
Double-layer diagonal lumber sheathing: 4:1
These aspect ratios apply to horizontal or sloped diaphragms.
Quiz Note
This slide features information that will be found on the post-course knowledge assessment.
What is the maximum aspect ratio for a blocked wood structural panel diaphragm?
2:1
3:1
4:1
No limit

## Slide 32: Open Front Structures
For resistance to seismic loads, wood-frame diaphragms in open front structures shall comply with the requirements of SDPWS Section 4.2.5.2.
[
]
This design technique
is not necessarily
desirable, especially
in seismic-prone areas
Notes: Say
In the 2015 edition of SDPWS, Section 4.2.5.2 Open Front Structures has been revised with terminology more consistent with ASCE 7-10 to clarify design requirements. Because of their increased vulnerability to torsional response, cantilevered diaphragms for open front structures have increased limitations compared to torsionally irregular structures that are not open front.
It should be noted that this design technique is not necessarily desirable. Problems involving rotation contributed to many failures of “open front” or “tuck under parking” in residential buildings in the 1971 San Fernando, 1989 Loma Prieta and 1994 Northridge earthquakes.
Say (Optional)
Wood-frame diaphragms in open front structures shall comply with all of the following:
The diaphragm conforms to Sections 4.2.7.1, 4.2.7.2, or 4.2.7.3. These sections provide the requirements for diaphragms to be used to resist seismic and wind forces.
The L/W ratio of the diaphragm (as shown in figure 4A) is not greater than 1.5:1 when sheathed in conformance with 4.2.7.1 or not greater than 1:1 when sheathed in conformance with 4.2.7.2 or 4.2.7.3. (Torsionally irregular structures have additional requirements).
For loading parallel to the open side, diaphragms shall be modeled as semi-rigid or idealized as rigid, and the maximum story drift at each edge of the structure shall not exceed the ASCE 7 allowable story drift when subject to seismic design forces including torsion and accidental torsion and shall include shear and bending deformations of the diaphragm.
The cantilevered diaphragm length, L’, (normal to the open side) shall not exceed 35 feet.
See Section 4.2.5.2 for more detailed requirements and exceptions.

## Slide 33: Diaphragm Deflection
    where:
    δdia = maximum diaphragm deflection determined by elastic analysis, in
    v = induced unit shear in diaphragm, lb/ft
    L = diaphragm length, ft
    E = modulus of elasticity of diaphragm chords, psi
    A = area of chord cross-section, in2
    W = diaphragm width, ft
    Ga = apparent diaphragm shear stiffness from nail slip and panel shear deformation, kips/in (from column A, Tables 4.2A through 4.2D)
    x = distance from chord splice to nearest support, ft
    Δc = chord splice slip, in, at the induced unit shear in diaphragm
(Eq. 4.2-1)
Notes: Say
Per Section 4.2.2, Calculations of diaphragm deflection shall account for bending and shear deflections, fastener deformation, chord splice slip, and other contributing sources of deflection.
The diaphragm deflection, δdia, is calculated by use of Equation 4.2-1 shown on the slide.
Do
Review the parameters for the shear wall deflection calculation.

## Slide 34: Diaphragm Deflection, cont.
Bending
Shear
Bending
CHORDS
SHEATHING
CHORD SPLICES
Chord Deformation (excluding slip)
Panel Deformation & Nail Slip
Chord Splice Slip
Notes: Say
The first term calculates the bending deflection of the diaphragm.
The next term gives you the deflection from shear forces and fastener deformation.
The last term calculates the deflection from splice slip.
Quiz Note
This slide features information that will be found on the post-course knowledge assessment.
Which of the following is not a term of the diaphragm deflection calculation:
Tension and Compression
Chord Deformation
Panel Deformation and Nail Slip
Chord Splice Slip

## Slide 35: High Load Blocked Diaphragms
Figure 4B
High load blocked diaphragms have a significantly higher shear capacity by utilizing multiple rows of fasteners
Wider blocking or supporting members are often required to avoid splitting
Minimum 3” nominal depth for blocked edges per SDPWS 4.2.7.1.2 item 4
1/2”
1/2”
3/8” min
3/8” min
Fastener spacing
3” nominal
2 lines of fasteners
2-1/2”
Notes: Say
High load blocked diaphragms have a significantly higher shear capacity by utilizing multiple rows of fasteners. Wider blocking or supporting members are often required to avoid splitting.
Figure 4B shows a 3” nominal supporting member with two lines of fasteners on each of the two panels. The figure satisfies SDPWS Section 4.2.7.1.2 item 4, which states “The depth of framing members and blocking into which the nail penetrates shall be 3” nominal or greater.”
This clarification is new to the 2015 SDPWS and was made to be consistent with similar provisions for stapled high load diaphragms in 2015 IBC Table 2306.2(2) footnote (e).

## Slide 36: Lesson Two Complete
Now that you’ve completed this lesson, you should be able to:
Identify the code and standard provisions related to the design of diaphragms
Notes: Do
Review the lesson objective summary.

## Slide 37
Diaphragm Behavior & Analysis
After completing this lesson, you will be able to:
Determine when a diaphragm may be classified as rigid, flexible, or semi-rigid for analysis purposes
L
3
Notes: Do
Review the lesson title and objective.

## Slide 38: Introduction to Distribution of Shear
4.2.5 Horizontal Distribution of Shear
The distribution of shear to vertical resisting ele-ments shall be based on an analysis where the dia-phragm is modeled as semi-rigid, idealized as flexible, or idealized as rigid.
❶
❷
❸
Idealized as
Flexible
Idealized as
Rigid
Modeled as
Semi-Rigid
❹
Enveloped
Analysis
●●●
Notes: Say
The method used to distribute shear to the vertical resisting elements is dependent on whether we idealize the diaphragm as rigid or flexible, model it as semi-rigid, or do an enveloped analysis. In the 2015 version of SDPWS, Section 4.2.5 was revised so that the terms “idealized as flexible”, “idealized as rigid”, and “modeled as semi-rigid” are consistent with ASCE 7-10.
Wood diaphragms will always have some rigidity. They can never be fully flexible or fully rigid, but we can idealize them as such if certain conditions are met. The purpose of idealizing a diaphragm as flexible or rigid is to simplify the structural analysis for the distribution of shear.
While there are requirements specific to each of those methods, the type of load (wind or seismic) will also influence how we select the proper method. More on that to come…

## Slide 39: Idealized as Flexible
Δsw
Δdia
Diaphragm may be idealized as flexible when Δdia > 2(Δsw)
A diaphragm is flexible for the purpose of distribution of story shear when the computed maximum in-plane deflection of the diaphragm under lateral load is greater than two times the average deflection of adjoining vertical elements (i.e. shear walls) or the story below under the same lateral load.
Flexible diaphragm conditions:
ASCE 7-10 Section 12.3.1.1 (seismic)
ASCE 7-10 Section 26.2 (wind)
Notes: Say
A diaphragm is flexible for the purpose of distribution of story shear when the computed maximum in-plane deflection of the diaphragm under lateral load is greater than two times the average deflection of adjoining vertical elements (i.e. shear walls) or the story below under the same lateral load.
Flexible diaphragm conditions are located in ASCE 7-10 Section 12.3.1.1 for seismic and in ASCE 7-10 Section 26.2 for wind.

## Slide 40: Idealized as Flexible, cont.
ASCE 7-10 Diaphragm Conditions
12.3.1.1 Flexible Diaphragm Condition
Diaphragms constructed of untopped steel decking or wood structural panels are permitted to be idealized as flexible if any of the following conditions exist:
In structures where the vertical elements are steel braced frames, steel and concrete composite braced frames or concrete, masonry, steel, or steel and concrete composite shear walls.
In one- and two-family dwellings.
In structures of light-frame construction where all of the following conditions are met:
  Topping of concrete or similar materials is not placed over wood structural panel diaphragms except for nonstructural topping no greater than 1 ½ in. (38 mm) thick.
  Each line of vertical elements of the seismic force-resisting system complies with the allowable story drift of Table 12.12-1.
  26.2 DEFINITIONS
  DIAPHRAGM: Roof, floor, or other membrane or bracing system acting to transfer lateral forces to the vertical Main Wind-Force Resisting System. For analysis under wind loads, diaphragms constructed of untopped steel decks, concrete filled steel decks, and concrete slabs, each having a span-to-depth ratio of two or less, shall be permitted to be idealized as rigid. Diaphragms constructed of wood structural panels are permitted to be idealized as flexible.
Notes: Do (if time allows)
Review ASCE 7-10 Sections 12.3.1.1 and 26.2.
---
ASCE 7 Section 12.3.1.1 Flexible Diaphragm Condition
Diaphragms constructed of untopped steel decking or wood structural panels are permitted to be idealized as flexible if any of the following conditions exist:
In structures where the vertical elements are steel braced frames, steel and concrete composite braced frames or concrete, masonry, steel, or steel and concrete composite shear walls.
In one- and two-family dwellings.
In structures of light-frame construction where all of the following conditions are met:
  Topping of concrete or similar materials is not placed over wood structural panel diaphragms except for nonstructural topping no greater than 1 ½ in. (38 mm) thick.
  Each line of vertical elements of the seismic force-resisting system complies with the allowable story drift of Table 12.12-1.
  ASCE 7 Section 26.2
  DIAPHRAGM: Roof, floor, or other membrane or bracing system acting to transfer lateral forces to the vertical Main Wind-Force Resisting System. For analysis under wind loads, diaphragms constructed of untopped steel decks, concrete filled steel decks, and concrete slabs, each having a span-to-depth ratio of two or less, shall be permitted to be idealized as rigid. Diaphragms constructed of wood structural panels are permitted to be idealized as flexible.

## Slide 41: Idealized as Rigid
Diaphragm may be idealized as rigid when Δdia ≤ 2(Δsw)
Δsw
Δdia
A diaphragm is rigid for the purpose of distribution of story shear and torsional moment when the computed maximum in-plane deflection of the diaphragm itself under lateral load is less than or equal to two times the average deflection of adjoining vertical elements of the lateral force-resisting system of the associated story under equivalent tributary lateral load.
Notes: Say
When diaphragms are idealized as rigid, shear forces distributed based on relative stiffness of vertical-resisting elements (i.e. shear walls) of the story below.
A diaphragm is rigid for the purpose of distribution of story shear and torsional moment when the computed maximum in-plane deflection of the diaphragm itself under lateral load is less than or equal to two times the average deflection of adjoining vertical elements of the lateral force-resisting system of the associated story under equivalent tributary lateral load. For analysis purposes, it can be assumed that a rigid diaphragm distributes story shear and torsional moment into lines of shear walls by the relative lateral stiffness of the shear walls.
Quiz Note
This slide features information that will be found on the post-course knowledge assessment.
True or false: A diaphragm may be idealized as rigid when the maximum in-plane deflection of the diaphragm is less than or equal to two times the average deflection of adjoining vertical elements:
True
False

## Slide 42: Semi-Rigid and Enveloped Analysis
Semi-Rigid Analysis
Enveloped Procedure
Most accurate method of predicting true distribution of horizontal diaphragm forces
Not practical in many cases due to extensive calculation and analysis required
Acceptable alternative to semi-rigid analysis; provides a conservative approach
Idealize the diaphragm as flexible then as rigid, taking the worst-case of each scenario per wall line
Specific recognition of the enveloped analysis method is new in SDPWS Section 4.2.5
*
Notes: Say
A semi-rigid analysis is the most accurate way of predicting true distribution of horizontal diaphragm forces. Per ASCE 7-10, modelling a diaphragm as semi-rigid is always permissible. However, it is not practical in many cases due to extensive calculations and analysis required.
An acceptable alternative is the enveloped analysis. An enveloped procedure uses the worst case per wall line from flexible and rigid analyses. Although it requires two separate analyses, it provides a conservative approach and may still save time compared to semi-rigid modelling and analysis. Specific recognition of the enveloped analysis method is new in SDPWS Section 4.2.5.
Quiz Note
This slide features information that will be found on the post-course knowledge assessment.
The enveloped procedure for predicting the distribution of horizontal diaphragm forces uses the __________ of each scenario per wall line from flexible and rigid analyses.
Best case
Worst case
Average value (mean)
None of the above

## Slide 43: Pros and Cons: Flexible Diaphragms
Distributes force to shear walls based on tributary area
Easy to calculate
Shear wall lines with multiple openings will be required to resist higher forces
Some shear walls will require thicker sheathing, tighter nailing and larger overturning compression posts and holdown devices
Flexible Diaphragms
Pros
Cons
Notes: Say
Advantages: Distributes force to shear walls based on tributary area (easy to calculate).
Disadvantages: In structures that have shear wall lines with many openings, because the shear forces are based on tributary area (and not wall stiffness), the design will require that these shear walls resist higher forces. These will be high-aspect shear walls that require thicker sheathing, tighter nailing and larger overturning compression posts and holdown devices.
Quiz Note
This slide features information that will be found on the post-course knowledge assessment.
Choose whether the statement relates to either flexible or rigid diaphragms:
Distributes force to shear walls based on tributary area :: Flexible / Rigid
Force distributed to shear walls based on stiffness :: Flexible / Rigid
Easy to calculate :: Flexible / Rigid
Reduces forces on high-aspect ratio shear walls :: Flexible / Rigid

## Slide 44: Pros and Cons: Rigid Diaphragms
Forces distributed to shear walls based on stiffness
Reduces forces on high-aspect ratio shear walls
Requires extensive drift and force distribution calculations
Typically an iterative process
Shear wall location and dimensions must be known for final design
Rigid Diaphragms
Pros
Cons
Notes: Say
Advantages: Forces are distributed to shear walls based on their rigidities (stiffness). This reduces forces on high-aspect ratio shear walls (i.e. the exterior walls of an apartment building that typically has a lot of window and door openings will have less force on it than the interior walls, which are typically long with few openings).
Disadvantages: Requires extensive drift and force distribution calculations. Typically an iterative process. Shear wall location and dimensions must be known for final design.
Quiz Note
This slide features information that will be found on the post-course knowledge assessment.
Choose whether the statement relates to either flexible or rigid diaphragms:
Distributes force to shear walls based on tributary area :: Flexible / Rigid
Force distributed to shear walls based on stiffness :: Flexible / Rigid
Easy to calculate :: Flexible / Rigid
Reduces forces on high-aspect ratio shear walls :: Flexible / Rigid

## Slide 45: Lesson Three Complete
Now that you’ve completed this lesson, you should be able to:
Determine when a diaphragm may be classified as rigid, flexible, or semi-rigid for analysis purposes

## Slide 46
Distribution of Diaphragm Forces
After completing this lesson, you will be able to:
Explain how forces are distributed to different elements within the diaphragm
L
4
Notes: Do
Review the lesson title and objective.
Say
There are three diaphragm elements that work together to resist lateral forces and create a safe and code compliant diaphragm.
Sheathing
Chords
Collectors
Calculating the forces acting on these elements is necessary to design a safe and compliant diaphragm.

## Slide 47: Diaphragm Element: Sheathing
The diaphragm acts like a short, deep beam that is simply supported.
Thus, the reaction at each end of the diaphragm where it is supported is the load on half of the span.
    where:
    L = span, ft
    b = depth, ft
    w = lateral force, lb/ft
Notes: Say
In the most basic form of typical diaphragm design, one assumes the diaphragm acts like a short, deep beam that is simply supported.
Thus the reaction at each end of the diaphragm where it is supported is the load on half of the span.
Knowing the diaphragm reaction force is essential for designing shear walls. R is equal to the shear demand load on the connected shear wall.
Do
Review equation and parameters on slide.

## Slide 48: Diaphragm Element: Sheathing, cont.
Simple Beam
Notes: Say
Shear is carried by the sheathing.
When designing a diaphragm, shear resistance should be considered. The unit shear demand in a diaphragm, v, is used in conjunction with Tables 4.2A, 4.2B, and 4.2C to find a viable sheathing and nailing combination.
Do
Review equations shown on slide.
Say
V and v are maximum at supports and zero at the center of the diaphragm. For this reason, the designer may choose to have tighter nailing near diaphragm supports. This may affect choice of blocked or unblocked diaphragm (see later discussion on blocked vs. unblocked).
Quiz Note
This slide features information that will be found on the post-course knowledge assessment.
The ___________ in a diaphragm is used in conjunction with Tables 4.2A, 4.2B and 4.2C to find a viable sheathing and nailing combination.
Unit shear demand
Maximum deflection
Maximum shear demand
Maximum moment

## Slide 49: Design Example: Sheathing
Find the unit shear demand, v, in a diaphragm. First, we’ll find the reaction force, R. Then, calculate v by dividing the reaction force by the diaphragm width, b = 20’.
Notes: Say
Let’s look at an example to find the unit shear demand, v, in a diaphragm. First, we’ll find the reaction force, R. Then, calculate v by dividing the reaction force by the diaphragm width, b = 20’.
Do
Review calculations on slide. Click for “check” animation upon finding v.

## Slide 50: Diaphragm Element: Chords
Chord Force
Simple Beam
    where:
    T = tension in chord
    C = compression in chord
    M = diaphragm moment
    L = diaphragm span
    b = diaphragm depth
Max at Mid Span
Notes: Say
Moment is carried by the chords.
When designing a diaphragm, moment resistance of the chords must be considered.
Do
Review equations and parameters shown on the slide.
Quiz Note
This slide features information that will be found on the post-course knowledge assessment.
Where is the maximum moment found on the deflected shape of a diaphragm?
Intersections of the chords and collectors
Distributed along the collectors
Connection points on the chords
Center of the chords

## Slide 51: Design Example: Chords
Using the formula from the previous slide, the maximum chord forces are:
Notes: Say
Using the formula from the previous slide, the maximum chord forces are:
T = C = wL2 / 8b
= (120 plf)(30 ft)2 / (8)(20 ft)
= 675 lb
In typical wood construction, one would compare chord forces to drag strut forces to design splice connection of wood top plates.

## Slide 52: Diaphragm Element: Collectors (Struts)
Collectors (struts) are designed to transmit diaphragm reactions to the shear walls. This becomes design consideration when the supporting shear walls are shorter in length than the diaphragm.
Notes: Say
The collectors (struts) are designed to transmit the diaphragm reactions to the shear walls. This becomes a design consideration when the supporting shear walls are shorter in length than the diaphragm.
Essentially, the unsupported diaphragm unit shear over an opening in a wall must be transmitted to the shear wall elements by the collector.

## Slide 53: Diaphragm Element: Collectors (Struts), cont.
The collector itself is subjected to axial forces (tension and compression). Below is an axial force diagram for the collector over the opening.
Collector (strut) transfers diaphragm shear over opening to shear walls
Notes: Say
In this figure, the left wall has no openings, and roof shear is transferred directly to the wall.
The right wall has a large opening and the collector transfers the roof diaphragm shear over the opening to the shear walls.

## Slide 54: Design Example: Collectors (Struts)
Step One
Determine the total shear force, V, in each shear wall line.
Notes: Say
The first step is to determine the total shear force (V) in each shear wall line. This is equal to the diaphragm reaction force, which we determined in the first design example (1,800 lb).

## Slide 55: Design Example: Collectors (Struts), cont.
Step Two
Determine the unit shear force acting on the collector in the top of the wall, vtop, and the unit shear force applied to each shear wall, vbottom.
Notes: Say
Next, we’ll determine the unit shear force acting on the collector in the top of the wall, vtop, and the unit shear force applied to each shear wall, vbottom.
Note that because shear walls only make up half the wall line, that our unit shear force applied to each shear wall will be greater than the unit shear in the collector.

## Slide 56: Design Example: Collectors (Struts), cont.
Step Three
Determine the tension force, T, and compression force, C, delivered by the collector to each shear wall.
Summing the horizontal forces in Shear Wall A and B, the maximum Tension (T) and Compression (C) force in the strut are:
V = (90 lb/ft)(4 ft)
= 360 lb
V = (90 lb/ft)(6 ft)
= 540 lb
V = (180 lb/ft)(4 ft)
= 720 lb
V = (180 lb/ft)(6 ft)
= 1080 lb
SWA
SWB
Notes: Say
As a final step, we’ll need to determine the tension force, T, and compression force, C, delivered by the collector to each shear wall. In order to do so, we will sum the horizontal forces of each wall as shown.

## Slide 57: Lesson Four Complete
Now that you’ve completed this lesson, you should be able to:
Explain how forces are distributed to different elements within the diaphragm
Notes: Do
Review the lesson objective summary.

## Slide 58
Blocked vs. Unblocked Diaphragms
After completing this lesson, you will be able to:
Describe the differences between blocked and unblocked diaphragms
L
5

## Slide 59: Introduction to Blocked vs. Unblocked
Blocked Diaphragm
Has all adjacent edges of all panels fastened to a common member
Unblocked Diaphragm
Only panel edges at support locations are fastened (2 of 4 edges)
Notes: Say
Blocked – A blocked diaphragm has all adjacent edges of all panels fastened to a common member.
Unblocked – With an unblocked diaphragm, only panel edges at support locations are fastened (2 of 4 edges). Panel edges between supporting members are not required to be blocked.
Note: Blocked diaphragms have higher shear capacity, hence a long diaphragm may be blocked near the ends of the diaphragm where shear demand is the highest, but leave the lower-stressed middle section of the diaphragm unblocked which saves material, labor and time.

## Slide 60: Roof System Without Blocking
The challenge: as the roof is experiencing lateral forces, the roof sheathing will attempt to cause rotation and/or lateral displacement of the rafters/trusses since there is no blocking
Notes: Say
Here’s the challenge of a roof system without blocking: As the roof is experiencing lateral forces, the roof sheathing will attempt to cause rotation and/or lateral displacement of the rafters/trusses since there is no blocking.
Quiz Note
This slide features information that will be found on the post-course knowledge assessment.
True or false: When a roof system without blocking is experiencing lateral forces, the roof sheathing will attempt to cause rotation and/or lateral displacement of the rafters/trusses.
True
False

## Slide 61: Roof System Without Blocking, cont.
Roof framing at top plate
of wall without blocking
Hurricane ties: sometimes used to transfer lateral forces on top of uplift forces
Notes: Say
Hurricane ties are sometimes used to transfer lateral forces on top of uplift forces. To do so requires analyzing the tie for simultaneous loading. Additionally, the only possible means of installing diaphragm boundary nailing is the fascia board, which is typically 1x material, and therefore non-structural.

## Slide 62: Roof System Without Blocking, cont.
Fascia board must be a minimum of 2x to be structural
Notes: Say
To install proper roof boundary nailing using a fascia board, it must, at minimum, be a 2x to be structural. As shown in the figure, the detailing for this alternative boundary member location is critical to transfer lateral forces through a proper continuous load path.

## Slide 63: Roof Blocking
3
functions
of roof blocking at plate line
1
Provides a framing member for code-
required nailing into diaphragm
boundary element
2
Provides rotation and lateral
displacement restraint of the rafter /
truss
3
Transfers shear load from the
diaphragm to the wall top
plates (collectors)
●●●
Wall top plates are
the chords for the
diaphragm
Roof framing at top plate
of wall with blocking
Notes: Say
Roof blocking at the plate line performs three functions:
Provides a framing member for code-required nailing into diaphragm boundary element.
Provides rotation and lateral displacement restraint of the rafter/truss.
Transfers shear load from the diaphragm to the wall top plates (collectors).
Quiz Note
This slide features information that will be found on the post-course knowledge assessment.
Which of the following is a function of roof blocking at the plate line:
Provides a framing member for code-required nailing into diaphragm boundary element
Provides rotation and lateral displacement restraint of the rafter / truss
Transfers shear load from the diaphragm to the wall top plates (collectors)
All of the above

## Slide 64: Roof Blocking Ventilation
Screen, Pre-bored Blocks
Staggered Blocking
Solid Blocking with Gaps
V-Notch Blocking
Notes: Say
For designers not used to specifying blocking in their buildings, attic ventilation ability is a top concern.
There are several ways to meet ventilation requirements while meeting blocking requirements. Here are four methods:
Screen, Pre-bored Blocks: Blocking provided in areas where overhangs are left exposed.
Staggered Blocking: Blocking turned horizontally (as required) for installation of insulation breather bats. This installation is very common in the west.
Sold Blocking with Gaps: Where soffits are used, no screening is required at block locations. Blocks can be gapped for ventilation.
V-Notch Blocking: Notches in blocking are also used as a simple method to create ventilation in some areas.
Do
Mention Strong-Tie Technical Bulletin F-C-RBC for more information on blocked vs. unblocked diaphragms, detailing, code references, etc.

## Slide 65: Lesson Five Complete
Now that you’ve completed this lesson, you should be able to:
Describe the differences between blocked and unblocked diaphragms

## Slide 66: Course Summary
When designing a building, a basic consideration is that each structural element must be designed to carry a load. These loads must be transferred through the structure’s elements and connections into the foundation. The main elements of a wood-frame building that transfer lateral loads are shear walls and diaphragms.
When subjected to wind loads, the walls push or pull the floor or roof system (diaphragm) in the direction of the wind.
The floor or roof diaphragm is supported by shear walls parallel to the load. Seismic and wind forces need to be resisted at various points along the load path from the roof to the foundation.
Diaphragms are the horizontal elements in the lateral force-resisting system. A diaphragm is a flat bracing system acting like a deep, thin beam, used to transfer loads to shear walls or frame. The term is usually applied to roofs and floors. Diaphragms are made up of chords (drag struts), collectors and sheathing.
L
1
Lateral Loads in a Wood-Frame Structure
Notes: Do
Review the course summary of Lesson 1.

## Slide 67: Course Summary
Factoring nominal unit shear capacities to ASD or LRFD levels is covered in Section 4.2.3. To convert the capacity to ASD, divide the nominal amount by 2. To convert the capacity to LRFD, multiply the nominal amount by 0.8.
Tabulated nominal unit shear capacities for seismic and wind design can be found in SDPWS Tables 4.2A, 4.2B 4.2C and 4.2D. The table relates nominal unit shear capacity with diaphragm sheathing thickness, nail size and spacing, and sheathing grade to help determine the appropriate design and construction of the diaphragm. These tabulated values help ensure that the capacity of your diaphragm design will exceed the demand shear.
High load blocked diaphragms have a significantly higher shear capacity by utilizing multiple rows of fasteners. Wider blocking or supporting members are often required to avoid splitting. SDPWS Section 4.2.7.1.2 item 4, which is new to the 2015 SDPWS, states “The depth of framing members and blocking into which the nail penetrates shall be 3” nominal or greater.”
L
2
Code and Standard Provisions
Notes: Do
Review the course summary of Lesson 2.

## Slide 68: Course Summary
The method used to distribute shear to the vertical resisting elements is dependent on whether we idealize the diaphragm as rigid or flexible, model it as semi-rigid, or do an enveloped analysis. In the 2015 version of SDPWS, Section 4.2.5 was revised so that the terms “idealized as flexible”, “idealized as rigid”, and “modeled as semi-rigid” are consistent with ASCE 7-10.
A diaphragm may be idealized as flexible when Δdia > 2(Δsw). Advantage of a flexible diaphragm: distributes force to shear walls based on tributary area (easy to calculate). A diaphragm may be idealized as rigid when Δdia ≤ 2(Δsw). Advantage of a rigid diaphragm: forces are distributed to shear walls based on their rigidities (stiffness). This reduces forces on high-aspect ratio shear walls.
Semi-rigid is the most accurate way of predicting true distribution of horizontal diaphragm forces. However, it is not practical in many cases due to extensive calculations and analysis required. An acceptable alternative is the enveloped analysis. An enveloped procedure uses the worst case per wall line from flexible and rigid analyses.
L
3
Diaphragm Behavior and Analysis
Notes: Do
Review the course summary of Lesson 3.

## Slide 69: Course Summary
In the most basic form of typical diaphragm design, one assumes the diaphragm acts like a short, deep beam that is simply supported. The reaction at each end of the diaphragm where it is supported is the load on half of the span (R=wL/2). Knowing the diaphragm reaction force is essential for designing shear walls. R is equal to the shear demand load on the connected shear wall.
Shear is carried by the sheathing. When designing a diaphragm, shear resistance should be considered. The unit shear demand in a diaphragm, v, is used in conjunction with Tables 4.3A, 4.3B, and 4.3C to find a viable sheathing and nailing combination.
Moment is carried by the chords. When designing a diaphragm, moment resistance of the chords must be considered.
The collectors (struts) are designed to transmit the diaphragm reactions to the shear walls. This becomes a design consideration when the supporting shear walls are shorter in length than the diaphragm.
L
4
Distribution of Diaphragm Forces
Notes: Do
Review the course summary of Lesson 4.

## Slide 70: Course Summary
A blocked diaphragm has all adjacent edges of all panels fastened to a common member. With an unblocked diaphragm, only panel edges at support locations are fastened (2 of 4 edges). Panel edges between supporting members are not required to be blocked.
Here’s the challenge of a roof system without blocking: As the roof is experiencing lateral forces, the roof sheathing will attempt to cause rotation and/or lateral displacement of the rafters/trusses since there is no blocking. Hurricane ties are sometimes used to transfer lateral forces on top of uplift forces. To install proper roof boundary nailing using a fascia board, it must, at minimum, be a 2x to be structural.
Roof blocking at the plate line performs three functions: (1) Provides a framing member for code-required nailing into diaphragm boundary element. (2) Provides rotation and lateral displacement restraint of the rafter/truss. (3) Transfers shear load from the diaphragm to the wall top plates (collectors).
L
5
Blocked vs. Unblocked Diaphragms
Notes: Do
Review the course summary of Lesson 5.

## Slide 71: Course Completion
Any Questions?

## Slide 72: Course Completion
Simpson Strong-Tie
This concludes the continuing education course.
For a library of Simpson Strong-Tie courses,
visit strongtie.com/workshops
Notes: Do
Draw the meeting to a close. Hand out literature and business cards.
Say
If you have ongoing projects that you would be interested in reviewing together, please let me know.

## Slide 73: Next Steps!
AIA: For those seeking AIA LU/HSW: You will receive an email with a link allowing access to print your Certificate. Congratulations, you will have earned 1 LU/HSW credit. If your AIA member number has been inserted into your profile, Simpson Strong-Tie will report your credits on your behalf to the AIA. No test is required in order to receive HSW credits.
IACET: For those seeking IACET CEUs: You will receive an email with a link allowing access to print your Certificate of Attendance and instructions directing you to the Simpson Student Center to take the exam before credits can be awarded. Once the exam is taken and passed, you will have earned 0.1 CEUs (1 hour of credit). You can then access your Certificate of Completion from the Course Content tab. You must self-report your credits to your certifying organization or agency.
If you have questions or need assistance, please contact training@strongtie.com.
Notes: Presenter Notes:
Review the email and notification process as outlined in this slide.
AIA LUs:
For those that want AIA HSW credit, be sure to provide your AIA number on the sign-in sheet and Simpson will report your credits to the AIA on your behalf.
No test is required for AIA credit.
CEUs:
For those seeking CEUs, watch for an email with instructions to access the online test. After you have passed the test, you may access your Certification of Completion from the course content tab.
You must self-report your credits to your certifying organization or agency.

## Slide 74: Next Steps!
ICC: For those seeking ICC CEUs: You will receive an email with a link allowing access to print your Certificate. Congratulations, you will have earned 0.1 ICC CEU (1 hour of credit). Please make sure your ICC member number has been inserted into your profile. It is your responsibility to self-report your credits to the ICC. Please retain your Completion Certificate for your records.
IACET: For those seeking IACET CEUs: You will receive an email with a link allowing access to print your Certificate of Attendance and instructions directing you to the Simpson Student Center to take the exam before credits can be awarded. Once the exam is taken and passed, you will have earned 0.1 CEUs (1 hour of credit). You can then access your Certificate of Completion from the Course Content tab. You must self-report your credits to your certifying organization or agency.
If you have questions or need assistance, please contact training@strongtie.com.
Notes: Presenter Notes:
Review the email and notification process as outlined in this slide.
Watch for an email directing you to the Student Center to print your certificate.
No test is required for ICC credit. You must self-report your credits to ICC.
For those seeking general IACET CEUs after you have passed the online test, you may access your Certification of Completion from the course content tab. You must self-report your credits to your certifying organization or agency.