## Slide 1
PLEASE READ
Dear Instructor,
This presentation is available in both AIA and ICC versions.
For AIA: Right click and un-hide slides 5 and 127
For ICC: Right click and un-hide slides 6 and 128
Slide 2 is an optional slide

## Slide 2: Welcome!
We will begin in a few minutes.
Please be sure to sign the registration form to receive credit for attending today’s learning event.
Notes: Do
Meet and greet participants as they arrive. Start learning names, make them feel comfortable and settled in the training environment.
Make sure your opening has PUNCH:
Promotes interest and enthusiasm for the session
Understands participants’ needs
Notes ground rules and administrative/housekeeping needs
Clarifies expectations
Helps everyone get to know each other
State your expectations around participation: Make it known and expected that you will be encouraging and inviting participation.
Tips to facilitate connections:
Thank participants for their contribution (ideally with their name)
Praise participation (especially the first person to speak)
Express confidence in the participants
Restate what someone said earlier (“As John mentioned earlier….”)
Encourage participants to share what others were saying in their small groups (without naming names)
Invite someone you heard speaking in a small group to share with the entire group
Encourage the group to respond to an individual’s comment/question
Physical Room / Training Venue Setup:
If using a table arrangement, consider grouping 4 to 6 students at each station. This will help encourage conversation and discussion during activities.
Get people standing at regular intervals during your training session. Research shows that people learn up to 15% more when standing up!

## Slide 3
AIA Provider: 50119826 | AIA Course: AIA-SDPWS216 | ICC Provider: 1025 | ICC Course: 6015
Instructor Name
Title / Role
Notes: Do
Be sure to mention the AIA provider and course number for those requiring AIA credit. Ask the attendees to write down this information for reference. For AIA members, we will submit this information for them.

## Slide 4: Credit Information
IACET Accreditation Information
Simpson Strong-Tie® has been accredited as an Authorized Provider by the International Association for Continuing Education and Training (IACET). As a result of their Authorized Provider accreditation status, Simpson Strong-Tie® is authorized to offer IACET CEUs for its programs that qualify under the ANSI/IACET Standard.
This course offers 0.2 CEU (2 hours of credit).
Notes: Review the submission process for audiences requiring IACET CEU credits.
For those seeking IACET credit, they must take and pass the online test. They must self-report CEU credits to their certifying organization or agency.
Explain the credits awarded: IACET: 0.2 (Equivalent to 2 hours) CEUs.

## Slide 5: Credit Information
AIA Member Information
This course is registered with AIA CES for continuing professional education. As such, it does not include content that may be deemed or construed to be an approval or endorsement by the AIA of any material of construction or any method or manner of handling, using, distributing, or dealing in any material or product. Upon completion of this course, Credit(s) earned will be reported to AIA CES for AIA members who pass the course and have entered their AIA member number on their Simpson profile page. A link to the Certificate of Completion will be available upon completion of this course. Only AIA LU/HSW will be reported.
This course offers 2 LU/HSW credit.
AIA Course Number: AIA- SDPWS216
Notes: Presenter Information
NOTE: Please be sure each attendee LEGIBLY signs the event sign-in sheet.
Say
All questions concerning proprietary products will be addressed after the conclusion of the AIA portion of the presentation. The meeting format is 110 minutes of content, followed by 10 minutes of Q & A.
Do
Explain the credits awarded for:
AIA: 2LU/HSW credit.
IACET: 0.2 (Equivalent to 2 hours) CEU credits.
Review the submission process for audiences requiring either AIA LU/HSW (health, safety and welfare) credits or CEU credits:
For those seeking AIA HSW credit, there is no test required. AIA members must be sure to provide their AIA member number on the sign-in sheet. Please make sure name, email and AIA member number are clearly printed so Simpson can report credits to the AIA on their behalf.
For those seeking IACET credit, they must take and pass the test. They must self-report CEU credits to their certifying organization or agency.

## Slide 6: Credit Information, cont.
ICC Member Information
This course has been approved by the International Code Council (ICC) for continuing professional education. For learners that complete this course, it is your responsibility to self-report your credits to the ICC. Please retain your Completion Certificate for your records.
Be sure that your ICC ID number is provided on the sign-in sheet or in your Simpson profile in order to have it displayed on your certificate.
This course offers 0.2 CEU (2 hours of credit).
ICC Course Number: 6015
Notes: Review the submission process for audiences requiring ICC CEU credits.
For those seeking ICC credit, there is no test required. ICC members must provide their ICC ID number on the sign-in sheet or in their Simpson profile in order to have it displayed on their certificate. It is the responsibility of the participant to self-report their credits to the ICC. Ask them to retain their Completion Certificate for their records.
Explain the credits awarded: ICC: 0.2 (Equivalent to 2 hours) CEUs.

## Slide 7: Additional Credit Offerings
Visit
strongtie.com/workshops
for more information
Course Name | CEUs | AIA | ICC
Introduction to Deck Design | 0.1 | ✔ | ✔
Introduction to Wind Design and the Wood Frame Construction Manual | 0.1 | ✔ | ✔
Shear Walls and Lateral Bracing in Light Frame Construction | 0.1 | ✔ | ✔
Understanding Restraint Rod Systems | 0.1 | ✔ | ✔
Cracking the Concrete Anchor Codes | 0.1 | ✔ | ✔
Concrete Deterioration | 0.1 | ✔ | ✔
Moment Frame Design | 0.1 | ✔ | ✔
Introduction to Wind Code Provisions and Meteorological Concepts | 0.1 | ✔ | ✔
Wind Design in Accordance with ASCE 7-10 | 0.1 | ✔ | ✔
Wood Framed Seismic Design 1: Code Provisions, Design Parameters | 0.1 | ✔ | ✔
Notes: Do
Explain that we have additional PK topics available that offer credit for ICC members and HSW credits for AIA members.
Explain that we have a library of online courses available in our Simpson Student Center that also offer ICC and AIA HSW credits. They can access our online courses at strongtie.com/workshops.

## Slide 8: Course Description
Shear Wall Design with SDPWS
This course was created to help familiarize structural engineers, designers, and architects with code-compliant shear wall design techniques using the SDPWS.
Course Contents
Introduction / Learning Objectives
Lesson 1: Mechanics of a Shear Wall
Lesson 2: Code and Standard Provisions
Lesson 3: Capacity Adjustments Based on Aspect Ratio
Lesson 4: Shear Wall Design Methods
Lesson 5: Pre-Fabricated Shear Walls
Wrap Up / Questions
Notes: Do
Review the course description and course contents.

## Slide 9: Learning Objectives
Upon completion of this seminar, you will be able to:
Describe the practical applications, basic functions and considerations for shear wall design
Identify the code and standard provisions in the 2015 SDPWS pertaining to shear wall design
Explain how and when to use the capacity adjustments for shear walls with high aspect ratios
Describe how to design segmented, perforated and force-transfer shear walls using the SDPWS
Identify which applications may require a pre-fabricated shear wall
Notes: Do
Review the learning objectives for the course.
Inform students that the assessment questions will be based on these learning objectives. Slides that may contain information relevant to the test have an orange graduation cap located in the bottom-left corner.

## Slide 10
Mechanics of a Shear Wall
After completing this lesson, you will be able to:
Describe the practical applications, basic functions and considerations for shear wall design
L
1
Notes: Do
Review the lesson title and objective.

## Slide 11: What is a Shear Wall?
Shear walls are vertical elements of the horizontal force-resisting system
They are typically wood-frame stud walls covered with a structural sheathing material (plywood, etc.)
Shear walls have five parts:
  Framing members
  Sheathing
  Nails
  Holdowns
  Shear Anchors
❶
❷
❸
❹
❺
Notes: Say
Shear walls are vertical elements of the horizontal force-resisting system. They are typically wood-frame stud walls covered with a structural sheathing material like plywood.
Shear walls have five parts:
Framing members
Sheathing
Nails
Holdowns
Shear Anchors

## Slide 12: Basic Functions of Shear Walls
Force
(seismic or wind)
Strength to
Resist Shear
Holdowns
(resist uplift)
Connections for
Sliding Resistance
Provides
Stiffness
Shear walls resist the effects of lateral loads acting on the structure and are typically used in wood buildings as the lateral force-resisting system.
When designed properly, they are capable of transferring horizontal forces to the next element in the load path below them.
Notes: Do
Review graphic.
Strength
Shear walls must provide the necessary lateral strength to resist horizontal earthquake forces.
When shear walls are designed properly, they are capable of transferring these horizontal forces to the next element in the load path below them, such as other shear walls, floors, foundation walls, slabs or footings.
Stiffness
Shear walls also provide lateral stiffness to prevent the roof or floor above from excessive side-sway.
When shear walls are stiff enough, they will prevent floor and roof framing members from moving off their supports.
Quiz Note
This slide features information that will be found on the post-course knowledge assessment.
True or false: When shear walls are designed properly, they are capable of transferring forces to the next element in the load path below them, such as other shear walls, floors, walls, slabs or footings.
True
False

## Slide 13: Basic Functions of Shear Walls, cont.
Seismic Loads
Wind Loads
There are two main lateral loads that need to be considered when designing shear walls:
Notes: Say
Wind and seismic loads are the most common loads that shear walls are designed to carry.
Do
Review graphic.

## Slide 14: Practical Applications of Shear Walls
Racking
When lateral forces engage the side of a structure, the load may cause it to lean over (rack) to one side.
Sliding
Lateral forces exerted against the side of a structure can also cause it to slide off of its foundation.
Overturning
When the structure is anchored in place to limit racking or sliding, the lateral force of wind or seismic loading causes the structure to rotate or overturn.
Notes: Say
Structures require lateral force-resisting systems in order to resist racking, sliding and overturning caused by wind or seismic forces.
When lateral (wind or seismic) forces engage the diaphragm of a structure, it’s easy to visualize the force pushing horizontally on the top of the shear wall. Sheathing then transfers the shear from the top of the wall to the bottom of the wall while holding the wall together to resist racking. If the bottom plate of the wall is anchored to the foundation to resist sliding; the far end of the wall will press down (compression force) and the near side of the wall will lift up (tension force) – this is overturning.

## Slide 15: Practical Applications of Shear Walls, cont.
Shear walls are not limited to single family homes
Also used in multi-unit wood-framed structures (apartments/condos)
Notes: Say
Shear walls are not limited to single family homes. They are also used in multi-unit wood-framed structures, such as apartment and condominium complexes.

## Slide 16: Considerations in Shear Wall Design
What’s to come…
Shear wall design methods
Shear panel proportions
Sheathing material and thickness
Fastener size and spacing
Anchorage requirements
Chord design (Tension/Compression)
Holdowns
Capacity adjustments
Notes: Say
There are several considerations to keep in mind when designing a shear wall, including:
Design method: We’ll discuss how to design Segmented, Perforated, and Force-Transfer Around Openings (FTAO) shear walls. We’ll also review when Pre-built shear walls would be beneficial.
Shear panel proportions: Another name for proportions is aspect ratio. Shear walls with a high aspect ratio may require capacity reduction adjustments.
Sheathing thickness and Sheathing edge and field nailing: Both have a direct effect on the nominal unit shear capacities for wood-frame shear walls. We’ll take a look at Table 4.3A to learn how these affect capacity.
Anchorage requirements: The bottom plate must be anchored to the foundation with connections capable of transferring this force. Otherwise, a brittle failure of the sill plate can occur.
Chord design (tension and compression) and Holdowns: Both are important for resisting overturning forces from intense seismic or wind activity.
Capacity Adjustments: New to 2015 is the equal deflection methodology for reducing capacity of high aspect ratio shear walls.
We’ll cover all these topics in detail throughout the course.
There are three main design methodologies for site-built shear walls, including:
Individual Full-height Wall Segments: designed as shear walls without openings.
Perforated Shear Walls: sheathed on one or both sides with wood structural panel sheathing.
Force-transfer Around Opening (FTAO) Shear Walls: shear walls with openings are designed for force transfer around the openings.
We will review a design example covering how to design all three types of site-built shear walls in Lesson 4.
If you prefer (or are unable to) design a site-built shear wall, some manufacturers offer pre-built shear walls. We’ll discuss where these would be beneficial for a light-framed wood structure project in Lesson 5.

## Slide 17: Lesson One Complete
Now that you’ve completed this lesson, you should be able to:
Describe the practical applications, basic functions and considerations for shear wall design
Notes: Do
Review the lesson objective summary.

## Slide 18
Code and Standard Provisions
After completing this lesson, you will be able to:
Identify the code and standard provisions in the 2015 SDPWS pertaining to shear wall design
L
2
Notes: Do
Review the lesson title and objective.

## Slide 19: Experiences with Shear Wall Design
Overcoming problems with shear wall design:
Break into groups of 2 or 3
Find out who drove the furthest this morning
Within your group, take one minute per person to find out:
    What was the most problematic situation you’ve seen or experienced when designing a site-built shear wall?
    How could this problem have been prevented?
Notes: Audience Interaction: 5 minutes.
Say
Before we begin our next lesson, I’d like to get some feedback on your experience designing shear walls.
So here’s what I’d like to do: Turn to your neighbors and break up into groups of __________ (2 or 3 depending on the size of the audience). Then take one minute per person and answer the following questions.
Who drove the furthest to be here this morning?
What was the most problematic situation you’ve seen or experienced when designing a site-built shear wall?
How could this problem have been prevented?
Pick one scenario from your group to discuss with the group.
The person who drove the furthest today will be the spokesperson.
Ask
Ok, raise your hand… Who has one they’d like to discuss?
Do
Call on one or two groups and ask what the problem was and how they solved it.
Ask
Did anyone with a similar problem solve it a different way?
Follow up: How did you / would you solve it?
Anyone else?
Do
Keep an eye on the clock and end the discussion after a couple minutes.
Say
It’s easy to see that shear wall design can be challenging. Hopefully after today, you will be aware of some other options and some tools to assist in the process.
Do
Return to the presentation.

## Slide 20: IBC §2305 and SDPWS
IBC 06
IBC 09, 12 and 15
Notes: Say
Historically, the IBC contained provisions and design tables for nailed and stapled wood diaphragms and shear walls. Prior to the 2009 edition, you were permitted to use the SDPWS as an alternative to these provisions, but still had to comply with requirements in the IBC.
Do
Click to show images and information for “IBC 09, 12, and 15.” Additional picture animations will continue automatically.
Say
Since 2009, the IBC states that “Structures using wood-frame shear walls or wood-frame diaphragms to resist wind, seismic or other lateral loads shall be designed and constructed in accordance with AF&PA SDPWS…” When the 2012 IBC came out, it had removed all nailed diaphragm and shear wall tables since they were duplicates to the SDPWS tables (however, the stapled tables remained).

## Slide 21: IBC §2306 and SDPWS
IBC 09, 12 and 15
http://www.awc.org/codesstandards.php
Notes: Say
Section 2306.3 (Wood-framed Shear Walls) simply refers to the SDPWS now -- except for the references to stapled tables.
Do
Point out that all AWC documents are now available for free viewing/downloading from their website at www.awc.org/standards/sdpws.php.

## Slide 22: Continuous Load Path is Required
Notes: Say
In Section 4.1.1 of the 2015 SDPWS, it states: “A continuous load path, or paths, with adequate strength and stiffness shall be provided to transfer all forces from the point of application to the final point of resistance.”
Do
Be sure to reinforce that Section 4.1.1 mentions both strength and stiffness.

## Slide 23: Factoring Nominal Unit Shear Capacities
Nominal Capacities
ASD = Nominal / 2.0
LRFD = Nominal x 0.8
Shear Wall Tables
Table 4.3A: Wood-based panels (structural, plywood, particle)
Table 4.3B: WSP applied over gypsum board
Table 4.3C: Gypsum board and plaster
Table 4.3D: Lumber
4.3.3 Unit Shear Capacities
The ASD allowable unit shear capacity shall be determined by dividing the tabulated nominal unit shear capacity, modified by applicable footnotes, by the ASD reduction factor of 2.0. The LRFD factored unit resistance shall be determined by multiplying the tabulated nominal unit shear capacity, modified by applicable footnotes, by a resistance factor, φD, of 0.80. No further increases shall be permitted.
4.3.3.1 Tabulated Nominal Unit Shear Capacities: Tabulated nominal unit shear capacities for seismic design are provided in Column A of Tables 4.3A, 4.3B, 4.3C, and 4.3D; and for wind design in Column B of Tables 4.3A, 4.3B, 4.3C, and 4.3D.
Notes: Say
Factoring nominal unit shear capacities to ASD or LRFD levels is a simple process covered briefly in Section 4.3.3 “Unit Shear Capacities.”
To convert the capacity to ASD, divide the nominal amount by 2.
To convert the capacity to LRFD, multiply the nominal amount by 0.8.
Tabulated nominal unit shear capacities for seismic and wind design can be found in Tables 4.3A, 4.3B and 4.3C.
Do
Review terminology if necessary.
ASD = Allowable Stress Design. A method of proportioning structural members and their connections such that stresses do not exceed specified allowable stresses when the structure is subjected to appropriate load combinations (also called working stress design).
LRFD = Load and Resistance Factor Design. A method of proportioning structural members and their connections using load and resistance factors such that no applicable limit state is reached when the structure is subjected to appropriate load combinations.
Quiz Note
This slide features information that will be found on the post-course knowledge assessment.
Tabulated nominal unit shear capacities for wood-based panels are provided in:
SDPWS Section 3.6.1
IBC Section 2305.1.3.1
SDPWS Table 4.3A
ASCE 7 Table 6-2

## Slide 24: Tabulated Nominal Unit Shear Capacities
Notes: Say
Here we have Table 4.3A “Nominal Unit Shear Capacities for Wood-Frame Shear Walls” shown on the slide. Let’s zoom in a bit for a better view.
Do
Click to show zoomed in animation of table highlighting the “WIND – Panel Edge Fastener Spacing” section.
Say
The nominal capacity varies due to the sheathing material considered, the minimum nominal panel thickness, and the panel edge fastener spacing. The table also shows the required minimum fastener penetration and required fastener type and size for the chosen sheathing material and panel thickness.
In addition to nominal unit shear capacities, the table provides apparent shear stiffness values (Ga) for use in the deflection calculation (which we will discuss in a later slide).
These are the same capacities that were previously available in the 2009 IBC and earlier (prior to the tables being removed). However, the values are presented in nominal and the table has been expanded to show both seismic and wind capacities – unlike the previous editions that showed only ASD and wind capacities, with an adjustment factor for seismic provided in a footnote.
Quiz Note
This slide features information that will be found on the post-course knowledge assessment.
Tabulated nominal unit shear capacities for wood-based panels are provided in:
SDPWS Section 3.6.1
IBC Section 2305.1.3.1
SDPWS Table 4.3A
ASCE 7 Table 6-2

## Slide 25: Tabulated Nominal Unit Shear Capacities, cont.
Remember, these are Nominal Values – for ASD, divide value by 2
Notes: Say
Please remember that these are nominal values. As we discussed previously, to convert to ASD levels, we will need to divide the nominal value by 2.

## Slide 26: Unblocked Shear Walls
History
Blocked shear wall is when all edges are supported by framing or blocking. In the past, all shear walls had to be blocked. Starting with 2008 SDPWS, reduction factors were provided for unblocked shear walls.
Requirements
Maximum Aspect Ratio = 2:1
16’ maximum height
Must be Wood Structural Panel (WSP) sheathing
Reduction Factors
  νub = νbCub
  νb = Nominal unit shear capacity (plf) from Table 4.3A for WSP sheathing at 6:12 nailing into 24” o.c. studs
Notes: Say
A “blocked shearwall” is when all edges are supported by framing or blocking. In the past, all shear walls had to be blocked. However, starting with the 2008 SDPWS, reduction factors were provided for unblocked shear walls.
Usually, the vertical edges of sheathing are supported by studs and the lowest edge is supported by the bottom plate. When the wall is taller than the height of the sheathing, there will be a horizontal joint with no framing behind it. Typically that required blocking. The blocking ensures load transfer from the upper panel to the lower panel.
And if there is one thing that contractors dislike installing more than connectors, it is blocking. This new provision will let you take advantage of the labor savings that occurs when walls are unblocked. The tradeoff is that a longer length of sheathed wall is required due to the loss of capacity.
Do
Review the requirements and reduction factors for unblocked shear walls (shown on the slide).
Say
In some areas of the country, the preference is to install the sheathing horizontally across the studs (rather than vertically), which leads to many unblocked panel edges. Assuming the edges are left unblocked, the provisions within this section shall be followed.

## Slide 27: Deformation of Connections
Notes: Say
A wall can only move so far until its integrity is compromised. But until that point of failure, the elements and connections attached to the shear wall must be able to support its movement. If a shear wall deflects an inch, its connections will also need to be able to travel the same distance without breaking the system. Section 4.1.3 introduces this criteria by stating “each elements and connection comprising the lateral force-resisting system is compatible with the deformations of the other lateral force-resisting elements and connections with the overall system.”

## Slide 28: Permissible Deflection Limits
Notes: Say
Section 4.3.1 “Application Requirements” expands on Section 4.1.3. It defines permissible deflection as the deflection that permits the shear wall and any attached elements to maintain their structural integrity and continue to support their prescribed loads.
Wood shear walls will have a maximum lateral deflection based on the maximum allowable shear load (per the code) being applied to them.
Quiz Note
This slide features information that will be found on the post-course knowledge assessment.
SDPWS Section 4.3.1 defines permissible deflection as the deflection that:
Does not exceed 2” of inter-story drift
Permits the shear wall and attached elements to maintain their structural integrity and continue to support their prescribed loads
Allows the continuous load path to transfer loads to the other elements of the lateral-force-resisting system
All of the above

## Slide 29: Permissible Deflection Limits, cont.
When it comes to deflection, remember to also consider what is inside or attached to the walls. Finishes, doors, and windows are all susceptible to damage from deflection.
Notes: Say
When it comes to deflection, remember to also consider what is inside of the walls or attached to the walls. Finishes, doors and windows are all susceptible to damage from deflection. Even if structural integrity isn’t compromised during a seismic or wind event, houses with multiple windows may require significant repair costs.
From the 2015 SDPWS Commentary, it states: While there is no prescribed deflection limit for wind design, consideration should be given to limiting deflections to avoid serviceability problems associated with finish materials and operability of doors and windows. Compliance with construction and materials requirements and associated design unit shear capacities in SDPWS for wind design have been considered to provide acceptable serviceability performance for resistance to wind loads.
Next, let’s take a look at how SDPWS calculates shear wall deflection.

## Slide 30: Calculating Deflection
    where:
    δsw = maximum shear wall deflection determined by elastic analysis, in
    v = induced unit shear, plf
    E = modulus of elasticity of end posts, psi
    A = area of end post cross-section, in2
    b = shear wall length, ft
    Ga = apparent diaphragm shear stiffness from nail slip and panel shear deformation, kips/in (from column A, Tables 4.3A through 4.3D)
    Δa = total vertical elongation of wall anchorage system
    h = shear wall height, ft
(Eq. 4.3-1)
Notes: Say
Calculations of shear wall deflection shall account for bending and shear deflections, fastener deformation, anchorage slip, and other contributing sources of deflection.
The shear wall deflection, δsw, is calculated by use of the equation shown on the slide.
Do
Review the parameters for the shear wall deflection calculation.

## Slide 31: Calculating Deflection, cont.
Bending
Shear
Anchorage
Notes: Say
The first term calculates the bending deflection of the shear wall.
The next term gives you the deflection from shear forces and fastener deformation.
The last term calculates the shear wall deflection from anchorage slip.
Quiz Note
This slide features information that will be found on the post-course knowledge assessment.
Which of the following is not a term of the simplified deflection calculation:
Bending
Tension
Shear
Anchorage

## Slide 32: Anchor Bolts: Requirements
Notes: Say
Plate washers and 3x sole plates were required by the UBC (Uniform Building Code) in high seismic regions to limit splitting of the plate. This requirement carried over to the 2006 IBC.
However, recent cyclic testing led to changes in the 2009 IBC, removing the section containing this requirement. Instead, the IBC referenced the 2008 SDPWS. Here they permit 2x sole plates for all applications, but require the sheathed edge of the sole plate to be supported with a plate washer (regardless of the sole plate size). Another change was that the use of this plate washer is no longer limited to seismic regions.
This requirement, however, does have some exceptions. We’ll discuss these in the upcoming slides.
Do
Review Section 4.3.6.4.3 Anchor Bolts on the slide.

## Slide 33: Anchor Bolts: Resulting Failures
Brittle failure (sill plate)
Ductile failure (nails)
Notes: Say
Shown on the slide are the failures of two nearly identical walls. The only difference was the .229x3x3 plate washers; the anchors for the wall on the right had them, while those for the wall on the left did not. The wall without the plate washers failed in a brittle manner - the sill plate split due to cross-grain tension or bending. Wood is inherently very weak when subjected to cross-grain forces and without plate washers to help restrain it, the sill plate failed. The wall with plate washers failed in a ductile manner - the nails bent and some pulled through the sheathing. Since the plate washers were able to restrain the sill plate and prevent a premature failure within the sill plate, the sheathing was able to fully engage and work the nails back and forth, eventually breaking the nails or pulling them through.
A ductile failure is preferable (especially in an earthquake) since it is a more gradual failure. When a brittle failure occurs, most of the capacity is suddenly lost and as a result can be catastrophic.
Quiz Note
This slide features information that will be found on the post-course knowledge assessment.
SDPWS Section 4.3.6.4.3 requires foundation anchor bolts to have a steel plate washer under each nut not less than 0.229”x3”x3” in size. Washers are necessary so that the __________ do not experience a __________.
Sill plates :: brittle failure
Sill plates :: ductile failure
Nails :: brittle failure
Nails :: ductile failure

## Slide 34: Anchor Bolts: Installation
Notes: Say
Being within ½” of the sheathed face of the wall isn’t too difficult with a 2x4 wall and 3x3 plate, but when you have a 2x6 wall this takes a little more forethought for anchor placement or choice (a mudsill anchor is another choice for walls sheathed on one side).
If you have a wall sheathed on both sides then you either have to stagger the 3x3 plate or go with our 3x4.5 plate. A mudsill anchor is no longer a great option.

## Slide 35: Anchor Bolts: Exceptions
Exceptions:
The unit shear capacity of the sheathing assembly does not exceed 200 plf ASD (400 plf nominal), or…
The foundation anchor bolts are designed to resist shear only and all of the following conditions are met:
  Individual Full-Height Wall Segment (not a Perforated or Force-Transfer shear wall)
  Dead load stabilizing moment is neglected when sizing the overturning uplift restraint (i.e., holdowns and their anchorage)
  Shear wall aspect ratio, h:b, does not exceed 2:1
  The allowable unit shear capacity of the sheathing assembly does not exceed 490 plf ASD (980 plf nominal) for seismic or 685 plf ASD (1,370 plf nominal) for wind
Notes: Say
What if you don’t want to install those pesky plate washers? Let’s take a look at some of the exceptions.
The first exception for 200 plf (ASD) is to allow single sided gypsum board shear walls without plate washers. In this case, the failure will be in the fasteners/gypsum, so plate splitting will not be a concern.
FYI: the unit shear limit in the last bullet point (2.d.) is based on 7/16” OSB with 8d nails at 3” on center edge spacing into DF lumber.

## Slide 36: Shear Wall Aspect Ratio Limitations
Notes: Say
In line with the previous 2008 edition of SDPWS, the size and shape of shear walls shall be limited to the aspect ratios in Table 4.3.4.
However, there are significant changes to the 2015 SDPWS with new provisions for the design of high aspect ratio shear walls.

## Slide 37: Shear Wall Aspect Ratio Limitations, cont.
2008 SDPWS
2015 SDPWS
In 2015 SDPWS, both wind and seismic governed designs will need to consider adjustment factors for aspect ratios greater than 2.0!
Notes: Say
The term high aspect ratio is considered to apply to walls with an aspect ratio greater than 2:1.
In the 2015 SDPWS, reduction factors for high aspect ratio shear walls are no longer contained in the footnotes to Table 4.3.4. Instead, these factors are included in new provisions accounting for the reduced strength and stiffness of high aspect ratio shear walls.
In the 2008 SDPWS, seismic governed designs would need to consider adjustment factors for aspect ratios greater than 2:1. However, in 2015, this has changed to include both wind and seismic.
In the next lesson, we’ll learn how to apply the two types of adjustment factors for high aspect ratio shear walls.
Quiz Note
This slide features information that will be found on the post-course knowledge assessment.
True or false: In the 2015 SDPWS, only seismic governed designs will need to consider adjustment factors for high aspect ratio shear walls.
True
False
Quiz Note
This slide features information that will be found on the post-course knowledge assessment.
The maximum permitted aspect ratio for a shear wall:
Varies based on the shear wall’s sheathing material.
Is not addressed in the 2015 SDPWS.
Is independent of the shear wall’s sheathing material.
Is always 1:1.

## Slide 38: Lesson Two Complete
Now that you’ve completed this lesson, you should be able to:
Identify the code and standard provisions in the 2015 SDPWS pertaining to shear wall design
Notes: Do
Review the lesson objective summary.

## Slide 39
Capacity Adjustments Based on Aspect Ratio
After completing this lesson, you will be able to:
Explain how and when to use the capacity adjustments for shear walls with high aspect ratios
L
3
Notes: Do
Review the lesson title and objective.

## Slide 40: Two Types of Adjustment Factors
Two methods available
For WSP shear walls with aspect ratios (h/bs) greater than 2:1
1
Equal Deflection Calculation
2
2bs/h
Adjustment Factor
SDPWS §4.3.3.4.1 & SDPWS §4.3.4.2
SDPWS §4.3.3.4.1 Exception 1
Notes: Say
There are two types of adjustment factors in the 2015 SDPWS for shear walls that exceed aspect ratio limitations in Table 4.3.4.
The first method that we’ll cover is the Equal Deflection Calculation (sometimes referred to as Relative Stiffness Method). While this concept is not new to the SDPWS, the organization of requirements related to distribution of shear is new in the 2015 edition. This method distributes the shear force to shear walls in a line based on relative stiffness of the individual shear walls. Prior to determining stiffness of the individual shear walls, however, any high aspect ratio shear wall must be adjusted by a new factor: 1.25-0.125h/bs.
The second method we'll discuss is the 2bs/h Adjustment Factor. If you've done any seismic design in the past, you may already be familiar with this calculation as it existed in the 2008 edition of SDPWS by way of a footnote to Table 4.3.4. It permits distribution of shear force to shear walls in a line based on nominal shear capacity of the individual shear walls, provided they meet some certain requirements (such as similar construction and material). When determining nominal shear capacities of the individual shear walls, any high aspect ratio segment must be multiplied by the 2bs/h factor.
We will review both methods, discuss how they impact shear distribution within a wall line, and compare results by running through an example.

## Slide 41: Overview of Equal Deflection Calculation
1
Equal Deflection Calculation Method
§4.3.3.4.1 + §4.3.4.2
Notes: Say
New Section 4.3.3.4.1 states that “Shear distribution to individual shear walls in a shear wall line shall provide the same calculated deflection, δsw, in each shear wall.” Using this equal deflection calculation method for distribution of shear, the unit shear assigned to each shear wall within a shear wall line varies based on its stiffness relative to that of the other shear walls in the shear wall line. Thus, a shear wall having relatively low stiffness, as is the case of a high aspect ratio shear wall within a shear wall line containing a longer shear wall, is assigned a reduced unit shear.
In addition, Section 4.3.4.2 contains a new aspect ratio factor, 1.25 – 0.125h/bs, that specifically accounts for the reduced unit shear capacity of high aspect ratio shear walls. The strength reduction varies linearly from 1.00 for a 2:1 aspect ratio shear wall to 0.81 for a 3.5:1 aspect ratio shear wall. Notably, this strength reduction applies for shear walls resisting either seismic forces or wind forces.
<!-- Written by Simpson Engineer Randy Shackelford and AWC Engineer Phil Line. More at: http://seblog.strongtie.com/2015/02/new-treatment-of-shear-wall-aspect-ratios-in-the-2015-sdpws/ -->

## Slide 42: Overview of 2bs/h Adjustment Factor
2
2bs/h
Adjustment Factor
§4.3.3.4.1 Exception 1
Notes: Say
The 2bs/h factor, previously addressed by Footnote 1 of Table 4.3.4, is now an alternative to the Equal Deflection Calculation method of 4.3.3.4.1 and applies to shear walls resisting either wind or seismic forces. This adjustment factor method allows the designer to distribute shear in proportion to shear wall strength, provided that shear walls with high aspect ratio have strength adjusted by the 2bs/h factor. The strength reduction varies linearly from 1.00 for 2:1 aspect ratio shear walls to 0.57 for 3.5:1 aspect ratio shear walls. This adjustment factor method provides roughly similar designs to the Equal Deflection Calculation method for a shear wall line comprised of a 1:1 aspect ratio wall segment in combination with a high aspect ratio shear wall segment.
In prior editions of SDPWS, a common misunderstanding was that the 2bs/h factor represented an actual reduction in unit shear capacity for high aspect ratio shear walls, as opposed to a reduction factor to account for stiffness compatibility. The actual reduction in unit shear capacity of high aspect ratio shear walls is represented by the factor, 1.25 – 0.125h/bs, as noted previously. The 2bs/h factor is the more severe of the two factors and is not applied simultaneously with the 1.25-0.125h/bs factor.
<!-- Written by Simpson Engineer Randy Shackelford and AWC Engineer Phil Line. More at: http://seblog.strongtie.com/2015/02/new-treatment-of-shear-wall-aspect-ratios-in-the-2015-sdpws/ -->
Quiz Note
This slide features information that will be found on the post-course knowledge assessment.
True or false: When determining reduced capacities for shear walls with high aspect ratios, the 2bs/h factor is not applied simultaneously with the 1.25-0.125h/bs factor.
True
False

## Slide 43: Major Implications for Design
Seismic
Wind
2bs/h factor (old method) remains unchanged; presented as alternative to equal deflection method (4.3.3.4.1)
Efficient designs between the two methods depends on relative stiffness of shear walls in the wall line
For wind design, high aspect ratio shear wall factors apply for the first time
For shear walls with 3.5:1 aspect ratio, unit shear capacity is reduced to not more than 81% of that used in prior editions
Notes: Say
For seismic design, the 2bs/h factor method continues unchanged, but is presented as an alternative to the Equal Deflection Calculation method in 4.3.3.4.1 for providing deflection compatibility. The Equal Deflection Calculation method can produce both more and less efficient designs than may result from the 2bs/h factor method depending on the relative stiffness of shear walls in the wall line. For example, design unit shear for shear wall lines comprised entirely of 3.5:1 aspect ratio shear walls can be as much as 40% greater (i.e. 0.81/0.57=1.42) than prior editions if not limited by seismic drift criteria.
For wind design, high aspect ratio shear wall factors apply for the first time. For shear walls with 3.5:1 aspect ratio, unit shear capacity is reduced to not more than 81% of that used in prior editions. The actual reduction will vary by actual method used to account for deflection compatibility.
<!-- Written by Simpson Engineer Randy Shackelford and AWC Engineer Phil Line. More at: http://seblog.strongtie.com/2015/02/new-treatment-of-shear-wall-aspect-ratios-in-the-2015-sdpws/ -->

## Slide 44: Introduction to Design Examples
Design Example 1
Calculate capacity of one wall line with given assumptions
  Wall line consists of two segments with very different aspect ratios
Determine using both methods:
  Equal Deflection Calculation
  2bs/h Adjustment Factor
Design Example 2
One wall line with same assumptions as Design Example 1
  Wall line consists of two segments with 3.5:1 aspect ratios
Determine using both methods:
  Equal Deflection Calculation
  2bs/h Adjustment Factor
Summarize
Compare the results of each method for each example. How do shear wall aspect ratios affect your choice between capacity adjustment methods?
Notes: Do
Review slide.
Say
Our two design examples are incredibly similar with one exception: Design Example 1 has two shear wall segments with very different aspect ratios, while Design Example 2 has two shear wall segments with 3.5:1 aspect ratios.

## Slide 45: Design Example 1: Assumptions
Calculate the capacity of this wall line, assuming:
15/32” structural sheathing
Southern Pine 2x4 framing (double 2x4 end posts)
8d nails at 6” o.c.
vnom = 520 plf (Table 4.3A)
Ga = 13 k/in
Δa = 0.125” at 3,500 lb
Calculate using both methods:
Equal Deflection Calculation (§4.3.3.4.1 / §4.3.4.2) (New Method)
2bs/h Adjustment Factor (§4.3.3.4.1.E1) (Alternative / Old Method)
8’
2.3’
8’
v
δ
δ
SW1
SW2
Notes: Say
For our first design example, we’ll calculate the capacity of a wall line consisting of two shear wall segments with very different aspect ratios. SW1 is 8’ x 8’, a ratio of 1:1 – requiring no capacity adjustment. SW2 is 8’ x 2.3’, a ratio of 3.5:1. The second shear wall will require capacity adjustments.
We’ll calculate the capacity of the wall line using both methods, and then compare the results.
Do
Review the assumptions for the Design Example.

## Slide 46: Design Example 1: Equal Deflection Calculation
ASD Unit Shear Capacity of SW1:
ASD Unit Shear Capacity of SW2:
Deflection of Stiffer SW1 at its ASD Unit Shear Capacity:
Notes: Say
Let’s begin with the Equal Deflection Calculation method, new to the 2015 SDPWS.
As a first step, we’ll check whether SW1 is a high aspect ratio shear wall. By dividing the height (8’) by the width (8’), we determine the aspect ratio is 1:1. No factoring is necessary since the ratio is less than 2:1. From here, we’ll convert the 520 plf nominal capacity to ASD by dividing by 2.0 (per Section 4.3.3). The ASD Unit Shear Capacity of SW1 is 260 plf.
Next, we’ll follow the same pattern for SW2. By dividing the height (8’) by the width (2.3’), we find the aspect ratio of SW2 is 3.5:1. This is considered a high aspect ratio and will require a factoring adjustment. By plugging the height (h=8’) and width (bs=2.3’) into the 1.25-0.125h/bs equation, we receive a reduction factor of 0.81. From here, we’ll convert the 520 plf nominal capacity to ASD the same way as previous, with a result of 260 plf. By multiplying the ASD capacity by the reduction factor of 0.81, we receive a reduced ASD Unit Shear Capacity of 210 plf.
The limiting deflection for a shear wall line will be associated with the individual segment whose design strength occurs at the smallest deflection of any segments within that line, which is SW1 in this example. (Note that the deflection could also be controlled by code drift limitations.)
Plugging in our SW1 values, we find a deflection of 0.242 inches for SW1.

## Slide 47: Design Example 1: Equal Deflection Calculation, cont.
ASD Unit Shear Capacity of Less Stiff SW2 at the Same Deflection of SW1 (0.242 in):
Recheck Deflection Using This Unit Shear and SW2 Parameters:
Total Capacity of Wall Line:
Notes: Say
Since the stiffer SW1 will reach its design strength at a lower deflection, we now need to determine what strength the less stiff SW2 is capable of developing at the same deflection. In order to do this, we’ll rearrange Equation 4.3-1, plug in the deflection we calculated for SW1, and solve for VSW2.
Requirements of 4.3.4.2 are in addition to those in 4.3.3.4.1 to ensure deflection compatibility between shear walls in a line and, therefore, the smaller of the design capacities associated with requirements of 4.3.4.2 and 4.3.3.4 is to be used as the controlling design capacity for each individual shear wall. For SW2 to match the same deflection of the stiffer SW1, 141 plf will control the design. This is the ASD Unit Shear Capacity of the less stiff SW2 at the same deflection of SW1 (0.242 inches).
Before continuing, let’s check our work using this unit shear (141 plf) and SW2 parameters. By receiving the same deflection of 0.242 inches, we confirm that 141 plf is correct in giving SW2 the same amount of deflection as SW1.
Finally, we’ll need to determine the total capacity of the wall line. Simply sum the product of SW1’s capacity (260 plf) and width (8 ft) and the product of SW2’s reduced capacity (141 plf) and width (2.3 ft). This gives us 2,404 pounds.

## Slide 48: Design Example 1: 2bs/h Adjustment Factor
ASD Unit Shear Capacity of SW1:
ASD Unit Shear Capacity of SW2:
Total Capacity of Wall Line:
Notes: Say
Now we’ll try an example with the easier, more familiar 2bs/h Adjustment Factor.
The first step is the same as before. We’ll check whether SW1 is a high aspect ratio shear wall. By dividing the height (8’) by the width (8’), we determine the aspect ratio is 1:1. No factoring is necessary since it is less than 2:1. From here, we’ll convert the 520 plf nominal capacity to ASD by dividing by 2.0 (per Section 4.3.3). The ASD Unit Shear Capacity of SW1 is 260 plf.
Next, we’ll follow the same pattern for SW2. By dividing the height (8’) by the width (2.3’), we find the aspect ratio of SW2 is 3.5:1. This is considered a high aspect ratio and will require an adjustment. By plugging the height (h=8’) and width (bs=2.3’) into the 2bs/h Adjustment Factor, we receive an adjustment factor of 0.57. From here, we’ll convert the 520 plf nominal capacity to ASD the same way as previous, with a result of 260 plf. By multiplying the ASD capacity by the adjustment factor of 0.57, we receive a reduced ASD Unit Shear Capacity of 148 plf.
Finally, we’ll need to determine the total capacity of the wall line. Simply sum the product of SW1’s capacity (260 plf) and width (8 ft) and the product of SW2’s reduced capacity (148 plf) and width (2.3 ft). This gives us 2,420 pounds.

## Slide 49: Design Example 1: Comparing Adjustment Methods
Comparing the Two Methods:
Similar capacity
using the new 1.25-0.125h/bs
Wall Line Capacities:
Notes: Say
Here we can see that both adjustment methods give very similar results when we have shear wall segments with different aspect ratios in the same wall line.

## Slide 50: Design Example 2: Assumptions
Calculate the capacity of this wall line, assuming:
15/32” structural sheathing
Southern Pine 2x4 framing (double 2x4 end posts)
8d nails at 6” o.c.
vnom = 520 plf (Table 4.3A)
Ga = 13 k/in
Δa = 0.125” at 3,500 lb
Calculate using both methods:
Equal Deflection Calculation (§4.3.3.4.1 / §4.3.4.2) (New Method)
2bs/h Adjustment Factor (§4.3.3.4.1.E1) (Alternative / Old Method)
2.3’
8’
v
δ
δ
SW1
SW2
2.3’
Notes: Say
For our second design example, we’ll use the exact same assumptions as the first, with the exception of the wall lengths. In this case, we’ll look at a wall line using two identical length shear walls (2.3 ft).
We’ll calculate the capacity of the wall line using both methods, and then compare the results. Our first example showed how the two methods can be very similar when a low aspect ratio and high aspect ratio wall are combined within the same line. This example will help illustrate how the two methods can differ.
Do
Review the assumptions for the Design Example.

## Slide 51: Design Example 2: Equal Deflection Calculation
ASD Unit Shear Capacity of SW1 & SW2:
Deflection of SW1 & SW2 at Reduced ASD Unit Shear Capacity:
Total Capacity of Wall Line:
* Since SW1 & SW2 are identical, they have the same stiffness and will deflect the same.
Notes: Say
As in the first example, we’ll begin with the Equal Deflection Calculation, sometimes referred to as the Relative Stiffness method, and use the new 1.25-0.125h/bs factor.
First, we’ll check whether the walls are considered high aspect ratio. We know from our previous example that SW2 had an aspect ratio of 3.5 and since we’ve now made SW1 identical, it too has an aspect ratio of 3.5. From here, we’ll convert the 520 plf nominal capacity to ASD by dividing by 2.0 (per Section 4.3.3) and reduce it by multiplying by 0.81. This was the same reduction we determined in our first example. Finally, we arrive at a reduced ASD Unit Shear Capacity of 210 plf.
Since both walls are identical in size, construction, and unit shear capacity, we know that they will have the same stiffness. Therefore, we also know that they will deflect the same amount. Our Equal Deflection Calculation is much simpler than the previous example, isn’t it?
Next, we determine the actual deflection for each wall by using Eq. 4.3-1. Plugging in all our variables, we arrive at a deflection of 0.213 inches. (Note that we didn’t actually need to calculate deflection to determine shear distribution since both our walls are identical. We would end up calculating it anyway at some point during our design, so now it’s done.)
Finally, we can multiply each unit shear capacity by each wall’s length and add them together, arriving at a total capacity for the wall line of 966 pounds.

## Slide 52: Design Example 2: 2bs/h Adjustment Factor
ASD Unit Shear Capacity of SW1 & SW2:
Total Capacity of Wall Line:
Notes: Say
Now we’ll determine the capacity for the same two walls using the 2bs/h Adjustment Factor.
We know from the Equal Deflection Method that both walls are considered high aspect ratio shear walls at 3.5. We determine that 2bs/h is equal to 0.57, just as it was in our first example.
Next, we’ll convert the 520 plf nominal capacity to ASD the same way as previous, with a result of 260 plf. By multiplying the ASD capacity by the 0.57 factor, we receive a reduced ASD Unit Shear Capacity of 148 plf.
Finally, we’ll need to determine the total capacity of the wall line. Simply sum the product of the two walls’ unit shear capacity and length, and we arrive at a total capacity of 681 pounds.

## Slide 53: Design Example 2: Comparing Adjustment Methods
42% increase in capacity
using the new 1.25-0.125h/bs
Wall Line Capacities:
Comparing the Two Methods:
Notes: Say
Here we can see how advantageous it is to not take the Exception 1 from Section 4.3.3.4.1 (2bs/h) and instead use the new 1.25-0.125h/bs factor. Since our walls were exactly the same, the deflection compatibility check required in Section 4.3.3.4.1 was inherently considered in our analysis. We ended up with a 42% better shear capacity for our wall line than we would have if we used the simple 2bs/h factor.

## Slide 54: Summary of Adjustment Factors
Aspect Ratio | §4.3.4.2 1.25-0.125h/bs | §4.3.3.4.1.E1 2bs/h | % Increase
≤ 2 | -- | -- | --
2.25 | 0.97 | 0.89 | 9%
2.5 | 0.94 | 0.80 | 17%
2.75 | 0.91 | 0.73 | 25%
3 | 0.88 | 0.67 | 31%
3.25 | 0.84 | 0.62 | 37%
3.5 | 0.81 | 0.57 | 42%
Both methods provide similar results when a low and high aspect ratio wall occur in the same wall line. However, for wall lines with multiple high aspect ratio walls, the 2bs/h is a more conservative factor than 1.25 – 0.125h/bs.
Notes: Say
As we saw in the first design example, both methods provide similar results when a low and high aspect ratio wall occur in the same wall line. However, for wall lines with multiple high aspect ratio walls, the 2bs/h is a more conservative factor than 1.25 – 0.125h/bs. This was shown in the second design example. Therefore, when you have a wall line composed of walls of identical high aspect ratios, you are better off using 1.25 – 0.125h/bs.
These percentages on the slide reflect the increase in shear capacity when using the new 1.25-0.125h/bs factor in lieu of the alternative 2bs/h factor for either a) a single high aspect ratio shear wall or b) a wall line with multiple identical high aspect ratio shear walls.
It's worth reiterating that the 2 methods have been shown to provide very similar results when a low aspect ratio wall (SW1) and 3.5 aspect ratio wall (SW2) occur within the same wall line. As previously discussed, however, the difference between the two methods can vary greatly depending on the makeup of the wall line. Therefore, the designer should consider whether there is a strength benefit in one method over the other depending on their specific wall configuration.
Quiz Note
This slide features information that will be found on the post-course knowledge assessment.
When is it most beneficial to use the new Equal Deflection Calculation (1.25-0.125h/bs)?
When you have a mixture of both high and low aspect ratio shear walls in a wall line.
When you have all low aspect ratio shear walls in a wall line.
When you have all high aspect ratio shear walls in a wall line.
When you are only analyzing a single shear wall line a wall line.

## Slide 55: Lesson Three Complete
Now that you’ve completed this lesson, you should be able to:
Explain how and when to use the capacity adjustments for shear walls with high aspect ratios
Notes: Do
Review the lesson objective summary.

## Slide 56
Shear Wall Design Methods
After completing this lesson, you will be able to:
Describe how to design segmented, perforated and force transfer wood shear walls using the SDPWS
L
4
Notes: Do
Review the lesson title and objective.

## Slide 57: Overview of Shear Wall Design Methods
1
Segmented
2
Perforated
3
Force Transfer
Individual Full-Height Wall Segments
SDPWS §4.3.5.1
Walls analyzed as isolated segments
Perforated Shear Walls
SDPWS §4.3.5.3
An empirical-based approach to shear walls
Force-Transfer Shear Walls
SDPWS §4.3.5.2
Designed for force transfer around the openings
Notes: Say
SDPWS identifies shear walls as one of the following “types”:
Individual Full-Height Wall Segment Shear Walls (i.e., no openings within an individual full-height segment);
Perforated Shear Walls (i.e., with openings, but rather than design for force-transfer around openings, reduced shear strength is used based on size of openings);
Force-transfer Shear Walls (i.e., with openings, but framing members, blocking, and connections around openings are designed for force-transfer).
Methods 2 and 3 consider total wall length with openings and require sheathing on all areas of wall. These methods typically result in fewer holdowns with lower capacities.

## Slide 58: Individual Full-Height Wall Segments
1
Segmented
Individual Full-Height Wall Segments
SDPWS §4.3.5.1

## Slide 59: Segmented Shear Wall Introduction
Notes: Say
In conventional (segmented) shear wall design, the shear wall segment is the portion of the shear wall that runs from the diaphragm above (such as a roof) to the floor diaphragm or foundation below.
In walls with openings (such as windows or doors), only the full-height segments may be used to transfer shear from the diaphragm above to the diaphragm (or foundation) below.
The segmented shear wall design method assumes each shear wall is a cantilevered element fixed at the base and free to deflect in-plane at the top.

## Slide 60: Segmented Shear Wall Limitations §4.3.5.1
Wall sections above/below openings don’t count
Full height wall segments must meet aspect ratio requirements in SDPWS Table 4.3.4
Holdowns are required at the ends of each full-height segment
Collectors for shear transfer shall be provided through the full length of shear wall line (i.e. top plates are detailed for shear transfer between plates at splices)
Where out-of-plane offsets occur, portions of the wall on each side of the offset shall be considered as separate force-transfer shear walls
Notes: Say
Each method has its own limitations. There are minimums, maximums and restrictions for when you may use each method.
Do
Review the limitations listed on the slide. Click to show new bullet points and their accompanying animations.
Say
One quick note about out-of-plane offsets. If a designer is dealing with IRC (International Residential Code) and doing wall bracing, the IRC allows for a 4’ offset from the wall bracing line to still count as one wall line. But with SDPWS, however, you would need to design it as a separate shear wall.

## Slide 61: Segmented Shear Wall Overview
The design shear force for this example is 3,500 lb at ASD (wind)
V = 3,500 lb
4’-0”
4’-0”
4’-0”
7’-0”
15’-0”
8’-0”
1’-6”
2’-6”
Segmented Shear Wall Dimensions and Anchorage Layout
Notes: Say
Shown on the slide is the wall that we’re going to design.
The segmented shear wall design method assumes each shear wall is a cantilevered element fixed at the base and free to deflect in-plane at the top.
Sheathing, if installed above or below openings, is neglected. The design shear force for this example is 3,500 pounds at ASD level, wind controlled.
Do
Read off parameters and dimensions (i.e., 4’ tall opening, two 8’x4’ segments, shear load of 3,500 pounds, designing for wind, holdowns at end of each full height wall segment, etc.).

## Slide 62: Segmented Shear Wall Design Process
Panel edge
nailing
Sheathing
Nails
Wall
height
End stud sized for compression forces
Interior studs 16” O.C.
Shearwall holdowns
Anchor bolts
Wall width
Interior nail spacing
Edge nail spacing
Edge nail spacing
Aspect Ratio of Full-height Segments
  Apply Equal Deflection Calculation or 2bs/h Reduction Factor to segments with ratios > 2:1
Sheathing Type / Thickness and Fastener Size / Spacing
  Calculate Nominal demand load in pounds per linear foot
  Use Table 4.3A to find sheathing type / thickness and fastener size / spacing
Notes: Do
Review the design process for segmented shear walls.

## Slide 63: Segmented Shear Wall Design Process, cont.
Panel edge
nailing
Sheathing
Nails
Wall
height
End stud sized for compression forces
Interior studs 16” O.C.
Shearwall holdowns
Anchor bolts
Wall width
Interior nail spacing
Edge nail spacing
Edge nail spacing
Anchorage for Overturning and Uplift
  Calculate overturning using statics and the sum of moments about the point of compression at the base of wall
  Choose best anchoring solutions for project
Notes: Do
Continue to review the design process for segmented shear walls.

## Slide 64: Segmented Shear Wall Design Example
SDPWS Table 4.3.4 limits aspect ratio of each wall segment.
For this example both walls are 8 ft tall and 4 ft wide.
Therefore:
Aspect Ratio of Full-height Segments
Notes: Say
The first step reverts us back to Lesson 3 where we discussed the aspect ratio limitations of shear walls (SDPWS Table 4.3.4 and SDPWS Section 4.3.3.4.1). The dimensions of our full-height shear wall segments are 8’ by 4’, giving us an aspect ratio of 2:1. According to Table 4.3.4, our design can be either blocked or unblocked. No capacity reduction adjustments are required.

## Slide 65: Segmented Shear Wall Design Example, cont.
Convert from ASD to Nominal level so we can easily use Table 4.3A.
SDPWS §4.3.3 gives Ω = 2.0, so:
Sheathing Type / Thickness and Fastener Size / Spacing
Convert design shear force to unit design force:
Notes: Say
Now we must determine the required sheathing and nailing for the shear walls using SDPWS Table 4.3A. Remember, this table uses nominal levels. The design shear force of our example is 3,500 pounds at ASD, so we’ll need to convert to nominal level load.
As a first step, let’s find our unit design force by dividing the shear force (3,500 pounds) by the width of both full-height segments (8 ft), giving us 438 plf. To convert this to a nominal load, multiply 438 plf by 2.0 (per SDPWS Section 4.3.3). This gives us a nominal unit shear capacity of 876 plf.
Now we can take that 876 plf and compare it to the capacities listed in the table to locate our optimal sheathing panel type / thickness and edge fastener size / spacing.

## Slide 66: Segmented Shear Wall Design Example, cont.
Sheathing Type / Thickness and Fastener Size / Spacing
Notes: Say
Here’s a close up of the relevant areas of Table 4.3A. Since we’re designing for wind in our example, the seismic columns have been cropped out of the table. Our goal is to find a sheathing panel type / thickness and panel edge fastener size / spacing that can withstand the demand of 876 plf (nominal). 3/8 or 7/16 inch rated sheathing nailed with 8d commons at 4”o.c. at edge (12”o.c. field) yields 895 or 980 plf of Nominal Shear Capacity.
When confronted with multiple options, consideration should be given to the potential cost and availability of sheathing material and labor force in your market. Generally, the thinner the sheathing and the wider the nail spacing, the more cost-effective the design will be.
Although it doesn’t apply to this example, be sure to take note of Footnote 2 of Table 4.3A: “Shears are permitted to be increased to values shown for 15/32 inch (nominal) sheathing with same nailing provided (a) studs are spaced a maximum 16 inches on center, or (b) panels are applied with long dimension across studs.”

## Slide 67: Segmented Shear Wall Design Example, cont.
Bottom level on concrete foundation:
Upper level or bottom level on raised wood floor:
Anchorage for Overturning and Shear
Notes: Say
Once the sheathing has transferred the shear at the top of the wall to the bottom of the wall, the bottom plate must be anchored to the foundation with connections capable of transferring this force. There are many different options to work with.
With a wood floor, nails, screws or clips may be used to transfer this in-plane shear force. With a concrete foundation, anchor bolts are typically used. Alternatively, mudsill anchors are a cost-effective solution, or for post-installed conditions, mechanical or adhesive anchors may be used.
Keep in mind that these anchors likely need to transfer other forces (like uplift or wind loads perpendicular to the shear wall) into the foundation as well, so space anchors accordingly.

## Slide 68: Segmented Shear Wall Design Example, cont.
We can easily determine the overturning moment:
What is the resisting moment arm?
Shearwall overturning moment arm = 8’-0”
Shearwall resisting moment arm
4’-0”
2’-0”
DL
v = 1750 lb
Unit shear v = 1750 lb / 4’0” = 438 plf
Anchorage for Overturning
Notes: Say
In our example, we have two identical shear walls, making design much simpler. The quick way to calculate overturning is to just multiply the unit shear (438 plf) by the wall height (8’), giving us 3,504 pounds. This method is acceptable for single-story or top-story applications (or when shear walls are longer), but it becomes un-conservative in multi-story applications where shear walls may have aspect ratios near code limits and cumulative overturning must be calculated.
To more accurately calculate overturning, we can use statics and the sum of moments about the point of compression at the foundation.
First, we will determine our overturning moment (OTM) caused by the design shear force. We will multiply the design shear force, v, of 1,750 pounds by its moment arm, h, of 8 ft, and arrive at an OTM equal to 14 ft-kips (or 14,000 ft-lb).
Next, we will calculate our resisting moment, but before we can do that we will have to determine what our resisting moment arm is. If we assumed the entire width of the wall, or 4 ft in our example, we would end up underestimating our required resisting overturning forces. Actually, our resisting moment arm is less than the full width of the wall, but what is it?

## Slide 69: Segmented Shear Wall Design Example, cont.
Resisting moment arm = center of compression to center of tension
Assume two end studs for T/C chords
Anchorage for Overturning, cont.
= centerline
Notes: Say
The resisting moment arm spans from the center of compression (center of post or stud pack) to the center of tension (holdown anchor bolt centerline).
Let us assume that our shear walls have two end studs for tension/compression chords. Each stud is approximately 1-1/2” wide (assuming we’re using 2-2x4’s). This makes the center of compression about 1-1/2” from the edge of the shear wall.
Let’s also assume that the holdowns we’re using have a distance of 1-1/2” from the back of the holdown to the centerline (℄) of the anchor bolt. Add this to the 3” of two end studs and the center of tension is about 4-1/2” from the edge of the wall.
By subtracting these distances from the full width of the shear wall (48” – 1.5” – 4.5”), we receive a distance of 42” between the center of tension and center of compression.
Do
Click to show table of holdown dimensions.
Say
Some holdown manufacture’s offer spec sheets of their holdowns that will assist in locating the centerline distance.

## Slide 70: Segmented Shear Wall Design Example, cont.
Dead load can also be used to resist overturning…
Assume 10 psf wall weight:
ASD load combination allows for 60% of dead load to be used:
Solve for tension:
Anchorage for Overturning, cont.
Notes: Say
Lastly, the dead load of the wall itself can be used to resist overturning (neglecting it is conservative). The controlling ASD load combination allows for 60% of dead load to be used. Assuming each segment weighs 10 psf, we determine it to weigh 320 pounds. 60% of 320 pounds gives us 192 pounds of dead load resisting at the center of the wall. (Floor dead load could also help resist overturning, but it is unknown.)
After plugging in our values, solving for tension yields 3,898 pounds.
Compression would be similar to tension, but slightly higher. The wall dead load does not resist compression, but actually would increase it slightly based on stud spacing.

## Slide 71: Segmented Shear Wall Design Example, cont.
Use a holdown (or straps if on upper level) to resist overturning
To verify post/stud (chord) capacity, use NDS or manufacturer’s tables
Anchorage for Overturning, cont.
Notes: Say
The graphic shows four different types of holdowns: bolted, nailed (post installed), nailed (cast in place), and screw styles. Manufacturers offer many types of holdowns for anchorage solutions. First you’ll choose an HDU, then check the capacity of the posts/studs (chords). To verify the chord capacity, use the NDS – or check with the manufacturer.
Do
Click to show “Post Tension Loads for Southern Pine” table.
Say
Shown is an example table of Post Tension Loads for Southern Pine. The posts and studs must resist the holdown force from the overturning calculation. For our example, we’ll need to resist 3,898 pounds. As mentioned when calculating the tension, our chords are assumed to be comprised of 2-2x4’s. If we were to use nailed holdowns – which have a 0” bolt diameter since they won’t need to be drilled – then our allowable tension would be 11,340 pounds. This is more than sufficient! (Remember, drilling into wood will reduce its capacity.)
<!-- Table taken from back of SST catalog, page 246 -->
Do
Click to show “Post Allowable Compression Loads for Southern Pine” table.
Say
This larger table shows the Post Allowable Compression Loads for Southern Pine. In the two main groups of columns, you’ll notice the only difference in the titles are the numbers “100” and “160”. The “160” column allows a higher capacity. The code lets you take advantage of increased capacity if it’s short term loading (i.e., the load isn’t always there) – such as the case when designing for wind or seismic. For our example, since we are designing for wind, we will take advantage of the “160” column. With double 2x4’s and an 8’ nominal top plate height, we have a compression capacity of 5,905 pounds. This is also sufficient.
<!-- Table taken from back of SST catalog, page 245-->

## Slide 72: Perforated Shear Walls
2
Perforated
Perforated Shear Walls
SDPWS §4.3.5.3

## Slide 73: Perforated Shear Wall Introduction
V = 3,500 lb
Perforated Shear Wall Segments Fully and
Partially Restrained for Overturning
Strong direction has full fixity, develops full unit shear, and carries about 75% of shear wall load
Weak direction segment has reduced uplift restraint, develops partial unit shear and carries about 25% of shear wall load
T
C
C
Notes: Say
A perforated shear wall allows a fully-sheathed wall with door and window openings to be treated as a single shear wall with slightly lower shear capacity. This means that all portions of the wall, those above and below window and door openings, are assumed to contribute to the lateral load-carrying capacity of the shear wall.
The concept of a perforated shear wall is that it relies on the inherent continuity provided by typical construction rather than requiring special detailing. Each full-height sheathed segment has a different degree of restraint for overturning forces and, as a result, has a varying capacity.
The advantage of this method is that the entire perforated wall only requires two holdowns, one on each end. The traditional methodology would have required that the wall be broken into segments, and each segment anchored with a pair of holdowns.
What we’ll be doing here is looking at the whole wall as one unit, then use reduction factors for the size and quantity of openings. We’ll go through a similar approach as the segmented shear wall in terms of calculating capacity, but we will reference a table to determine a capacity reduction factor.
In the wall used for the example problem, and for the direction of load shown, the right-hand segment has a tie-down that resists wall uplift, and can be considered fully restrained for overturning; therefore, the right-hand segment can reach full design capacity. The left-hand segment develops a lower degree of overturning restraint, and therefore has reduced capacity. The shear resistance adjustment factor Co is used to adjust the shear wall for the combination of fully restrained and partially restrained segments.
Do
Discuss notes to the left and right of the graphic.

## Slide 74: Perforated Shear Wall Limitations §4.3.5.3
Fully-sheathed wall with door and window openings can be treated as a single shear wall with slightly lower shear capacity
Entire perforated wall only requires two holdowns, one on each end
The perforated shear wall height, h, shall not exceed 20 ft
Collectors for shear transfer shall be provided through the full length of shear wall line (i.e. top plates are detailed for shear transfer between plates at splices)
Where out-of-plane offsets occur, portions of the wall on each side of the offset shall be considered as separate force-transfer shear walls
Notes: Do
Review the limitations listed on the slide. Click to show new bullet points and their accompanying animations.

## Slide 75: Perforated Shear Wall Limitations §4.3.5.3, cont.
Must have a full height wall segment at each end
Notes: Say
If there is a wall opening at the wall end, a perforated shear wall is still permitted -- but without utilizing the end length of the wall opening. In other words, the ends are defined based on where last full height segment is.
Where Ltot = length of perforated shear wall including full height segments and segments with openings.
Do
Click to show picture with permitted opening at the end of a wall line.

## Slide 76: Perforated Shear Wall Limitations §4.3.5.3, cont.
Must have uniform top- and bottom-of-wall elevations
Notes: Say
A perforated shear wall shall have uniform top-of-wall and bottom-of-wall elevations (the top and bottom have to be identical). No stepped foundations or raked walls are allowed. Perforated shear walls not having uniform elevations shall be designed by other methods.

## Slide 77: Perforated Shear Wall Design Overview
V = 3,500 lb
4’-0”
4’-0”
4’-0”
7’-0”
15’-0”
8’-0”
1’-6”
2’-6”
The design shear force for this example is 3,500 lb at ASD (wind)
Perforated Shear Wall Dimensions and Anchorage Layout
Notes: Say
Here’s the design example for our perforated shear wall.
Compared to the segmented approach, it has more anchorage and sheathing, but fewer holdowns. It is the most commonly used approach by designers.

## Slide 78: Perforated Shear Wall Design Process
Aspect Ratio of Full-height Segments
  Apply 2bs/h reduction factor to segments with ratios > 2:1
  Sum total length of segments with ratios ≤ 3.5:1 (∑Li)
Shear Resistance Adjustment Factor, Co
  Find percentage of full-height sheathing
  Find ratio of max opening height to wall clear height
Maximum Induced Unit Shear, vmax
Notes: Do
Review the design process for perforated shear walls.

## Slide 79: Perforated Shear Wall Design Process, cont.
Sheathing Type / Thickness and Fastener Size / Spacing
  Calculate Nominal demand load in pounds per linear foot
  Use Table 4.3A to find sheathing thickness and fastener spacing
Anchorage for Overturning and Uplift
  Calculate unit uplift force, t
  Calculate tension chord uplift force, T, and compression chord force, C
  Determine best anchoring solutions for project
Notes: Do
Continue to review the design process for perforated shear walls.

## Slide 80: Perforated Shear Wall Design Example
Full-height segments must comply with Table 4.3.4, but not 4.3.4.2
Aspect Ratio of Full-height Segments
Notes: Say
Per Section 4.3.4.3, the length of each perforated shear wall segment with an aspect ratio greater than 2:1 shall be multiplied by 2bs/h for the purposes of determining Li and ∑Li. The provisions of Section 4.3.4.2 and the exceptions to Section 4.3.3.4.1 do not apply to perforated shear wall segments.
Looking at the middle level of Figure 4C (right of slide), notice that the space between the door and window isn’t counted as a shear wall. Section 4.3.4.3 states that “Portions of walls with aspect ratios exceeding 3.5:1 shall not be considered in the sum of shear wall segments.”

## Slide 81: Perforated Shear Wall Design Example, cont.
Aspect Ratio of Full-height Segments, cont.
Notes: <!-- Optional slide for if students are having trouble grasping the concept. -->
Say
Here’s an illustration that gives a visual interpretation of Figure 4C on the previous slide. As shown, all full-height segments must have a height to width ratio of less than 3.5:1 if wood structural panel (blocked) sheathing is used. If a segment exceeds that aspect ratio, then that segment does not count toward the sum of shear wall segment lengths.

## Slide 82: Perforated Shear Wall Design Example, cont.
4’-0”
8’-0”
4’-0”
2:1
2:1
Full-height Segments have an Aspect Ratio ≤ 2:1
No adjustments required
Aspect Ratio of Full-height Segments, cont.
Length of Segments with Aspect Ratio ≤ 3.5:1 = 8’
Notes: Say
Let’s apply these rules to our perforated shear wall design example.
Our full-height segments are 8’ in height and 4’ in width, an aspect ratio of 2:1. Since they are not greater than 2:1, no adjustments are required.
Both of these full-height segments are counted when summing the length of segments because they are not greater than 3.5:1. The total length of the segments is 8’.

## Slide 83: Perforated Shear Wall Design Example, cont.
Shear Capacity Adjustment Factor, Co
4’-0”
4’-0”
15’-0”
8’-0”
4’-0”
Percentage of Full-height Sheathing in Wall Line
Ratio of Maximum Opening Height to Wall Height
27%
27%
h/2
Notes: Say
SDPWS Section 4.3.3.5 addresses perforated shear wall capacity.
We’ll use the shear capacity adjustment factor, Co, to calculate adjusted shear demand in pounds per linear foot (ASD). In a roundabout way, the shear capacity adjustment factor is used to reduce capacity of our wall line to account for the strength reduction caused by the large opening. To do this, Co effectively increases demand load to force us to design a stronger wall.
There are a couple parameters we’ll need to calculate in order to determine Co. We’ll first need to find:
The percentage of full-height sheathing in the wall line, and
The ratio of maximum opening height in the wall line to the wall clear height
Do
Click to show animation depicting that each full-height segment is 27% of the full width of the wall.
Say
The percentage of full-height sheathing is calculated as the sum of widths of full-height wall segments (those which meet the ≤ 3.5:1 aspect ratio requirement) (∑Li) divided by the out-to-out width of the wall (Ltot). In this case, (4’+4’)/15’ = 0.53, or 53 percent.
Do
Click to show animation depicting that the opening is half the size of the total wall height (h/2).
Say
The ratio of the maximum opening height to the wall clear height is taken as 4’ divided by 8’ -- or a maximum opening height of h / 2, where h is the wall clear height.

## Slide 84: Perforated Shear Wall Design Example, cont.
    where:
    r = sheathing area ratio
    Ltot = total length or perforated shear wall, ft
    AO = total area of openings in the perforated shear wall, ft2
    h = shear wall height, ft
    ∑Li = sum of perforated shear wall segment lengths Li, ft
Shear Capacity Adjustment Factor, Co, cont.
Notes: Say
There are two methods for finding the appropriate shear capacity adjustment factor: solve a complicated equation, or estimate it using Table 4.3.3.5. Let’s first review how the equation works.
Section 4.3.3.5 of the 2015 SDPWS states “The nominal shear capacity of a perforated shear wall shall be take as the tabulated nominal unit shear capacity multiplied by the sum of the shear wall segment lengths, ∑Li, and the appropriate shear capacity adjustment factor, Co, from Table 4.3.3.5 or calculated using the following equation.”
The calculated shear capacity adjustment factor has five parameters:
Do
Review the equation parameters.
r = sheathing area ratio
Ltot = total length of a perforated shear wall including the lengths of perforated shear wall segments and the lengths of segments containing openings, ft
AO = total area of openings in the perforated shear wall where individual opening areas are calculated as the opening width times the clear opening height, ft2. Where sheathing is not applied to framing above or below the opening, these areas shall be included in the total area of openings. Where the opening height is less than h/3, an opening height of h/3 shall be used
h = height of the perforated shear wall, ft
∑Li = sum of perforated shear wall segment lengths Li, ft. Lengths of perforated shear wall segments with aspect ratios greater than 2:1 shall be adjusted in accordance with 4.3.4.3
Do
Point out that it can be complicated to calculate all this. Because of that, SDPWS has setup Table 4.3.3.5 to assist. See next slide.

## Slide 85: Perforated Shear Wall Design Example, cont.
Use percent fully sheathed and maximum opening height to find Co factor
Shear Capacity Adjustment Factor, Co, cont.
Notes: Say
Shear demand on the full-height segments of a perforated shear wall are increased because of the holes (windows/doors) in the other segments. In Table 4.3.3.5 you can see that the Co factor is less than 1.00 for all cases other than very low height openings (i.e. doggy door or small window).
When using the tabulated Shear Capacity Adjustment Factor, Co, it is based on the tallest opening in the wall.
But if you have one tall opening and lots of smaller openings, it can be conservative. In that case, it may be worth the effort to calculate the actual Shear Capacity Adjustment Factor using the equation on the previous slide.
With approximately 50% of full-height sheathing and a maximum opening height of h/2, Table 4.3.3.5 gives us reduction factor of 0.80.
Quiz Note
This slide features information that will be found on the post-course knowledge assessment.
To find the Shear Capacity Adjustment Factor (Co) for a perforated shear wall, SDPWS Table 4.3.3.5 requires the designer to know the percent of full-height sheathing and the __________.
Maximum induced unit shear
Maximum opening height
Uniform uplift force
Tension and compression

## Slide 86: Perforated Shear Wall Design Example, cont.
Calculate maximum induced unit shear for anchorage per Eq. 4.3-9:
Co = shear capacity adjustment factor from Table 4.3.3.5
v = induced shear force in perforated shear wall, lb
∑ Li = sum of perforated shear wall segment lengths, ft
Maximum Induced Unit Shear, vmax
Notes: Say
The maximum induced unit shear force, vmax, transmitted into the top of a perforated shear wall, out of the base of the perforated shear wall at full height sheathing, and into collectors connecting shear wall segments, shall be calculated in accordance with the Equation 4.3-9 on the slide.
The equation for the adjusted unit shear demand (vmax) goes back to what we were talking about: reducing capacity due to openings the lessen the strength and stiffness of our shear wall. This equation creates the same effect by increasing demand load, forcing us to design a stronger wall. Notice that because the Co factor is less than 1 (0.80 for our example), and because it is in the denominator, it will increase total shear demand.

## Slide 87: Perforated Shear Wall Design Example, cont.
V = 3,500 lb (ASD wind load)
Co = 0.80 (from Table 4.3.3.5)
∑Li = 8 ft
vmax = 547 plf
t
t
t
t
t
t
v
Maximum Induced Unit Shear, vmax, cont.
T
C
C
t
t
t
t
t
t
v
Notes: Say
This is where the Co factor of 0.8 comes into play. The denominator of (0.8)(8 ft) creates a vmax with 25% more demand.
Do
Review calculation shown on slide.

## Slide 88: Perforated Shear Wall Design Example, cont.
Sheathing Thickness and Fastener Spacing
Notes: Say
On this step, we’ll follow the same approach as for Segmented Shear Walls by using Table 4.3A to locate the best sheathing thickness and panel edge fastener spacing.
First, we’ll covert our Maximum Induced Unit Shear from ASD to a Nominal value by multiplying by 2.0. This gives us 1,094 plf (nominal).
From here, we find that 3/8 or 7/16 inch rated sheathing nailed with 8d commons at 3”o.c. at edge yields 1150 or 1260 plf of Nominal Shear Capacity.

## Slide 89: Perforated Shear Wall Design Example, cont.
Anchorage for Overturning and Uplift
Uniform Uplift
Force, t
Accounting for Unit Uplift Force, t, is necessary to resist uplift forces acting on individual wall segments.
Notes: Say
Next, we’ll visit the steps to determine the proper anchorage to resist overturning.
Due to the fact that holdowns are only required at each end of a perforated shear wall, additional anchors are needed along the full-height sheathing segments to resist uplift from overturning forces acting on the individual segments. The uniform uplift force, t, is equal to the maximum induced unit shear, vmax, that we calculated previously.
Note that this uniform uplift force, t, for the perforated shear wall method is in addition to any other tension forces that the anchors may be subjected to (for example, wind uplift).

## Slide 90: Perforated Shear Wall Design Example, cont.
Co = shear capacity adjustment factor from Table 4.3.3.5
V = total shear force in perforated shear wall, lb
∑ Li = sum of perforated shear wall segment lengths, ft
h = shear wall height, ft
Equation 4.3-8
Anchorage for Overturning and Uplift, cont.
Notes: Say
We will also need to design for the tension and compression forces acting on the chords of our perforated shear wall.
The ASD tension chord uplift force due to overturning is calculated by Equation 4.3-8 shown on the slide. The result is similar to multiplying vmax by the shear wall height.

## Slide 91: Perforated Shear Wall Design Example, cont.
t
t
t
t
t
t
V = 3,500 lb (ASD)
h = 8 ft
∑Li = 8 ft
Co = 0.80 from Table 4.3.3.5
Anchorage for Overturning and Uplift, cont.
T
C
C
t
t
t
t
t
t
V = 3,500 lb
Notes: Say
Perforated shear wall overturning anchorage and load path are addressed in SDPWS Section 4.3.6.1.3. Tension chords tie-downs are provided at each end of the perforated shear wall. The ASD tension chord uplift force due to overturning is calculated on the slide.
This calculates how much capacity is needed for studs and holdowns. Each is designed for 4,375 pounds.
Do
Click to show animation of circle highlighting compression forces.
Say
Remember that we’re designing tension for each end of each perforated shear wall line (not each segment). However, compression forces will act on each segment. This is illustrated on the figure.

## Slide 92: Force Transfer Around Openings Shear Walls
3
Force Transfer
Force Transfer Around Openings Shear Walls
SDPWS §4.3.5.2

## Slide 93: Force Transfer Shear Wall Introduction
Notes: Say
Another method in the building code for the design of site-built shear walls is the Force Transfer Method. It allows the designer to design a shear wall with a large opening and maintain a high shear capacity by transferring shear around the opening.
This is usually the site-built shear wall design method of last resort before having to use a pre-fabricated shear wall or a different lateral force resisting system all together (i.e. moment frame).
Architectural limitations such as lack of available shear wall length and/or openings in critical locations, or possibly just an attempt to reduce the number of holdowns may lead a designer to choose this method.

## Slide 94: Force Transfer Shear Wall Limitations §4.3.5.2
b ≥ 24” for each wall pier
Full-height wall segments located at each end
Collectors for shear transfer shall be provided through the full length of the force transfer shear wall (i.e. top plates are detailed for shear transfer between plates at splices)
Where out-of-plane offsets occur, portions of the wall on each side of the offset shall be considered as separate force-transfer shear walls
Notes: Do
Review the limitations listed on the slide. Click to show new bullet points and their accompanying animations.

## Slide 95: Force Transfer Shear Wall Uses Rational Approach
Three most common “rational approaches” are:
Drag Strut technique
Cantilever Beam technique
Deikmann technique
www.apawood.org
“Joint Research Report: Evaluation of Force Transfer Around Openings,” Form M410
Notes: Say
There are a few different “rational approaches” out there for designing site-built shear walls for Force-Transfer around openings (FTAO). The three most common are:
Drag Strut technique
Cantilever Beam technique
Deikmann technique
APA, the Engineered Wood Association, conducted full-scale tests on a variety of wall specimens and compared measured forces to those predicted by the three methods. The results are written up in this research paper, “Joint Research Report: Evaluation of Force Transfer Around Openings,” Form M410.
They concluded the following:
The drag strut technique was consistently un-conservative.
The Cantilever Beam technique was consistently ultra-conservative.
Deikmann technique provided reasonable agreement with measured strap forces.
There is a fourth approach that has been introduced recently called the SEAOC or Thompson method, developed by Doug Thompson. It hasn’t gained widespread acceptance yet, but its results are very similar to the Deikmann technique.
We’ll be using the Deikmann technique for our example. The design example in this presentation is provided by: Bryer, D.E., Fridley, K.J., Cobeen, K.E., and Polluck, D.G. (2007). Design of Wood Structures. New York, NY: McGraw-Hill.
Quiz Note
This slide features information that will be found on the post-course knowledge assessment.
Out of the three common rational approaches for designing a force-transfer shear wall, which technique provided the most reasonable agreement with strap forces measured from full-scale testing?
Drag strut technique
Cantilever technique
Deikmann technique
None of the above

## Slide 96: Force Transfer Shear Wall Design Overview
V = 3,500 lb
4’-0”
4’-0”
4’-0”
7’-0”
1’-6”
2’-6”
The design shear force for this example is 3,500 lb at ASD (wind)
h = wall pier
height
wall pier
b1 = wall pier
width ≥ 2’-0”
b2 = wall pier
width ≥ 2’-0”
C
T
V
Notes: Say
Here’s the design example for a force transfer around openings shear wall. In line with the previous examples, our design shear force is 3,500 pounds at ASD level (wind).
This detail shows that the wall pier segments on either side of the opening are used to qualify the aspect ratio limit of the wall (rather than the full height segments).
This method reduces the number of holdowns required, but it does require additional detailing of connectors around the opening (i.e. blocking and coil strapping) and extensive calculations to design the wall.

## Slide 97: Force Transfer Shear Wall Design Process
Deikmann Technique Analysis
  Determine Tension and Compression Overturning Forces
  Divide shear wall into zones
  Determine demand shear acting on each zone
  Check resulting analysis
Aspect Ratios of Shear Walls, Openings and Wall Piers
  Check that the overall shear wall, openings and wall piers do not exceed the aspect ratio limitations of Table 4.3.4
Notes: Do
Review the design process for force transfer around openings (FTAO) shear walls.

## Slide 98: Force Transfer Shear Wall Design Process, cont.
Sheathing Thickness and Fastener Spacing
  Calculate Nominal demand load in pounds per linear foot
  Use Table 4.3A to find sheathing thickness and fastener spacing
Design for Overturning
  Design for Tension and Compression of outer boundary members
  Design for boundary members around openings
Notes: Do
Continue to review the design process for force transfer around openings (FTAO) shear walls.

## Slide 99: Force Transfer Shear Wall Design Example
Deikmann Technique Analysis
V = 3,500 lb
Free Body Diaphragm Shear Wall Designed for Force Transfer Around Opening
C
T
3,500 lb
Straps
Blocking
Notes: Say
The design method of using “force transfer around openings” means that the entire wall will be considered to overturn as a unit, resulting in the free body diagram shown here.
The idea here is to design around the opening, then reinforce the opening so that we do not need to make capacity reduction adjustments (like with perforated shear walls). The use of additional blocking and straps will be required so that we don’t need to reduce capacity or increase demand load.
We’ll start by determining the Compression, C, and Tension, T, of the shear wall. These forces, along with the shear demand load, V, will help us find the forces acting upon the individual zones that we’ll figuratively “cut” into the shear wall.
To find the Tension and Compression forces, multiply the shear demand load, 3,500 pounds, by the moment arm of 8 feet (the height of our shear wall). Then divide by the resisting moment arm of 15 feet (the width of our shear wall). This gives us a Tension/Compression force of 1,867 pounds.

## Slide 100: Force Transfer Shear Wall Design Example, cont.
Deikmann Technique Analysis, cont.
V = 3,500 lb
C
T
3,500 lb
Beam Behavior of Sheathed Areas Above and Below Window
Notes: Say
In order for sheathing areas above and below the opening to be able to provide the behavior of overturning as a unit, the sheathing areas need to be capable of acting like beams, carrying shear forces, and having flexural continuity at each end.
The shear forces are carried by the sheathing. Flexural forces are resisted by framing members at the opening (header and 2X plates), and continuity into the full height wall at each end is provided by strapping for tension forces and blocking for compression forces.
Assuming the shear wall will turn as one piece, we need to figure out the force to design for around openings in order to make that happen. Our goal is to break it up so that sheathing itself acts as beams to bring shear forces across the wall. In short, everything will need to be pretty rigid.
Depicted in the figure:
Up and down lines = shear forces
Rotating lines = moment/flexural forces
The shear forces are carried by the sheathing. Flexural forces are resisted by framing members at the opening (header and 2x plates) and continuity into the full height wall at each end is provided by strapping for tension forces and blocking for compression forces.

## Slide 101: Force Transfer Shear Wall Design Example, cont.
Deikmann Technique Analysis, cont.
3,500 lb
3,500 lb
Zones for Rational Analysis of Shear Wall
1,867 lb
1,867 lb
4
3
2
1
5
6
7
8
A
B
C
E
H
G
F
D
Notes: Say
The Diekmann technique assumes the wall acts as a singular unit and internal forces are resolved using principles of mechanics. The shear wall is divided into eight different zones A to H as follows.

## Slide 102: Force Transfer Shear Wall Design Example, cont.
Deikmann Technique Analysis, cont.
3,500 lb
3,500 lb
1,867 lb
1,867 lb
A
B
C
E
H
G
F
D
B
G
B & G: Horiz.
4
3
2
1
5
6
7
8
4’-0”
4’-0”
Notes: Say
The shear in each of these zones will be established. The shear in segments B and G can first be determined by statics by making a horizontal cut at wall mid-height and summing horizontal forces.
Zones B and G will need to resist a total of 3,500 pounds. Our goal is to figure out the force (in pounds per linear foot) acting on each zone. Assuming the full force is acting on two sections, and each section is four feet in width, we find that zones B and G will each need to resist 438 pounds per linear foot. [ (3500 lb / (4’ +4’) = 438 plf ]

## Slide 103: Force Transfer Shear Wall Design Example, cont.
Deikmann Technique Analysis, cont.
3,500 lb
3,500 lb
1,867 lb
1,867 lb
A
C
E
H
F
D
B
G
4
3
2
1
5
6
7
8
E
D
D & E: Vert.
1’-6”
2’-6”
Notes: Say
Similarly the shear in zones D and E can be determined by making a vertical cut and summing vertical forces.
Zones D and E will need to resist a total of 1,867 pounds. This is the reason why we determined Tension and Compression as a first step to the Deikmann Analysis. Like the previous slide, our goal is to figure out the force (in pounds per linear foot) acting on each zone. Assume the full force is acting on the two sections. The top section is 1’-6” in height, while the bottom section is 2’-6” in height. Using the same approach as before, we find that zones D and E will each need to resist 467 pounds per linear foot. [ (1,867 lb / (1.5’ +2.5’) = 467 plf ]

## Slide 104: Force Transfer Shear Wall Design Example, cont.
Deikmann Technique Analysis, cont.
3,500 lb
3,500 lb
1,867 lb
1,867 lb
4
3
2
1
5
6
7
8
A
B
C
E
H
G
F
D
438 plf
438 plf
467 plf
467 plf
T&C = 0
T&C = 467 plf x 3.5’ = 1,635 lb
F & H: Horiz.
A & C: Horiz.
Notes: Say
The figure on the slide shows our results for zones B, D, E and G. Next we’ll need to determine the forces acting on the corner zones.
An assumption will be made as to where the coupling beam has a zero moment. Because the full-height shear wall segments on each side of the opening are the same width (both 4’-0”), the point of zero moment will be set at mid-length of the opening. Here the chord tension force (T) and compression force (C) can be set to zero.
Taking Line 2 above the window and starting with T = 0 at the midpoint, the boundary member force at the upper right-hand corner of the window (intersection of Lines 2 and 7) can be calculated as the uniform shear in zone D of 467 plf times the distance, 3.5 ft. The force in Line 2 needs to reduce back down to 0 at intersection of Lines 2 and 8. As a result, between 7 and 8 a uniform force of 409 plf needs to be transferred back out of the boundary member. 438 plf is already known to go into zone G. The difference (438 – 409 = 29 plf) will go into zone F. The same pattern can be used to calculate boundary member force and unit shears at the other three corners of the opening.
---
Difficulties understanding? Let’s look at it another way.
Assume there is zero force at dead center, where tension and compression cancel out (T&C = 0). Forces are going to increase to the left and right, but in middle it’s zero. Moving to the right, we need to find the force at the intersection of lines 2 and 7. Let’s take a look at our inputs:
The distance from the zero force moment to the intersection of lines 2 and 7 is 3’-6” (or 3.5’)
The unit force of zone D is 467 pounds per linear foot
So if we take 467 plf and multiply it by the distance, it will give us the force at that point. (467 plf)(3.5’) = 1,635 lb.
If we continue moving to the right and reach the intersection of lines 2 and 8, there is no force remaining (because there is no wall remaining). As such, the force must be zero when we intersect line 8. The force will evenly reduce from 1,635 pounds to 0 pounds over the course of four feet (the width of the wall segment). Dividing 1,635 pounds by 4 feet results in a unit force of 409 pounds per linear foot for the portion of line 2 that is in between lines 7 and 8. From here, it is easy to find the unit force for zone F. All forces need to cancel out, so the difference between zone G (438 plf) and our unit force for the portion of line 2 that is in between lines 7 and 8 (409 plf) leaves 29 plf for zone F.

## Slide 105: Force Transfer Shear Wall Design Example, cont.
Deikmann Technique Analysis, cont.
3,500 lb
3,500 lb
1,867 lb
1,867 lb
4
3
2
1
5
6
7
8
A
B
C
E
H
G
F
D
438 plf
438 plf
467 plf
467 plf
29 plf
29 plf
29 plf
29 plf
Lines 6 & 7 Check:
Lines 5 & 8 Check:
Notes: Say
The resulting analysis can be checked by making sure that the vertical reactions on Lines 5 and 8 add up to 1867 lb, and on Lines 6 an 7 add up to 0. This check is made and the rational analysis is verified.

## Slide 106: Force Transfer Shear Wall Design Example, cont.
Aspect Ratios of Shear Wall, Openings and Wall Piers
Notes: Say
SDPWS Section 4.3.4.4 states that the aspect ratio limitations of Table 4.3.4 shall apply to the overall shear wall including openings and to each wall pier at the sides of openings. The height of a wall pier with an opening on one side shall be defined as the clear height of the pier at the side of the opening. The height of a wall pier with an opening on each side shall be defined as the larger of the clear heights of the pier at the sides of the openings. The length of a wall pier shall be defined as the sheathed length of the pier. Wall piers with aspect ratios exceeding 3.5:1 shall not be considered as portions of force-transfer shear walls.
The definition of a wall pier changes depending on height of the opening adjacent to it (as shown in the figure). Like the previous two methods, wall piers with an aspect ratio greater than 3.5:1 shall not be considered as portions of the shear wall because they do not contain the necessary strength and stiffness.
Quiz Note
This slide features information that will be found on the post-course knowledge assessment.
True or false: When designing force-transfer shear walls, the definition of a wall pier changes depending on the height of the opening adjacent to it.
True
False

## Slide 107: Force Transfer Shear Wall Design Example, cont.
0.53
1.0
4’-0”
4’-0”
15’-0”
8’-0”
4’-0”
1.0
Aspect Ratios of Shear Wall, Openings and Wall Piers
Notes: Do
Click to show full wall aspect ratio animation.
Say
The aspect ratio of the full wall is 0.53:1.
Do
Click to show wall pier aspect ratio animation.
Say
We need to check if the wall piers comply with the aspect ratio limitations of Table 4.3.4. As mentioned earlier, the definition of a wall pier changes depending on height of the opening adjacent to it. The wall piers in our example match the height of the opening, 4’-0”. Since the width of each segment is also 4’-0”, the wall piers have an aspect ratio of 1:1. This meets the criteria of ≤ 3.5:1.

## Slide 108: Force Transfer Shear Wall Design Example, cont.
Sheathing Thickness and Fastener Spacing
Notes: Say
On this step, we’ll follow the same approach as the previous design examples by using Table 4.3A to locate the best sheathing thickness and panel edge fastener spacing.
First, we’ll covert our Maximum Induced Unit Shear from ASD to a Nominal value by multiplying by 2.0. This gives us 934 plf (nominal).
From here, we find that 7/16 inch rated sheathing nailed with 8d commons at 4”o.c. at edge yields 980 plf of Nominal Shear Capacity.
Edge fasteners will be applied to the entire outside of the wall line, around the opening, and continuing along those lines to form a “tic-tac-toe” grid of nails.

## Slide 109: Force Transfer Shear Wall Design Example, cont.
4
3
2
1
5
6
A
B
C
438 plf
29 plf
29 plf
Design for Overturning and Uplift
Notes: Say
We previously determined our tension and compression forces for the chords at each end of our shear wall. However, we still need to determine the maximum tension and compression forces that occur around the opening so we can properly design our studs, blocking and straps.
Line 6 at Line 1 starts out with a force of 0. Between Lines 1 and 2, the force increases at a rate of 467 – 29 = 438 plf to 657 pounds. Between Lines 2 and 3, the unit shear direction reverses and the force decreases by 438 plf x 4 ft = 1752 pounds, with a resulting force of 1095 pounds. There are commonly two or three studs supporting the header at window and door openings, so the capacity of chord members is generally not an issue. Edge nailing of the sheathing does need to be provided to these chord members over the full height of Lines 6 and 7.

## Slide 110: Force Transfer Shear Wall Design Example, cont.
4
3
2
1
5
6
A
B
C
438 plf
29 plf
29 plf
3,500 lb
7
8
E
H
G
F
D
438 plf
467 plf
29 plf
29 plf
467 plf
Studs, straps and blocking on lines 2, 3, 6 and 7 act as boundary members. Provide edge nailing for the full length of these lines.
Boundary Members and Fastening for Shear Wall Designed with Continuity Around Openings
Design for Overturning and Uplift, cont.
Notes: Say
Studs, straps and blocking on lines 2, 3, 6 and 7 act as boundary members. Provide edge nailing for the full length of these lines.
Window studs and blocking are being designed for the same nailing that we would normally put on the edge of our shear walls.

## Slide 111: Force Transfer Shear Wall Design Example, cont.
Design for Overturning and Uplift, cont.
Boundary Members and Fastening for Shear Wall Designed with Continuity Around Openings
Double studs or posts serve as shear wall chords (vertical boundary members) carrying tension and compression T=C=1,867 lb edge nailing sheathing for full height of studs or posts
Double top plates serve as collector
C
T
Notes: Say
Similar boundary or chord member forces can be calculated along Lines 2 and 3 using the same approach. Because no continuous framing exists along Lines 2 and 3, it is common to provide continuous straps to carry tension loads and continuous blocking to carry compression loads. Edge nailing of the sheathing is required over the full length of these lines also. Nailing through the steel strap into the sheathing and framing is often used to meet the edge nailing requirement.
It should be noted that the dead load resistance to overturning is not considered in this shear wall design method. When designing for force transfer around openings, additional checks will need to be made for adequate load paths for gravity loads using ASD or LRFD load combinations.

## Slide 112: Summary of Three Methods
 | Segmented | Perforated | FTAO Deikmann
v (max) | 438 plf | 547 plf | 467 plf
Fastening & WSP Sheathing | 8d @ 4” oc 3/8” thick | 8d @ 3” oc 3/8” thick | 8d @ 4” oc 7/16” thick
Chord T/C | 3,898 lb | 4,375 lb | 1,867 lb
Additional Requirements | Holdown each end of each segment | Holdown each end t=v for sill anchorage | Holdown each end Straps / blocking
Edge Fastening Requirements | Nailing around each segment | Nailing around full wall line | Nailing around full wall line and continuing past all boundary members
Notes: Do
Review the summary of the three design methods.

## Slide 113: Lesson Four Complete
Now that you’ve completed this lesson, you should be able to:
Describe how to design segmented, perforated and force transfer wood shear walls using the SDPWS

## Slide 114
Pre-Fabricated Shear Walls
After completing this lesson, you will be able to:
Identify which applications may require a pre-fabricated shear wall
L
5

## Slide 115: Site-Built vs. Pre-Fabricated
Site-Built Shear Walls
Most common lateral resisting system for light-framed structures
Usually the most economical solution
Pre-Fabricated Shear Walls
Allow for more openings in a structure
Help streamline quality, consistency and performance
Reduce design and labor time
Notes: Say
Site-built shear walls are the most commonly used lateral resisting system for light-framed structures.
They are typically used because engineers try to pick the most economical system, balanced with the most optimal performance for the building.
The introduction of pre-fabricated shear walls came about as more openings and larger openings decreased the available wall space for lateral resisting systems. There narrow wall segments frequently make it impossible to meet code prescribed aspect ratio limitations. Pre-fabricated shear walls help streamline the quality, consistency and performance of shear walls in the field.
Quiz Note
This slide features information that will be found on the post-course knowledge assessment.
Which of the following is not true about pre-fabricated shear walls:
Usually the most economical solution
Allow for more openings in a structure
Help streamline quality, consistency and performance
Reduce design and labor time

## Slide 116: Site-Built – Pros and Cons
Uses typical framing materials
Simple to modify load capacity by adjusting the nail pattern and sheathing thickness
Usually most cost-effective solution
Use up to six stories
3.5:1 maximum aspect ratio
Calculations can be tedious and time-consuming without software
Variation in construction quality may lead to inconsistent performance
Site-Built Shear Walls
Pros
Cons
Notes: Say
Site-built is generally the way to go as designers look for simplicity while keeping costs in mind.
Do
Review the pros and cons of site-built shear walls listed on the slide.

## Slide 117: Pre-Fabricated – Pros and Cons
Reduces design and labor time
Fully tested
Validated performance
Hardware is pre-attached
Predesigned anchorage solutions and templates available
Overall cost is higher for most applications
Limited to two story stacked applications
Pre-Fabricated Shear Walls
Pros
Cons
Notes: Say
If a site-built design is too costly or complex, or cant meet aspect ratio requirements, then pre-fabricated shear wall is needed. There is additional labor and there are inspections required for shear walls that have sheathing on both sides. In those situations, pre-fabricated may be a better solution.
Some manufacturers of pre-fabricated shear walls offer the following benefits:
Prefabricated: The wall panel comes with the sheathing and holdowns pre-attached. Additional installation hardware is included.
Easy To Install: Reusable templates locate the required holdown and mudsill anchor bolts accurately in the foundation. The walls are then placed over the anchor bolts followed by a simple top and bottom plate attachment.
Installation Guide: Detailed instructions attached to every wall.
State-of-the-Art Testing: Third-party documentation of cyclic testing verifies high design loads.
Quality Assurance: Quality-controlled manufacturing reduces inspection problems commonly faced with site-built shear walls.
Support and Service: Easy to access engineering technical support and experienced field representation to assist you.
Do
Review the pros and cons of pre-fabricated shear walls listed on the slide.

## Slide 118: When To Use Pre-Fabricated Shear Walls
When you need sheathing and holdowns pre-attached
When your structure contains multiple large openings
When increased productivity is necessary to finish the job on time
When a client specifies a code-listed ready-made shear wall that confirms to ICC-ES Acceptance Criteria
Notes: Say
Here are some situations where it may be beneficial to use a pre-fabricated shear wall over a site-built shear wall.
When you need sheathing and holdowns pre-attached: Some manufacturers offer wood shear walls with the sheathing and holdowns pre-attached, while including additional installation hardware. This reduces labor costs and increases consistency of shear wall installation.
When increased productivity is necessary to finish the job on time: Fewer anchor bolts and fasteners coupled with easy access to the top and bottom of the wall result in more efficient installation. Pre-fabricated shear walls from some manufacturers have available reusable templates to locate the required holdown and mudsill anchor bolts accurately in the foundation.
When your structure contains multiple large openings: Steel shear walls can have load values two to three times higher than wood shear walls, allowing for more windows, doors and other large openings in a building while still maintaining its structural integrity.
When a client specifies a code-listed ready-made shear wall that confirms to ICC-ES Acceptance Criteria: Some manufacturers offer pre-fabricated shear walls that are code-listed to the latest edition of the IBC and IRC, and conform to ICC-ES Acceptance Criteria. Some offer included bearing-stress calculations in the load tables of the code report for concrete foundations, providing a complete solution.

## Slide 119: Lesson Five Complete
Now that you’ve completed this lesson, you should be able to:
Identify which applications may require a pre-fabricated shear wall

## Slide 120: Course Summary
Shear walls resist the effects of lateral load acting on the structure and are typically used in wood buildings as the lateral force-resisting system. Shear walls are most commonly designed to carry wind and seismic loads.
Structures require lateral-force-resisting systems in order to resist racking, sliding and overturning caused by wind or seismic forces.
There are several considerations to keep in mind when designing a shear wall, including: Design method, shear panel proportions, sheathing type / thickness, fastener size / spacing, anchorage requirements, chord design, capacity adjustments.
L
1
Mechanics of a Shear Wall
Notes: Do
Review the course summary of Lesson 1.

## Slide 121: Course Summary
Factoring nominal unit shear capacities to ASD or LRFD levels is covered in Section 4.3.3. To convert the capacity to ASD, divide the nominal amount by 2. To convert the capacity to LRFD, multiply the nominal amount by 0.8.
Tabulated nominal unit shear capacities for seismic and wind design can be found in Tables 4.3A, 4.3B, 4.3C and 4.3D.
Elements and connections attached to the shear wall must be able to support its movement. If a shear wall deflects an inch, its connections will also need to be able to travel the same distance without breaking the system. Section 4.3.1 defines permissible deflection as the deflection that permits the shear wall and any attached elements to maintain their structural integrity and continue to support their prescribed loads.
SDPWS Section 4.3.6.4.3 states that foundation anchor bolts shall have a steel plate washer under each nut not less than 0.229"x3"x3" in size. This plate washer is no longer limited to seismic regions. Without a washer, the sill plate can split from a brittle failure, causing most of the structural capacity to be lost.
L
2
Code and Standard Provisions
Notes: Do
Review the course summary of Lesson 2.

## Slide 122: Course Summary
In 2015 SDPWS, both wind and seismic governed designs will need to consider adjustment factors for shear wall aspect ratios greater than 2:1. Reduction factors for high aspect ratio shear walls are no longer contained in the footnotes to Table 4.3.4. Instead, these factors are included in new provisions accounting for the reduced strength and stiffness of high aspect ratio shear walls.
There are two types of adjustment factors in the 2015 SDPWS for shear walls that exceed aspect ratio limitations. The Equal Deflection Calculation allows the designer to distribute shear by stiffness by reducing unit shear capacity for high aspect ratio shear walls. A second (now alternative) method is the 2bs/h Adjustment Factor. It allows the designer to distribute shear by strength by accounting for stiffness compatibility.
The Equal Deflection Calculation method can produce both more and less efficient designs that may result from the 2bs/h factor method depending on the relative stiffness of shear walls in the wall line. For example, design unit shear for shear wall lines comprised entirely of 3.5:1 aspect ratio shear walls can be as much as 40% greater than prior editions.
L
3
Aspect Ratio Capacity Reduction Adjustments
Notes: Do
Review the course summary of Lesson 3.

## Slide 123: Course Summary
In segmented shear wall design, the segment is the portion of the shear wall that runs from the diaphragm above to the floor diaphragm or foundation below. In walls with openings, only the full-height segments may be used to transfer shear from the diaphragm above to the diaphragm below. The segmented shear wall design method assumes each shear wall is a cantilevered element fixed at the base and free to deflect in-plane at the top.
Perforated shear walls allow a fully-sheathed wall with door and window openings to be treated as a single wall with slightly lower shear capacity. All portions of the wall are assumed to contribute to the lateral load-carrying capacity. The concept of a perforated shear wall is that it relies on the inherent continuity provided by typical construction. Each full-height segment has a different degree of restraint for overturning forces and has a varying capacity.
The force-transfer method allows for the design of a shear wall with a large opening while maintaining a high shear capacity by transferring shear around the opening. This is usually the site-built shear wall design method of last resort before having to use a pre-fabricated shear wall. Designers may choose this method due to lack of available shear wall length and/or openings in critical locations, or possible just an attempt to reduce the number of holdowns.
L
4
Shear Wall Design Methods
Notes: Do
Review the course summary of Lesson 4.

## Slide 124: Course Summary
The introduction of pre-fabricated shear walls came about as more openings or larger openings decreased the available wall space for lateral resisting systems. These narrow wall segments make it impossible to meet code prescribed aspect ratio limitations. Pre-fabricated shear walls help streamline the quality, consistency and performance of shear walls in the field.
Some of the benefits of pre-fabricated shear walls include: They reduce design and labor time, they're fully tested, performance is validated through cyclic testing, hardware is pre-attached, and templates are included for anchorage bolts.
Situations where it may be beneficial to use a pre-fabricated shear wall over a site-built shear wall include: When you need sheathing and holdowns pre-attached; When increased productivity is necessary to finish the job on time; When your structure contains multiple large openings; When a client specifies a code-listed ready-made shear wall that confirms to ICC-ES Acceptance Criteria
L
5
Pre-Fabricated Shear Walls
Notes: Do
Review the course summary of Lesson 5.

## Slide 125: Course Completion
Any Questions?

## Slide 126: Course Completion
Simpson Strong-Tie
This concludes the continuing education course.
For a library of Simpson Strong-Tie courses,
visit strongtie.com/workshops
Notes: Do
Draw the meeting to a close. Hand out literature and business cards.
Say
If you have ongoing projects that you would be interested in reviewing together, please let me know.

## Slide 127: Next Steps!
AIA: For those seeking AIA LU/HSW: You will receive an email with a link allowing access to print your Certificate. Congratulations, you will have earned 2 LU/HSW credits. If your AIA member number has been inserted into your profile, Simpson Strong-Tie will report your credits on your behalf to the AIA. No test is required in order to receive HSW credits.
IACET: For those seeking IACET CEUs: You will receive an email with a link allowing access to print your Certificate of Attendance and instructions directing you to the Simpson Student Center to take the exam before credits can be awarded. Once the exam is taken and passed, you will have earned 0.2 CEUs (2 hours of credit). You can then access your Certificate of Completion from the Course Content tab. You must self-report your credits to your certifying organization or agency.
If you have questions or need assistance, please contact training@strongtie.com.
Notes: Presenter Notes:
Review the email and notification process as outlined in this slide.
AIA LUs:
For those that want AIA HSW credit, be sure to provide your AIA number on the sign-in sheet and Simpson will report your credits to the AIA on your behalf.
No test is required for AIA credit.
CEUs:
For those seeking CEUs, watch for an email with instructions to access the online test. After you have passed the test, you may access your Certification of Completion from the course content tab.
You must self-report your credits to your certifying organization or agency.

## Slide 128: Next Steps!
ICC: For those seeking ICC CEUs: You will receive an email with a link allowing access to print your Certificate. Congratulations, you will have earned 0.2 ICC CEU (2 hours of credit). Please make sure your ICC member number has been inserted into your profile. It is your responsibility to self-report your credits to the ICC. Please retain your Completion Certificate for your records.
IACET: For those seeking IACET CEUs: You will receive an email with a link allowing access to print your Certificate of Attendance and instructions directing you to the Simpson Student Center to take the exam before credits can be awarded. Once the exam is taken and passed, you will have earned 0.2 CEUs (2 hours of credit). You can then access your Certificate of Completion from the Course Content tab. You must self-report your credits to your certifying organization or agency.
If you have questions or need assistance, please contact training@strongtie.com.
Notes: Presenter Notes:
Review the email and notification process as outlined in this slide.
Watch for an email directing you to the Student Center to print your certificate.
No test is required for ICC credit. You must self-report your credits to ICC.
For those seeking general IACET CEUs after you have passed the online test, you may access your Certification of Completion from the course content tab. You must self-report your credits to your certifying organization or agency.