## Slide 1
PLEASE READ
Dear Instructor,
This presentation is available in both AIA and ICC versions.
For AIA: Right click and un-hide slides 5 and 177
For ICC: Right click and un-hide slides 6 and 178
Slide 2 is an optional slide

## Slide 2: Welcome!
We will begin in a few minutes.
Please be sure to sign the registration form to receive credit for attending today’s learning event.

## Slide 3
Instructor Name
Title/Role
AIA Provider:
50119826
AIA Course:
AIA-WSD10316

## Slide 4: Credit Information
IACET Accreditation Information
Simpson Strong-Tie® has been accredited as an Authorized Provider by the International Association for Continuing Education and Training (IACET). As a result of their Authorized Provider accreditation status, Simpson Strong-Tie® is authorized to offer IACET CEUs for its programs that qualify under the ANSI/IACET Standard.
This course offers 0.3 CEU (3 hours of credit).
Notes: Review the submission process for audiences requiring IACET CEU credits.
For those seeking IACET credit, they must take and pass the online test. They must self-report CEU credits to their certifying organization or agency.
Explain the credits awarded: IACET: 0.3 (Equivalent to 3 hours) CEUs.

## Slide 5: Credit Information
AIA Member Information
This course is registered with AIA CES for continuing professional education. As such, it does not include content that may be deemed or construed to be an approval or endorsement by the AIA of any material of construction or any method or manner of handling, using, distributing, or dealing in any material or product. Upon completion of this course, Credit(s) earned will be reported to AIA CES for AIA members who pass the course and have entered their AIA member number on their Simpson profile page. A link to the Certificate of Completion will be available upon completion of this course. Only AIA LU/HSW will be reported.
This course offers 3 LU/HSW credits.
AIA Course Number: AIA-WSD10316
Notes: Presenter Information
NOTE: Please be sure each attendee LEGIBLY signs the event sign-in sheet.
Say
All questions concerning proprietary products will be addressed after the conclusion of the AIA portion of the presentation. The meeting format is 170 minutes of content, followed by 10 minutes of Q & A.
Do
Explain the credits awarded for:
AIA: 1LU/HSW credit.
IACET: 0.3 (Equivalent to 3 hours) CEU credits.
Review the submission process for audiences requiring either AIA LU/HSW (health, safety and welfare) credits or CEU credits:
For those seeking AIA HSW credit, there is no test required. AIA members must be sure to provide their AIA member number on the sign-in sheet. Please make sure name, email and AIA member number are clearly printed so Simpson can report credits to the AIA on their behalf.
For those seeking IACET credit, they must take and pass the test. They must self-report CEU credits to their certifying organization or agency.

## Slide 6: Credit Information, cont.
ICC Member Information
This course has been approved by the International Code Council (ICC) for continuing professional education. For learners that complete this course, it is your responsibility to self-report your credits to the ICC. Please retain your Completion Certificate for your records.
Be sure that your ICC ID number is provided on the sign-in sheet or in your Simpson profile in order to have it displayed on your certificate.
This course offers 0.3 CEU (3 hours of credit).
ICC Course Number: 8890
Notes: Review the submission process for audiences requiring ICC CEU credits.
For those seeking ICC credit, there is no test required. ICC members must provide their ICC ID number on the sign-in sheet or in their Simpson profile in order to have it displayed on their certificate. It is the responsibility of the participant to self-report their credits to the ICC. Ask them to retain their Completion Certificate for their records.
Explain the credits awarded: ICC: 0.3 (Equivalent to 3 hours) CEUs.

## Slide 7: Additional Credit Offerings
Visit
strongtie.com/workshops
for more information
Course Name | CEUs | AIA | ICC
Introduction to Deck Design | 0.1 | ✔ | ✔
Introduction to Wind Design and the Wood Frame Construction Manual | 0.1 | ✔ | ✔
Shear Walls and Lateral Bracing in Light Frame Construction | 0.1 | ✔ | ✔
Understanding Restraint Rod Systems | 0.1 | ✔ | ✔
Cracking the Concrete Anchor Codes | 0.1 | ✔ | ✔
Concrete Deterioration | 0.1 | ✔ | ✔
Moment Frame Design | 0.1 | ✔ | ✔
Introduction to Wind Code Provisions and Meteorological Concepts | 0.1 | ✔ | ✔
Wind Design in Accordance with ASCE 7-10 | 0.1 | ✔ | ✔
Wood Framed Seismic Design 1: Code Provisions, Design Parameters | 0.1 | ✔ | ✔
Notes: Do
Explain that we have additional PK topics available that offer credit for ICC members and HSW credits for AIA members.
Explain that we have a library of online courses available in our Simpson Student Center that also offer ICC and AIA HSW credits. They can access our online courses at strongtie.com/workshops.

## Slide 8: Course Description
This is a three-hour instructor-led course intended for structural engineers and architects interested in seismic design for wood-framed construction. Course topics include 2015 IBC code provisions, ASCE 7-10 code provisions, seismic design parameters, structural irregularities, design base shear, distribution of seismic forces, diaphragm design, shear wall shear design, shear wall overturning design, and drift analysis.
Throughout the course, we will simultaneously discuss a building design example as an aid for the understanding and interpretation of the learning objectives.
Course Contents
Part One: Code Provisions, Seismic Design Parameters & Structural Irregularities
Part Two: Design Base Shear, Distribution of Seismic Forces & Diaphragm Design
Part Three: Shear Wall Shear Design, Shear Wall Overturning Design & Drift Analysis
Notes: Do
Review the course description and course contents.

## Slide 9: Learning Objectives (Part One)
Upon completion of this seminar, you will be able to:
Summarize code provisions relating to seismic design in ASCE 7-10 and 2015 IBC
Explain and discuss the importance of site classifications, seismic design parameters, and seismic design categories
Use USGS Seismic Design Mapping online tool to determine seismic design parameters and seismic design category
Evaluate and explain structural irregularities as they relate to seismic design for wood framed construction
Notes: Do
Review the learning objectives for the course.
Inform students that the assessment questions will be based on these learning objectives. Slides that may contain information relevant to the test have an orange graduation cap located in the bottom-left corner.

## Slide 10: Learning Objectives (Part Two)
Upon completion of this seminar, you will be able to:
Evaluate and explain structural design base shear for use in the equivalent lateral force procedure
Calculate and confirm the seismic response coefficient for use in the seismic base shear equation
Explain the distribution of seismic forces for use in the equivalent lateral force procedure
Summarize how to design diaphragms for wood framed construction to resist seismic forces
Notes: Do
Review the learning objectives for the course.
Inform students that the assessment questions will be based on these learning objectives. Slides that may contain information relevant to the test have an orange graduation cap located in the bottom-left corner.

## Slide 11: Learning Objectives (Part Three)
Upon completion of this seminar, you will be able to:
Identify and compare the three methods for wood shear wall design
Analyze and explain the proper methods for shear wall nailing design and for the floor to floor transfer of shear
Explain how to design structures to resist overturning forces
Summarize methods to calculate and resist seismic story drift
Notes: Do
Review the learning objectives for the course.
Inform students that the assessment questions will be based on these learning objectives. Slides that may contain information relevant to the test have an orange graduation cap located in the bottom-left corner.

## Slide 12
Design Example Preface
Notes: Do
Direct students to their Design Example handout. They should reference this paper when slides are presented discussing the design example.

## Slide 13: Purpose & Structure Information
Purpose
Design the end-walls along gridlines 1 and 5 for seismic structural forces using the 2015 IBC allowable stress seismic provisions (based on ASCE/SEI 7-10)
Structure Information
3-story multi-family structure (Risk Category II)
Located in Sacramento, CA (38.634, -121.293)
Stiff Soil (Site Class D)
Entire building uses wood framing (studs and plate members are DF No. 1 or No. 2)
Roof trusses span the entire width
Conditions meet the parameters described in ASCE 7-10 Section 12.3.1, therefore a Flexible Diaphragm assumption is allowed
DESIGN EXAMPLE SLIDE
Notes: Say
The purpose of including a design example is to help with the understanding and interpretation of the learning objectives. By applying the course material to a real-life scenario, we hope to improve your confidence when it comes to implementing these lessons in the field.
By the end of this course, we’ll have designed the end-walls along gridlines 1 and 5 for seismic structural forces using the 2015 IBC allowable stress seismic provisions based on ASCE 7-10.
Our example building is a 3-story multi-family structure in Risk Category II. It is located Sacramento, CA just north of the American river, between highways 50 and 80. For simplicity, we’ll assume the site has stiff soil and is in Site Class D. IBC 1613.3.2 states that “where the soil properties are not known in sufficient detail to determine site class, Site Class D shall be used unless the building official or geotech data determines Site Class E or F soils are present.”
The entire building uses wood framing and roof trusses span the entire width.
Our design example meets all parameters described in Condition C of ASCE 7-10 Section 12.3.1.1, therefore a flexible diaphragm assumption is allowed. Conditions met: (1) Our structure does not have concrete or similar materials placed over wood structural panel diaphragms, and (2) each line of vertical elements of the seismic force-resisting system complies with the allowable story drift of Table 12.12-1.
Slides that contain calculations or information regarding our design example will have indicating text shown on the bottom-right-hand corner.

## Slide 14: Building Plan
Eight units on each level
Overall dimensions of 105’-4” x 65’-0”; Roof has 1’-0” overhang
Roof framing spans in the N-S direction
Symmetrical in both directions
DESIGN EXAMPLE SLIDE
N (REF)
Notes: Say
There are eight units on each level. The overall plan dimensions are 105’-4” by 65’-0”.
Roof framing spans in the north-south direction. The building plan is symmetrical in both directions (east to west at gridline 3; north to south between gridlines B and C).

## Slide 15: Building Site Elevation
Building repeats the floor plan at each level
Illustration shows the side of the high pitched gable roof
DESIGN EXAMPLE SLIDE
Notes: Say
The building repeats the same floor pattern on each of the three levels. This illustration shows the side of the high pitched gable roof.

## Slide 16: Building End Elevation
Gable Roof has 6:12 pitch
All floors have an 8’ plate height with floor depths of 16”
Median roof height equals 35’-4”
Ridge height equals approximately 44’
DESIGN EXAMPLE SLIDE
Notes: Say
The gable roof has a 6:12 pitch and all floors have an 8’ plate height with floor depths of 16”. The median roof height equals 35’-4” while the ridge height equals approximately 44’.

## Slide 17: Part One Contents
LESSON 1
2015 IBC and ASCE 7-10 Code Provisions
Summarize code provisions relating to seismic design in ASCE 7-10 and 2015 IBC
LESSON 2
Finding Seismic Design Parameters
Explain and discuss the importance of site classifications, seismic design parameters, and seismic design categories
LESSON 3
Structural Irregularities
Evaluate and explain structural irregularities as they relate to seismic design for wood framed construction
Notes: Do
Review the slide.

## Slide 18
Part 1 Lesson 1: 2015 IBC & ASCE 7-10 Code Provisions
After completing this lesson, you will be able to:
Summarize code provisions relating to seismic design in ASCE 7-10 and 2015 IBC

## Slide 19: Referencing IBC vs. ASCE 7
2015 IBC
Most seismic sections refer to ASCE Chapters 11-22
IBC notes amendments to the ASCE 7-10
ASCE 7-10
Contains majority of information for seismic design
Always reference 2015 IBC first, then check ASCE 7-10 if needed
Notes: Say
In the 2015IBC, most seismic sections still refer to ASCE 7-10 (Chapters 11-22) but now the IBC notes amendments to the ASCE 7-10.
The current ASCE 7-2010 reference standard has most of the information required for the seismic design and analysis. However, always reference the 2015 IBC first (before ASCE 7-10).

## Slide 20: Layout of IBC vs. ASCE 7
2015 IBC Section
1613: Earthquake Loads
  1613.1: Scope
  1613.2: Definitions
  1613.3: Seismic Ground Motion Values
  1613.4: Alternatives to ASCE 7
  1613.5: Amendments to ASCE 7
  1613.6 Ballasted photovoltaic panel systems
ASCE 7-10 Section
11: Seismic Design Criteria
12: Seismic Design Requirements
13: Nonstructural Components
14: Material Specific Requirements
15: Non-Building Structures
16: Seismic Response History
17: Structurally Isolated Structures
18: Damping Systems
19: Soil-Structure Interaction
20: Site Classification
21: Site Specific Procedures
22: Long-Period Transition & Risk Coefficient Maps
Notes: Say
ASCE 7-10 contains much more seismic information and design requirements. However, it is essential to first check the IBC as the ICC may have made modifications to ASCE 7-10. All “Earthquake Loads” material in the 2015 IBC can be found in Section 1613. In ASCE 7-10, seismic material is located in Chapters 11 to 22.

## Slide 21: What’s New in 2015 IBC
Seismic Changes in 2015 IBC
Flexible and Rigid diaphragm definitions were deleted and replaced by procedure as outlined in ASCE 7-10.
Definition of Risk Category III was updated. This is different from ASCE. IBC will govern.
Provisions for Ballasted Photovoltaic panel system was added.
Amendment to ASCE 7 related to diaphragm anchorage requirements was added.

## Slide 22: Scope of Seismic Analysis
2015 IBC 1613.1
2015 IBC 1604.10
“Lateral-force-resisting systems shall meet seismic detailing requirements and limitations prescribed in this code and ASCE 7, excluding Ch. 14 and Appendix 11A, even when wind code prescribed load effects are greater than seismic load effects.”
“Every structure […] shall be designed and constructed to resist the effects of earthquake motions in accordance with ASCE 7, excluding Ch. 14 and Appendix A. The seismic design category for a structure is permitted to be determined in accordance with Section 1613 or ASCE 7”
Notes: Say
The following section quotations explain what structures must be subject to seismic analysis.
Section 1613.1 of the 2015 IBC states that every structure shall be designed and constructed to resist the effects of earthquake motions in accordance with ASCE 7.
Section 1604.10 states that lateral-force-resisting systems shall meet seismic detailing requirements and limitations prescribed in this code and ASCE 7 – even when wind code prescribed load effects are greater than seismic load effects.
The extent of the design is based on the Seismic Design Category, the use of the structure, and the configuration of the structure (irregularities).

## Slide 23: Exceptions
Detached One- and Two-Family Dwellings in Seismic Design Categories A, B, and C
Detached One- and Two-Family Dwellings where the Short Period Spectral Response Acceleration, SS, is < 0.4 g
Wood frame buildings built per Conventional Wood Framing requirements in IBC Section 2308
Agriculture storage buildings
Structures that require special consideration of their environment and response characteristics
Structures which other regulations provide seismic criteria
Structures that do not follow the 2015 IBC and ASCE 7-10 seismic provisions:
Notes: Say
Every structure shall be designed to resist earthquakes with a few exceptions, including:
- Detached one- and two-family dwellings in Seismic Design Categories A, B, and C
- Detached one- and two-family dwellings where the Short Period Spectral Response Acceleration, SS, is less than 0.4 g
- Wood frame buildings built per Conventional Wood Framing requirements in IBC Section 2308
- Agriculture storage buildings
- Structures that require special consideration of their environment and response characteristics, which are not addressed by the IBC or ASCE 7
- Structures which other regulations provide seismic criteria

## Slide 24
Now that you’ve completed this lesson, you should be able to:
Summarize code provisions relating to seismic design in ASCE 7-10 and 2015 IBC

## Slide 25
Part 1 Lesson 2: Finding Seismic Design Parameters
After completing this lesson, you will be able to:
Explain and discuss the importance of site classifications, seismic design parameters, and seismic design categories
Use USGS Seismic Design Mapping online tool to determine seismic design parameters and seismic design category

## Slide 26: Seismic Design Category
The Seismic Design Category reveals many aspects of design, including:
Permissible structural system
Limitations on height and irregularity
Components of the structure that must be designed for seismic forces
Types of lateral force analysis that may be used
Structural material detailing
Special inspection requirements
Structural observation requirements
Notes: Say
Seismic design parameters are necessary to determine the Seismic Design Category. The SDC is a classification assigned to a structure based on its Risk Category and the severity of the design earthquake ground motion.
The Seismic Design Category reveals many aspects of design, including:
Permissible structural system
Limitations on height and irregularity
Components of the structure that must be designed for seismic forces
Types of lateral force analysis that may be used
Structural material detailing
Special inspection requirements
Structural observation requirements
Presenter Note
This slide features information that will be found on the post-training knowledge assessment:
What aspects of design can be revealed by knowing the Seismic Design Category?
Permissible structural system
Limitations on height and irregularity
Types of lateral force analysis that may be used
Special inspection requirements
All of the above

## Slide 27: Determining the Seismic Design Category
Mapped Acceleration Parameters (SS & S1)
Site Class (A, B, C, D, E or F)
Site Coefficients (Fa & FV)
Site Adjusted Spectral Response Acceleration (SMS & SM1)
Design Spectral Response Acceleration (SDS & SD1)
Risk Category (I, II ,III or IV)
PARAMETERS
❶
❷
❸
❹
❺
❻
Parameters for Determining SDC
Seismic Design Category
Notes: Say
To determine the Seismic Design Category, the designer must know the location of the structure, the site soil information, and know how to refer to the code maps and tables (or be able to use the USGS Seismic Design Parameters web app). These elements allow the designer to find the relevant parameters needed to determine the SDC.
The first step is to use seismic ground maps to find the Mapped Acceleration Parameters (SS and S1) based on the structure’s location.
Second, determine the Site Class based on its location and soil engineering properties.
Third, use the information from the Mapped Acceleration Parameters and Site Class to determine the Site Coefficients (Fa and FV).
Fourth, using the Mapped Acceleration Parameters and the Site Coefficients, determine the Site Adjusted Spectral Response Acceleration parameters (SMS and SM1).
The fifth step is to use the Site Adjusted Spectral Response Acceleration parameters in a simple equation to find the Design Spectral Response Acceleration parameters (SDS and SD1).
Sixth, determine the Risk Category of the structure based on how essential the building is to society.
Finally, after determining all relevant parameters, the designer is able to determine the Seismic Design Category by using a table that takes into consideration the Design Spectral Response Parameters and the building’s Risk Category.
In this lesson, we’ll briefly review how to find each of these parameters by referencing ASCE 7-10, 2015 IBC, and our design example.

## Slide 28: Mapped Acceleration Parameter (Short Period)
SS: Mapped MCER, 5 percent damped, spectral response acceleration parameter at short periods (0.2 second)
53% of g for Sacramento
DESIGN EXAMPLE SLIDE
Notes: Say
The Spectral Response Acceleration for Short Periods, SS, can be found using seismic ground motion maps.
In the 2012 IBC, the seismic ground motion maps have been updated to match ASCE 7-10. The titles of the maps in IBC were revised from “Maximum Considered Earthquake Ground Motion” to “Risk-Targeted Maximum Considered Earthquake (MCER) Ground Motion Response Accelerations” in order to reflect the titles in 2009 NEHRP and ASCE 7-10.
Our design example is located in Sacramento, just north of the American River between highways 50 and 80. Using the seismic ground motion maps, we find an SS of roughly 53% of g (gravitational acceleration).
Some of these maps can be difficult to read. After we locate our values using the traditional way, we’ll try another solution using the web app available from USGS.gov.

## Slide 29: Mapped Acceleration Parameter (1 Second Period)
S1: Mapped MCER, 5 percent damped, spectral response acceleration parameter at a period of 1 second
25% of g for Sacramento
DESIGN EXAMPLE SLIDE
Notes: Say
The Spectral Response Acceleration for 1 Second Periods, S1, is similarly found using the seismic ground motion maps. For our Sacramento design example, S1 is approximately 25% of g (gravitational acceleration).

## Slide 30: Site Class
Based on site soil properties
Classified as Site Class A, B, C, D, E, or F
If soil properties not known, Site Class D shall be used
Site Class D for our Design Example
DESIGN EXAMPLE SLIDE
Notes: Say
The Site Class is a classification assigned to a site based on the types of soils present and their engineering properties. Table 20.3-1 in ASCE 7-10 provides a breakdown of the different types.
Ask
How would you determine the Site Class if you do not know the soil’s engineering properties?
Say
Where the soil properties are not known in sufficient detail to determine the Site Class, Site Class D shall be used unless the authority having jurisdiction or geotechnical data determines Site Class E or F soil are present at the site. If you’re still not sure, hire a geotechnical engineer to obtain a soils report for the site.
Per ASCE 7-10 Section 11.8.2, a “geotechnical investigation is required for structures assigned a seismic design category C, D, E, or F.” If the structure ends up being a design category C or higher, a geotech report is required. However, per the “EXCEPTION”, actual field borings may not be required if prior evaluations of nearby sites exist, when approved by the building department.
For the design example in this presentation, we will assume Site Class D for simplicity. Also, per IBC 1613.3.2, “where the soil properties are not known in sufficient detail to determine the site class, Site Class D shall be used unless the building official or geotech data determines Site Class E or F soils are present.” This is repeated in ASCE 7-10 Section 20.1.
Presenter Note
This slide features information that will be found on the post-training knowledge assessment:
Per IBC 2012 Section 1613.5.2 (Exception): If soil properties are not known in sufficient detail, then Site Class ____ shall be used unless the building official or geotechnical data determines a higher Site Class soil is likely present at the site.
Site Class A
Site Class B
Site Class C
Site Class D

## Slide 31: Site Coefficient (Short Period)
Fa: Short period site coefficient (at 0.2 second period)
Found using IBC 2015 Table 1613.3.3(1)
  Fa interpolated to 1.3
Site Class | Mapped Spectral Response Acceleration at Short Periods |  |  |  | 
 | SS>0.25 | SS=0.50 | SS=0.75 | SS=1.00 | SS>1.25
A | 0.8 | 0.8 | 0.8 | 0.8 | 0.8
B | 1.0 | 1.0 | 1.0 | 1.0 | 1.0
C | 1.2 | 1.2 | 1.1 | 1.0 | 1.0
D | 1.6 | 1.4 | 1.2 | 1.1 | 1.0
E | 2.5 | 1.7 | 1.2 | 0.9 | 0.9
F | Note b | Note b | Note b | Note b | Note b
DESIGN EXAMPLE SLIDE
Notes: Say
Once we’ve determined the Mapped Acceleration Parameter and the Site Class, we can find the Site Coefficients using IBC 2012 Table 1613.3.3(1).
Because our example structure is Site Class D and its Short Period Mapped Acceleration Parameter (SS) equals 0.53g, we find the Short Period Site Coefficient (Fa) to be approximately interpolated to 1.3.

## Slide 32: Site Coefficient (1 Second Period)
Site Class | Mapped Spectral Response Acceleration At 1 Sec. Period |  |  |  | 
 | S1>0.1 | S1=0.2 | S1=0.3 | S1=0.4 | S1>0.5
A | 0.8 | 0.8 | 0.8 | 0.8 | 0.8
B | 1.0 | 1.0 | 1.0 | 1.0 | 1.0
C | 1.7 | 1.6 | 1.5 | 1.4 | 1.3
D | 2.4 | 2.0 | 1.8 | 1.6 | 1.5
E | 3.5 | 3.2 | 2.8 | 2.4 | 2.4
F | Note b | Note b | Note b | Note b | Note b
FV: Short period site coefficient (at 0.2 second period)
Found using IBC 2015 Table 1613.3.3(1)
  FV interpolated to 1.9
DESIGN EXAMPLE SLIDE
Notes: Say
Finding the 1 Second Period Site Coefficient has the same process. Because our example structure is Site Class D and its 1 Second Period Mapped Acceleration Parameter (S1) equals 0.25g, we find the Short Period Site Coefficient (FV) to be approximately interpolated to 1.9.

## Slide 33: Site Adjusted Spectral Response Acceleration
Short period
(IBC Eq. 16-37)
(ASCE 7-10 Eq. 11.4-1)
1-second period
(IBC Eq. 16-38)
(ASCE 7-10 Eq. 11.4-2)
475
DESIGN EXAMPLE SLIDE
Notes: Say
Now that we’ve found the Site Coefficients (Fa and FV) and Mapped Acceleration Parameters (SS and S1), we can find determine the Site Adjusted Spectral Response Acceleration parameters (SMS and SM1) using equations found in IBC 16-37/38 and ASCE 7-10 11.4-1/2.
SMS and SM1 are the maximum considered earthquake response acceleration for short periods and 1-second periods.
Using these equations in our design example is easy. By plugging in our short period values, we find an SMS of 0.689. And by plugging in our 1 second values, we find an SM1 of 0.475.

## Slide 34: Design Spectral Response Acceleration
Short period
(IBC Eq. 16-39)
(ASCE 7-10 Eq. 11.4-3)
1-second period
(IBC Eq. 16-40)
(ASCE 7-10 Eq. 11.4-4)
316
DESIGN EXAMPLE SLIDE
Notes: Say
The five-percent damped design spectral response acceleration at short periods, SDS, and at 1-second period, SD1, can be derived using these simple equations provided in both the IBC and ASCE 7.
Back to our design example: By plugging in our SMS and SM1 values, we receive an SDS of 0.455 and an SD1 or 0.316.

## Slide 35: Risk Category
I
Low Hazard Structures
Barns, storages, gatehouses
II
Common Buildings
Most residential, commercial, industrial
III
Substantial Public Hazard
IV
Schools, prisons, small healthcare facilities
Hospitals, police stations, emergency centers
Essential for Recovery
DESIGN EXAMPLE SLIDE
Notes: Say
A rational basis should be used to determine the Risk Category for structural design, which is primarily based on the number of persons whose lives would be endangered or whose welfare would be affected in the event of failure. Four levels of risk are identified and structures are assigned to one of the categories according to the criteria listed in ASCE 7-10 Table 1.5-1. Classification reflects a progression of the anticipated seriousness of the consequence of failure from lowest risk to human life to highest.
Risk Category I contains low hazard structures, such as barns, storages, and gatehouses.
Risk Category III contains structures that pose substantial public hazard in the event of failure. This includes schools, prisons, and small healthcare facilities.
Buildings and structures in Risk Category IV are essential for recovery. This category is reserved for hospitals, police stations, emergency centers, and other similar facilities.
All other structures belong in Risk Category II, where you will find most residential, commercial, and industrial buildings.
For simplicity, the Sacramento building in our design example will fall into Risk Category II.

## Slide 36: Seismic Design Category
 | Risk Category | 
Value of SDS | I or II or III | IV
SDS < 0.167 | A | A
0.167 ≤ SDS < 0.33 | B | C
0.33 ≤ SDS < 0.50 | C | D
0.50 ≤ SDS | D | D
 | Risk Category | 
Value of SD1 | I or II or III | IV
SD1 < 0.067 | A | A
0.067 ≤ SD1 < 0.133 | B | C
0.133 ≤ SD1 < 0.20 | C | D
0.20 ≤ SD1 | D | D
Table 11.6-1 Seismic Design Category Based on
Short Period Response Acceleration Parameter
Table 11.6-2 Seismic Design Category Based on
1-S Period Response Acceleration Parameter
By assigning the most severe category to the structure, we receive Seismic Design Category D
DESIGN EXAMPLE SLIDE
Seismic Design Category of a structure is based on the Risk Category and Design Spectral Response Acceleration Parameters (SDS and SD1)
Notes: Say
Once you know your Risk Category, you can use tables in ASCE 7-10 or 2015 IBC to find the Seismic Design Category.
Use 2015 IBC Table 1613.3.5(1) or ASCE 7-10 Table 11.6-1 with SDS.
Use 2015 IBC Table 1613.3.5(2) or ASCE 7-10 Table 11.6-2 with SD1.
By matching our Risk Category to the value of SDS (0.455) and SD1 (0.316), we receive Seismic Design Category D for our example. It is important to remember that you must assign the most severe category you find based on both tables.
Here’s a breakdown of the assigned classifications:
Seismic Design Category A: Corresponds to buildings in areas where expected ground shaking will be minor. Good soils.
Seismic Design Category B: Corresponds to buildings of Risk Categories I, II, and III where expected ground shaking will be moderate. Stratified soils with good and poor soils.
Seismic Design Category C: Corresponds to buildings of Risk Category IV where expected ground shaking will be moderate; also corresponds to buildings of Risk Categories I, II, and III where more severe ground shaking will occur.
Seismic Design Category D: Corresponds to buildings and structures in areas expected to experience severe and destructive ground shaking but not located close to a major fault.
Seismic Design Category E: Corresponds to buildings of Risk Categories I, II, and III in areas near major active faults. Soil or rock is of no consequence.
Seismic Design Category F: Corresponds to buildings of Risk Category IV near major active faults. Soil or rock is of no consequence.
Presenter Note
This slide features information that will be found on the post-training knowledge assessment:
The Seismic Design Category of a structure is based on which two values?
Seismic Use Group and Importance Factor (Ie)
Soil Site Class and Site Coefficient (Fa & FV)
Risk Category and Design Spectral Response Acceleration Parameters (SDS & SD1)
Risk Category and Importance Factor (Ie)

## Slide 37: USGS Seismic Design Online Tool
Visit http://earthquake.usgs.gov/designmaps/us/application.php for access
DESIGN EXAMPLE SLIDE
Notes: <!-- This slide contains many click-enabled animations to help guide the class through the steps to use the USGS Seismic Design Tool. Please reference instructor notes below. -->
Say
But what if we can’t read those maps well enough to figure out our site’s S1 and SS parameters? Thankfully, USGS has an easy-to-use online solution.
Instead of using the maps in the code book to find the Seismic Design Parameters it is easier (not to mention, more exact) to use the USGS website.
Visit http://earthquake.usgs.gov/designmaps/us/application.php to access the application.
*1 CLICK MOUSE FOR ANIMATION – Shows “Design Code Reference Document”*
From here, select the Design Code Reference Document from the drop down list. For our example, select the ASCE 7-10.
*2 CLICK MOUSE FOR ANIMATION – Shows “Site Soil Classification”*
Next, we select the Site Soil Classification. Our design example is Class D.
*3 CLICK MOUSE FOR ANIMATION – Shows “Risk Category”*
There are only two choices when picking a Risk Category: essential facilities (IV) or everything else (I – III). Since our example is Risk Category II, we’ll choose the “I or II or III” option from the drop-down menu.
*4 CLICK MOUSE FOR ANIMATION – Shows “Site Latitude and Longitude”*
Finally, we’ll add the location of the building or structure using its latitude and longitude in decimal degrees. Our Sacramento design example is located at 38.634, -121.293. or you can use the map on the right side of the page to enter the address and the Site latitude and longitude will be automatically populated
*5 CLICK MOUSE FOR ANIMATION – Shows “Compute values”*
With our specified inputs, the USGS Seismic Design Tool returns a summarized list of our seismic parameters. The parameters that we obtained by hand are actually very close to the web app results! To view more details, including the Seismic Design Category, click the detailed report link in the top-right corner.
*6 CLICK MOUSE FOR ANIMATION – Shows “Design Maps Detailed Report”*
As shown on the report, the SS and S1 values are much more accurate compared to when we estimated them using a seismic ground map.
*7 CLICK MOUSE FOR ANIMATION – Scrolls down midway of “Design Maps Detailed Report”*
The online app is able to interpolate the Fa and FV values at a much higher degree of certainty than we are able to do by simply using a table. For instance, we found an Fa of 1.3 using the table, while the app gave us a more precise value of 1.375.
*8 CLICK MOUSE FOR ANIMATION – Scrolls down to the bottom of “Design Maps Detailed Report”*
At the bottom of the detailed report, the app shows the Seismic Design Category and how it reached that conclusion.
The Seismic Design Tool available from the USGS website has proven to be much more quick and accurate than obtaining results by hand.
Presenter Note
This slide features information that will be found on the post-training knowledge assessment:
Which organization’s website should you visit to find the seismic design parameters for the site of your project?
CNN
USGS
Farmer’s Almanac
Simpson Strong-Tie

## Slide 38: Analysis Types Allowed
For our Sacramento example, all three analytical procedures in this table are permitted
DESIGN EXAMPLE SLIDE
Notes: Say
Table 12.6-1 in ASCE 7-10 shows the permitted analytical procedures for structures based on the SDC and structural characteristics of the building. SDC A is not in the table and neither is the reference to the Index Force Analysis. This is because a structure with SDC A need only comply with Section 11.7 – which uses the Index Force Analysis. It is also important to note that the “Simplified Analysis Procedure” has been deleted from this table – it does exist, in ASCE 7-10 Section 12.14, but there are now more conditions that govern whether you may use this procedure. The table is basically the same as previous editions, but with references updated (and no more Seismic Use Group, but now Risk Category).
For our Sacramento design example, all three analytical procedures in this table are permitted.

## Slide 39
Now that you’ve completed this lesson, you should be able to:
Explain and discuss the importance of site classifications, seismic design parameters, and seismic design categories
Use USGS Seismic Design Mapping online tool to determine seismic design parameters and seismic design category

## Slide 40
Part 1 Lesson 3:
Structural Irregularities
After completing this lesson, you will be able to:
Evaluate and explain structural irregularities as they relate to seismic design for wood framed construction

## Slide 41: Experiences with Seismic Design
Overcoming problems in seismic design:
Break into groups of 2 or 3
Find out who drove the furthest distance to get here today
Within your group, take one minute per person to find out:
    What was the most problematic situation you’ve experienced in designing or building a structure with a horizontal or vertical irregularity?
    What was the problem you had to overcome?
    How did you overcome it?
Notes: Presenter’s Notes:
Audience Interaction: 5 minutes.
Say: “Before we begin our next lesson, I’d like to get some feedback on your most memorable moments when designing or building a structure with a horizontal or vertical irregularity.
So here’s what I’d like to do: Turn to your neighbors and break up into groups of __________ (2 or 3 depending on the size of the audience). Then take one minute per person and answer the following questions.
Who drove the furthest distance to get to the seminar today?
What was the most problematic situation you’ve experienced in designing or building a structure with a horizontal or vertical irregularity?
What was the problem you had to overcome?
How did you overcome it?
Pick one scenario from your group to discuss with the group.
The person who drove the furthest today will be the spokesperson.
Ok, raise your hand… Who has one they’d like to discuss?”
(Call on one or two groups and ask what the problem was and how they solved it)
When one shares their story, ask:
“Did anyone with a similar problem solve it a different way?”
Call on someone who responds and ask:
“How did you solve it?”
“Anyone else?”
Do: Keep an eye on the clock and end the discussion after a couple minutes.
Then say:
“It’s easy to see that seismic design can be challenging. Hopefully after today, you will be aware of some other options and some tools to assist in the process.”
Return to the presentation.

## Slide 42: Types of Irregularities
Type | Horizontal Structural Irregularities (ASCE 7-10 Table 12.3-1) | Vertical Structural Irregularities (ASCE 7-10 Table 12.3-2)
1a | Torsional Irregularity | Stiffness Irregularity – Soft Story
1b | Extreme Torsional Irregularity | Stiffness Irregularity – Extreme Soft Story
2 | Re-entrant Corners | Weight (Mass) Irregularity
3 | Diaphragm Discontinuity | Vertical Geometric Irregularity
4 | Out-of-plane Offsets | In-plane Discontinuity
5 | Nonparallel Systems | 5a: Discontinuity in Lateral Strength – Weak Story Irregularity 5b: Discontinuity in Lateral Strength – Extreme Weak Story Irregularity
Notes: Say
This table refers to Horizontal (formerly referred to as “Plan”) and Vertical Irregularities. This slide gives the general definition of each type of irregularity. Our design example is a “regular” structure and these tables (or the following examples) do not apply.
In this lesson, we’ll review each type of horizontal and vertical irregularities.

## Slide 43: Irregularities and Design Forces
ASCE 7-10 12.3.3.4 For structures assigned to SDC D, E, or F and having a horizontal structural irregularity of Type 1a, 1b, 2, 3, or 4 or a vertical structural irregularity of Type 4, the design forces shall be increased 25% for the following elements of the seismic force resisting system:
Connections of diaphragms to vertical elements and to collectors.
Collectors and their connections, including connections to vertical elements, of the seismic force-resisting system.
Notes: Say
With a Seismic Design Category of D, E, or F, design forces shall be increased 25% for connections of diaphragms to vertical elements and to collectors, and for connections of collectors to vertical elements (ASCE 7-10 12.3.3.4).
Presenter Note
This slide features information that will be found on the post-training knowledge assessment:
In which Seismic Design Categories do the design forces need to be increased by 25% for connections of diaphragms to vertical elements and to collectors, and for connections of collectors to vertical elements per ASCE 7-10 Section 12.3.3.4?
  Seismic Design Categories A, B, and C
  Seismic Design Categories E and F only
  Seismic Design Categories A and B only
  Seismic Design Categories D, E, and F
None of the above

## Slide 44: Horizontal Irregularity 1a & 1b
Torsional Irregularity considered to exist where:
Extreme Torsional Irregularity considered to exist where:
Δ2
Δ1
1a: Torsional & 1b: Extreme Torsional
Notes: Say
Per ASCE 7-10 Section 12.3.2.1, structures having one or more of the irregularity types listed in Table 12.3-1 shall be designated as having horizontal structural irregularity. The first horizontal irregularities we’ll discuss are 1a Torsional and 1b Extreme Torsional.
Torsional irregularity is defined to exist where the maximum story drift at one end of the structure transverse to an axis is more than 1.2 times the average of the story drifts at the two ends of the structure.
Extreme torsional irregularity is defined to exist where the maximum story drift at one end of the structure transverse to an axis is more than 1.4 times the average of the story drifts at the two ends of the structure.
Both torsional and extreme torsional irregularities are computed including accidental torsion with Ax=1.0 and apply only to structures in which the diaphragms are rigid or semirigid.

## Slide 45: Horizontal Irregularity 1a & 1b, cont.
Left Wall Drift at 2nd floor
Right Wall Drift at 2nd floor
Average Drift at 2nd floor
Max Drift at 2nd floor
>1.2, Type 1a Irregularity exists
>1.4, Type 1b Irregularity exists
1a: Torsional & 1b: Extreme Torsional
Notes: Say
This slide shows an example calculation of an Extreme Torsional (Type 1b) Horizontal Irregularity. The diaphragm has been classified as rigid.
As a first step, we need to determine the drift of the left and right walls at the 2nd level. Deduct the first floor deflection from the second floor deflection for each side. This results in a 1” drift at the left wall and a 0.25” drift at the right wall.
Next, we need to find how much the drift varies between the right and left walls at the 2nd floor. This is accomplished by dividing the maximum drift of the two walls (Left Wall: 1.0”) by the average drift of the two walls (Average Drift at Level 2: 0.625”). This gives us a ratio of 1.6.
Because the ratio is greater than 1.4, the figure depicts a type 1b horizontal irregularity.

## Slide 46: Horizontal Irregularity 2
Reentrant Corners Irregularity considered to exist where:
and
Re-entrant corner
a
b
c
d
2: Reentrant Corners
Notes: Say
A reentrant corner irregularity is defined to exist where both plan projections of the structure beyond a reentrant corner are greater than 15% of the plan dimension of the structure in the given direction.
Other configurations than shown on the slide, such as H or U shapes, shall be considered.
With a Seismic Design Category of D, E, or F, design forces shall be increased 25% for connections of diaphragms to vertical elements and to collectors, and for connections of collectors to vertical elements (ASCE 7-10 12.3.3.4) – unless designed with load combos with overstrength factor noted in Section 12.4.3.2 of ASCE 7-10.

## Slide 47: Horizontal Irregularity 2, cont.
Along Gridline 1: Projection beyond Re-entrant Corner = 15’
Alone Gridline D: Projection beyond Re-entrant Corner = 20’
As both projections are > 15%, Type 2 Irregularity exists
2: Reentrant Corners
Notes: Say
This slide shows an example calculation of a Reentrant Corner (Type 2) Horizontal Irregularity.
To determine whether this irregularity exists, divide the length of the projection by the full length of the plan dimension in the same direction. Calculate this ratio for both plan projections.
If both plan projections are greater than 15% of the plan dimension, as they are in this figure, then a Type 2 Horizontal Irregularity exists.

## Slide 48: Horizontal Irregularity 3
Diaphragm Discontinuity
Irregularity considered to exist where:
or
Where ΔEDS represents the Change in Effective Diaphragm Stiffness from floor to floor
w
l
3: Diaphragm Discontinuity
Notes: Say
Diaphragm discontinuity irregularity is defined to exist where there is a diaphragm with an abrupt discontinuity or variation in stiffness, including one having a cutout or open
area greater than 50% of the gross enclosed diaphragm area, or a change in effective diaphragm stiffness of more than 50% from one story to the next.
With a Seismic Design Category of D, E, or F, design forces shall be increased 25% for connections of diaphragms to vertical elements and to collectors, and for connections of collectors to vertical elements (ASCE 7-10 12.3.3.4) – unless designed with load combos with overstrength factor noted in Section 12.4.3.2 of ASCE 7-10.

## Slide 49: Horizontal Irregularity 3, cont.
No Horizontal Irregularity Type 3
Horizontal Irregularity Type 3 Exists
Area of Opening
Diaphragm Deflection
3: Diaphragm Discontinuity
Notes: Say
Determining whether there is a diaphragm discontinuity requires us to check two separate calculations.
First, we’ll see if the area of the opening is larger than 50% of the total area. To find the total area, multiply the width and the length of the diaphragm (7,200 sqft). Then find the area of the openings using the same method (1,800 sqft). By dividing the opening area by the total area (1,800/7,200), we find that the opening area is only 25% of the total area. With this calculation, there is no type 3 horizontal irregularity.
However, we’ll also need to check the change in effective diaphragm stiffness. If the change between levels is greater than 50% (factor of 1.5), we’ll have an irregularity. By dividing the drift at level 2 (1.5”) by the drift at level 3 (0.8”), we receive a ratio of 1.88. This amount is great enough for a type 3 horizontal irregularity.

## Slide 50: Horizontal Irregularity 3, cont.
To transfer shear properly:
Diaphragms with openings have additional chords and collectors
Blocking between joists and strapping over the diaphragm may be required to create “drag struts”
3: Diaphragm Discontinuity
Notes: Say
In order to transfer the shear properly, diaphragms with openings have additional diaphragm chords and collectors (drag struts) which form the boundary of the diaphragm opening.
Blocking between joists and strapping over the diaphragm may be required to create ‘drag struts’ capable of transferring the tension and compression load demand around the opening.
Per IBC 2305.1.1, this type of analysis applies to wood shear panels whether or not the opening in the diaphragm is large enough to be considered a type 3 horizontal irregularity.

## Slide 51: Horizontal Irregularity 4
SIDE ELEVATION
PLAN SECTION A - A
Out-of-Plane Offset Irregularities considered to exist where:
There are discontinuities in the lateral force resistance path, such as out-of-plane offsets of the vertical elements
4: Out-of-Plane Offsets
Notes: Say
Out-of-plane offset irregularity is defined to exist where there is a discontinuity in a lateral force-resistance path, such as an out-of-plane offset of at least one of the vertical elements.
ASCE 7-10 Section 12.3.3.3 states that elements supporting discontinuous walls or frames shall have the design strength to resist special seismic load combinations of Section 12.4.3.2. The connections from the discontinuous elements to the supporting members shall be adequate to transmit the forces for which the discontinuous elements were required to be designed.
With a Seismic Design Category of D, E, or F, design forces shall be increased 25% for connections of diaphragms to vertical elements and to collectors, and for connections of collectors to vertical elements (ASCE 7-10 12.3.3.4).

## Slide 52: Horizontal Irregularity 5
Nonparallel System Irregularities considered to exist where:
Vertical lateral force-resisting elements are not parallel to or symmetric about the major orthogonal axes of the seismic force-resisting system
5: Nonparallel Systems
Notes: Say
If the vertical lateral force-resisting elements are not parallel to or symmetric about the major orthogonal axes of the seismic force-resisting system, you have a “nonparallel system”. When this happens, the structure must be analyzed by the “Orthogonal Combination Procedure” (100% force in one direction and 30% in the other direction) or by using “Simultaneous Application of Orthogonal Ground Motion”.
Per ASCE 7 Section 12.5.3, structures in SDC C or higher that have horizontal irregularity type 5 shall be designed with consideration to loads in both orthogonal directions (combined loading).
Per ASCE 7 Section 12.5.2, structures in SDC B may neglect combined loading effects.

## Slide 53: Vertical Irregularity Type 1a & 1b
Soft Story Irregularity:
Story stiffness < 70% story stiffness above, or…
Story stiffness < 80% average stiffness of three stories above
Extreme Soft Story Irregularity:
Story stiffness < 60% story stiffness above, or…
Story stiffness < 70% average stiffness of three stories above
1a: Soft Story Irregularity & 1b: Extreme Soft Story
The Loma Prieta earthquake of 1989 and the Northridge earthquake of 1994 were the catalysts for exposing the nation to the dangers of soft stories
Notes: Say
Per ASCE 7-10 Section 12.3.2.2, structures having one or more of the irregularity types listed in Table 12.3-2 shall be designated as having vertical structural irregularity.
The Loma Prieta earthquake in 1989 and the Northridge earthquake in 1994 were the catalysts for exposing the nation to the dangers of soft story design. Many apartments were designed with posts between each bay supporting 2 or 3 floors of living space above, and they failed in these earthquakes causing excessive monetary damage and avoidable loss of life. For this reason the code requires more in depth dynamic analysis for buildings with this design in SDC D, E, or F; and the code does not allow for an extreme soft story irregularity in SDC E or F.
A soft story irregularity is defined to exist where there is a story in which the lateral stiffness is less than 70% of that in the story above or less than 80% of the average
stiffness of the three stories above.
An extreme soft story irregularity is defined to exist where there is a story in which the lateral stiffness is less than 60% of that in the story above or less than 70% of the
average stiffness of the three stories above.
Presenter Note
This slide features information that will be found on the post-training knowledge assessment:
The Loma Prieta earthquake of 1989 and the Northridge earthquake of 1994 were the catalysts for exposing the nation to the dangers of which vertical irregularity?
  Stiffness irregularity (soft story)
  Weight (mass) irregularity
  In-plane discontinuity with vertical lateral force-resisting element irregularity
Vertical geometric irregularity

## Slide 54: Vertical Irregularity Type 1a & 1b, cont.
Level | Story Displacement [in] | Story Drift [in] | Story Shear Force [kip] | Story Stiffness [k/in] | % of Story Stiffness of Story Above | Check <70% | Check <60% | Avg. Story Stiff of 3 Above [k/in] | % | Check <80% | Check <70%
Roof | 5.00 | 0.75 | 60 | 80 |  |  |  |  |  |  | 
4th | 4.25 | 0.75 | 90 | 120 | 150% | Reg | Reg |  |  |  | 
3rd | 3.50 | 1.00 | 90 | 90 | 75% | Reg | Reg |  |  |  | 
2nd | 2.50 | 2.50 | 100 | 40 | 44% | Irreg | X-Irr | 96.7 | 41 | Irreg | X-Irr
1a: Soft Story Irregularity
1b: Extreme Soft Story
Extreme Soft Story on Level 2:
2nd Story Stiffness is 44% of 3rd Story Stiffness
2nd Story Stiffness is 41% of Avg. Story Stiffness of 3 Stories Above
Notes: Say
This figure depicts an Extreme Soft Story Irregularity. For this calculation, you will need to know the Story Displacement (inches), Story Drift (inches), Story Shear Force (kips), and Story Stiffness (k/in) for each level of the structure beforehand.
As a first step, we’ll determine the percentage of story stiffness of the story above. For the 2nd level, we divide its story stiffness (40 k/in) by the story stiffness of the 3rd level (90 k/in) – resulting in 44%. This equates to an Extreme Soft Story at level 2 because the story stiffness is less than 60% of the story stiffness above.
Continuing this process for the 3rd and 4th floors, we find 75% and 150% respectably. These levels are not considered irregular because these their story stiffness is not less than 70% of the story stiffness above.
Although we’ve already determined there is an Extreme Soft Story at level 2, let’s also try the second approach. For this method, we first need to find the average story stiffness of the 3 stories above the 2nd level. First, add up the story stiffness in kips for the 3rd, 4th, and roof levels (90 + 120 + 80 = 290 k/in). Then, compute the average stiffness of the three levels (290/3 = 96.7 k/in). Dividing the story stiffness of level 2 (40 k/in) by the average of the 3 stories above (96.7 k/in) gives us 41%. This figure also depicts an Extreme Soft Story at level 2 since the story stiffness is less than 70% of the averaged 3 stories above.
We cannot attempt this method for the 3rd, 4th, or roof levels. None of them have at least 3 stories above them.

## Slide 55: Vertical Irregularity Type 2
Mass Irregularities considered to exist where:
The effective mass of any story is more than 150% of the effective mass of the adjacent story
However, a roof that is lighter than a floor need not be considered.
2: Mass Irregularity
Notes: Say
As the seismic forces in a structure are dependent upon the mass of the structure, an unequal distribution of mass will cause some peculiar seismic responses. Weight (mass) irregularity is defined to exist where the effective mass of any story is more than 150% of the effective mass of an adjacent story. A roof that is lighter than the floor below need not be considered.
Per ASCE 12.7.2.5, weight of landscaping and other materials at the off gardens and similar areas is required to be included in the effective seismic weight.

## Slide 56: Vertical Irregularity Type 2, cont.
Weight of Roof + Landscape Weight
Area of Landscape
Weight of Floor
Effective Weight of Roof (0.7 x 50psf x Area)
Effective Weight of Floor
= 50 psf
= 70% plan
= 20 psf
= 35 psf x Area
= 20 psf x Area
Vertical Irregularity Type 2 Exists
2: Mass Irregularity
Notes: Say
Determining whether there is a type 2 vertical irregularity involves dividing the effective weight of the roof by the effective weight of the floor. If the ratio is larger than 1.5 (150%), the building is considered to have a mass irregularity.
It is important to remember that the weight of landscaping on the roof is a part of the effective weight.
Do
Review the slide.

## Slide 57: Vertical Irregularity Type 3
The horizontal dimension of the lateral-force-resisting system in any story is more than 130% of that in an adjacent story.
3: Geometric Irregularity
Notes: Say
Vertical geometric irregularity is defined to exist where the horizontal dimension of the seismic force-resisting system in any story is more than 130% of that in an adjacent story.
The Sears tower, as seen in the photo on the slide, is a good example.

## Slide 58: Vertical Irregularity Type 3, cont.
BUILDING ELEVATION
Vertical Irregularity Type 3 Exists
3: Geometric Irregularity
Notes: Say
To determine whether the horizontal dimension of the lateral-force-resisting system on level 1 is more than 130% of that on level 2 is a case of simple division. By dividing the horizontal length of the level 1 shear wall by the horizontal length of the level 2 shear wall, we receive a ratio of 1.67. This would equate to a type 3 vertical geometric irregularity because the ratio is greater than 1.3.

## Slide 59: Vertical Irregularity Type 4
Discontinuity in Vertical Lateral Force-resisting Elements is considered to exist where:
There is an in-plane offset of a vertical seismic force-resisting element resulting in overturning demands on a supporting beam, column, truss or slab
BUILDING ELEVATION
4: In Plane Discontinuity
Notes: Say
In-plane discontinuity in vertical lateral force-resisting elements irregularity is defined to exist where there is an in-plane offset of a vertical seismic force-resisting element resulting in overturning demands on a supporting beam, column, truss, or slab (i.e., if the shear wall above doesn’t at least partially ‘stack’ with the shear wall below, then you have this irregularity).
ASCE 7-10 Section 12.3.3.3 states that elements supporting Discontinuous Walls or Frames shall have the design strength to resist special seismic load combinations with over strength factor of Section 12.4.3.2. The connections from the discontinuous elements to the supporting members shall be adequate to transmit the forces for which the discontinuous elements were required to be designed.
ASCE 7-10 Section 12.3.3.4 states that in Seismic Design Category D, E, or F, design forces shall be increased 25% for connections of diaphragms to vertical elements and to collectors, for connections of collectors to vertical elements.

## Slide 60: Vertical Irregularity Type 5a & 5b
A Weak Story Irregularity is considered to exist where:
The story lateral strength is less than 80% of that in the story above.
An Extreme Weak Story Irregularity is considered to exist where:
The story lateral strength is less than 65% of that in the story above.
Stiff Resisting Elements
Notes: Say
A weak story irregularity is defined to exist where the story lateral strength is less than 80% of that in the story above.
An extreme weak story irregularity is defined to exist where the story lateral strength is less than 65% of that in the story above.
For both irregularities, the story lateral strength is the total lateral strength of all seismic-resisting elements sharing the story shear for the direction under consideration.
Design is not permitted in Seismic Design Category E or F for either irregularity.
Structures with an extreme weak story shall not be over two stories or 30 feet in height. See ASCE 7-10 Section 12.3.3.2 for an exception to this rule.

## Slide 61: Vertical Irregularity Type 5a & 5b, cont.
5a: Lateral Strength Weak Story
5b: Lateral Strength Extreme Weak Story
Level | Shear Wall Length per Elevation [ft] | Shear Wall Cap [plf] | Shear Capacity Vcap [k] - One Side | Total Story Shear Capacity Vcap [k] | % of Capacity of Story Above | Check <80% | Check <65%
Roof | 8 | 185 | 14.8 | 29.6 |  |  | 
3rd | 30 | 185 | 55.5 | 111.0 | 375% | Reg | Reg
2nd | 12 | 280 | 33.6 | 67.2 | 61% | Irreg | Ex-Irr
Extreme Weak Story on Level 2:
2nd Story Shear Capacity is 61% of 3rd Story Shear Capacity
Notes: Say
Shown is an example calculation of an Extreme Weak Story on Level 2. After determining the Total Shear Capacity for each level, we can easily determine whether the structure has a 5a or 5b vertical irregularity.
First, find the percentage of total shear capacity for the stories above. For the 2nd level, divide its total shear capacity (67.2 kips) by the total shear capacity of the 3rd level (111.0 kips) – resulting in 61%. This figure depicts an Extreme Weak Story at level 2 since the total story shear capacity is less than 65% of the level above.
Continuing this process for the 3rd floor, we find 375%. The 3rd level is not considered irregular because its shear capacity is not less than 80% of the shear capacity above.

## Slide 62
Now that you’ve complete this lesson, you should be able to:
Evaluate and explain structural irregularities as they relate to seismic design for wood framed construction

## Slide 63: Part Two Contents
LESSON 1
Design Base Shear
Evaluate and explain structural design base shear for use in the equivalent lateral force procedure
LESSON 2
Distribution of Seismic Forces
Explain the distribution of seismic forces for use in the equivalent lateral force procedure
LESSON 3
Diaphragm Design
Summarize how to design diaphragms with wood framed construction to resist seismic forces
Notes: Do
Review the slide.

## Slide 64
Part 2 Lesson 1:
Design Base Shear
After completing this lesson, you will be able to:
Evaluate and explain structural design base shear for use in the equivalent lateral force procedure
Calculate and confirm the seismic response coefficient for use in the seismic base shear equation

## Slide 65: Equivalent Lateral Force Procedure
12.8.1: Seismic Base Shear
12.8.2: Period Determination
12.8.3: Vertical Distribution of Seismic Forces
12.8.4: Horizontal Distribution of Seismic Forces
12.8.5: Overturning
12.8.6: Story Drift Determination
12.8.7: P-Delta Effects
This lesson will review the usage of
Seismic Base Shear and
Period Determination equations
for the Lateral Force Procedure
Notes: Say
In this lesson, we’ll review the usage of Seismic Base Shear and Period Determination equations for the Equivalent Lateral Force Procedure.

## Slide 66: Seismic Base Shear
Seismic Base Shear
Seismic Base Shear
𝒗=𝑪_𝑺 𝑾
Effective Seismic Weight
Effective Seismic Weight
𝑾
Seismic Response Coefficient
Seismic Response Coefficient
𝑪_𝑺=𝑺_𝑫𝑺/(𝑹∕𝑰_𝒆 )
Short Period Design Spectral Response Acceleration
Short Period Design Spectral Response Acceleration
𝑺_𝑫𝑺
Response Modification Factor
Response Modification Factor
𝑹
Importance Factor
Importance Factor
𝑰_𝒆
12.8.1.1
12.7.2
12.8.1
11.4.4
Table 12.2-1
Table 1.5-2
Notes: Say
Seismic Base Shear is an estimate of the maximum expected lateral force that will occur due to seismic ground motion at the base of a structure. Calculations depend on:
Soil conditions at the site
Proximity to potential sources of seismic activity (such as geological faults)
Probability of significant seismic ground motion
The level of ductility and overstrength associated with various structural configurations and the total weight of the structure
The fundamental (natural) period of vibration of the structure when subjected to dynamic loading
The equation to determine the Seismic Base Shear, v, is rather easy: multiply the Effective Seismic Weight and Seismic Response Coefficient together. The difficult portion is obtaining the values of each of the parameters.
Our first step will be to find the Effective Seismic Weight by adding together the total roof and floor dead loads.
Second, we’ll need to find the Seismic Response Coefficient by locating its relevant parameters. The Short Period Design Spectral Response Acceleration (SDS) parameter for our design example has already been determined in Part 1 of Seismic Design for Wood Framed Construction. However, the Response Modification Factor, R, and the Importance Factor, Ie, will need to be found by referencing ASCE 7-10.
Finally, before we can use the Seismic Response Coefficient to find the Seismic Base Shear, we will need to check whether our CS value is within the usable range. These equations will involve finding the (Approximate) Fundamental Period of the structure.
Presenter Note
This slide features information that will be found on the post-training knowledge assessment:
Which two parameters comprise the Seismic Base Shear?
  Response Modification Factor and Effective Seismic Weight
  Effective Seismic Weight and Seismic Response Coefficient
  Seismic Response Coefficient and Importance Factor
  Importance Factor and Response Modification Factor

## Slide 67: Effective Seismic Weight
Measured Weights in PSF
Roof Weights
Floor Weights
Load Distribution
Apply loads to lateral-resisting elements
Tributary Area Loads in Kips
Roof Loads + Floor Loads = Total Effective Weight
Wall Weights
Notes: Say
Let’s start by finding the Effective Seismic Weight.
A dead load consists of all materials of construction incorporated into the building. Generally, anything that is a fixed part of the structure is a dead load. Items that can be considered to be dead loads include construction materials (beams, columns, doors, windows, floor coverings, wall coverings, cabinets, etc), heating and ventilation systems, electrical trays, piping, etc. Items that are not considered to be dead loads include shelving, desks, chairs, beds, or anything that may be moved around.
The Effective Seismic Weight equals the total dead load plus a few other loads, such as:
25% of Floor Live Load for areas used as storage
Actual partition weights or minimum 10 psf of floor area
Total opening weight of permanent equipment
20% of flat roof snow load where it exceeds 30 psf
Finding the Effective Seismic Weight has three steps:
First, measure roof, floor, and wall weights in pounds per square foot.
Second, take the wall, roof and floor areas and apply their loads to the lateral-resisting elements. The tributary area, in our case, represents half the area all around the supporting element to the next supporting element. This means that the top-half of our wall weights will be integrated into the roof/floor above, and the lower-half of our wall weights will be integrated into the floor below.
Third, convert the roof and floor loads from pounds per square foot to the total weight in kips (kilo-pounds; 1,000lbs = 1 kip) -- then add together the roof and floor loads for the Total Effective Weight.

## Slide 68: Roof Weights
Component | Load (psf)
Roofing | 3.5
½” Sheathing | 1.5
Trusses | 3.5
Insulation | 1.5
Gyp Ceiling | 2.8
Sprinkler | 1.5
Mech./Elect. | 1.0
Misc. | 0.7
DLSL = Total Roof Load (along slope) | 16.0
DESIGN EXAMPLE SLIDE
Notes: Say
Start by measuring the components that make up the roof in pounds per square foot. Adding all these parts together for our design example gives us a total roof load of 16 psf along the slope.
Unit loads for roof areas that are sloped are commonly expressed in terms of weight per unit area of horizontal projection. This is done because most load computations are done in terms of plan view unit areas. However, our measurements calculated the load along the slope of the roof. Our figure requires a slope adjustment as the weight of a sloped surface expressed in terms of weight per unit area of horizontal projection is larger than the weight per unit area along the surface.
If the roof slope is 4:12 or less, then the adjustment is less than 4% and is not considered to be significant. Consequently, the slope adjustment is commonly done only for slopes greater than 4:12.
For our design example, recall that our gable roof’s pitch is 6:12. By using an equation that multiplies the sloped load by the quotient of the root-sum-square of the rise and run divided by the slope run, we find that the horizontal load is 18 pounds per square foot.

## Slide 69: Floor and Wall Weights
Component | Load (psf)
Flooring | 1.0
1” Lt. Wt. Concrete | 10.0
¾” Floor Sheathing | 3.0
Floor Framing | 3.0
Gyp Ceiling | 2.8
Sprinkler | 1.5
Misc. | 0.7
Total Floor Load | 22.0
Component | Load (psf)
Exterior Walls (Walls only) | 12.0
Interior Walls (Uniform load over entire floor surface) | 10.0*
*Typically, the actual weight of the interior walls would be calculated and applied to the seismic lateral forces. The uniform load over the floor surface is used here is for simplicity. A minimum 10 psf partition loading is required per ASCE 7-10 12.7.2.2. | 
Floor Weights
Wall Weights
DESIGN EXAMPLE SLIDE
Notes: Say
Weighing the floor weight components, we get a total load of 22 pounds per square foot for our design example.
The wall weights can get a little tricky as the exterior and interior walls in our design example are measured differently from one another. Like our floor weights, the interior walls are measured as a uniform load over the entire floor. Typically, the actual weight of the interior walls would be calculated and applied to the seismic lateral forces. The uniform load over the floor surface is used here for simplicity. A minimum 10 psf partition loading is required per ASCE 7-10 12.7.2.2.
The exterior walls measurement isn’t spread over the entire floor. Instead, our figure is the walls-only weight in pounds per square foot.
We won’t be adding together our wall weights since they will be distributed to the roof and floor lateral-resisting elements as a next step.
It should be noted that storage loads, permanent equipment, a percentage of snow load, and landscaping loads for the roof may need to be added if they are present in the building. Refer to ASCE 7-10 12.7.2 for effective seismic weight.

## Slide 70: Recall the Floor Plan
The building has 8 units on each level and has overall dimensions of 105’-4” by 65’-0” (Note: Roof framing spans in the N-S direction). It is symmetrical in both directions (at vertical gridline 3 and between horizontal gridlines B & C).
DESIGN EXAMPLE SLIDE
N (REF)
Notes: Say
Looking back on our design example’s floor plan, we see that the building has 8 units on each level. The overall dimensions are 105’-4” by 65’. The roof framing spans in the north-south direction. And it is symmetrical in both directions: vertically at gridline 3 and horizontally between gridlines B and C.

## Slide 71: Tributary Load Distribution
To distribute loads correctly:
Take wall, roof, and floor areas and apply their dead loads to the correct diaphragm that will transfer this load to the lateral-resisting elements.
Wr
W3
W2
DESIGN EXAMPLE SLIDE
Notes: Say
Transferring the loads to the lateral-resisting elements involves applying wall weights to the roof and to the floors above and below. Referencing the figure on the slide, the tributary roof load (Wr) will contain the roof weight and the top-half of the wall weights on the third floor. The bottom-half wall weights of the third floor and the top-half wall weights of the second floor will be applied to the third floor tributary load (W3). Similarly, the bottom-half wall weights of the second floor and the top-half wall weights of the first floor will be applied to the second floor tributary load (W2).

## Slide 72: Determine Roof Dead Loads
Weight of Roof
DESIGN EXAMPLE SLIDE
(with overhang)
Notes: Say
To determine the seismic force at the roof level, we need to find the total weight of the roof and the total weight of the upper-half of the third-floor walls.
As the roof has a 1 foot overhang along the perimeter of the building the roof area at 7191 sqft is slightly larger than the floor area at 6847 sqft.
First we take the Roof horizontal Dead load value of 48 psf and multiply it by roof area. This will give us the weight of 129,438 lbs.
Second we find the weight of the upper half of the interior wall by dividing 10psf by 2 and multiplying it by the floor area to get a weight of 34,230 lbs.
Then we calculate the weight of the North and south walls by multiplying 12psf by two and half the wall height (8feet divided by 2= 4 feet) and multiplying by the length of the wall at 105.33’ to get 10,112 lbs.
Similarly we calculate the weight of the end walls but use a median height of 12.67’ as these wall extend to the attic area. We add all the weights to get a total weight of 193.5 kips

## Slide 73: Determine Floor Dead Loads
Weight of Floor
DESIGN EXAMPLE SLIDE
Notes: Say
Following the same procedure, we find the total dead load for each floor is 257.2 kips. Note that half the walls from the floor above and half the walls from the floor below contribute to the floor diaphragm dead load.
Do
Review the slide.

## Slide 74: Next Step to Determine Seismic Base Shear
❶
❷
✓
DESIGN EXAMPLE SLIDE
W
CS
Notes: Say
Adding the roof and two floor dead loads together gives us a Total Effective Weight of 707.9 kips for our design example.
To determine the base shear, v, we will continue with the Equivalent Lateral Force Procedure found in ASCE 7-10 Section 12.8.
We have already determined the weights, W, at each diaphragm. To find the Seismic Base Shear, v, we will also need to find the Seismic Design Coefficient, CS, determined from Section 12.8.1.1.

## Slide 75: Seismic Response Coefficient Overview
Seismic Response Coefficient
Seismic Response Coefficient
𝑪_𝑺=𝑺_𝑫𝑺/(𝑹∕𝑰_𝒆 )
Short Period Design Spectral Response Acceleration
Short Period Design Spectral Response Acceleration
𝑺_𝑫𝑺=𝟎.𝟒𝟖𝟕
Response Modification Factor
Response Modification Factor
𝑹
Importance Factor
Importance Factor
𝑰_𝒆
For T ≤ TL
For T > TL
For Ie ≥ 0.01
For S1 ≥ 0.6g
CS Need Not Exceed
CS Not Less Than
DESIGN EXAMPLE SLIDE
Notes: Say
Finding the parameters to determine the Seismic Response Coefficient is a little more elaborative than simply plugging in values. It will require referencing tables and figures in ASCE 7-10 and then using additional equations to check whether the CS value is within the usable range.
First we’ll calculate the Seismic Response Coefficient – then we’ll check our answer to see if it is within range.
The Short Period Design Spectral Response Acceleration is 0.487 for our design example. This calculation was covered in Part 1 of Seismic Design for Wood Framed Construction. On the next couple slides, we’ll reference our code books to find the Response Modification Factor (R) and the Importance Factor (Ie).

## Slide 76: Response Modification Factor
ASCE 7-10 Table 12.2-1 |  |  |  |  |  |  | 
Seismic Force Resisting System | Response Modification Factor, R | Overstrength Factor, Ωo | Deflection Amplification Factor, Cd | STRUCTURAL SYSTEM LIMITATIONS AND BUILDING HEIGHT (feet) LIMITATIONS |  |  | 
 |  |  |  | Seismic Design Category |  |  | 
 |  |  |  | B | C | D | E/F
A. BEARING WALL SYSTEMS |  |  |  |  |  |  | 
15. Light framed wood walls sheathed with wood structural panels rated for shear resistance | 6 ½ | 3 | 4 | NL | NL | 65 | 65
16. Light framed (cold-formed steel) walls sheathed with wood structural panels or steel sheets rated for shear resistance | 6 ½ | 3 | 4 | NL | NL | 65 | 65
DESIGN EXAMPLE SLIDE
Notes: Say
The Response Modification Factor is 6 ½ for light framed walls with shear panels. Notice that Seismic Design Category A is not part of this table as structures in this category need only comply with the requirements of Section 1.4. For our design example, we are limited to 65 feet of height in Seismic Design Category D, which is much higher than our structure. Using light framed walls with shear panels as our seismic force-resisting system is acceptable.
Presenter Note
This slide features information that will be found on the post-training knowledge assessment:
What is the Response Modification Factor, R, for light framed structures with wood structural shear panels used for the basic seismic force-resisting system?
  R = 4.5
  R = 6.0
  R = 6.5
  R = 3.0
None of the above

## Slide 77: Importance Factor
Risk Category | Importance Factor, Ie
I or II | 1.0
III | 1.25
IV | 1.5
Recall from Part 1 of Seismic Design for Wood Framed Construction, our design example structure is in Risk Category II
ASCE 7-10 Table 1.5-2
DESIGN EXAMPLE SLIDE
Notes: Say
See ASCE 7-10 Table 1.5-2 for the Seismic Importance Factor. It is now based on the Risk Category – which replaced the Occupancy Category found in the previous edition. Refer to Chapter 1 Table 1.5-1 to find a structure’s Risk Category. Our design example structure is in Risk Category II. Therefore, Table 1.5-2 states the Importance Factor is 1.0.

## Slide 78: Determine Seismic Design Coefficient
Parameters for CS
Solving for CS
But does the Seismic Design Coefficient we obtained fit within the usable range?
DESIGN EXAMPLE SLIDE
Notes: Say
Now that we’ve obtained the Short Period Design Spectral Response Acceleration (SDS), the Response Modification Factor (R), and the Importance Factor (Ie), we can easily solve for the Seismic Design Coefficient by plugging in our parameters to the equation. Solving for CS, we receive a result of 0.075.
Before we can plug this number into the Seismic Base Shear equation, we first need to check whether our Seismic Design Coefficient is within the usable range.

## Slide 79: Seismic Design Coefficient Limitations
Need Not Exceed
Not Less Than
For T ≤ TL (Eq. 12.8-3)
For T > TL (Eq. 12.8-4)
(Eq. 12.8-5)
For S1 ≥ 0.6g (Eq. 12.8-6)
DESIGN EXAMPLE SLIDE
Notes: Say
To check whether the Seismic Design Coefficient can be used, we will need to find a couple more parameters.
The Fundamental Period of a Structure, T
The Long-Period Transition Period, TL
Once we find T and TL, we can plug the values into the proper equations on this slide.

## Slide 80: Fundamental Period Determination
Approximate Period Equation
DESIGN EXAMPLE SLIDE
Notes: Say
The analysis of a structure’s period, T, can be an arduous task. ASCE 7-10 Section 12.8.2 states, “The fundamental period of the structure, T, in the direction under consideration shall be established using the structural properties and deformational characteristics of the resisting elements in a properly substantiated analysis”.
The code allows us to find an approximate period, Ta, per ASCE 7-10 Equation 12.8-7 for quicker analysis.
To find the Approximate Fundamental Period, Ta, we need the values from Table 12.8-2 which are based on the seismic force-resisting system type. You also must know how to determine hn.
Ask
Can anyone tell the class what hn represents in the Approximate Period Equation?
Say
hn represents the height (in feet) from the base to the highest level in the structure. SEAOC's Seismic Design Manual Vol. 2 for the 2006 IBC does a better job of explaining what is meant by the definition of hn. SEAOC explains that this means the average height of the highest diaphragm (in our example this is the mean roof height of the pitched roof diaphragm).
Recall that the mean roof height of the pitched roof diaphragm in our design example is 35’-4”, which translates in decimal to 35.33.
By plugging in 0.02 for Ct, 35.33 for hn, and 0.75 for x, we receive an Approximate Fundamental Period of 0.29 second.

## Slide 81: Fundamental Period Limitations
Fundamental Period Limiting Equation
SD1 | Cu
≥ 0.40 | 1.4
0.30 | 1.4
0.20 | 1.5
0.15 | 1.6
≤ 0.10 | 1.7
Notes: Say
However, if you need to determine the actual fundamental period by measuring the structural properties, then it is limited by the equation shown on this slide. To find the value of parameter Cu, the designer needs to know the SD1 value for the site and will need to use Table 12.8-1. The SD1 value for our design example, which we found in Part 1 of Seismic Engineering for Wood Framed Construction, is 0.323 g – giving us a Cu value of 1.4. By plugging in 1.4 for Cu and multiplying it by our Approximate Period of 0.29 second, we’re shown that T should be equal or less than 0.41 of a second.
As we are using the Approximate Period for our design example calculations, this limit does not apply.

## Slide 82: Determine Long-Period Transition Period
Long-Period Transition Period
Based on ASCE 7-10 Section 11.4.5 and Figure 22-12
Sacramento design example value is 12
For Sacramento
DESIGN EXAMPLE SLIDE
Notes: Say
We have to find the new Long-period Transition Period for our structure (based on its location, see ASCE Section 11.4.5 and Figure 22-12). In Sacramento, our value is 12 seconds. It becomes pretty obvious when looking at these tables that to have a building with a period greater than TL is going to be a rather tall building because TL ranges from 4 to 16 seconds...while our mid-rise design example structure has a period of less than 1 second.

## Slide 83: Seismic Design Coefficient Limitations
Need Not Exceed
Not Less Than
≥0.01
For T ≤ TL (Eq. 12.8-3)
For T > TL (Eq. 12.8-4)
=0.021 ≥ 0.01 (Eq. 12.8-5)
For S1 ≥ 0.6g (Eq. 12.8-6)
Parameters
✓
✓
✗
✗
DESIGN EXAMPLE SLIDE
Notes: Say
After finding TL, we have discovered the parameters necessary to determine which equations to use and the ability to solve them.
For the CS Need Not Exceed set, we’ll use Equation 12.8-3 because T (Ta) is less than TL.
Likewise, for the CS Not Less Than set, we’ll use Equation 12.8-5 to get the minimum value of 0.044SDSIe which is equal to 0.214 is greater than 0.01. Additionally as S1 is less than 0.6g equation 12.8-6 does not apply

## Slide 84: Seismic Design Coefficient Limitations, cont.
Need Not Exceed
Not Less Than
Use for design
✓
✓
DESIGN EXAMPLE SLIDE
Notes: Say
The CS we calculated falls within the prescribed limits so we can use it for our design example.

## Slide 85: Calculating the Seismic Base Shear
❶
❷
✓
✓
W
CS
DESIGN EXAMPLE SLIDE
Notes: Say
Plugging in the Seismic Design Coefficient and Effective Seismic Weight, we find a Seismic Base Shear of 53.1 kips.

## Slide 86
Now that you’ve completed this lesson, you should be able to:
Evaluate and explain structural design base shear for use in the equivalent lateral force procedure
Calculate and confirm the seismic response coefficient for use in the seismic base shear equation

## Slide 87
Part 2 Lesson 2:
Distribution of Forces
After completing this lesson, you will be able to:
Explain the distribution of seismic forces for use in the equivalent lateral force procedure

## Slide 88: Equivalent Lateral Force Procedure
12.8.1: Seismic Base Shear
12.8.2: Period Determination
12.8.3: Vertical Distribution of Seismic Forces
12.8.4: Horizontal Distribution of Seismic Forces
12.8.5: Overturning
12.8.6: Story Drift Determination
12.8.7: P-Delta Effects
This lesson will review the usage of
Vertical and Horizontal Distribution
equations for the Lateral Force Procedure
Notes: Say
In this lesson, we’ll review the usage of Vertical and Horizontal Distribution equations for the Equivalent Lateral Force Procedure.

## Slide 89: Vertical Distribution of Seismic Forces
FX depicts the lateral seismic force induced at any level
Necessary for the design of the lateral force-resisting system at each level
Next step is to locate Vertical Distribution Factor, Cvx
Lateral Seismic Force
DESIGN EXAMPLE SLIDE
Notes: Say
FX depicts the lateral seismic force induced at any level. This parameter helps with the design of the lateral force-resisting system at each level. It is easily determined by multiplying the Base Shear, v, by the Vertical Distribution Factor, CVX (ASCE 7-10 Equation 12.8-11).
Since the Base Shear for our design example was found in the previous lesson, the next step will to be to locate the Vertical Distribution Factor, CVX.

## Slide 90: Vertical Distribution Factor
Cvx dependent on:
  weight of the structure level
  height of the structure level
  building period
wi and wx = the portion of the total gravity load of the building (w) located or assigned to level i or x
hi and hx = the height in feet from the base to level i or x
k = distribution exponent related to the building period
Equation 12.8-12
k = 1 when buildings have period of ≤ 0.5 second
k = 2 when buildings have period ≥ 2.5 seconds
k = 2 (or can be interpolated between 1 and 2) when buildings have period between 0.5 and 2.5 seconds
DESIGN EXAMPLE SLIDE
Notes: Say
The Vertical Distribution Factor, Cvx, is determined by using Equation 12.8-4 in ASCE 7-10. It is dependent on the weight and height of the structure at each level and the building’s period.
The wi and wx parameters are the portion of the total gravity load of the building (w) located or assigned to level i or x.
The hi and hx parameters are the height in feet from the base to level i or x.
k is a distribution exponent related to the building’s period. For buildings that have a period of 0.5 or less, k=1. For buildings that have a period of 2.5 or more, k=2. For buildings with a period between 0.5 and 2.5 seconds, k can either equal 2 or can be interpolated between 1 and 2.
Presenter Note
This slide features information that will be found on the post-training knowledge assessment:
The Vertical Distribution Factor, Cvx, is dependent upon the structure weight (at each level), the height of the structure (at each level), and the structure’s period.
  True
  False

## Slide 91: Vertical Force Distribution
Level | Weight (wx) (kips) | Height (h) (feet) | wxhx | wxhx / ∑wihi | Fx (k) | Cumulative ∑Fx (k)
Roof | 193.5 | 35.33* | 6,837 | 0.487 | 25.9 | 25.9
3rd Floor | 257.2 | 18.67 | 4,801 | 0.342 | 18.2 | 44.0
2nd Floor | 257.2 | 9.33 | 2,401 | 0.171 | 9.1 | 53.1
Sum | 707.9 |  | 14,039 |  | 56.70 | 
Because Ta = 0.29 and k = 1, equation simplifies to:
*The height used should approximate the centroid of the roof level mass.
DESIGN EXAMPLE SLIDE
Notes: Say
This table shows how the loading is vertically distributed in our design example. The top two levels receive roughly the same amount of force at their respective diaphragms and the 2nd floor only receives about half that force. It is plain to see that this redistribution will bring more of the force to the upper levels in order to strengthen the force-resisting elements at these levels. The shear force is cumulative, so the force-resisting elements have to be able to withstand the shear from their diaphragm and that from the level(s) above.
Note that values are at Strength Design Level (Ultimate).
Do
Review results with class.

## Slide 92: Vertical Force Distribution, cont.
Cumulative ∑Fx
DESIGN EXAMPLE SLIDE
Figure representing table results from previous slide
25.9 k
9.1 k
18.2 k
25.9 k
44.0 k
53.1 k
Notes: Say
Shown is a figure representing the table results on the previous slide.
Do
Review the slide.

## Slide 93: Horizontal Distribution of Seismic Forces
Seismic Design
Story Shear
Seismic design story shear in any story (vx) (kip or kN) shall be determined from the following equation:
Portion of Seismic Base Shear Induced at Level i
The portion of the seismic base shear (v) induced at level i shall be determined from the following equation:
DESIGN EXAMPLE SLIDE
Notes: Say
Section 12.8.4 of ASCE 7-10 states that: The seismic design story shear (vx) shall be distributed to the various vertical elements of the seismic force-resisting system in the story under consideration based on the relative lateral stiffness of the vertical resisting elements and the diaphragm. This is the cumulative shear, vx, from the diaphragm under consideration and the shear from the stories above.

## Slide 94: Redundancy Factor
ρ=1.0
Structures assigned to SDC B or C
Structures assigned to SDC D, E or F that meet a condition in Table 12.3-3
ρ=1.3
Structures assigned to SDC D, E or F
DESIGN EXAMPLE SLIDE
Notes: Say
The effect of the redundancy factor is to increase the seismic load effect for structures with low redundancy. It is either 1.0 or 1.3. Structures with adequate redundancy result in a ρ = 1.0 (ρ shall not be less than 1.0 nor greater than 1.3).
- ρ = 1.0 is allowed to be used for (8) conditions; the first of which is structures in SDC B or C. The other categories are for calculations and design of certain components, elements, loads, and systems (see 12.3.4.1).
- For SDC D through F the redundancy factor, ρ, shall be 1.3 unless one of two conditions is met, and then it is permitted to take ρ as 1.0. See Section 12.3.4.2 for these conditions, one of which will require using Table 12.3-3.
One could assume ρ = 1.0 and check after design; or use 1.3 to be conservative; or check 12.3.4.2 to see if the structure being designed will allow for ρ = 1.0.

## Slide 95: Redundancy Factor, cont.
DESIGN EXAMPLE SLIDE
Notes: Say
To find if the Redundancy Factor is 1.0 and not 1.3, we must see if either Exception A or B of ASCE 7-10 Section 12.3.4.2 applies to our structure. Recall that in Part 1 of Seismic Design for Wood Framed Construction, our design example building was determined to be in Seismic Design Category D.
Exception A states that each story resisting more than 35% of the base shear in the direction of interest shall comply with Table 12.3-3. According to the table, structures with shear walls that have aspect ratios greater than 1.0 must be able to remove one shear wall without having a 33% reduction in capacity. This is probably true for our structure, but would require a few calculations to prove it so. We should check if we can meet Exception B.
For Exception B, ρ=1.0 is allowed if the structure is regular in plan at all levels -- provided that the seismic force-resisting systems consist of at least two bays of seismic force-resisting perimeter framing on each side of the structure in each orthogonal direction at each story resisting more than 35% of the base shear. The number of bays for a shear wall shall be calculated as the length of shear wall divided by the story height or two times the length of shear wall divided by the story height, hsx, for light-frame construction.
Our structure is a regular plan 3-story building of light-framed construction.
Exception B seems to be easier to calculate for our design example since we already know our shear wall lengths. It is possible to find if we have two or more “bays” that are required to make ρ = 1.0.

## Slide 96: Shear Wall Locations for Redundancy Factor
Level | Fx | ΣFx | Story Height | %V | Number of Bays | >2 Bays?
3rd | 22.45k | 22.45k | 8’-0” | 39.6% | 9.7 | Yes
2nd | 22.85k | 45.30k | 9’-4” | 79.9% | 8.4 | Yes
1st | 11.40k | 56.70k | 9’-4” | 100% | 8.4 | Yes
}
ρ = 1.0
Short-side Shear Wall Length = 39’
DESIGN EXAMPLE SLIDE
Number of Bays = 2 * Shear Wall Length / Story Height
5’-6”
5’-6”
Notes: Say
We have to check both orthogonal directions, but we can check the long direction (that has more shear wall length) by inspection. Knowing the shear wall length on the short length side of the building and the shear at each level, we can easily determine the percentage of base shear and the number of bays. Each level in our example has a percentage of base shear greater than 35%, and the number of bays at each level is greater than two, thus ρ = 1.0.

## Slide 97
Now that you’ve completed this lesson, you should be able to:
Explain the distribution of seismic forces for use in the equivalent lateral force procedure

## Slide 98
Part 2 Lesson 3:
Diaphragm Design
After completing this lesson, you will be able to:
Summarize how to design diaphragms with wood framed construction to resist seismic forces

## Slide 99: Additional Design of Diaphragms
Equation 12.10-1
Fi = Design force at level i
wi = weight tributary to level i
wpx = weight tributary to the diaphragm at level x
Parameters
ρ applies in SDC D, E, or F
Notes: Say
Floor and roof diaphragms shall be designed to resist design seismic forces from the structural analysis, but shall not be less than that determined by Equation 12.10-1 (shown on the slide). The redundancy factor, ρ, applies to structures assigned to Seismic Design Category D, E, or F. For the inertial forces calculated in accordance with Equation 12.10-1, ρ shall equal 1.0. For transfer forces, ρ shall be the same as that used for the structure. For structures having horizontal or vertical irregularities (indicated in Section 12.3.3.4), the requirements of that section shall also apply.
Seismic forces change rapidly and the building is forced into different modes of vibration so it is unlikely that the maximum force on each diaphragm will occur simultaneously, thus a separate diaphragm formula is given to account for the possible larger instantaneous forces that could occur.
Remember to only use this for sizing sheathing and nailing for diaphragm shear unless irregularities are present.

## Slide 100: Diaphragm Load Distribution
Controlling Fpx
Level | (wpx) | Fx | ∑Fi | ∑wi | Fpx | 0.2SDSwpx | 0.4SDSwpx
Roof | 19.5 | 25.9 | 25.9 | 193.5 | .134wpx | .097wpx | .195wpx
3rd | 257.2 | 18.2 | 44.0 | 450.7 | .098wpx | .097wpx | .195wpx
2nd | 257.2 | 9.1 | 53.1 | 707.9 | .075wpx | .097wpx | .195wpx
Sum | 707.9 | 53.1 |  |  |  |  | 
Diaphragm forces need not consider the weight of the shear walls
which receive load from the diaphragm
DESIGN EXAMPLE SLIDE
Notes: Say
For our design example, we can calculate the Fpx at each level (using Equation 12.10-1) and verify it is between the minimum and maximum allowed. If it falls below the minimum, then the minimum governs. If it falls above the maximum, then the maximum governs.
Do
Review the table results with the class.

## Slide 101: Max Horizontal Diaphragm Dimension Ratios
Type | Maximum Length-Width Ratio
Wood structural panel, unblocked | 3:1
Wood structural panel, blocked | 4:1
Single-layer straight lumber sheathing | 2:1
Single-layer diagonal lumber sheathing | 3:1
Double-layer diagonal lumber sheathing | 4:1
b (width)
=65’-0”
l (length) = 105’-4”
l /w= 105’-4”/65’-0”=1.6 <3.0
✓
Notes: Say
The diaphragm aspect ratios are limited by AWC 2015 SDPWS Table 4.2.4.
The maximum horizontal diaphragm dimension ratio allowed if the diaphragm is constructed of wood structural panels which is blocked so that the sheathing is nailed at all edges is 4:1, while an unblocked wood structural panel diaphragm is 3:1
We get the example diaphragm the aspect ratio by dividing the length of 105’-4” by the width of 65; which gives us 1.6 which is within the maximum limit of 3:1 for unblocked diaphragm <Click>
Presenter Note
This slide features information that will be found on the post-training knowledge assessment:
What is the maximum horizontal diaphragm dimension ratio allowed if the diaphragm is constructed of wood structural panels and nailed at all edges (with no unblocked edges)?
  6:1
  5:1
  4:1
  3:1

## Slide 102: Diaphragm Design
wpx | Fpx(k) | wx | R | vult | vasd
193.5 | .134wpx=25.9 | 245 plf | 12.9 kips | 199 plf | 139 plf
257.2 | .098wpx=25.1 | 238 plf | 12.6 kips | 193 plf | 135 plf
257.2 | .097wpx=25.1 | 238 plf | 12.5 kips | 193 plf | 135 plf
❶
❷
❸
❹
❶
❷
❸
❹
DESIGN EXAMPLE SLIDE
-4”
Notes: Say
The diaphragm must be able to withstand the shear and bending forces that are in response to seismic inertia. In our design example, we assumed that only the exterior walls have shear walls to resist the seismic forces. Idealizing the diaphragm to act like a simply supported beam, we can easily find the reactions at each end for the distribution load. From the reaction, we can find the shear plf along the line of resistance at each end.
Do
Review equations and diagram with class.

## Slide 103: Diaphragm Nailing Design
AWC 2015 SDPWS Table 4.2C
= 360plf/2 = 180plf > 139plf “OK”
DESIGN EXAMPLE SLIDE
Notes: Say
This slide shows Table 4.2C in the AWC 2015 SDPWS, discussing the nominal capacities for wood-frame diaphragms.
Our roof shear is 139 plf. Using 15/32” thick sheathing to span the 22.5” gap between the truss that are at 24”o.c. and attaching to these 2xDF trusses with 8d nails – with the minimum nailing per code at an unblocked diaphragm – gives us a diaphragm nominal capacity of 360plf. Use the ASD reduction factor of 2.0 per section 4.2.3 we obtain the allowable shear capacity as 360/2=180 plf.

## Slide 104: Roof Chords
Finding Chord Force
DESIGN EXAMPLE SLIDE
-4”
Notes: Say
Again, idealizing our diaphragm to be a simple span beam, we can find our chord force (our maximum tension and compression force) is equal to 3666 lbs.
Note that for all other parts of the lateral system, design using “Non-Diaphragm” Forces.

## Slide 105: Chord Splice Design
Chord Force = 3,666 lbs
Transfer chord tension load at plate splice using 16d Common Nails:
16d common to 1 ½” DF Side Member = 141 lbs / nail (Base Value, z)
Per NDS Table 2.3.2 Earthquake Loads, Load duration factor Cd = 1.6
16d Common Nail @ 160% = 225 lbs / nail
(3666)/225 = 17 nails each side of splice
Alternately, could use 9 SDS25300 screws e.g. (448 lbs / screw (Cd=1.6)) = 4,032 lbs or CMSTC16 Strap with 20-16d sinkers each side of Splice (3,668#)
DESIGN EXAMPLE SLIDE
Notes: Say
When using a double top plate, which is standard practice, after checking to ensure that our 2x4 or 2x6 plate can take the tensile force (roof or floor provides sufficient lateral bracing to prevent buckling under compression), you have to ensure that you properly transfer the force between plates. This is typically done by nailing the plates together on either side of the splice. Other methods of accomplishing this could be using wood screws (so fewer fasteners are used) or by using straps on the sides of the plate.

## Slide 106: Shear Transfer Details
Notes: Say
Trusses are intended to carry loads applied parallel to their plan (i.e., depth) and not perpendicular to it. The lateral load transfer through the truss as depicted in Figure B8-7 occurs unless blocking or some other means is provided that will transfer this load directly between the roof sheathing and top plate of the wall. The truss industry places the following general limits on this load transfer through the truss:
Trusses shall be permitted to transfer load between diaphragms and supporting shear walls, provided that the distance between the diaphragm and the shear wall does not exceed 6”, the trusses are spaced no greater than 24” on center, and the horizontal load transfer between the diaphragm and the shear wall does not exceed 50 plf.

## Slide 107: Shear Transfer Details, cont.
❶
❷
Figures 1 and 2 show blocking between
trusses and fastened to the top plate,
preventing rotation and lateral displacement of the truss at the wall connection..
Notes: Say
When shear is transferring from the diaphragm to the top plate, the designer must ensure that lateral displacement of the rafter/truss as well as rotation of the rafter/truss does not occur.
Figures 1 and 2 show blocking installed between trusses and fastened to the top plate, preventing rotation and lateral displacement of the truss at the wall connection. Blocking also allows for diaphragm boundary nailing required by code. Blocking may be turned flat every few bays allowing for eave ventilation.
Presenter Note
This slide features information that will be found on the post-training knowledge assessment:
Blocking between roof trusses (or roof rafters) allows for edge nailing of the roof diaphragm and gives a direct load path for shear transfer. Blocking will also help the designer prevent which of the following structural concerns:
  Rotation of the truss/rafter and lateral displacement of the truss/rafter
  Rotation of the truss/rafter and uplift of the truss/rafter
  Uplift of the truss/rafter and lateral displacement of the truss/rafter
  Uplift of the truss/rafter and obstructing eve ventilation
  None of the above

## Slide 108: Diaphragm to Shear Wall at Gable Ends
139 plf
DESIGN EXAMPLE SLIDE
Notes: Say
As calculated previously for our design example, the shear along the ends of the building in the north-south direction (gridlines 1 and 5) is 139 plf.
Do
Review the slide.

## Slide 109: Diaphragm to Shear Wall at Gable Ends, cont.
Design Shear = 139 plf
Assume lateral tie plate installation
Assume top plates are DF, therefore allowable capacity of connector LTP4 = 670 lbs
(Or place 1 lateral tie plate @ 57” o.c.)
DESIGN EXAMPLE SLIDE
Notes: Say
To transfer our shear load to our top plate, we can boundary nail the sheathing to the gable truss and then we can use lateral tie plates to attach the truss to the top plate. Following the calculation in the slide, we find the required spacing to install the lateral tie plates.
Alternatively, we could use toe-nailing to transfer the shear load from the gable truss to the wall top plate since the load is less than 150 plf. (In Seismic Design Categories D, E, & F, transferring shear with toenails is limited to 150 plf per section 4.1.7 of the AF&PA 2008 SDPWS.)

## Slide 110: Diaphragm Deflection
AWC 2015 SDPWS Equation 4.2-1
Panel Shear and Fastener Slip Deflection
Chord Splice
Slip Deflection
DESIGN EXAMPLE SLIDE
Bending
Deflection
Notes: Say
Permissible deflection shall be that deflection up to which the diaphragm and any attached distributing or resisting element will maintain its structural integrity under design load conditions, such that the resisting element will continue to support design loads without danger to occupants of the structure. Each term in this equation represents an aspect of the diaphragm that will contribute to the total deflection.
Time will not permit detailed calculations for diaphragm deflection on our Design Example. Some manufacturers offer training sessions with more detailed discussions regarding diaphragm deflection.
Tables are based on blocked diaphragms and consideration should be given for amplifying non-blocked diaphragms (2.5x per Breyer’s “Design of Wood Structures” 6th Edition).
We’ll continue with a quick discussion on the terms that make up SDPWS Equation 4.2-1, and then return to Rigid vs. Flexible Diaphragms.
Presenter Note
This slide features information that will be found on the post-training knowledge assessment:
Which of the following does not contribute to diaphragm deflection?
  Panel shear and fastener slip deflection
  Chord splice slip deflection
  Perpendicular to grain compression
  Bending deflection
  None of the above

## Slide 111: Bending Deflection
DESIGN EXAMPLE SLIDE
  = diaphragm length (feet) = shear (plf)
= chord modulus of elasticity (psi) = area of chord (in2)
= diaphragm width (feet)
Parameters
Notes: Say
The first term calculates the deflection from the diaphragm bending.

## Slide 112: Panel Shear and Fastener Slip Deflection
DESIGN EXAMPLE SLIDE
  = diaphragm length (feet)
= shear (plf)
= apparent diaphragm stiffness from nail slip and panel shear deformation (kips/in)
Parameters
Notes: Say
This term gives you the deflection from fastener slip and shear forces acting on your diaphragm. The “Ga” term which is the apparent diaphragm stiffness from nail slip and panel shear deformation can be found in Column A of AWC 2015 SDPWS Tables 4.2A, 4.2B &4.2C and knowing information about your diaphragm sheathing. Ga differs from OSB and ply and new code makes the distinction.

## Slide 113: Chord Splice Slip Deflection
DESIGN EXAMPLE SLIDE
  = sum of individual chord – splice slip values on both sides of the diaphragm, each multiplied by its distance to the nearest support
= diaphragm width, in feet, in direction of the load applied
Parameters
Notes: Say
This Chord Splice Slip value depends on how you connect your top plate splices (i.e., if you are using nails, screws, or strapping the splice).

## Slide 114: Rigid vs. Flexible
2015 SDPWS
Section 4.2.5: Rigid Diaphragm
ASCE 7-10
Section 12.3.1.1: Flexible Diaphragm Conditions
Section 12.3.1.3: Calculated Flexible Diaphragm Condition
Notes: Say
Once you have calculated the diaphragm deflection, you must compare that to the story drift, a.k.a. deflection of your lateral-force resisting system for the story below (i.e. shear walls). Using the definitions given in the code you can verify whether or not your diaphragm is flexible or rigid. There are, of course, conditions – and for those you must refer to ASCE 7-10 sections 12.3.1.1 and 12.3.1.3. IBC Removed definitions of Rigid and flexible diaphragms to eliminate any confusion between it and ASCE.
Section 12.3.1.1 states that “Diaphragms constructed of untopped steel decking or wood structural panels are permitted to be idealized as flexible (see required provisions in this Code section).”
Regarding Calculated Flexible Diaphragm Conditions, Section 12.3.1.3 says “…where the computed maximum in-plane deflection of the diaphragm under lateral load is more than two times the average story drift of adjoining vertical elements of the seismic force-resisting system of the associated story under…”
Per ASCE 7-10 section 12.3.1.1, we will assume that our design example diaphragm (roof and floor) is flexible. Due to this assumption we do not have to account for additional forces in our shear walls due to torsion.
New SDPWS section 4.2.5- idealized as rigid when Maximum in plane deflection of the diaphragm itself under lateral load is less than or equal to two times the average defection of adjoining vertical elements of the lateral force resisting system of the associated story under equivalent tributary lateral load.
Our design example meets all parameters described in Condition C of ASCE 7-10 Section 12.3.1.1, therefore a flexible diaphragm assumption is allowed. Conditions met: (1) Our structure does not have concrete or similar materials placed over wood structural panel diaphragms, and (2) each line of vertical elements of the seismic force-resisting system complies with the allowable story drift of Table 12.12-1.
Diaphragms constructed of untopped steel decking or wood structural panels are permitted to be idealized as flexible if any of the following conditions exist:
a. In structures where the vertical elements are steel braced frames, steel and concrete composite braced frames or concrete, masonry, steel, or steel and concrete composite shear walls.
b. In one- and two-family dwellings.
c. In structures of light-frame construction where all of the following conditions are met:
1. Topping of concrete or similar materials is not placed over wood structural panel diaphragms except for nonstructural topping no greater than 1 1/2 in. (38 mm) thick.
2. Each line of vertical elements of the seismic force-resisting system complies with the allowable story drift of Table 12.12-1.

## Slide 115: Rigid vs. Flexible, cont.
MDD = Max Deflection of Diaphragm
ADVE = Average Deflection of Vertical Elements
Notes: Say
This illustration gives you an idea of what deflections you are comparing.
2015: New SDPWS section 4.2.5- idealized as rigid when Max Deflection of Diaphragm (MDD) is less than or equal to 2x Average Deflection of Vertical Elements (ADVE.)
MDD =
ADVE =

## Slide 116: Distribution of Shear
Rigid Diaphragms
Rigid Distribute vx to elements based on relative stiffness of the lateral-force resisting elements
Flexible Diaphragms
Flexible Distribute vx based on the tributary area of each lateral-force resisting element
Notes: Say
The determination as to whether or not your diaphragm is rigid or flexible will have a big impact on how the forces are distributed to your seismic lateral-force resisting elements (i.e. shear walls).
Do
Review the slide.

## Slide 117
Now that you’ve complete this lesson, you should be able to:
Summarize how to design diaphragms with wood framed construction to resist seismic forces

## Slide 118: Part Three Contents
LESSON 1
Shear Wall
Shear Design
Identify and compare the three methods for wood shear wall design
LESSON 2
Shear Wall Overturning Design
Explain how to design structures to resist overturning forces
LESSON 3
Drift
Analysis
Summarize methods to calculate and resist story drift
Notes: Do
Review the slide.

## Slide 119
Part 3 Lesson 1: Shear Wall Shear Design
After completing this lesson, you will be able to:
Identify and compare the three methods for wood shear wall design
Analyze and explain the proper methods for shear wall nailing design and for the floor to floor transfer of shear

## Slide 120: Shear Wall Load Distribution
Rigid vs. Flexible
Floor and roof diaphragms are assumed to be flexible in our design example
ASCE 7-10 12.8.4.1: inherent torsion need only be considered where diaphragms are not flexible
ASCE 7-10 12.8.4.2: accidental torsion need only be considered where diaphragms are not flexible
DESIGN EXAMPLE SLIDE
Notes: Say
We will assume that the floor and roof diaphragms of our design example is flexible. Due to this assumption we do not have to account for additional forces in our shear walls due to torsion.
Our design example meets all parameters described in Condition C of ASCE 7-10 Section 12.3.1.1, therefore a flexible diaphragm assumption is allowed. Condition C is met because: (1) Our structure does not have concrete or similar materials placed over wood structural panel diaphragms, and (2) each line of vertical elements of the seismic force-resisting system complies with the allowable story drift of Table 12.12-1.
Other possible conditions for a flexible diaphragm classification are: (A) In structures where the vertical elements are steel braced frames, steel and concrete composite braced frames or concrete, masonry, steel, or steel and concrete composite shear walls; or (B) In one- and two-family dwellings.
Per ASCE 7-10 12.8.4.1, inherent torsion need only be considered where diaphragms are NOT flexible.
Per ASCE 7-10 12.8.4.2, accidental torsion need only be considered where diaphragms are NOT flexible.
There has been a lot of discussion and debate regarding the use of flexible vs. rigid diaphragm analysis for wood buildings, without a clear direction. Currently both analyses are being used by engineers and some building departments. Using a flexible assumption is acceptable per the code. It should also be noted that determining whether the diaphragm is rigid or not is relative to the rigidity of the shear wall. If you have a building with irregularities or a unique layout, it would be best to seek the advice of a structural engineer familiar with the guidelines of the ruling jurisdiction. Some engineers use the envelope method where they use both the flexible and rigid analyses to design the shear walls for the worst case loads from both diaphragm types.

## Slide 121: Drag Strut Design
East-West Wall: Double top plate acts like a drag strut in these locations (over openings)
Top Plate Drag Struts
Design Shear = 139 plf
EW Wall Total Shear = 139 plf x 65’ = 9,035 lbs
Design for Drag Strut = 139 plf x6.5’ = 904 lbs
DESIGN EXAMPLE SLIDE
5’-6”
4’-9”
7’-0”
5’-6”
4’-9”
Notes: Say
Looking at shear line 1: As the design has all the exterior walls as being shear walls, the drag struts will only be the length of the windows and doors – making our longest drag strut 6’-6”.
To find the drag strut force, multiply the length of the longest drag strut (6’-6”) by the design shear along the same line. The design shear acting on the 65’ East-West wall of our example was calculated in Part 2 of this course and found to be 139 plf. The conservatively design drag strut for the longest, non-shear wall span is 904 lbs.
If there were portions of walls that are not shear walls, the top plate would be a drag at these locations as well.

## Slide 122: Wall Strut Splice Design
If Strut Force governed, then we would transfer tension load at plate splice using 16d Common Nails:
From 2015 NDS Table 12N
16d Common to 1 ½” DF Side Member = 141 lbs/nail (base value, z)
Per NDS Table 2.3.2 EQ Loads, Cd = 1.6
16d Common Nail @ 160% = 225 lbs/nail
1,396 / 225 = 7 nails on each side of splice (min. is (8) 16d nails per 2015 IBC Table 2304.10.1)
904 lbs Strut Force < 1,396 lbs Chord Force
DESIGN EXAMPLE SLIDE
Notes: Say
To determine what governs the design of your splices, you must find the chord force and the strut force along a shear line. The chord force of 1,396 lbs shown on the slide was calculated using the same method as we used in Part 2 of the course -- but this time in the orthogonal direction. For our design example, the chord force governs since it is larger than the strut force. However, if we had a longer drag strut, the outcome could be reversed.
If Strut Force governed, then we would transfer tension load at plate splice using 16d Common Nails as shown on the slide. However, this calculation is not required for our example since the Chord Force is higher than the Strut Force.

## Slide 123: Considerations When Designing Shear Walls
When designing a shear wall, all of these items must be considered:
Shear panel aspect ratio
Sheathing thickness
Shear wall nailing
Framing material
Chord design
Anchorage requirements
  Shear
  Holdowns
Deflection
Notes: Say
When designing a shear wall, all of these items must be considered:
-Shear panel aspect ratio
-Sheathing thickness
-Shear wall nailing
-Framing material
-Chord design
-Anchorage requirements (shear, holdowns)
-Deflection

## Slide 124: Shear Wall Aspect Ratios
Per Section 4.3.4 of 015 SDPWS for wood structural panel Shearwalls with aspect ratio greater than 2:1 the nominal unit shear capacity is multiplied by 1.25-0.125h/bs.
Walls with aspect ratios exceeding 3½:1 shall not be considered shear resistance walls.
Example: 9’x3’ shear wall is acceptable, but the nominal shear capacity is reduced by a factor of 1.25-0.125*(9/3) =0.875
Wall Height | Aspect Ratio | 
 | 3½:1 (blocked) | 2:1 (unblocked)
8’ | 2’-4” | 4’-0”
9’ | 2’-7” | 4’-6”
10’ | 2’-11” | 5’-0”
12’ | 3’-6” | 6’-0”
Per AWC 2015 SDPWS Table 4.3.4
Notes: Say
The height to length aspect ratio is limited for seismic and wind design per AWC 2015 SDPWS Table 4.3.4. The limit is there to help control the deflection of the shear wall – if you multiply the amount a shear wall end lifts up at the bottom (overturning) by the aspect ratio, you can get a good idea of how much the shear wall will deflect at the top. Although the sheathing thickness and nailing pattern amongst other items will affect this deflection, this method yields a rough estimate.
2015: 4.3.4.2 DOES NOT APPLY TO PERFORATED SWs
For the design to resist seismic forces per Table 4.3.4, the shear wall aspect ratio shall not exceed 2:1 unless the nominal unit shear capacity is multiplied by 1.25-0.125h/bs. Walls with aspect ratios exceeding 3½:1 shall not be considered shear resistance walls. This means that a 9’-0” tall shear wall that is 3’-0” wide is acceptable, but the shear capacity is 87.5% of the tabulated capacity.

## Slide 125: Three Methods for Shear Wall Design
Segmented Shear Wall
Shear Wall Opening with Force Transfer
Perforated Shear Wall
Can only consider the distance between the openings as possible shear walls
The framing and connections around the openings are designed to transfer the force around it
Permits the height and width of the shear wall segments to be the full height of the wall and the width of the full height segment adjacent to the opening
Notes: Say
When designing the lateral force-resisting system, you must consider how the openings will affect your design. There are 3 basic methods for shear wall design:
1. Segmented Shear Walls (Traditional):
Here you only consider the distance between the openings as possible shear walls.
2. Force Transfer Method:
The framing and connections around the openings are designed to transfer the force around it and hence special detailing is required around each opening. Using this method limits the wall piers on the sides of the openings, the openings themselves, and the overall shear wall to the aspect ratio limits of AWC 2015 SDPWS Section 4.3.4.4.
3. Perforated Shear Wall Method (No Force Transfer):
Permit the height and width of the shear wall segments to be the full height of the wall per SDPWS section 4.3.5.2 and the width of the full height segment adjacent to the opening.

## Slide 126: Segmented Wood Shear Walls
Only full height segments are considered
Maximum aspect ratio in Seismic Design Category D or higher:
  2:1
  3.5:1 (with capacity reduction)
Current code design values based on monotonic testing of 8’x8’ walls dating back to the 1950s
Holdown at each end of each shear wall segment
Notes: Say
Segmented shear walls do not allow for openings. Therefore, if a segmented shear wall is adjacent to an opening, holdowns are required at each end of the shear wall.
The values for the shear panels is based on APA testing completed in the 1950s. The sheathing thickness is based on 2015 SDPWS Tables 4.3A for wood structural panels.
There is a maximum aspect ratio of 2:1 for segmented wood shear walls on structures in Seismic Design Category D, E, or F.
3½:1 aspect ratio is allowed with capacity reduction.
Presenter Note
How would a designer install holdowns on a segmented wood shear wall that is adjacent to an opening?
  One holdown per shear wall segment; installed in the center of the segment
  Two holdowns per shear wall segment; one installed at each end of the segment
  Zero holdowns required for segmented shear walls
  Three holdowns per shear wall segment; one installed at each end of the segment and one installed in the center of the segment

## Slide 127: Shear Wall Opening with Force Transfer
SDWPS Section 4.3.5.2
Openings accounted for by strapping or framing based on a rational analysis
Requires additional detailing (blocking, nailing, strapping)
Height-width ratio defined by wall pier
2’ min width
Wall
Pier
Notes: Say
Intensive calculations are required to use the Force Transfer Method. IBC Seismic Design Manuals and the APA give examples of how to use this method of analysis. An obvious positive of using this method is it allows for openings in shear walls while maintaining high shear capacity. It does require additional detailing (i.e. blocking, nailing, strapping) around the openings in order to withstand the high forces.
Presenter Note
This slide features information that will be found on the post-training knowledge assessment:
Which of the three methods described in ASCE 7-10 for analyzing wood shear walls requires special detailing around each opening that is within a shear wall?
  Segmented Shear Wall Method
  Perforated Shear Wall Method
  Force Transfer Method
  Torsional Equilibrium Method

## Slide 128: Shear Wall Opening with Force Transfer, cont.
4x Post
4x Full height king stud with plywood edge nailing
4x Blocking
CS16 full length strap with 10d nails at 3” o/c. Placed over plywood sheathing.
2x Sill plate with sill anchorage per wall schedule
2-2x Top plates
2x Trimmer stud
Header beam per plan
2-2x Sill plates
Strap to GLB
❶
❷
❸
❹
❺
❻
❼
❽
❾
❿
Notes: Say
This graphic shows some of the detailing required for the Force Transfer Method. Using this method you can have holdowns on either side of the opening or you can design the wall such that the forces go out-to-out and the holdowns are only at the ends.

## Slide 129: Perforated Shear Wall
SDWPS Section 4.3.5.3
Openings accounted for by empirical adjustment factors
Holdowns only required at ends, even if dead load is sufficient to resist OT force (See SDWPS Equation 4.3-8)
Sill/sole uplift anchorage between holdowns, t, at full height segments is also required
Notes: Say
A perforated shear wall is defined in IBC Section 2302 as a wood-structural, panel-sheathed wall with openings that have not been specifically designed and detailed for force transfer around the openings. The perforated shear wall design method of IBC Section 2305.3.8.2 is a recently developed empirical method that recognizes the strength and stiffness contributed by sheathing above and below the wall openings.
Section 4.3.5.3 of the AWC 2015 SDPWS gives the requirements for Perforated Shear Wall Analysis. This method has many limitations. One of the positives for this design is it is relatively easy (if your design fits within the limitations) and you can eliminate all holdowns except for one at each end of your entire perforated shear wall. One major difference is that you must calculate the bottom plate fasteners for shear and tension instead of just for shear. Per Section 4.3.6.4.2.1, the bottom plate anchorage, t, must be designed for a uniform uplift force equal to the wall unit shear force, v, determined in Section 4.3.6.4.2.1.

## Slide 130: Perforated Shear Wall Limitations
The aspect ratio limitations of SDPWS Section 4.3.4.3 shall apply
The nominal unit shear capacity for a single sided wall shall not exceed 1,740 plf for seismic or 2,435 plf for wind as given in Table 4.3A
Uniform top and bottom of wall elevation
Maximum height of 20 feet
Collectors through full length of wall
Walls either side of out-of-plane offsets shall be separate perforated walls
SDWPS Section 4.3.5.3
Notes: Say
SDPWS Section 4.3.5.3 shows the limitations for a perforated shear wall design.
Do
Review the the slide.
Presenter Note
This slide features information that will be found on the post-training knowledge assessment:
Perforated shear walls have a maximum allowable height of:
10 feet
  15 feet
  20 feet
  30 feet

## Slide 131: Shear Resistance in Perforated Shear Wall
Uplift at full height segments (t) must resist unit shear load divided by Co (See SDPWS Equation 4.3-9)
Total wall deflection is based on sum of full height segments and v (unit shear load) divided by Co
Holdown anchorage calculated per 2008 SDPWS section 4.3.6.1.2
SDWPS Equation 4.3-8
Minimum tension chord uplift force
Notes: Say
We can calculate the shear resistance in a perforated shear wall by multiplying the adjusted shear resistance by the sum of the widths of the perforated shear wall segments. To do this, you must know the percentage of full-height sheathing (sum of the widths of perforated shear wall segments divided by the total width of the perforated shear wall, including openings) and the maximum opening height. Knowing these parameters allows you to use 2015 SDPWS Table 4.3.3.5 (on the next slide) to find the Co (the shear resistance adjustment factor). To find the adjusted shear resistance, multiply the unadjusted shear resistance (from allowable shear set forth in Table 4.3A) by Co.

## Slide 132: Shear Resistance in Perforated Shear Wall, cont.
Notes: Do
Review the table.

## Slide 133: Calculating ASD Unit Shear
Level | Fx | SFx | Vshear wall | ASD Vsw
3rd | 25.9/2=12.9 | 12.9 | 331 plf | 232 plf
2nd | 18.2/2=9.1 | 22.0 | 564 plf | 395 plf
1st | 9.1/2=4.5 | 26.5 | 681 plf | 476 plf
ASD Unit Shear
DESIGN EXAMPLE SLIDE
5’-6”
4’-9”
7’-0”
5’-6”
4’-9”
Notes: Say
There are only 2 lines of shear resistance in either direction since each end wall has shear walls. To design the shear walls, we must figure out the unit shear at each level. This can be completed by dividing the shear at each level by 2, then dividing the result by the length of shear wall (39’ in this case). As a final step, multiply by 0.70 to get the ASD values.
Do
Review the table.

## Slide 134: Shear Wall Nailing Design
Level | Shear Demand (plf) | Dbl. Sided | Nail Sp. | Nominal Shear | Allowable Shear
3rd | 232 | No | 6 | 520 | 260
2nd | 395 | No | 3 | 980 | 490
1st | 476 | No | 3 | 980 | 490
DESIGN EXAMPLE SLIDE
SDPWS Table 4.3A
Notes: Say
Table 4.3A in the 2015 SDPWS gives the nominal shear for wood structural panel shear walls with DF or SP framing (which gets its values from the testing the APA has completed). For allowable loads, divide by an ASD reduction factor of 2.0.
This allows us to specify a sheathing thickness, nail size, and pattern in order to have enough shear capacity to handle the demand.
Pay close attention to footnotes of this table regarding sill plate size and studs at abutting panel edges.

## Slide 135: Floor to Floor Shear Transfer
SDPWS Section 4.1.7
In SDC D, E, or F, toenails shall not be used to transfer lateral forces in excess of 150 plf for ASD from diaphragms to shear walls, drag struts (or collectors), or from shear walls to other elements
DESIGN EXAMPLE SLIDE
?
?
Notes: Say
Toenails cannot transfer more than 150plf in Seismic Design Category D, E, or F.
Ask
What can transfer the shear from floor to floor?
(Answer on next slide)
Presenter Note
This slide features information that will be found on the post-training knowledge assessment:
Toenails cannot transfer more than __________ of shear from floor to floor in Seismic Design Category D, E, or F.
  100 plf
  120 plf
  150 plf
  180 plf
  200 plf

## Slide 136: Floor to Floor Shear Transfer, cont.
Required Quantity Throughout the Shear Wall |  |  |  |  |  | 
Level | Shear Wall Demand (plf) | Force (lbs) | 16d Nails | SDS1/4x4 1/2 | LTP4 | A34
3rd | 202 | 1414 | 12” o.c (8 Total) | 42” o.c. (3 Total) | 42” o.c. (3 Total) | 28” o.c. (4 Total)
2nd | 407 | 2849 | 7” o.c. (13 Total) | 21” o.c. (5 Total) | 21” o.c. (5 Total) | 16” o.c. (6 Total)
1st | 509 | 3563 | N/A | N/A | N/A | N/A
Review 7’-0” Shear Wall
(or sheathing could span floor system)
❶
❷
❷
❸
❶
❶
❷
❸
DESIGN EXAMPLE SLIDE
Notes: Say
To transfer the force from the shear wall, you must calculate how many fasteners or connectors are required at each connection. To transfer the shear from floor to floor, the bottom plate must be connected to the floor truss or joist rim board or blocking (typically by nails, screws, a connector, or a combination thereof). Also, the truss or rim board must be connected to the top plate below. It is also possible to build your shear walls such that the sheathing spans the floor system connecting bottom plate above to top plate below.
Important point: The table on the slide shows what connectors are required for the demand load, not the shear wall capacity. Typically, designers will create shear wall tables that gives the nailing for the shear wall and connector requirements that meet the capacity that the shear wall can transfer – this way the table can be used over and over and a specific shear wall call out can be used on the plans based on the shear capacity.
An N/A value means there is no floor to floor connection as the 1st floor bottom plate transfers force into the foundation through different means.
Do
Review the slide.

## Slide 137
Now that you’ve completed this lesson, you should be able to:
Identify and compare the three methods for wood shear wall design
Analyze and explain the proper methods for shear wall nailing design and for the floor to floor transfer of shear

## Slide 138
Part 3 Lesson 2: Shear Wall Overturning Design
After completing this lesson, you will be able to:
Explain how to design structures to resist overturning forces

## Slide 139: Overturning
Fi = portion of base shear, v, induced at level i
hi and hx = height (feet) from the base to level i or x
Overturning Moments at
Level x, Mx
Notes: Say
Section 12.8.5 of ASCE 7-10 states: “The structure shall be designed to resist overturning effects caused by the seismic forces determined in Section 12.8.3.” The equation shown on this slide displays how the overturning moment in shear walls should be calculated using simple Statics. Building must be designed to resist overturning forces resulting from the seismic forces at each level.
Do
Review the slide.

## Slide 140: Load Combinations
D + F
D + L + H + F
D + H + F + (Lr or S or R )
D + H + F + 0.75(L ) + 0.75(Lr or S or R )
D + H + F + (0.6W or 0.7E )
D + H + F + 0.75(0.6W ) + 0.75L + 0.75(Lr or S or R )
D + H + F + 0.75(0.7E ) + 0.75L + 0.75S
0.6D + 0.6W + H
0.6(D + F ) + 0.7E + H
Basic Load Combinations
Alt. Basic Load Combinations
IBC 1605.3.1
IBC 1605.3.2
D + L + (Lr or S or R )
D + L + 0.6 ωW
D + L + 0.6 ωW + S/2
D + L + S + 0.6 ωW/2
D + L + S + E/1.4
0.9D + E/1.4
0.7E or E/1.4 converts Strength forces to ASD forces
Removed the self-straining loads, T
Include wind load Strength to ASD level reduction factor of 0.6

## Slide 141: Calculate Overturning
Assume overturning resisted by a 6 feet lever arm to determine overturning forces in design example
Use load combination Equation 16-16:
0.6(D + F ) + 0.7E + H ⤦
0.6D + 0.7E
H and F factors do not apply to our design example
DESIGN EXAMPLE SLIDE
Notes: Say
For our design example, assume overturning is resisted by a 6 ft (7 ft wall width – 1ft) lever arm to determine approximate OT forces.
The 1 ft reduction of the shear wall length to find the appropriate lever arm is due to correctly measuring from the center of the tension member and the compression member. In this example, we are using a system where the compression studs are symmetric on each side of the all-thread rod at each side of the shear wall. Therefore, you measure from center of rod to center of rod.
Max Overturning for Tension is calculated using load combo Equation 16-16: 0.6D + 0.7E (H and F do not apply to this building).
The H factor does not apply because that is the “load due to lateral earth pressure, ground water pressure, or pressure of bulk materials” and the F factor does not apply because that is the “load due to fluids” – none of which exist to affect our example structure.

## Slide 142: Vertical EQ Forces
The Basic Load combination which typically controls OT design is:
Tension use 0.6D + 0.7E (IBC Equation 16-16)
Compression, floor perpendicular to wall, use D + 0.75(0.7E ) + 0.75L + 0.75S (IBC Equation 16-14)
Compression, floor parallel to wall, use D + 0.7E (IBC Equation 16-12)
(for Equations 16-12 and 16-14)
(for Equation 16-16)
ASCE 7-10 Section 12.4.2.3
Notes: Say
Notice we are not including the effects of H (load due to lateral earth pressure, ground water pressure, or pressure of bulk materials) or S (snow load) or R (rain load) or F (load due to fluids with well-defined pressures and maximum heights). This is because we are assuming they will not govern the design on this structure. We can find the required answer by inserting the equation for E into load combinations 16-12, 16-14, and 16-16. However, this has already been done for us in Section 12.4.2.3 of ASCE 7-10.
When calculating overturning, the tension and compressive forces must take the thrust component of the earthquake force into consideration.
Do
Review the slide.

## Slide 143: Vertical EQ Forces, cont.
Tension ~ (0.6 – 0.14SDS)D + 0.7QE = 0.531D + 0.7QE
Compression, floor perpendicular to wall ~ (1.0 + 0.105SDS)D + 0.525QE + 0.75L = 1.051D + 0.525QE + 0.75L
Compression, floor parallel to wall ~ (1.0 + 0.14SDS)D + 0.7QE = 1.068D + 0.7QE
SDS = 0.487, = 1.0, and Section 12.4.2.3 of ASCE 7-10 results in:
Notes: Say
Substituting the values for SDS and rho (r), the load combinations are reduced to 0.524D+0.7QE, which implies you can only use 53.1% of design dead load to resist the earthquake uplift. Similarly for compression loads, you need to consider 1.051 times the dead load for floor perpendicular to wall and 1.068 times the dead load for floor parallel to the wall. Do note that the load combinations with live loads may govern and should be independently checked.
Do
Review the slide.

## Slide 144: Vertical Component, ±0.2SDSD
May be taken as zero for either of the following conditions:
In Equations 12.4-1, 12.4-5, and 12.4-6 where SDS is equal to or less than 0.125
In Equation 12.4-2 where determining demands on the soil-structure interface of foundations
Exceptions for Vertical Seismic Load Effect
Vertical Component shall be considered for: | Vertical Component need not be considered for:
Overturning anchorage | Horizontal diaphragm
Shear wall compression posts | Vertical shear wall diaphragm
Collector beams | Etc.
Ledger attachment | 
Etc. | 
Notes: Say
The vertical component need not be considered when designing the diaphragm.
± accounts for the forces acting vertically by either reducing the dead load for overturning resistance or increasing the dead load for vertical reactions.
Do
Review the slide.

## Slide 145: Calculate Overturning Moment
Overturning Moments at
Level x, Mx
(232 plf)(7’ ) = 1,414lbs
(395 plf)(7’) - 1,624lbs
= 1,141lbs
(476 plf)(7’) - 1,624lbs
- 1,414lbs = 567lbs
DESIGN EXAMPLE SLIDE
1624 lbs
1141 lbs
567 lbs
8 ft
Notes: Say
Using Simple Statics, we can find the correct overturning moment by multiplying the diaphragm forces by the correct height (or moment arm).
The shear shown on the illustration to the right is the diaphragm shear for a single shear wall at each level used to design the wall system for overturning. The shear is not the cumulative shear, which would be used to design the wall for shear.
Do
Review the slide.

## Slide 146: Calculate Resisting Moment
Resisting Moment
Structure Dead Load
DESIGN EXAMPLE SLIDE
8 ft
Notes: Say
Using the dead load of the structure we can calculate the moment that will resist overturning. The resisting moment is taken about the bottom corner of the shear wall in question.
We’re assuming both the roof and floor framing are parallel with the wall and spaced 24” o.c.
Do
Review the slide.

## Slide 147: Calculate Holdown Tension Forces
Note: Lever Arm = Distance from centerline (CL) of tension resistance to CL of compression resistance
8 ft
Notes: Say
If we insert the Resisting Moment as our “D” and the Overturning Moment as our “QE”, we can find the Tension and Compression loads at each level of our structure so we can design our studs or posts and our tension connectors at the ends of the shear wall.
For calculating the uplift at the end of the shear wall, we can only use 53.1% of the dead load (as previously calculated). 6ft is the distance between the anchorage points of the hold-down which is the resisting lever arm. Using the appropriate loads at each corresponding level we can calculate the Tension at each level of our structure so we can design our tension connectors at the ends of the shear wall. Note that that overturning moments already have the 0.7 factor applied to them when we calculated the shear loads.
Do
Review the slide.

## Slide 148: Calculate End Stud/Post Compression Forces
As floor joists are parallel to this shear wall…
*not including live loads
8 ft
Notes: Say
Similarly, using the load appropriate combinations we can obtain the worst case compression loads for the design of the studs or posts at the ends of the shear wall.
Do
Review the slide.

## Slide 149: Floor to Floor Anchorage for Holdown Tension
Shear Wall Boundary Posts (DFL – Stud Ground) | ASD Tension Demand (lbs) | Holdown Type (Allowable Load in lbs)
2-2x6 | 1,880 | HDU2 3,075
2-2x6 | 5,923 | HDU8 6,765
6x6* | 10,854 | HDU14 14,445
*HDU14 requires minimum wood thickness of 5 1/2“
Holdown
Between Floors
Notes: Say
A minimum of two studs are typically provided at the end of each shear wall. If we are in a 2x6 wall, (2) 2x6 studs will be able to handle the compression load at each end of the shear wall at each level. The illustrated example on the slide shows what would be required if holdowns were used at each level, but obviously there are many more possible solutions.
Some manufacturers have anchor tiedown software available to help with your design. These applications offer a solution for required all-thread rod, take up device, and compression studs or posts.
It is also possible (and more typical) to use strap solutions for low to moderate load conditions for floor to floor connections, with a holdown only at 1st floor level.

## Slide 150: Typical Holdown Capacity Chart
Notes: Say
Holdowns are pre-deflected and attach to the compression studs/post of a shear wall with structural wood screws. This is an extremely cost effective holdown choice due to ease of installation; higher load capacities; and lower installed cost.

## Slide 151: Sill Anchorage to Foundation
Anchor bolts are normally used to transfer shear from the wood sill plate to the concrete foundation
Section 1905.1.8 modifies section 17.3.3.5.2 of ACI 318-14 Appendix D and permits the use of lateral design values for bolts loaded parallel to grain, without the need to check concrete failure modes, provided a number of conditions are met (max. 5/8” diameter, min. 7” embedment, etc.)
Notes: Say
2015: ACI318 was completely rearranged. Before this referenced Appendix D. Now it is all in Section 1723 of the ACI 318-14. IBC 1905.1.8 modifies the ACI so that shear bolts can be designed per NDS Table 12E for lateral design values parallel to grain, provided a bunch of conditions are met. Note that the IBC references Table 11E- this is WRONG- should say 12E!
Normally anchor bolts are used to transfer shear from the wood sill plate to the concrete foundation.
The capacity of the anchor bolts for wood sill plates are limited by bolt capacity parallel to the grain in the wood and strength of the anchor bolt in concrete.

## Slide 152: Dowel Bearing Capacity for DF
Dowel Bearing Capacity (lbs) 2015 NDS Table 12E |  | 
Dia. | (133) | (160)
1/2 | 864 | 1040
5/8 | 1237 | 1488
Notes: Say
Determining the dowel bearing capacity is necessary to find the spacing requirements for the anchor bolt/sill plate connection. This value is dependent on the bolt diameter, wood species, and the minimum embedment of the dowel into the concrete (which can be found in NDS 2015 Table 12E).

## Slide 153: Sill Plate Splitting
Designing anchor bolt connection:
  2015 SDWPS Section 4.3.6.4.3 requires use of steel plate washers for shear walls with min. 0.229”x3” in size
  Diagonally slotted hole with width up to 3/16” larger than bolt diameter
  Slot length not to exceed 1 ¾”
Plate washer shall extend to within ½” of edge of bottom plate with sheathing (or other material with shear greater than 400 plf for wind or seismic)
½” MAX
Notes: Say
When designing the anchor bolt connection, the 2015 SDWPS Section 4.3.6.4.3 requires to use steel plate washers for shear walls with min. 0.229”x3”x3” in size. The hole in the plate washer is permitted to be diagonally slotted with a width of up to 3/16” larger than the bolt diameter and a slot length not to exceed 1¾” (provided a standard cut washer is placed between the plate washer and the nut).
When the shear wall starts racking due to the shear load, the sill plate tries to lift up and the steel plate washers connected to the anchor bolt restrain the lift up and the prying action.
The plate washer shall extend to within ½” of the edge of the bottom plate on the side(s) with sheathing or other material with nominal unit shear capacity greater than 400 plf for wind or seismic.

## Slide 154: Sill Plate Splitting, cont.
2015 SDPWS for Seismic Design Category D, E, or F:
3x3x0.229” (BP1/2-3 or BPS1/2-3) steel plates are required to prevent splitting
Steel plates extend to within ½” of the edge > 400 plf nominal unit shear
(Exception: Standard cut washers are allowed when:
Segmented shearwall design with holdowns neglecting dead load stabilizing moment
h/b ≤ 2:1
Nominal unit shear ≤ 980 plf for Seismic or ≤ 1370 plf for wind.
Notes: Say
A 3” x 3” x 0.229” bearing plate is required with foundation anchor bolts in order to prevent sill plate splitting, according to the 2015 SDPWS Section 4.3.6.4.3.
Do
Review the slide.
Presenter Note
According to the SDPWS Section 2305.3.11 for seismic design, which size bearing plate is required with foundation anchor bolts in order to prevent sill plate splitting?
  2” x 2” x 3/16”
  3” x 3” x 0.229”
  3” x 3” x 3/16”
  2” x 2” x 0.229”
  None of the above

## Slide 155
Now that you’ve completed this lesson, you should be able to:
Explain how to design structures to resist overturning forces

## Slide 156
Part 3 Lesson 3:
Drift Analysis
After completing this lesson, you will be able to:
Summarize methods to calculate and resist story drift

## Slide 157: Story Drift
Deflection at
Level x, δx
ASCE 7-10 Equation 12.8-15
Cd = Deflection amplification factor in ASCE 7-10 Table 12.2-1
δxe = Deflection determined by an elastic analysis
Ie = Importance Factor
Design Story Drift, Δ = The difference in deflections at the center of mass at the top and bottom of the story under consideration
Notes: Say
Where allowable stress design is used, the design story drift, Δ, shall be computed using the Strength Level seismic forces specified in Section 12.8 without reduction for Allowable Stress Design.
Inelastic deflection is calculated by multiplying the deflection determined by elastic analysis by the deflection amplification factor found in ASCS 7-10 table 12-.2-1 and dividing it by the importance factor.
Do
Review the slide.

## Slide 158: Deflection Amplification Factor, Cd
ASCE 7-10 Table 12.2-1 Design Coefficients and Factors for Seismic Force Resisting Systems |  |  |  |  |  |  | 
Seismic Force Resisting System | Response Modification Factor, R | Overstrength Factor, Ωo | Deflection Amplification Factor, Cd | STRUCTURAL SYSTEM LIMITATIONS AND BUILDING HEIGHT (feet) LIMITATIONS |  |  | 
 |  |  |  | Seismic Design Category |  |  | 
 |  |  |  | B | C | D | E/F
A. BEARING WALL SYSTEMS |  |  |  |  |  |  | 
15. Light framed wood walls sheathed with wood structural panels rated for shear resistance | 6 ½ | 3 | 4 | NL | NL | 65 | 65
16. Light framed (cold-formed steel) walls sheathed with wood structural panels or steel sheets rated for shear resistance | 6 ½ | 3 | 4 | NL | NL | 65 | 65
Notes: Say
For light-framed construction, like our design example, the Deflection Amplification Factor, Cd, is 4 according to ASCE 7-10 Table 12.2-1.

## Slide 159: Allowable Story Drift, Δa
ASCE 7-10 Table 12.12-1 Allowable Story Drift, Δa a,b
Structure | Risk Category |  | 
 | I or II | III | IV
Structures, other than masonry shear wall structures, four stories or less in height with interior walls, partitions, ceilings and exterior wall systems that have been designed to accommodate story drifts. | 0.025hsxc | 0.020hsx | 0.015hsx
Masonry cantilever shear wall structures d | 0.010hsx | 0.010hsx | 0.010hsx
Other masonry shear wall structures | 0.007hsx | 0.007hsx | 0.007hsx
All other structures | 0.020hsx | 0.015hsx | 0.010hsx
hsx is the story height below level x.
For seismic force-resisting systems comprised solely of moment frames in SDC D, E, and F, the allowable story drift shall comply with the requirements of Section 12.12.1.1.
There shall be no drift limit for single-story structures with interior walls, partitions, ceilings and exterior wall systems that have been designed to accommodate the story drifts. The structure separation requirements of Section 12.12.3 is not waived.
Structures in which the basic structural system consists of masonry shear walls designed as vertical elements cantilevered from their base or foundation support which are so constructed that moment transfer between shear walls (coupling) is negligible.
Notes: Say
The allowable story drift is dependent on the Risk Category and the type of construction material used for the seismic force-resisting system.
Do
Review the slide.
Presenter Note
This slide features information that will be found on the post-training knowledge assessment:
The allowable story drift of a structure is dependent on:
  Risk Category and type of construction material used for the seismic force-resisting system
  Importance Factor and Mapped Acceleration Parameters
  Deflection Amplification Factor and Importance Factor
  Overturning Moment and the Effective Seismic Weight
  None of the above

## Slide 160: Shear Wall Deflection
AWC 2015 SDPWS Equation 4.3-1
Bending
Deflection
Shear and Fastener
Slip Detection
Tie-Down Nail
Slip Deflection
Notes: Say
Permissible deflection shall be that deflection up to which the shear wall and any attached distributing or resisting element will maintain its structural integrity under design load conditions (that is, continue to support design loads without danger to occupants of the structure). The three terms in 2015 SDWPS IBC Equation 4.3-1 are deflection due to “bending”, “shear & fastener slip”, and “tie-down nail slip” (assembly).

## Slide 161: Shear Wall Deflection, cont.
Level | Shear Wall Demand ASD (plf) | Shear Wall Demand Strength (plf)
3rd | 232 | 331
2nd | 395 | 564
1st | 476 | 681
Per ASCE 7-10 Section 12.8.6, where ASD is used,
Design Story Drift, Δ, shall be computed using code specified
earthquake forces without reduction (i.e. using strength level forces).
Notes: Do
Review the slide.

## Slide 162: Bending Deflection
Level | v (plf) | h (plf) | b (ft) | (#Studs) * A (in2) | E (psi) | Δbending
3rd | 331 | 8 | 7 | (2)1.5(5.5)=16.5 | 1,400,000 | 0.008
2nd | 564 | 8 | 7 | (2)1.5(5.5)=16.5 | 1,400,000 | 0.014
1st | 681 | 8 | 7 | (5.5)(5.5)=30.25 | 1,400,000 | 0.010
h = Height of shear wall (ft)
v = Shear (plf)
E = Chord modulus of elasticity
A = Area of chord (in2)
b = Width of wall (ft)
Notes: Say
To calculate your deflection due to bending you must know your shear wall height and width as well as what you will use for your end studs as they act as your chord.
Do
Review the slide.

## Slide 163: Shear & Fastener Slip Deflection
Level | v (plf) | h (plf) | Ga (kips/in)* | Δshear
3rd | 331 | 8 | 10 | 0.265
2nd | 564 | 8 | 15 | 0.301
1st | 681 | 8 | 15 | 0.363
h = Height of shear wall (ft)
v = Shear (plf)
Ga = Apparent shear stiffness (kips/in)
*See Table 4.3A of the 2015 SDPWS. Example uses 15/32” 3-ply plywood (Wood Structural Panels-Sheathing) and 8d nails
Notes: Say
Unlike the previous code, Gt is no longer a used term. Ga is now the apparent shear wall shear stiffness from nail slip and panel shear deformation, kips/inch – refer to 2015 SDPWS Table 4.3A for values.
Do
Review the slide.

## Slide 164: Assembly Deflection
h = Height of shear wall (ft)
b = Width of shear wall (ft)
da = Anchorage slippage; accounts for:
  Holdown slippage or rod elongation
  Shrinkage
  Crushing of compression posts
Notes: Say
The NDS calls this term “tie-down nail slip”, but both are the same and account for the deflection from the issues stated on this slide.
In the next few slides, we’ll calculate the holdown slippage, rod elongation, and wood shrinkage, then add the values together to receive the anchorage slippage.
Do
Review the slide.

## Slide 165: Holdown & Rod Deflections
Level | dhd | Load | Capacity | %Stressed | Δs * | Δelongation
3rd | (2) HDU2 | 1880 | 3075 | 0.876 | 0.108” | 0.147”
2nd | (2) HDU8 | 5923 | 6765 | 0.876 | 0.161” | 0.141”
1st | (1) HDU14 | 10854 | 14445 | 0.751 | 0.239” | 0.180”
Holdown Hardware Deflections
Level | Rod Diameter | Rod Length | Ae (in2) | Pu (lbs) | Δelongation
3rd | 5/8” | 30” | 0.226 | 1.4*1880 = 2631 | 0.012”
2nd | 5/8” | 30” | 0.226 | 1.4*5923 = 8293 | 0.038”
1st | 1” | 6” | All inclusive in ESR-2330 Table 1B footnote 9 |  | 
Rod Elongation Deflections
* Holdown Elongation values shown in ICC-ES ESR-2330 at strength levels. Deflection calculations should be at least strength level, so Δelongation is at strength level. ** Drod = PuL/AeE
DESIGN EXAMPLE SLIDE
Notes: Say
For the 1st portion of this term: Add up the elongation from the holdown hardware and the threaded rod that attaches the holdown to the foundation at the first floor and from floor to floor on the levels above. The holdown code report provides elongation values at both allowable load and strength load. Deflection should be calculated at strength level load.
Do
Review the slide.

## Slide 166: Holdown & Rod Deflections, cont.
Level | ΔHD_Elongation | ΔR_Elongation | ΣΔElongation
3rd | 0.147” | 0.012” | 0.159”
2nd | 0.141” | 0.038” | 0.179”
1st | 0.180” | - | 0.180”
Sum of Holdown & Rod Elongations
DESIGN EXAMPLE SLIDE
Notes: Do
Review the slide.

## Slide 167: Wood Shrinkage
Level | Plates | Plate Shrinkage | Joist Shrinkage | Δshrinkage
3rd | 2 | 0.072” | 0 | 0.072”
2nd | 3 | 0.108” | 0 | 0.108”
1st | 4 | 0.144” | 0 | 0.144”
From Breyer’s Design of Wood Structures, 6th Ed. pg. 148
Shrinkage (S) = (0.002)(d)(DMC)
Assume MCinitial = 19% and MCfinal = 7%
Shrinkage Calculations
S2X-Plate = (0.002)(1.5)(19-7) = 0.036
S16” TJI = Resist Shrinkage per manufacture
DESIGN EXAMPLE SLIDE
3rd (2 plates)
2nd (3 Plates)
& joist
1st (4 Plates)
& joist
Notes: Say
For the 2nd portion of this term: find the shrinkage at each floor perpendicular to grain for the plates and floor joists. The coupling take-up device would account for this shrinkage we have in this system.
Equation for calculating wood shrinkage:
S = D * M * C
S: Shrinkage, inches
D: Dimension, inches [d in our formula]
M: Change in moisture content, percent [DMC in our formula]
C: Shrinkage coefficient, 0.0020 for Western softwood species (including Redwood) except 0.0017 for Western Red Cedar [0.002 in our formula]

## Slide 168: Assembly Deflection
Level | Δelongation | Δshrinkage | h [ft] | b [ft] | Δassembly
3rd | 0.159” | 0.072” | 8 | 7 | 0.264”
2nd | 0.179” | 0.108” | 8 | 7 | 0.328”
1st | 0.180” | 0.144” | 8 | 7 | 0.370”
W/O TUD
W/ TUD
DESIGN EXAMPLE SLIDE
Level | Δelongation | Δshrinkage | h [ft] | b [ft] | Δassembly
3rd | 0.159” | 0 | 8 | 7 | 0.182”
2nd | 0.179” | 0 | 8 | 7 | 0.204”
1st | 0.180” | 0 | 8 | 7 | 0.205”
Notes: Say
If a take up device were utilized at each level there would not be any shrinkage – which makes up the majority of the deflection in this example. The assembly elongation would be a bit different if using the ATS, due to the rods going the full length of each level and the fact that there would not be any holdowns at each level (the coupling take-up device and rod work together to act as your holdown at each level).

## Slide 169: Total Story Deflection / Drift
Level | Δbending | Δfastenerslip&shear | Δassembly | Δstory
3rd | 0.008 | 0.265 | 0.264 | 0.538”
2nd | 0.014 | 0.301 | 0.643 | 0.643”
1st | 0.010 | 0.363 | 0.743 | 0.743”
Level | Δbending | Δfastenerslip&shear | Δassembly | Δstory
3rd | 0.008 | 0.265 | 0.182 | 0.456”
2nd | 0.014 | 0.301 | 0.204 | 0.520”
1st | 0.010 | 0.363 | 0.205 | 0.578”
Without Take-Up Device
With Take-Up Device
DESIGN EXAMPLE SLIDE
Notes: Say
Adding up all 3 terms to find our total deflection at each level we can see that the system without the take up device deflects a lot more than the system with the take-up device, in fact over three levels it deflects a half inch or less!

## Slide 170: Story Drift Limitation
ASCE 7-10 Equation 12.8-15
Cd = 4 (ASCE 7-10 Table 12.2-1)
δx_allowable = 0.025hsx (ASCE 7-10 Table 12.12-1)
hsx = Story height above level x (in)
Notes: Say
The allowable story drift is limited by Table 12.12-1. The deflection at each level is 4 x the elastic deformation for our light-framed shear wall structure. The deflection we have been calculating on the previous slides is the elastic deformation at each story.

## Slide 171: Total Story Deflection
Level | δstory | 4(δ) | δ Allow. | δ ≤ δ Allow.
3rd | 0.538 | 2.152 | 2.4 | Yes
2nd | 0.643 | 2.573 | 2.4 | No *
1st | 0.743 | 2.972 | 2.4 | No *
Level | δstory | 4(δ) | δ ≤ Allow. | δ ≤ δ Allow.
3rd | 0.456 | 1.823 | 2.4 | Yes
2nd | 0.520 | 2.079 | 2.4 | Yes
1st | 0.578 | 2.314 | 2.4 | Yes
* Increasing the post size, lumber grade, lumber species, or the use of sheathing are
all changes that could bring these floors into compliance
With Take-Up Device
Without Take-Up Device
Notes: Say
Our allowable story drift is 2.4”, the top level of our design example is within the limits, but it would not work for the bottom two floors using standard holdowns at each level. However, it would work at all levels if the same example structure is designed using an anchor tiedown product with a take-up device at each level.

## Slide 172
Now that you’ve complete this lesson, you should be able to:
Summarize methods to calculate and resist seismic story drift

## Slide 173: Course Summary of Part One
Code Provisions
Layout of 2015 IBC and ASCE 7-10
Changes and updates to 2015 IBC and ASCE 7-10
Seismic Design Parameters
SS and S1
Fa and FV
Structural Irregularities
Horizontal Structural Irregularities
Vertical Structural Irregularities
Scope of seismic analysis
Seismic provisions exceptions
Site Class
SMS and SM1
SDS and SD1
Risk Category
Seismic Design Category
Calculation Examples
Notes: Say
We’ve covered quite a bit of material today.
Initially we reviewed the code provisions for seismic design located in ASCE 7-10 and the 2012 IBC. Although the ASCE 7-10 reference standard has most of the information required for the seismic design and analysis, always remember to reference the 2012 IBC first.
We talked about the updates to ASCE 7 and IBC, such as the new seismic ground maps, the introduction of “Risk Categories”, and how the way designers use factors for systems and design has been revised. We also touched upon the scope and exceptions for seismic design put forth by ASCE 7.
We learned how to find the parameters necessary for determining a Seismic Design Category by referencing our code books. After doing it the hard way, we took a spin at using the convenient Seismic Design Tool available on the USGS website.
Regardless of which method you prefer, it is essential to know how to find the SDC and to understand the purpose of all the seismic design parameters. The SDC can help us to determine:
Permissible structural system
Limitations on height and irregularity
Components of the structure that must be designed for seismic forces
Types of lateral force analysis that may be used
Structural material detailing
Special inspection requirements
Structural observation requirements
Finally, we took a look at the ten major types of structural irregularities to show us what to be mindful of when designing to combat seismic activity.

## Slide 174: Course Summary of Part Two
Design Base Shear
Seismic Base Shear Equation
Period Determination
Distribution of Seismic Forces
Lateral Seismic Force Equation
Vertical Distribution Factor
Diaphragm Design
Load Distribution
Nailing, Roof Chords, and Shear Transfer
Redundancy Factor
Rigid vs. Flexible
Notes: Say
We reviewed the process for determining the Seismic Base Shear (v=CSW). This involved finding the total Effective Seismic Weight of our design example, which includes of the total dead load of our structure -- plus 25% of floor live loads, the total weight of operating equipment, and the actual partition weights. The second half of the Seismic Base Shear equation is known as the Seismic Response Coefficient. To determine this portion, we had to reference ASCE 7-10 to locate the Response Modification Factor and Importance Factor of our structure. We also had to find the building’s Approximate Period for the use an equation that shows whether our CS value is within range. By finding the Effective Seismic Weight and Seismic Response Coefficient, we were able to determine the Seismic Base Shear.
Continuing into the second lesson, we discussed the vertical and horizontal Distribution of Seismic Forces. We started with the Lateral Seismic Force calculation, which depicts the lateral seismic activity at any level. This equation multiplies our Seismic Base Shear (found in the first lesson) by a new term called the Vertical Distribution Factor, or Cvx.
Next we discussed the Redundancy Factor, which is used to increase the seismic load effect for structures with low redundancy. A factor of 1.0 is allowed to be used for eight conditions outlined in ASCE 7-10 Section 12.3.4.1. The most notable allowable condition is structures that are assigned to Seismic Design Category B or C. A Redundancy Factor of 1.3 is generally assigned to structures in SDC D, E, or F -- unless one of two conditions, outlined in Table 12.3-3, is met.
Finally, we talked about designing diaphragms that are able to withstand the shear and bending forces that are in response to seismic inertia. These designs take into consideration load distribution, nailing, roof chords, and shear transfer. As a final topic, we discussed the difference between rigid and flexible structures and how to determine which category our design example would fall within.
In Part 3 of Seismic Design for Wood Framed Construction, we’ll discuss Shear Wall Shear Design, Shear Wall Overturning Design, and Drift Analysis.

## Slide 175: Course Summary of Part Three
Shear Wall Shear Design
Strut Design
Shear Wall Design
Shear Wall Overturning Design
Overturning / Resistance
Load Combos
Drift Analysis
Story Drift
Deflection: Shear Wall, Bending, Fastener, Assembly, Holdown
Tension & Compression
Wood Shrinkage
Nailing Design
Shear Transfer
Sill Plates
Foundation Anchorage
Notes: Say
Here are a few of the topics we covered:
Drag Strut Design: Multiply the length of the longest drag strut by the design shear along the same line.
Segmented Shear Walls: This method of shear wall design does not allow for openings. Holdowns are required at each end of the shear wall.
Shear Wall Opening with Force Transfer Method: Openings are accounted for by strapping or framing based on a rational analysis. Requires additional detailing (blocking, nailing, strapping). This method is beneficial because it allows for openings while maintaining high shear capacity.
Perforated Shear Wall: Panel-sheathed wall with openings that aren’t designed with the force-transfer method. Instead, it uses sheathing above and below the wall openings. Relatively easy to construct if your design falls within the limitations.
Shear Wall Nailing Design: Use SDPWS Table 4.3A to find Allowable Shear for each level per panel grade, mail size, and nail spacing.
Floor-to-floor Shear Transfer: Bottom plate must be connected to floor truss or joist rim board or blocking. The trust or rim board must be connected to the top plate below.
--
Load Combinations: Updated to remove the self-straining loads T and to include the 0.6 wind load Strength to ASD reduction factor.
Exceptions for Vertical Seismic Load Effect: May be taken as zero if (a) Equations 12.4-1, 12.4-5, or 12.4-6 where SDS is equal to or less than 0.125, or (b) Equation 12.4-2 where determining demands on the soil structure interface of foundations.
Calculating Overturning Moment: Using Simple Statics, we found the correct overturning moment by multiplying the diaphragm forces by the correct height (or moment arm).
Calculating Resisting Moment: Using the dead load of the structure, we calculated the moment that would resist overturning.
Calculating Holdown Tension and End Stud/Post Compression Forces: Using equations that take into consideration the Resisting Moment and Overturning Moment, we calculated the holdown tension and end stud/post compression forces.
Sill Anchorage to Foundation: Use Strength design method for anchor bolts per ACI 318-11 Appendix D.
Sill Plate Splitting: Stud plate washers are required for shear walls. A hole in the plate washer is permitted to be diagonally slotted with a width up to 3/16” larger than the bolt diameter and a slot length not to exceed 1 ¾”.
--
Story Drift: Where ASD is used, the design story drift shall be computed using Strength Level seismic forces with reduction for ASD.
Deflection Amplification Factor: Determine by referencing ASCE 7-10 Table 12.2-1.
Allowable Story Drift: Determine by referencing ASCE 7-10 Table 12.12-1. Takes into consideration the Risk Category and the construction material.
Shear Wall Deflection: The deflection up to which the shear wall will maintain its structural integrity under design load conditions. Comprised of the sum of three terms: bending deflection, shear and fastener slip, and tie-down nail slip.
Anchorage Slippage: Also known as Tie-Down Nail Slip. Comprised of the sum of three terms: holdown slippage, rod elongation, and wood shrinkage.
Allowable Story Drift: Determined by Table 12.12-1.

## Slide 176: Course Completion
Simpson Strong-Tie
This concludes the continuing education course.
For a library of Simpson Strong-Tie courses,
visit strongtie.com/workshops
Notes: Do
Draw the meeting to a close. Hand out literature and business cards.
Say
If you have ongoing projects that you would be interested in reviewing together, please let me know.

## Slide 177: Next Steps!
AIA: For those seeking AIA LU/HSW: You will receive an email with a link allowing access to print your Certificate. Congratulations, you will have earned 3 LU/HSW credits. If your AIA member number has been inserted into your profile, Simpson Strong-Tie will report your credits on your behalf to the AIA. No test is required in order to receive HSW credits.
IACET: For those seeking IACET CEUs: You will receive an email with a link allowing access to print your Certificate of Attendance and instructions directing you to the Simpson Student Center to take the exam before credits can be awarded. Once the exam is taken and passed, you will have earned 0.3 CEUs (3 hours of credit). You can then access your Certificate of Completion from the Course Content tab. You must self-report your credits to your certifying organization or agency.
If you have questions or need assistance, please contact training@strongtie.com.
Notes: Presenter Notes:
Review the email and notification process as outlined in this slide.
AIA LUs:
For those that want AIA HSW credit, be sure to provide your AIA number on the sign-in sheet and Simpson will report your credits to the AIA on your behalf.
No test is required for AIA credit.
CEUs:
For those seeking CEUs, watch for an email with instructions to access the online test. After you have passed the test, you may access your Certification of Completion from the course content tab.
You must self-report your credits to your certifying organization or agency.

## Slide 178: Next Steps!
ICC: For those seeking ICC CEUs: You will receive an email with a link allowing access to print your Certificate. Congratulations, you will have earned 0.3 ICC CEU (3 hours of credit). Please make sure your ICC member number has been inserted into your profile. It is your responsibility to self-report your credits to the ICC. Please retain your Completion Certificate for your records.
IACET: For those seeking IACET CEUs: You will receive an email with a link allowing access to print your Certificate of Attendance and instructions directing you to the Simpson Student Center to take the exam before credits can be awarded. Once the exam is taken and passed, you will have earned 0.3 CEUs (3 hours of credit). You can then access your Certificate of Completion from the Course Content tab. You must self-report your credits to your certifying organization or agency.
If you have questions or need assistance, please contact training@strongtie.com.
Notes: Presenter Notes:
Review the email and notification process as outlined in this slide.
Watch for an email directing you to the Student Center to print your certificate.
No test is required for ICC credit. You must self-report your credits to ICC.
For those seeking general IACET CEUs after you have passed the online test, you may access your Certification of Completion from the course content tab. You must self-report your credits to your certifying organization or agency.