## Slide 1: BUILDER TRAINING SERIES
Code Requirements for Conventionally Framed Roofs
Notes: Welcome
Welcome to this course on Code Requirements for Conventionally Framed Roofs
Presented by Simpson Strong-Tie

## Slide 2: Credit Information
Professional Development Hours
Simpson Strong-Tie® offers Professional Development Hours for completing this course. No other continuing education or accredited credits are available for this course.
This course offers .5 PDH (1/2 hour of PDH credit).
Notes: Credit Information – Professional Development Hours
Simpson Strong-Tie offers Professional Development Hours for completing this course. No other continuing education or accredited credits are available for this course.

## Slide 3: Course Requirements
Pass the Class to Earn Personal Development Hours
READ & LISTEN
Read and listen to all course material in sequence
PASS ASSESSMENT
Pass the Final Assessment at the end of the course
EXERCISES
Complete the Knowledge Checks in the course
Notes: Course Requirements
To pass the class and earn Professional Development Hours, read and listen to all course material in sequence, complete the Knowledge Checks in the course, and pass the final assessment at the end of the course.

## Slide 4: About this Course
Technical course for Builders, Building Officials and Inspectors regarding code requirements for stick-framed roofs.
Reviews Chapter 8 (IRC) - conventionally framed roofing.
Course Learning Objectives
Upon completion of this training, you will be able to:
Describe basic components of conventional roof framing (eg hip and valley rafters, ridge boards, and ridge beams)
Identify the correct application of rafters, joists and other members
Recognize the relationship between critical connections and their role in building a stable roof
Identify correct application of IRC building codes for conventionally framed roof construction, also known as stick-framing
Notes: About this Course
Course Description
This is a technical course intended for Builders, Building Officials, and Inspectors interested in code requirements for stick-framed roofs. This course reviews Chapter 8 of the International Residential Code (IRC) as it applies to conventionally framed roofing.
Course Learning Objectives
Upon completion of this training, you will be able to:
Describe the basic components of conventional roof framing such as hip and valley rafters, ridge boards, and ridge beams; and identify the correct application of rafters, joists and other members
Recognize the relationship between critical connections and their role in building a stable roof
Identify correct application of IRC building codes for conventionally framed roof construction, also known as stick-framing

## Slide 5: Course Agenda
LESSON 1 Basic Concepts of Conventional Roofing
LESSON 2 Critical Connections in the Continuous Load Path (CLP)
LESSON 3 Conventional Roofing IRC Code Sections
Notes: Course Agenda
The topics covered in this course include the following:
Lesson 1 Basic Concepts of Conventional Roofing
Lesson 2 Critical Connections in the Continuous Load Path (CLP)
Lesson 3 Conventional Roofing IRC Code Sections

## Slide 6
Code Requirements for Conventionally Framed Roofs
LESSON 1
Basic Concepts of Conventional Roofing
Notes: LESSON 1: Basic Concepts of Conventional Roofing
This lesson introduces basic wood roof systems, framing members, and concepts

## Slide 7: IRC Chapter 8
Roof-Ceiling Construction
The International Residential Code (IRC) and the International Building Code (IBC) define guidelines for building conventional light-frame wood structures without the need for engineering analysis of each component (prescriptive framing).
This prescriptive approach (Conventional Construction) is used in stick-frame roof systems.
Notes: IRC Chapter 8
Roof-Ceiling Construction
The International Residential Code (IRC) and the International Building Code (IBC) define guidelines for building conventional light-frame wood structures without the need for engineering analysis of each component, also known as prescriptive framing. The construction style following prescriptive approaches is called Conventional Construction and is used in stick-frame roof systems.

## Slide 8: Framing Design Variety
Consistent Design
Houses are never perfectly symmetrical boxes.
Design choices will be different to accommodate taste, location, and environment.
Variety of Design
Conventional framing has a “cookbook” building approach.
The code supplies the guidance, or “recipe” for various construction applications.
However, it only defines the minimum requirements.
Conventional Framing
Notes: Framing Design Variety
Convetional Framing
In a perfect world, all residential construction would consist of perfectly symmetrical boxes. In reality, choices need to accommodate a variety of different designs, based on taste, location, and environment.
Conventional framing has developed a cookbook building approach, in which the code supplies the recipe for various construction applications. However, while the code provides guidance, it only defines the minimum requirements.

## Slide 9: Two Wood Roof Construction Methods
Truss Roof System
Truss Roof Systems - prefabricated trusses placed at a prescribed spacing.
Constructed at a component manufacturer in a controlled environment.
Consistent quality control and quick installation.
Stick-Frame Roof System
Stick-Frame Systems - repetitive rafters & ceiling joists.
Constructed onsite according to prescriptive code requirements.
Allows for roofline flexibility, more complex framing, provides usable attic or living space.
Truss System vs. Stick-Framed Roof System
Notes: Two Wood Roof Construction Methods
Truss System vs. Stick-Framed Roof system
The two most common wood roof construction types are a Truss Roof System and a Stick-Frame Roof System. Both approaches are widely used today. Even though stick-framing has been around the longest, today four out of five new homes built in the U.S. use truss roof systems
Truss Roof Systems are prefabricated trusses placed at a prescribed spacing. Roof trusses are constructed at a component manufacturer in a controlled environment, resulting in consistent quality control and quick installation.
Stick-Frame Systems consist of repetitive rafters and ceiling joists constructed onsite according to prescriptive code requirements. Stick-framing allows for more flexibility of the roofline and more complex framing applications. In addition, stick-framing provides a usable space within the structure for attic storage or living area.
This course focuses on prescriptive stick-framed construction.
Student Handout Material

## Slide 10: Types of Roofs
Consideration for Climate, Style, and Preferences
Gable
Flat
Hip
Shed
Combination
Mansard
Gable with Dormer
Gambrel
The roof protects the structure and inhabitants.
Roofs consider climate, style and design preferences.
Notes: Types of Roofs
Consideration for Climate, Style, and Preferences
The primary job of a roof is to protect the structure and inhabitants, with consideration for climate, regional style, and design preferences. There is a variety of different roof shapes. The four basic roof shapes are Gable, Flat, Hip, and Shed. Different designs can be built off these four shapes. For example, the mansard is a hip roof with a flat top and a gambrel is a gable with an added bend.

## Slide 11: Ridge Beam and Ridge Board
Ridge Beam
A ridge beam holds up the rafters. The ridge beam is a structural member that supports the weight of the rafters and must be specifically designed for the project.
Ridge Board
A ridge board is held up by the rafters. The ridge board is a non-structural member that does not support the weight of the rafters, instead they are held up by the force of opposing rafters. The board provides a nailing surface and can be a 1x as it is non-structural.
Two Types of Ridge Connections
Notes: Ridge Beam and Ridge Board
Two Types of Ridge Connections
There are two types of ridge connections, a ridge beam and a ridge board.
A ridge beam holds up the rafters. The ridge beam is a structural member that supports the weight of the rafters and must be specifically designed for the project.
A ridge board is held up by the rafters. The ridge board is a non-structural member that does not support the weight of the rafters, instead they are held up by the force of opposing rafters. The board provides a nailing surface and can be a 1-by since it is non-structural.
Student Handout Material

## Slide 12: Valley and Hip Rafters
Roof Load Support
Valley rafters follow the line of the valley, where two perpendicular sides of the roof meet.
Hip rafters form the angles at the junction of inclined planes of the roof.
Valley Rafter
Area of roof supported by Valley Rafter
Hip Rafter
Area of roof supported by Hip Rafter
Hip
Valley
External View
Notes: Valley and Hip Rafters
Roof Load Support
Valley rafters follow the line of the valley, where two perpendicular sides of the roof meet. Valley rafters are structural members, which need to be deeper than common rafters because they support a greater load and provide full bearing for the rafter ends, also called jack rafters.
Click: The single valley rafter supports the shaded area of the roof.
Hip rafters form the angles at the junction of inclined planes of the roof. Hip rafters attach to a ridge with the brace landing on a wall.
Click: The Hip rafter supports the shaded area of the roof.
Student Handout Material

## Slide 13: Roof Pitch and Slope
Pitch 12:12
Flat
Pitched
Notes: Roof Pitch and Slope
Roofs can be flat or pitched, with varying levels of steepness, shown in this grid. Knowing the slope of the roof is important, since code requirements for conventionally framed roofs differ depending on the slope.
Click: The slope on this home is 12 for each side, stated 12:12.

## Slide 14: Check Your Knowledge
Which roof shape is NOT ideal for high snow areas?
Gable
Hip
Flat
Shed
Notes: Check Your Knowledge

## Slide 15
Code Requirements for Conventionally Framed Roofs
LESSON 2
Critical Connections in the Continuous Load Path (CLP)
Notes: LESSON 2: Critical Connections in the Continuous Load Path (CLP)
This lesson discusses how connections through a structure create a continuous load path to counteract the impact of wind and other forces on the structure

## Slide 16: Critical Connections & Code
Conventionally Framed Roofs - the prescriptive code is often applied to areas where connection points meet (shown here, 2015 IRC).
To understand code applications, the following slides review:
Continuous load path connections.
Continuous ties.
Four code-compliant roof cases.
For SI: 1 inch = 25.4 mm, 1 foot = 305 mm, 1 degree = 0.018 rad. Note: Where ceiling joists run perpendicular to the rafter, rafter ties shall be installed in accordance with Section R802.3.1.
HC = Height of ceiling joists or rafter ties measured vertically above the top of rafter support walls.
HR= Height of roof ridge measured vertically above the top of the rafter support walls.
FIGURE R802.5.1 BRACED RAFTER CONSTRUCTION
Notes: Critical Connections & Code
Code requirements define standards for safer construction practices. For Conventional Roof Framing the prescriptive code is often applied to areas where there will be connection points as shown here in Figure R802.5.1 from the 2015 IRC.
To understand the code applications, the following slides review the critical connections with a focus on the continuous load path and continuous ties, and a review of four code-compliant roof cases.

## Slide 17: Continuous Load Path
The continuous load path is a construction method using framing, connectors and fasteners to transfer all loads from where they act on the structure to the ground.
Notes: Continuous Load Path
Click: The continuous load path is a construction method using framing, connectors, and fasteners to transfer all loads from where they act on the structure to the ground.
Click: Wind pressures create forces that challenge the integrity of a structure when the simultaneous application of loads occurs in multiple directions. These loads must be transferred through resisting elements in the structure, which requires a series of connections from the roof and walls to the foundation, creating a continuous load path.
Student Handout Material

## Slide 18: Wind Forces
Vertical Force
Horizontal Force
Vertical wind pressure can create uplift forces strong enough to lift the roof off the structure or lift the entire structure.
This is called uplift.
Horizontal wind pressure can cause lateral overturning, racking, and sliding failures. These multi-directional forces can damage buildings.
Notes: Wind Forces
Wind forces act on a structure with vertical force and horizontal force. The building stability depends on the capability of the structure to resist forces, and carry the loads created by forces without moving or breaking.
Vertical Forces
Vertical wind pressure can create uplift forces strong enough to lift the roof off of the structure, or lift the entire structure. This is called uplift.
Horizontal Forces
Horizontal wind pressure can cause lateral overturning, racking, and sliding failures. Without proper design and construction, these multi-directional forces can produce building damage.

## Slide 19: Continuous Tie System
Live load forces (eg, people, snow etc) also act on a structure.
To withstand and resist rafter thrust that can happen when live loads are applied, a roof joist-to-rafter and joist-to-joist connection is developed to create a continuous tie along the joist span.
Notes: Continuous Tie System
Live load forces also act on a structure, such as people, snow, or other environmental forces.
Click: To withstand and resist rafter thrust, that can happen when live loads are applied, a roof joist-to-rafter and joist-to-joist connection is developed to create a continuous tie along the joist span.
Student Handout Material

## Slide 20: Code Compliant Conventional Roof Cases
Parallel Rafters and Ceiling Joist Connection with Collar Ties
Parallel Rafters with Rafters Ties
Rafters and Ridge Beam
Perpendicular Rafters
with Rafter Ties
Stick-framed roof construction is complicated
Specialized crews are required.
Code requirements for stick-framing roofs have become more complex.
Meeting IRC roof framing code requires builders to construct simple triangles using the rafters and ceiling joists.
Triangles are a stable geometric shape.
To maintain the shape, specific requirements show how to fasten the triangle corners together.
Notes: Code Compliant Conventional Roof Cases
Constructing a stick-framed roof is not always easy. For example, in Texas where stick-framing is common, there are entire crews specializing only in roof framing. Due in part to the growing size of houses and the increased complexity of roofs, code requirements for stick-framing roofs have become more complex.
Meeting current IRC roof framing requirements requires builders to construct very simple triangles using the rafters and ceiling joists, because triangles are known to be the most stable geometric shape. In order to maintain the triangle shape, there are specific requirements on how to fasten the corners of the triangle together.
The following slides review four different roof cases for conventional roof framing and the end of the section includes the IRC code table for the connection fastening requirements.

## Slide 21: Parallel Rafters with Rafter Ties
Table R802.3(1)
Where ceiling joists are not connected to the rafters at the top wall plate, joists connected higher in the attic shall be installed as rafter ties, or rafter ties shall be installed to provide a continuous tie.
Ridge Board
Rafter to Top Plate
Rafter to Rafter Tie
Rafter to Collar Tie
*Fastening intentionally left off
**Collar tie or ridge strap shown per code requirement from fastening Table R602.3(1)
Notes: Parallel Rafters with Rafter Ties
The first case is parallel rafters with rafter ties.
In this rafter system, the builder omits the joists at the base of the roof, resulting in increased height in the ceiling area. Since joists are not installed at the top wall plate, rafter ties must be installed, as noted here in R802.3.1.
It is important to note that rafter ties and collar ties are not the same product and are not interchangeable. Rafter ties are located in the bottom third of the attic and provide a tension tie, helping keep the roof and walls together. Collar ties are located only in the upper third of the attic, helping keep the rafters together at the ridge and resist uplift or unbalanced loads. If there is no collar tie, then ridge straps are required. The important connections for code compliance is the ridge board, the rafter to collar tie, rafter to rafter tie, and rafter to top plate.

## Slide 22: Perpendicular Rafters and Rafter Ties
Where ceiling joists are
not parallel to rafters, rafter ties shall be installed.
Table R802.3(1)
Ridge Board
Rafter to Rafter Tie
Joist to Top Plate
Rafter to Top Plate
*Fastening intentionally left off
**Collar tie or ridge strap shown per code requirement from fastening Table R602.3(1)
Notes: Perpendicular Rafters and Rafter Ties
The second case is perpendicular rafters and rafter ties.
When ceiling joists are perpendicular to rafters then rafter ties should be installed to complete the simple triangle. The rafter-to-rafter-tie fastening is factored from the rafter to joist connection.
A proper triangle shape allows easier securing of the ridge board because all the weight of the roof is assumed to transfer down to the bearing at the top plate. The nonstructural ridge board can consist of 1-by lumber. In this case, there is a ridge strap instead of a collar tie, which meets the IRC code requirement. The important connections for code compliance are the joist to top plate and rafter to top plate.

## Slide 23: Parallel Rafters and Ceiling Joist Connection
Ceiling joists and rafters shall be nailed to each other in accordance with Table R802.5.1(9), and the rafter shall be nailed to the top wall plate in accordance with Table R602.3 (1).
Table R802.3(1)
Ridge Board
Collar Tie
Joist/Rafter
Rafter to Top Plate
Joist to Top Plate
*Fastening intentionally left off
**Collar tie or ridge strap shown per code requirement from fastening Table R602.3(1)
Notes: Parallel Rafters and Ceiling Joist Connection
The next case is the parallel rafters and ceiling joist connection.
This is a common case for a stick-framed roof rafter system. The parallel rafter and joists are attached to each other. A collar tie is installed in the upper third of the attic space. The stable triangle is made from the rafter/joist, rafter to ridge, and top plate connection. The continuous tie between the joist/rafter connection keeps the walls together and prevents rafter thrust.

## Slide 24: Rafters and Ridge Beam Connection
Table R802.3(1)
Where ceiling joists or rafter ties are not provided, the ridge formed by these rafters must be supported by a wall or girder.
Ridge Board
Rafter to Top Plate
*Fastening intentionally left off
**Collar tie or ridge strap shown per code requirement from fastening Table R602.3(1)
Notes: Rafters and Ridge Beam Connection
The final case is the rafters and ridge beam connection.
In this case the ceiling joists that form the bottom leg of the triangle might not be present or might not connect rafters together, such as in cathedral or vaulted ceilings. The load-resisting concepts of the vaulted ceiling are unique. Without the tie at the bottom, the rafters must be supported at their upper ends to prevent rafter thrust at the lower end. Since half the load is now supported at the ridge, the ridge member becomes a load bearing ridge beam and must be designed to bridge the span between the supports, which carry the vertical load to the ground. This requires a secure connection of the rafters to the ridge beam, which must be supported by a wall or girder. In this example, ridge straps are also installed to prevent uplift.

## Slide 25: Table R602.3(1)
FASTENING SCHEDULE FOR ROOF CEILINGS
Notes: Table R602.3(1)
Table R602.3.1 lists fastening requirements for roof-ceilings that applies to all four cases and is provided here for reference

## Slide 26: Check Your Knowledge
The continuous load path is a construction method using framing, connectors and fasteners to transfer all loads from where they act on the structure to the ground.
True
False
Notes: Check Your Knowledge

## Slide 27
Code Requirements for Conventionally Framed Roofs
LESSON 3
Conventional Roofing IRC Code Sections
Notes: Lesson 3: Conventional Roofing IRC Code Sections
This lesson cites IRC code sections that apply directly to Conventionally Framed Roof construction.

## Slide 28: Code Topics
Prescriptive Wood Roof Framing
IRC, Chapter 8, Section R802
  Grade mark, size, and identification
  Design and Construction
        Framing details
        Ceiling joist/rafter connections
        Ceiling joists lapping
  Fastening requirements
  Ceiling joist and rafter span
  Bearing
  Cutting & notching
  Lateral support
  Bridging
  Framing of openings
10. Wood Trusses
11. Roof Tie-Down
This lesson focuses on the code sections applicable to Building Inspectors, Building Officials, and Builders.
Notes: IRC Chapter 8 Roof-Ceiling Construction
The prescriptive wood roof framing topics in this course focus on the IRC, Chapter 8, Section R802. This lesson cites the specific code for Conventionally Framed Roof Construction, focusing on the parts applicable to Building Inspectors, Building Officials, and Builders. Review the IRC, Chapter 8, Section R802 topics on the right before proceeding.

## Slide 29: R802.2 Design and Construction
The framing details required in Section R802 apply to roofs having a minimum slope of three units vertical in 12 units horizontal (25-percent slope) or greater. Roof-ceilings shall be designed and constructed in accordance with the provisions of this chapter and Figures R606.11(1), R606.11(2) and R606.11(3) or in accordance with AWC NDS. Components of roof-ceilings shall be fastened in accordance with Table R602.3(1).
1
Notes: R802.2 Design and Construction
R802.2 contains several instructions for roof framing details.
The first section states that framing details apply to roofs with a minimum slope of 3:12
The middle section of the code focuses on concrete and masonry, which is not a focus of this course.
The final section discusses component fastening of roof-ceilings, which was discussed in the previous lesson and will be reviewed later in the course.
Take a moment to read the entire code before proceeding.
Student Handout Material

## Slide 30: Roof Slope
When the roof slope is lower, ridge and rafters work like a joint, instead of a stable structure.
Roof Slope 3:12
Roof Slope
The framing details in section R802.2 apply to roofs with a minimum slope of 3:12. Roofs with higher rafter slopes and parallel joists are built to be a rigid triangle. When the roof slope is lower, the ridge and rafters work like a joint, instead of a stable structure. This changes the load dynamics that would no longer fit the prescriptive requirements.
Notes: Roof Slope
The framing details in section R802.2 apply to roofs with a minimum slope of 3:12. Roofs with higher rafter slopes and parallel joists are built to be a rigid triangle.
Click: When the roof slope is lower, the ridge and rafters work like a joint, instead of a stable structure. This changes the load dynamics that would no longer fit the prescriptive requirements.

## Slide 31: Slope and Skew Calculator
Calculators help determine the roof slope and skew, direction and angles for framing members and connections
Simpson Strong-Tie’s calculator shown right.
Notes: Slope and Skew Calculator
Some manufacturers offer web tools to help determine the roof slope and skew, such as this one on the Simpson Strong Tie website. Calculator applications are useful tools for defining the direction and precise angles for framing members and connectors.

## Slide 32: R802.3 Framing Details
2
Rafters shall be framed not more than 1½-inches offset from each other to ridge board or directly opposite from each other with a gusset plate as a tie.
Ridge board shall be not less than 1-inch nominal thickness and not less in depth than the cut end of the rafter.
Notes: R802.3 Framing Details
R802.3 addresses several additional framing details regarding the ridge board. The first section states the rafter offset should be not more than 1 ½ inches and the second section states the ridge board should not be less than 1 inch nominal thickness.
Take a moment to read the entire code before proceeding.
Student Handout Material

## Slide 33: Ridge Board
Ridge Board
Ridge Board
Ridge board shall not be less in depth than the cut end of the rafter. Rafters shall be framed not more than 1½" offset from each other.
Notes: Ridge Board
The ridge board is a non-structural member that keeps the opposite ends of the rafters in place. The rafters push against each other and keep the roof shape stable.
The code states the ridge board depth should not be less than the end of the rafter. The code also states that rafters should be framed not more than 1½-inches offset. Rafters set too far apart create a weak construction, as shown in the image on the left.

## Slide 34: R802.3 Framing Details
2
At valleys and hips there shall be a valley or hip rafter not less than 2-inch nominal thickness and not less in depth than the cut end of the rafter.
Hip and valley rafters shall be supported at the ridge by a brace to a bearing partition or be designed to carry and distribute the specific load at that point.
Where the roof pitch is less than 3:12 units horizontal structural members that support rafters and ceiling joists — such as ridge beams, hips and valleys — shall be designed as beams.
Notes: R802.3 Framing Details
The IRC requirements for hip and valley rafters are:
Valley and Hip rafters should be at least 2 inches thick
Hip and valley rafters should be supported by a brace to a bearing partition or be designed to carry a specific load at that point
If the roof is less than 3:12 all members that support rafters and ceiling joists should be designed as beams
Student Handout Material

## Slide 35: Valley Rafters
Valley Rafter
Valley Rafter
Nominal thickness of 2 inches. Not less depth than the cut end of the rafters.
Notes: Valley Rafter
Unlike non-structural ridge boards, valley rafters are structural members. As a structural member, they need to be deeper than rafters because they support more load and provide full bearing for the rafter tails. In this image, the valley is deeper than the cut-end of the jack rafter.

## Slide 36: Valley and Hip Rafters
Valley and Hip Rafters
Hip and valley rafters are load bearing structural members. Hip Jacks can benefit from additional support from manufactured components.
Notes: Valley and Hip Rafters
Hip rafters are also load bearing structural members that support smaller hip jack rafters. These installations can be difficult because the rafter is angled. As a result, manufacturers provide sloped and skewed hanger connectors. Since the hip is supporting the hip jacks, consider additional support for hip jack connections.

## Slide 37: Valley and Hip Rafters
Valley and Hip Rafters
Valley and hip rafters should be supported by a brace to a bearing partition or be designed to carry a specific load at that point.
Notes: Valley and Hip Rafters
Hip and valley rafters should be supported by a brace to a bearing partition or designed to carry a specific load at that point. Hip rafters need to have braces at the upper ends. If this is not possible then an engineered connection is required to the supported ridge beam. Connecting hip and valley rafters to ridge beams can be challenging. In some cases, attaching multiple members to the end of the ridge would require so many nails it could cause the ridge to split.

## Slide 38: Ridge Beam
Ridge Beam
Ridge Beam
Where the roof pitch is less than 3:12, structural members shall be designed as beams.
Notes: Ridge Beam
When the roof pitch is low, the rafters act as a simple span between the exterior wall and the ridge, so the rafter must be supported on both ends. The ridge beam is a structural member supporting the rafters. Ridge beams are thicker members and must designed for the project. They are structural members that carry loads and in this case transfer the loads to post or walls.

## Slide 39: R802.3.1 Ceiling Joists and Rafter Connections
3
Ceiling joists and rafters shall be nailed to each other in accordance with Table R802.5.1 (9), and the rafter shall be nailed to the top wall plate in accordance with Table R602.3 (1).
Ceiling joists shall be continuous or securely joined in accordance with Table R802.5.1 (9) where they meet over interior partitions and are nailed to adjacent rafters to provide a continuous tie across the building when such joists are parallel to the rafters.
Notes: R802.3.1 Ceiling Joists and Rafter Connections
This section of the code specifies the requirements for ceiling joist and rafter connections, referencing two different connection tables:
Table R802.5.1(9) shows the fastening requirements for the joist/rafter connection.
Table R602.3(1) details the other required fastenings for general roof construction connections
Please read the entire code before proceeding.
Student Handout Material

## Slide 40: Continuous Tie
Ridge Board
Rafter
Joist
compression
tension
Notes: Continuous Tie
Critical connections in the rafter system are the joist-to-rafter and joist-to-joist combination. These connections create a continuous tie. The rafters and ceiling joists act as a rigid triangle, which is the most stable shape to withstand rafter thrust.
Click: Rafter thrust can occur when environmental loads such as snow, or live loads such as people are applied to the structure.

## Slide 41: Fastening Table R802.5.1(9)
Notes: Fastening Table R802.5.1(9)
The connection between the rafter and joist is prescribed in Table R802.5.1(9). Newer requirements require a lot more nails to fasten joists-to-rafters and joist-to-joist lap connections.
In this example, a 7:12 roof slope, with rafters spaced 24” on center, with a 20 psf ground snow load will require nine 16d common nails for fastening the rafter to the joist.

## Slide 42: Fastening Table R602.3.1
Notes: Fastening Table R602.3.1
The requirements for the ceiling joist to top plate, joist/rafter connection, and rafter to top plate are highlighted on this fastening table.
Click: After the rafters are connected to the joists, fastening the rafter on both sides would be difficult to implement. A footnote on the table addresses the issue.

## Slide 43: Rafter and Joist Fastening Connection
Table R602.3.1*
Three 10d nails rafter to plate. Two on one side, one on the other.
Table R802.5.1(9)
Where the roof pitch is less 3:12 structural members will be designed as beams.
Table R602.3.1
Four 8d nails ceiling joist to top plate connection.
*Footnote i
The toe nail on opposite side of rafters is not required when there is a parallel joist/rafter connection.
Notes: Rafter and Joist Fastening Connection
This is an example of the joist/rafter fastening with the parameters of a 7:12 pitch and a 36 ft span. Table 802.5.1.(9) requires nine 16d nails. Table R602.3.1 requires three nails from rafter to top plate. In addition, four nails are required for the ceiling joist to top plate connection.
Click: Based on Footnote i. one nail facing the rafter on the joist side can be omitted.

## Slide 44: Continuous Tie Fail
Notes: Continuous Tie Fail
The rafters and joists in this image are offset and are not fastened together. When the rafter joist connection isn’t made, the roof doesn’t have a continuous tie, resulting in a less safe structure.

## Slide 45: R802.5.1(9) Footnotes
a. 40d box nails shall be permitted to be substituted for 16d common nails.
b. Nailing requirements shall be permitted to be reduced 25 percent if nails are clinched. (the pointed ends of nails are bent over).
c. Heel joint connections are not required when the ridge is supported by a load-bearing wall, header or ridge beam.
d. When intermediate support of the rafter is provided by vertical struts or purlins to a load bearing wall, the tabulated heel joint connection requirements shall be permitted to be reduced proportionally to the reduction in span.
e. Equivalent nailing patterns are required for ceiling joist to ceiling joist lap splices.
f. When rafter ties are substituted for ceiling joists, the heel joint connection requirement shall be taken as the tabulated heel joint connection requirement for two-thirds of the actual rafter-slope.
The following are exceptions to the nail requirements:
Notes: Table R802.5.1(9) Footnotes
Several footnotes in the table allow for nail requirement reductions.
A few footnotes are highlighted on the next slides. Take a moment to read these footnotes before proceeding.

## Slide 46: Table R802.5.1(9) Footnote: d
Nailing Reduction
Footnote d. allows for a reduction in the nailing. Intermediate support provided by purlins or vertical struts allows a reduction in span.
Notes: Table R802.5.1(9) Footnote d
Purlins or vertical struts reduce the nailing on the rafter/joist and joist-to-joist lap connections, because it shortens the span value in the table. A purlin at 10 ft. for a 24 ft. span, can reduce the fastening to 14 ft.
-----
d. When intermediate support of the rafter is provided by vertical struts or purlins to a load bearing wall, the tabulated heel joint connection requirements shall be permitted to be reduced proportionally to the reduction in span.

## Slide 47: R802.5.1(9) Footnote: e
R802.5.1(9) - Lapped Joists
Footnote e. lapped joists have the same nailing requirement as the rafter/joist connection.
R802.3.2 - Lapped Joists
Where ceiling joists are providing resistance to rafter thrust, lapped joists shall be nailed in accordance with R802.5.1(9).
Notes: R802.5.1(9) Footnote : e
Footnote e refers to lapped ceiling joists. The joist-to-joist splice over walls has to be fastened with the same requirements as the joist rafter connection. In this example that would be nine nails.
R802.3.2 states where ceiling joists are providing resistance to rafter thrust, lapped joists shall be nailed in accordance with R802.5.1(9)
Ceiling joists parallel to and attached to rafters require lap splices nailed per Table R802.5.1(9). Perpendicular joists that do not resist thrust can be nailed in accordance with R602.3.1.
-----
Table R802.5.1(9)
e. Lapped joists have the same nailing requirement as the rafter/joist connection

## Slide 48: Table R802.5.1(9) Footnote: h
Footnote h. Tabulated heel joint connection requirements assume that ceiling joists or rafter ties are located at the bottom of the attic space. Where ceiling joists or rafters are located higher in the attic, heel joint connection requirements shall be increased as follows:
Rafter Tie
Notes: Table R802.5.1(9) Footnote: h
Footnote h applies to the fastening on rafter ties. Rafter ties are installed in the lower third of the attic space when there is NOT a tension tie along the base. This requirement is the joist and rafter connection listed in Table R802.5.1(9) multiplied by the factor in the table.
For example, 1/6 of the way up results in a requirement to increase that fastening by 1.2. If we apply this to our previous fastening requirement of nine nails, the requirement would increase to eleven nails.
Rafter ties should not be confused with collar ties that are positioned in the upper third of the rafters.
-----
Table R802.5.1(9)
h. Where ceiling joists or rafter ties are located higher in the attic, heel joint connection requirements shall be increased as follows:

## Slide 49: R802.3.1 Ceiling Joists and Rafter Connections Rafter Tie
3
Where ceiling joists are not connected to the rafters at the top wall plate, joists connected higher in the attic shall be installed as rafter ties, or rafter ties shall be installed to provide a continuous tie.
Rafter ties will not be less than 2 inches by 4 inches, installed in accordance with the connection requirements in Table R802.5.1(9), or equivalent capacities shall be provided.
Notes: R802.3.1 Ceiling Joists and Rafter Connections
Rafter Tie
The IRC code specifies requirements for Rafter Ties as follows:
When there are no joists at the top plate, joists are installed in the lower third of the rafter as rafter ties.
Rafter ties are in tension and provide a continuous tie
Rafter Ties will not be less than a 2 x 4 and installed with the connections requirements in Table R802.5.1(9)
Read the entire code section before continuing.
Student Handout Material

## Slide 50: Ceiling Joists and Rafter Connections
Ceiling Joists and Rafter Connections
Joists need to make a tension connection across beams when rafters and joists are parallel. Use straps and/or sheathing to create a continuous tie. Hangers alone do not provide a tie.
Notes: Ceiling Joists and Rafter Connections
When joists do NOT span the entire length of a roof, they do NOT create a continuous tie, unless they are fastened or connected together. The joists are in tension. Use straps and/or sheathing to create a continuous tie. Hangers alone do not help provide a continuous tie because they are not rated for tension.

## Slide 51: Rafter Ties
Rafter Ties
Ceiling joist and rafter ties prevent walls from spreading under downward loads. Joists that are not installed at the plate level are Rafter Ties. Rafter Ties are used to transfer tension across ceiling.
Notes: Rafter Ties
When there are no joists at the top plate, joists are installed in the lower third of the rafter as rafter ties. Rafter Ties are used to transfer tension across the ceiling and prevent walls from spreading under downward loads. The joist may be the rafter tie when it is installed above the plate level.

## Slide 52: Rafter Ties with Perpendicular Joists
Rafter Ties
Rafter Ties
Rafters with perpendicular joists require a Rafter Tie. Spacing is now the same as rafters at a maximum of 24”. Rafter ties are located in the lower third of attic space.
Notes: Rafter Tie with Perpendicular Joists
Rafters with perpendicular joists require a rafter tie in order to resist thrust. Where rafters are oriented perpendicular to the ceiling joists, rafter ties should be installed just above the ceiling joists, providing a tension tie. The code allows rafter ties to be raised up to 1/3 the total vertical height of the roof.
Rafter ties need to be spaced 24 in. on center and should not be less than 2 by 4.

## Slide 53: Continuous Tie Example
Ties spaced > 48” o.c and not adequately connected to lookout
Lookout
Straps
Continuous Tie
Lookout nailed to rafters. Metal straps connects lookouts to joists across floor.
Notes: Continuous Tie Example
In this image a lookout has been added, but there is too much distance between the ties, spaced more than 48” on center. Even if the joists are perpendicular, a continuous tie is still achievable. To create a continuous tie with this configuration use metal straps across joists. Nail straps will have an equivalent nailing with Table R802.5.1(9)

## Slide 54: R802.3.1 Ceiling Joists and Rafter Connections Ridge Beam and Collar Ties
3
Where ceiling joists or rafter ties are not provided, the ridge formed by these rafters shall be supported by a wall or girder designed in accordance with accepted engineering practice.
Collar Ties or ridge straps to resist wind uplift shall be connected in the upper thirds of the attic space in accordance with Table R602.3(1).
Collar ties shall be not less than 1 inch by 4 inches, spaced not more that 4 feet o.c.
Notes: R802.3.1 Ceiling Joists and Rafter Connections Ridge Beam and Collar Ties
The next section of IRC code addresses the use of a ridge beam and collar ties as follows:
When there are no ceiling joists or rafter ties, the ridge must be supported by a wall or girder (ridge beam)
Collar ties or ridge straps to resist wind uplift are installed in the upper thirds in accordance with Table R602.3.1
Collar ties cannot be less than 1 x 4 and spaced 4 feet o.c.
Read each section of the code before continuing.
Student Handout Material

## Slide 55: Ridge Beam
Ridge Beam
When rafter or collar ties are not provided the ridge must be supported by an engineered wall or girder. Ridge beams are structural members.
Notes: R802.3.1 Ridge Beam
To meet the IRC code requirements, when there are no ceiling joists or rafter ties, the rafters must be supported by an engineered wall or girder, which is also called a ridge beam. The ridge beam is a structural member supporting the rafters and can be used for roofs with higher slopes, such as a cathedral ceiling.
If there are no rafter or collar ties, then the ridge must be supported. This protects against thrust by preventing the top of the rafter from moving down and allows the loads to be transferred down through the structure.

## Slide 56: Collar Ties
Collar ties or ridge straps to resist wind uplift shall be connected in the upper third of the attic space in accordance with Table R602.3(1). Collar ties shall be a minimum of 1-inch by 4-inch (nominal), spaced not more than 4 feet on center.
Ridge Strap
Notes: R802.3.1 Collar Ties
All regions, not just high wind regions, must use a collar tie or ridge strap in the upper third of the attic space to resist wind uplift. Joists and rafter ties are intended to keep the rafters from spreading and collar ties keep rafters from coming apart at the top. Collar ties are structural members, but do not provide a continuous tie. Collar ties should be at least 1 by 4 and spaced not more than 4 feet on center, with rafters spaced at 24 inches, this usually works out to every other rafter. The fastening requirements are shown in the table.

## Slide 57: R802.4 Allowable Ceiling Joist Spans
4
Spans for ceiling joists shall be in accordance with Tables R802.4(1) and R802.4(2).
  Table R802.4(1) for uninhabitable attics without storage (Live Load = 10 psf)
  Table R802.4(2) for uninhabitable attics with limited storage (Live Load = 20 psf)
  For other grades and loading conditions refer to AF & PA Span Tables for Joists and Rafters.
Ceiling Joist Spans
Measure joist span horizontally from the (interior of) exterior wall.
Notes: R802.4 Allowable Ceiling Joist Spans
The IRC code for allowable ceiling joist spans has two tables, R802.4(1) and R802.4(2). The tables determine the maximum unsupported horizontal distance for ceiling joist span. Joist span is measured along the span of the joists, to the interior of the walls.
Student Handout Material

## Slide 58: Ceiling Joist Span Table
R802.4(1) and R802.4(2) are similar in the types of wood and sizes listed but cover different allowable loads to allow for the weight of attic storage.
Lumber is listed by species and grades. All lumber species have different material properties, for example southern pine is much stronger and stiffer than spruce. The maximum span will reflect this.
Notes: Ceiling Joist Span Table
Tables R802.4 (1) and R802.4(2) are similar in the types of wood and sizes listed, but cover different allowable loads to allow for the weight of attic storage. Lumber is listed by species and grades. All lumber species have different material properties, for example southern pine is much stronger and stiffer than spruce. The maximum span will reflect this.

## Slide 59: R802.5 - Allowable Rafter Spans
5
Tables R802.5.1(1) to R802.5.1(8)
Roof LL=20 psf, ceiling not attached to rafters
Roof LL=20 psf, ceiling attached to rafters
Ground snow load = 30 psf, ceiling not attached to rafters
Ground snow load = 50 psf, ceiling not attached to rafters
Ground snow load = 30 psf, ceiling attached to rafters
Ground snow load = 50 psf, ceiling attached to rafters
Ground snow load = 70 psf, ceiling not attached to rafters
Ground snow load = 70 psf, ceiling attached to rafters
Rafter Spans
Measure rafter span from (interior of) exterior wall to ridge board. Check requirements in applicable table based on loads.
Notes: R802.5 - Allowable Rafter Spans
The IRC code for rafter spans is similar to the code for joists. There are seven tables with varying allowable loads, deflection limits, and conditions. Measure common rafter spans horizontally, beginning at the interior of the exterior wall and ending at the ridge board. Measure jack rafter spans horizontally, beginning at the hip or valley rafter and ending at the ridge board. Do not measure rafter spans along the actual length of the rafter. Then select the size, span, and spacing of rafters relative to the roof design from the tables.
Student Handout Material

## Slide 60: Table R802.5.1(1) Footnote
The tabulated rafter spans assume that ceiling joists are located at the bottom of the attic space or that some other method such as rafter ties is provided at that location. Where ceiling joists or rafter ties are located higher in the attic space the rafter spans shall be multiplied by the following factors:
Notes: Table R802.5.1(1) Footnote
Allowable rafter spans assume that ceiling joists are positioned at the bottom of the attic space. When the joist is moved up to be used as a rafter tie, extra bending force is put on the rafter. In this exception, the code requires that the rafter span is reduced to account for the additional force created.
A rafter tie located 1/6 of the way up the attic space, will have a lesser span once the adjustment factor is applied.
-----
Table R802.5.1(9)
a. When ceiling joists or rafter ties are located higher in the attic space, the rafter spans shall be multiplied by the factors given below:

## Slide 61: Crosstie Location
Weight on roof
The bending force is caused by the weight on the roof plus the tension tie.
Tension Force
Tension Force
Tension in the tie can cause the rafter to fail. The rafter span must be adjusted to account for the load added to the downward and bending forces. If not, the bending force will cause shear stress resulting in tearing on the rafter.
Notes: Crosstie Location
Tension in the tie can cause the rafter to fail. The rafter span must be adjusted to account for the load added to the downward and bending forces.
Click: If not, the bending force will cause shear stress resulting in tearing on the rafter. The bending force is caused by the weight of the roof plus the tension tie.

## Slide 62: Check Your Knowledge
When a joist becomes a rafter tie
by being located higher in the attic,
the allowable rafter span_________________.
increases
decreases
is factored by ten
Notes: Check Your Knowledge

## Slide 63: R802.5.1 Purlins
6
Installation of purlins to reduce the span of rafters is permitted as shown. Purlins shall be sized no less than the required size of the rafters that they support.
Purlins shall be continuous and shall be supported by 2-inch by 4-inch braces installed to bearing walls at a slope not less than 45 degrees from the horizontal. The braces shall be spaced not more than 4 feet on center and the unbraced length of braces shall not exceed 8 feet.
Notes: R802.5.1 Purlins
Purlins can be used to reduce the clear span of rafters and provide extra support to the roof. Purlins run under and perpendicular to rafters and should not have less depth than the rafter, as noted in the illustration. Purlins are continuous and supported by 2 by 4 braces installed at bearing walls.
Student Handout Material

## Slide 64: Purlin Example
Purlins
Purlins should not be less than the size of the rafter.
Braces are 2-inches by 4-inches.
Braces are installed to bearing walls at not less than 45 degrees.
Braces are spaced not more than 4 feet o.c.
The unbraced length of the braces should not be more than 8 feet.
Notes: Purlin Example
Studs under compression tend to buckle and lose load carrying capacity. The longer the unbraced length, the more likely this is to happen. In this example, the studs are nailed in a perpendicular lay-up to the braces to reduce or eliminate the unbraced length. Purlin braces should not be spaced more than four feet apart and the unbraced length of braces should not be more than 8 feet. Review the purlin guidelines before proceeding.

## Slide 65: R802.6 Bearing
7
The ends of each rafter or ceiling joist shall have not less than 1-1/2 inches of bearing on wood or metal and not less than 3 inches on masonry or concrete.
The bearing on masonry or concrete shall be direct, or a sill plate of 2-inch minimum nominal thickness shall be provided under the rafter or ceiling joist. The sill plate shall provide a minimum nominal bearing area of 48 square inches.
Notes: R802.6 Bearing
To meet this IRC requirement, the ends of rafters or ceiling joists should not have less than 1 ½ of bearing on wood or metal and not less than 3 inches on masonry or concrete.
Student Handout Material

## Slide 66: Bearing
Top Hanger
Bottom Hanger
Adjustable Hanger
Bearing Hangers
Hangers are needed when there is less than 1-1/2” bearing on wood.
Notes: Bearing
When there is less than 1 ½ inches bearing on wood, an engineered solution such as hangers is needed. There is a wide array of hangers available for specific applications. The image shows an installation that contains a horizontal cut at the heel of the rafter. The connector won’t work if it is a sloped rafter without this cut. Manufacturers provide hangers to address this sloped configuration.

## Slide 67: R802.7 Cutting, Drilling, and Notching
8
Notches in solid lumber joists, rafters, blocking and beams shall not exceed one-sixth of the depth of the member, shall not be longer than one-third of the depth of the member and shall not be located in the middle one-third of the span.
Notches at the ends of the member shall not exceed one-fourth the depth of the member. The tension side of members four inches or greater in nominal thickness shall not be notched except at the ends of the members.
Notes: R802.7 Cutting and Notching
This IRC code addresses cutting and notching. It is important to note both where and what is cut to comply with the code.There should be no notches in the middle of rafters and beams. There can be notches in the outer thirds, top or bottom if less than 1/6 inch. Notches at the very end should be less than ¼ of depth. No notches are allowed for a member that is four inches or greater in width, except at the ends. The tension side is the bottom edge.
Student Handout Material

## Slide 68: R802.7 Cutting, Drilling, and Notching
8
The diameter of the holes bored or cut into members shall not exceed one-third the depth of the member.
Holes shall not be closer than 2 in. to the top or bottom of the member, or to any other hole located in the member. Where the member is also notched, the hole shall not be closer than 2 inches to the notch.
Notes: R802.7.1 Cutting and Notching
Here the IRC code addresses the specifications for holes. For “cuts,” the diameter of holes bored or cut into members should not exceed one third the depth of the member. Holes should be 2 inches away from top and bottom or from any other hole located in the member. If the member is already notched, the hole should not be closer than two inches to the notch.

## Slide 69: R802.8 Lateral Support
9
Roof framing members and ceiling joists having a depth-to-thickness ratio exceeding 5 to 1 based on nominal dimensions shall be provided with lateral support at points of bearing to prevent rotation.
For roof rafters with ceiling joists attached per Table R602.3(1), the depth-thickness ratio for the total assembly shall be determined using the combined thickness of the rafter plus the attached ceiling joist.
Blocking to rafter or
ceiling joist per code
Blocking or other lateral
support per code
Fastening to Plate
Notes: R802.8 Lateral Support
According to this IRC code section, lateral support is required to stop rafters from rolling over when the depth to thickness ratio exceeds 5 to 1.
An example of exceeding 5 to 1 would be 2 by 12 or greater, which is an uncommon occurrence. If the rafters have the ceiling joists attached, the width of the ceiling joist is added. The ceiling joist is usually at least a 2-by, which would result in a 3 to 1 depth to thickness ratio. Illustrated here is blocking to a rafter for lateral support and fastening to plate. The table lists the fastening requirements when blocking is prescribed.
Student Handout Material

## Slide 70: R802.8.1 Bridging
10
Rafters and ceiling joists having a depth to-thickness ratio exceeding 6 to 1 based on nominal dimensions shall be supported laterally by solid blocking, diagonal bridging (wood or metal) or a continuous 1-inch by 3-inch wood strip nailed across the rafters or ceiling joists at intervals not exceeding 8 feet.
Notes: R802.8.1 Bridging
The code requires bridging only when the member ratio exceeds 6 to 1, which would be a 2 by 14. Bridging is also uncommon. Bridging keeps the joists from rotating away from their supports under loads and losing the load carrying capacity. Blocking keeps rafters and joists from rolling at the supports. Shown are three types of bridging: solid bridging, diagonal bridging, or straps.
Student Handout Material

## Slide 71: R802.9 Framing of Openings
11
When the header joist span exceeds 4 feet, the trimmer joists and the header joist shall be doubled. Approved hangers shall be used for the header joist to trimmer joist connections when the header joist span exceeds 6 feet. Tail joists over 12 feet long shall be supported at the header by framing anchors or on ledger strips not less than 2 inches by 2 inches.
Rafter
Ridge Board
Double Trimmer Rafter
Double
Header
Notes: R802.9 Framing of Openings
This code section addresses framing of openings. Similar to walls, when framing members are removed, framing around the outside has to be reinforced to carry the extra load, and headers must be installed to transfer the load to those trimmer joists or in this case a trimmer rafter. When the header joist span exceeds four feet, the trimmer joists and header joists will be doubled as shown here.
Student Handout Material

## Slide 72: Framing of Openings
Header
Trimmer
Header
Trimmer
Notes: Framing of Openings
Approved hangers are required when the header joist span is more than six feet. Shown in the first image is a common trayed ceiling where these framing of opening requirements apply. While the code is talking about openings in ceilings, it could be applied to other areas, like the second image where the joists are headered off because of congestion in framing at that location.

## Slide 73: R802.11 Roof Tie-Down
12
Roof assemblies shall have uplift resistance in accordance with Sections R802.11.1.1 and R802.11.1.2. Where the uplift force does not exceed 200 pounds, rafters and trusses spaced not more than 24 inches on center shall be permitted to be attached to their supporting wall assemblies in accordance with Table R602.3(1).
Where the basic wind speed does not exceed 115 mph, the wind exposure category is B, the roof pitch is 5:12 or greater, and the roof span is 32 feet or less, rafters and trusses spaced not more than 24 inches on center shall be permitted to be attached to their supporting wall assemblies in accordance with Table R602.3(1).
Notes: R802.11 Roof Tie-Down
This code section refers to roof truss tie-downs and is only summarized here. This code states that when uplift forces do NOT exceed 200 pounds, rafters and trusses spaced not more than 24 inches on center can be attached per Table R602.3(1). The second part lists conditions that must exist in order to attach using 3 10d nails. Read the code before proceeding.
Student Handout Material

## Slide 74: R802.11.1.2 Rafter Uplift Resistance
13
Rafter uplift resistance. Individual rafters shall be attached to supporting wall assemblies by connections capable of resisting uplift forces as determined by Table R802.11 or as determined by accepted engineering practice. Connections for beams used in a roof system shall be designed in accordance with accepted engineering practice.
Notes: R802.11.1.2 Rafter Uplift Resistance
The IRC code in this section addresses rafter uplift resistance stating that when the uplift force exceeds 200 pounds, referenced in the previous slide, then an enhanced rafter to wall connection is required. This can either be in accordance with the table R802.11 or an accepted engineering practice. As an example, a connector with the required load capacity can be used.
Student Handout Material

## Slide 75: Uplift Resistance >200 Pounds
When uplift is greater than 200 pounds, then a designed connection must be provided beyond the basic requirement for toenails.
Table R802.11
Notes: Uplift Resistance >200 Pounds
When uplift is greater than 200 pounds, then a designed connection must be provided beyond the basic requirement for toenails. This table gives the uplift for various situations. The connector needs to have the capacity in the table or be designed in accordance with engineering practice.
This is a section of Table R802.11 showing the required tie-down for roof framing. This example identifies a 32’ roof span and >5:12 roof pitch.

## Slide 76: Uplift Resistance <200 Pounds
R602.3(1)
When uplift does not exceed 200 pounds rafters can be attached per Table R602.3(1).
Notes: Uplift Resistance <200 Pounds
When the uplift force does not exceed 200 pounds, rafters or trusses can be attached per Table R602.3(1). The fastening has changed from 2 toenails to 3 toenails, the connection has an increase of 50% in capacity.

## Slide 77: Check Your Knowledge
When uplift is greater than _______,
a design connection must be provided.
24 inches on center
150 lbs.
12:12 pitch
200 lbs.
Notes: Check Your Knowledge

## Slide 78: Summary
This training covered many different topics on the code requirements for conventionally framed roofs.
Lesson 1 Basic wood roof systems and various roof types. Common framing members and roof concepts.
Lesson 2 Critical roof system connections. How connections through a structure create a continuous load path to counteract wind and other forces.
Lesson 3 IRC code sections for Conventionally Framed Roof construction.
Notes: SUMMARY
This training covered many different topics on the code requirements for conventionally framed roofs.
The first lesson introduced basic wood roof systems and various roof types. The lesson identified common framing members and discussed common roof concepts including pitch and slope.
The second lesson discussed critical connections in the roof system and how connections through a structure create a continuous load path to counteract the impact of wind and other forces.
The third lesson cites IRC code sections that apply directly to Conventionally Framed Roof construction and presents the most important aspects of each code section.

## Slide 79
Code Requirements for Conventionally Framed Roofs
ASSESSMENT
Final Assessment
There are 10 questions. You must pass with a score of at least 70%.
Notes: Assessment: Final Assessment
There are 10 questions in the final assessment and you must pass with a score of at least 70%.

## Slide 80: Congratulations!
You have completed this course. Use the Exit button to close the training.
SST-198-10_CodeRequirementsforConventionallyFramedRoofs_v001 Copyright © 2020 Simpson Strong-Tie. All rights reserved.
Notes: Congratulations!
You have completed this course. Use the Exit button to close the training.