## Slide 1: Important – Read Me Before Presenting
Instructors:
This presentation has been approved for either AIA or ICC credit.
For AIA credits: Unhide the AIA credit information slides in the beginning and at the end of this presentation.
For ICC credits: Unhide the ICC credit information slides in the beginning and at the end of this presentation.

## Slide 2: Welcome!
We will begin in a few minutes.
Please be sure to sign the registration form to receive credit for attending today’s learning event.
Notes: Do
Meet and greet participants as they arrive. Start learning names, make them feel comfortable and settled in the training environment.
Make sure your opening has PUNCH:
Promotes interest and enthusiasm for the session
Understands participants’ needs
Notes ground rules and administrative/housekeeping needs
Clarifies expectations
Helps everyone get to know each other
State your expectations around participation: Make it known and expected that you will be encouraging and inviting participation.
Tips to facilitate connections:
Thank participants for their contribution (ideally with their name)
Praise participation (especially the first person to speak)
Express confidence in the participants
Restate what someone said earlier (“As John mentioned earlier….”)
Encourage participants to share what others were saying in their small groups (without naming names)
Invite someone you heard speaking in a small group to share with the entire group
Encourage the group to respond to an individual’s comment/question
Physical Room / Training Venue Setup:
If using a table arrangement, consider grouping 4 to 6 students at each station. This will help encourage conversation and discussion during activities.
Get people standing at regular intervals during your training session. Research shows that people learn up to 15% more when standing up!

## Slide 3: Inspection of New and Existing Deck Construction
Simpson Strong-Tie® Training
Presenter Name | Title

## Slide 4: Credit Information
IACET Accreditation Information
Simpson Strong-Tie® has been accredited as an Authorized Provider by the International Association for Continuing Education and Training (IACET). As a result of their Authorized Provider accreditation status, Simpson Strong-Tie® is authorized to offer IACET CEUs for its programs that qualify under the ANSI/IACET Standard.
This course offers 0.1 CEU (1 hour of credit).
Notes: Review the submission process for audiences requiring IACET CEU credits.
For those seeking IACET credit, they must take and pass the online test. They must self-report CEU credits to their certifying organization or agency.
Explain the credits awarded: IACET: 0.1 (Equivalent to 1 hour) CEUs.

## Slide 5: Credit Information
AIA Member Information
This course is registered with AIA CES for continuing professional education. As such, it does not include content that may be deemed or construed to be an approval or endorsement by the AIA of any material of construction or any method or manner of handling, using, distributing, or dealing in any material or product. Upon completion of this course, Credit(s) earned will be reported to AIA CES for AIA members who pass the course and have entered their AIA member number on their Simpson profile page. A link to the Certificate of Completion will be available upon completion of this course. Only AIA LU/HSW will be reported.
This course offers 1 LU/HSW credit.
AIA Course Number: AIA-DCKIN118
Notes: Presenter Information
NOTE: Please be sure each attendee LEGIBLY signs the event sign-in sheet.
Say
All questions concerning proprietary products will be addressed after the conclusion of the AIA portion of the presentation. The meeting format is 50 minutes of content, followed by 10 minutes of Q & A.
Do
Explain the credits awarded for:
AIA: 1LU/HSW credit.
IACET: 0.1 (Equivalent to 1 hour) CEU credits.
Review the submission process for audiences requiring either AIA LU/HSW (health, safety and welfare) credits or CEU credits:
For those seeking AIA HSW credit, there is no test required. AIA members must be sure to provide their AIA member number on the sign-in sheet. Please make sure name, email and AIA member number are clearly printed so Simpson can report credits to the AIA on their behalf.
For those seeking IACET credit, they must take and pass the test. They must self-report CEU credits to their certifying organization or agency.

## Slide 6: Credit Information
ICC Member Information
This course has been approved by the International Code Council (ICC) for continuing professional education. For learners that complete this course, it is your responsibility to self-report your credits to the ICC. Please retain your Completion Certificate for your records.
Be sure that your ICC ID number is provided on the sign-in sheet or in your Simpson profile in order to have it displayed on your certificate.
This course offers 0.1 CEU (1 hour of credit).
ICC Course Number: 17777
Notes: Review the submission process for audiences requiring ICC CEU credits.
For those seeking ICC credit, there is no test required. ICC members must provide their ICC ID number on the sign-in sheet or in their Simpson profile in order to have it displayed on their certificate. It is the responsibility of the participant to self-report their credits to the ICC. Ask them to retain their Completion Certificate for their records.
Explain the credits awarded: ICC: 0.1 (Equivalent to 1 hour) CEUs.

## Slide 7: Additional Credit Offerings
Visit
strongtie.com/workshops
for more information
Course Name | CEUs | AIA | ICC
Introduction to Deck Design | 0.1 | ✔ | ✔
Introduction to Wind Design and the Wood Frame Construction Manual | 0.1 | ✔ | ✔
Shear Walls and Lateral Bracing in Light Frame Construction | 0.1 | ✔ | ✔
Understanding Restraint Rod Systems | 0.1 | ✔ | ✔
Cracking the Concrete Anchor Codes | 0.1 | ✔ | ✔
Concrete Deterioration | 0.1 | ✔ | ✔
Moment Frame Design | 0.1 | ✔ | ✔
Introduction to Wind Code Provisions and Meteorological Concepts | 0.1 | ✔ | ✔
Wind Design in Accordance with ASCE 7-10 | 0.1 | ✔ | ✔
Wood Framed Seismic Design 1: Code Provisions, Design Parameters | 0.1 | ✔ | ✔
Notes: Do
Explain that we have additional topics available that offer credits for AIA and ICC members.
Explain that we have a library of online courses available in our Simpson Student Center. They can access our online courses at strongtie.com/workshops.

## Slide 8: Course Description
Deck Inspection for New and Existing Construction
This course provides a detailed overview of the AWC DCA 6, International Residential Code and International Building Code requirements for the construction of decks to ensure they are safe, strong and code-compliant. This material is primarily intended for home inspectors, building inspectors and building officials; however, anyone involved in deck design and construction can also benefit from familiarity with these requirements.
Course Contents
Introduction / Learning Objectives
Lesson 1: Code Concerns
Lesson 2: Inspection of New Construction
Lesson 3: Inspection of Existing Construction
Conclusion / Questions
Notes: Do
Review the course description and course contents.
Say
This course provides a detailed overview of the AWC DCA 6, International Residential Code and International Building Code requirements for the construction of decks to ensure they are safe, strong and code-compliant. This material is primarily intended for home inspectors, building inspectors and building officials; however, anyone involved in deck design and construction can also benefit from familiarity with these requirements.
If differences occur between this program and the interpretation of the Authority Having Jurisdiction, then the interpretation of the Authority Having Jurisdiction will determine the requirement.

## Slide 9: Learning Objectives
Upon completion of this seminar, you will be able to:
Identify the code and standard provisions in the International Building Code and International Residential Code for the construction of a safe, strong and code-compliant deck
Summarize the common code violations found during an inspection of new deck construction
Detect if an existing deck has developed a potentially unsafe issue and is no longer code-compliant
Utilize a home inspection checklist for deck construction as a preliminary safety assessment
Notes: Do
Review the learning objectives for the course.
Inform students that the assessment questions will be based on these learning objectives. Slides that may contain information relevant to the test have an orange graduation cap located in the bottom-left corner.

## Slide 10: A Word About Building Codes
The IRC and IBC feature regulations on the connections and materials used to construct or retrofit a deck.
The information contained here is a summary of the requirements of these codes as they pertain to the common concerns found in a typical inspection. The building codes contain other requirements regarding aspects of deck construction that are not addressed here; check the codes for details.
Any selection of products for a specific application should be made by a qualified professional.
Notes: Say
The International Residential Code and International Building Code feature regulations on the connections and materials used to construct or retrofit a deck.
The information contained here is a summary of the requirements of these codes as they pertain to the common concerns found in a typical home inspection. The building codes contain other requirements regarding aspects of deck construction that are not addressed here; check the codes for details. Check with your local building department to verify what building codes have been adopted in your area.
Any selection of products for a specific application should be made by a qualified professional. Simpson Strong-Tie recommends that deck designs be approved by the local building department before construction begins.
The information in this course contains code references from the 2012, 2015 and 2018 editions of the International Residential Code (IRC) and International Building Code (IBC).

## Slide 11: CODE CONCERNS
After completing this lesson, you will be able to:
Summarize the importance of code and standard provisions in the IBC and IRC for the construction of a safe, strong and code-compliant deck
Notes: Do
Review the lesson title and objective.

## Slide 12: Continuous Load Path
As with your home, your deck should be built using a “continuous load path.”
Assures loads are transferred from point of application to the foundation via the structural components and connections
Contains forces from gravity, lateral and uplift loads
Transfers weight from deck through its frame and then to the foundation and support structure
Continuous load path better equips deck to resist occupancy, wind, snow and earthquake forces
Notes: Say
As with your home, your deck should be built using a “continuous load path.”
The continuous load path is an engineering concept that, when constructed, assures loads are completely transferred from point of application to the foundation via the structural components and connections.
The load path, which contains forces from gravity (vertical), lateral (horizontal) and uplift loads, effectively transfers the weight (load) from the deck through its frame and then to the foundation and the adjacent support structure (typically
your home).
If your deck is built with a continuous load path, it will be better equipped to resist forces, such as occupancy, wind, snow
and earthquakes.

## Slide 13: Do Decks Really Need to Meet Code Requirements?
Many people do not realize that decks are structures that need to be designed to meet minimum standards and resist certain stresses
A deck must be designed to support the weight of people and objects placed on it, as well as lateral and uplift loads that can act on it.
The construction of buildings and structures in accordance with the provisions of this code shall result in a system that provides a complete load path that meets all requirements for the transfer of all loads from their point of origin through the load-resisting elements to the foundation.
Notes: Say
Because decks may look relatively simple to build, many people do not realize that they are structures that need to be designed to meet minimum standards and resist certain stresses. Like a house, or any other building, a deck must be designed to support the weight of people and objects placed on it, as well as lateral and uplift loads that can act on the deck as a result of occupant movement, wind or seismic activity. The 2009-2018 versions of both the IBC and IRC contain language outlining the general design requirements of structures. This excerpt from IRC Section R301.1 represents a summary of the intent of both codes:
“The construction of buildings and structures in accordance with the provisions of this code shall result in a system that provides a complete load path that meets all requirements for the transfer of all loads from their point of origin through the load-resisting elements to the foundation.”
The concept of a complete or continuous load path refers to a series of solid connections and structural members within the deck that transfer load to the ground or adjacent supporting structure (commonly a building). This same principle is applied to the design of all types of wood-frame buildings. This continuous load path is created by using a system of structural connectors and fasteners to connect the wood members together.

## Slide 14: Ensuring the Safety of All Structures, cont.
Three people viewing a house for sale in York, PA fell from a second-floor deck when it collapsed on August 6, 2006.
Where is the “due diligence?”
A two-story deck structure failed catastrophically while a real estate agent was showing a house for sale in Stone Harbor, NJ.
PA Deck Collapse
NJ Deck Failure
1
2
Notes: Say
A Realtor should provide due diligence during the evaluation of a property for sale. However, this is not always the case.
In one incident, three people viewing a house for sale in York, Pennsylvania fell from a second-floor deck when it collapsed on August 6th, 2008.
In another incident, a two-story deck structure failed catastrophically while a real estate agent was showing a house for sale in Stone Harbor, New Jersey. The collapse of the second-story deck was nearly simultaneous with the floor on the first-floor porch giving way. [April 2, 2014; https://www.capemaycountyherald.com/news/accidents/article_e0470865-2bd8-5888-9618-d591db052d2a.html]
---
Pic 1: David Willin
Pic 2: Jen Mara (http://www.jlconline.com/how-to/exteriors/deck-collapse-while-showing-house-ruins-realtors-day_o)

## Slide 15: Ensuring the Safety of All Structures, cont.
Notes: [Pics from previous slide]

## Slide 16: Structures that are Deemed Unsafe
If due diligence is provided, what shall be done with unsafe structures?
Structures that are dangerous to human life shall be deemed an unsafe condition.
Unsafe structures shall be taken down and removed or made safe, as the building official deems necessary.
12-18 IBC 116.1 Conditions. 12-18 IEBC 115.1 Conditions. 12-18 IPMC 108.1.1 Unsafe structures.
Notes: Say
If due diligence is provided, what shall be done with unsafe structures?
Structures that are unsafe or otherwise dangerous to human life shall be deemed an unsafe condition. Unsafe structures shall be taken down and removed or made safe, as the building official deems necessary.
Red tag is a term used by building officials to describe the posting of notices on a property deemed dangerous or unfit for human habitation at the time such hazard is discovered by the building department. It does not necessarily mean that the building must be condemned, but it is an official warning that remediation is required.

## Slide 17: No Grandfathering of Unsafe Conditions
Is there an exemption for deck construction from new regulations or requirements that would allow unsafe conditions to be acceptable?
Unsafe systems or components should be repaired immediately regardless of when the deck or porch was built or whether the system or component passed an inspection.
THERE IS
NO GRANDFATHERING
OF UNSAFE CONDITIONS
Notes: Say
Is there an exemption for deck construction from new regulations or requirements that would allow unsafe conditions to be acceptable?
Unsafe systems or components should be repaired immediately regardless of when the deck or porch was built or whether the system or component passed an inspection.
There is no grandfathering of unsafe conditions.

## Slide 18: The Life Expectancy of Outdoor Components
Life expectancy (in years)
a National Association of Home Builders/Bank of America Home Equity, Study of Life Expectancy of Home Components 2/07.
b Wood Myths Facts and Fiction, Paul Fisette, 2005 Building Material and Wood Technology-UMass @ Amherst.
c A technical report in the Forest Products Journal / 1998 indicated that the average PPT deck only lasts 9 years due to the fact that PPT wood soaks and loses moisture. As a result, the wood twists, bends, cracks and virtually tears itself apart.
5
10
15
20
25
30
20 YEARS
15–20 YEARS
20 YEARS
10–15 YEARS
~ 10–20 YEARS
Asphalt shingles a
Aluminum and vinyl windows a
Deck (estimate 1) a
Deck (estimate 2) b
Deck (combined estimates)
~ 9 YEARS
Deck (estimate 3) c
Notes: Say
In 2007, the Study of Life Expectancy of Home Components was completed by the National Association of Home Builders. The results concluded that the average life expectancy of asphalt shingles is approximately 20 years and the expectancy of aluminum and vinyl windows can range from 15 to 20 years. Most importantly, they stated the lifespan of a deck is about 20 years. It was noted that: “Because they are subject to a wide range of conditions in different climates, the life expectancy of wooden decks can vary significantly. Under ideal conditions – life expectancy of about 20 years.”
Another study found in Wood Myths and Fiction by Paul Fisette estimated the life expectancy of a deck to be between 10 and 15 years.
Data from a technical report in the Forest Products Journal in 1998 indicated that the average preservative pressure treated (PPT) wood deck only lasts 9 years due to the fact that PPT wood soaks and loses moisture. As a result, the wood twists, bends, cracks and virtually tears itself apart.
Therefore, the life expectancy of a deck is generally 10 to 20 years.
---
Source A: National Association of Home Builders/Bank of America Home Equity, Study of Life Expectancy of Home Components 2/07.
Source B: Wood Myths Facts and Fiction, Paul Fisette, 2005 Building Material and Wood Technology-UMass @ Amherst.
Source C: A technical report in the Forest Products Journal/1998 indicated that the average PPT deck only lasts 9 years due to the fact that PPT wood soaks and loses moisture. As a result, the wood twists, bends, cracks and virtually tears itself apart.

## Slide 19: Older Structures May Be Past Their Useful Lifespan
Is the deck or structure still safe after so many years?
There is the possibility that time and environmental factors have deteriorated the deck to a potentially dangerous condition.
Since deck building started more than 35 years ago, many structures are past their useful life and need to be removed or replaced.
What can happen?
Notes: Say
Even if a deck was built to code or passed an inspection once upon a time, there is the possibility that time and environmental factors have deteriorated the deck to a potentially dangerous condition.
Since deck building started more than 35 years ago, many structures are past their useful life and need to be removed and replaced.

## Slide 20: Older Structures May Be Past Their Useful Lifespan, cont.
44-year-old apartment complex
Safety maintenance was not properly done
Heavy paint was applied to hide the rotted wood and corroded fasteners
Stairway collapsed, sending a man 10 feet to his death
Notes: Say
This is a 44-year-old apartment complex where safety maintenance was not properly done. The keep up the illusion of a safe structure, heavy paint was applied to hide the rotted wood and corroded fasteners. Unfortunately, the stairway collapsed sending a man 10 feet to his death.

## Slide 21: Lesson One Complete
Now that we’ve completed this lesson, you should be able to:
Summarize the importance of code and standard provisions in the IBC and IRC for the construction of a safe, strong and code-compliant deck
Let’s Continue to
Lesson Two
Notes: Do
Review the lesson objective summary.

## Slide 22: INSPECTION OF NEW CONSTRUCTION
After completing this lesson, you will be able to:
Summarize the common code violations found during an inspection of new deck construction
Notes: Do
Review the lesson title and objective.

## Slide 23: Preventing Common Code Violations
1.
Proper fastening of the ledger connection
The building code prohibits the “use of toenails or nails subject to withdrawal” when making this connection, yet a number of deck failures result due to using these or other types of improper fasteners.
The following code requirements can be easily overlooked in deck construction:
Notes: Say
The following code requirements can be easily overlooked in deck construction:
1. Proper fastening of the ledger connection. The building code prohibits the “use of toenails or nails subject to withdrawal” when making this connection, yet a number of deck failures result due to using these or other types of improper fasteners.

## Slide 24: Preventing Common Code Violations
2.
Proper fastening of the guard posts to the deck
The building code requires the guard post to resist a 200-pound load. This load, applied to the top of the guard post, creates a large leverage force where the guard post attaches to the deck framing.
The following code requirements can be easily overlooked in deck construction:
Notes: Say
2. Proper fastening of the guard posts to the deck. The building code requires the guard post to resist a 200-pound load. This load, applied to the top of the guard post, creates a large leverage force where the guard post attaches to the deck framing.

## Slide 25: Preventing Common Code Violations
3.
Post-base connections
The building code requires posts to “be restrained to prevent lateral displacement at the bottom end.” This requirement is important because most decks cannot safely support part or all of their load if a post can move.
The following code requirements can be easily overlooked in deck construction:
Notes: Say
3. Post-base connections. The building code requires posts to “be restrained to prevent lateral displacement at the bottom end.” This requirement is important because most decks cannot safely support part or all of their load if a post can move.

## Slide 26: Preventing Common Code Violations
4.
Openings in guards and stair railings
The building code places a limit on the size of openings, for the occupants’ safety in case of tripping or falling, and for the safety of small children.
The following code requirements can be easily overlooked in deck construction:
Notes: Say
4. Openings in guards and stair railings. The building code places a limit on the size of openings, for the occupants’ safety in case of tripping or falling, and for the safety of small children.
We’ll review the code requirements for these common violations next.

## Slide 27: Part 1: Deck Ledger to Rim Joist Connection
1
Deck Ledger to Rim Joist
Connection
Toenails and Nails Subject to Withdrawal
Through-Bolts and Lag Screws
Proprietary Structural Wood Screws
Rim Board Identification
We’ll review the following topics:
Notes: Part 1: Deck Ledger to Rim Joist Connection.
We’ll review the following topics:
Toenails and Nails Subject to Withdrawal
Through-Bolts and Lag Screws
Proprietary Structural Wood Screws
Rim Board Identification

## Slide 28: Deck Ledger to Rim Joist Connection
Toenails and Nails Subject to Withdrawal
Toenails or nails subject to withdrawal shall not be used to attach the deck ledger to the rim board.
Bolts, lag screws or proprietary structural wood screws shall be used to positively anchor the deck to the primary structure.
Connection must be designed to support both vertical and lateral loads.
12-15 IRC R507.1, 18 IRC R507.8 12-18 IBC 1604.8.3
Notes: Say
The code states that “where positive connections to the primary building structure cannot be verified during inspection, decks shall be self-supporting.”
Therefore, all connections into the ledger and rim joist must be able to be verified as to the suitability of the applications. Otherwise, decks shall be free-standing. This usually requires a series of beams and columns, so that the joists can be cantilevered over the beam.
Correct ledger attachment is crucial when building a deck that is attached to another structure. One of the most common causes for deck failure are ledgers that pull away from the primary structure, resulting in complete collapse.
Toenails or nails subject to withdrawal shall not be used to attached the deck ledger to the rim board. The practice of using nails, only, has not been permitted since prior to the 2000 IRC.
The most common ways to attach a ledger to a structure are lag screws, bolts or proprietary wood screws through the ledger and into the rest of the supporting structure. The installation of through-bolts requires access to the back side of the rim joist which, in some cases, is not possible without significant removal of drywall within the structure. These methods can work, but must meet specific requirements for size, spacing and penetration to be approved.
The connection between the deck ledger and rim board must be designed to support both vertical and lateral loads.

## Slide 29: Deck Ledger to Rim Joist Connection
Through-Bolts and Lag Screws
1/2" diameter lag screws or bolts with washers can be used per the IRC provided that:
Fastener stagger pattern is followed
Maximum 1/2" gap between ledger face and wall sheathing (bolts only)
When attached to a minimum 1" thick engineered wood rim, the ledger attachment is designed per accepted engineering practice
CONNECTION DETAILS | JOIST SPAN |  |  |  |  |  | 
 | 6' and less | 6'1" - 8' | 8'1" - 10' | 10'1" - 12' | 12'1" - 14' | 14'1" - 16' | 16'1" - 18'
 | On-center spacing of fasteners |  |  |  |  |  | 
1/2" dia. lag screw, 1/2" max sheathing | 30 | 23 | 18 | 15 | 13 | 11 | 10
1/2" dia. bolt, 1/2" max sheathing | 36 | 36 | 34 | 29 | 24 | 21 | 19
1/2" dia. bolt, 1" max sheathing | 36 | 36 | 29 | 24 | 21 | 18 | 16
12-15 IRC Table R507.2, 18 IRC Table R507.9.1.3(1): DECK LEDGER CONNECTION TO BAND JOIST
Notes: Say
In December 2005, the Building Safety Journal published a prescriptive spacing chart for bolts and lag screws. Prior to then, spacing would have to be determined based on a calculation of the fastener using the AWC NDS.
1/2-inch diameter lag screws or bolts with washers can be used per the IRC provided that the fastener stagger pattern is followed, there is a maximum 1/2-inch gap between ledger face and wall sheathing (for bolts only), and when attached to a minimum 1-inch thick engineered wood rim, ledger attachment is designed per accepted engineering practice. Other requirements may apply.
Note that accepted engineering practice rules out the use of 1/2-inch diameter lag screws when the combined net thickness of rim and sheathing is less than 2-inches, as 1/2-inch diameter lag screws require a minimum penetration of 4 diameters (2-inches) to achieve holding capacity. (NDS ’15-12.1.4.6, NDS ’12-11.1.4.6)
---
Proper Lag Screw Installation:
Two pre-bored holes are required for proper lag screw installation.
100% of the screw diameter for the shank portion of the screw (2015 NDS 12.1.4.2a, 2012 NDS 11.1.4.2a, 2005 NDS 11.1.3.2a)
40% – 75% of the screw diameter for the threaded portion (2015 NDS 12.1.4.2b, 2012 NDS 11.1.4.2b, 2005 NDS 11.1.3.2b)

## Slide 30: Deck Ledger to Rim Joist Connection
Proprietary Structural Wood Screws
Benefits of a pre-engineered ledger connection:
Additional engineering fees are not necessary
There is no down time waiting for a site-specific solution
Code compliance issues have already been addressed based on testing of the ledger assembly to determine performance
Structural wood screws may be used if:
Assembly is pre-engineered for compliance with the IRC
Screws meet the load carrying requirements of the design
Quantity and spacing is specified
Notes: Say
An alternative to a specific engineered design when prescriptive solutions can’t be met is to use a pre-engineered ledger connection that is code compliant.
Benefits include:
Additional engineering fees are not necessary
There is no down time waiting for a site-specific solution
Code compliance issues have already been addressed based on testing of the ledger assembly to determine performance.
Structural wood screws may be used as an alternative to lag screws and through-bolts if the assembly is pre-engineered for compliance with the IRC, the screws meet the load carrying requirements of the design, and the quantity and spacing is specified.

## Slide 31: Deck Ledger to Rim Joist Connection
Single Shear Connection Between Ledger and Rim Board
AWC NDS assumes connected members are in direct contact with each other
Adding structural or non-structural sheathing between the ledger and rim board may change the dynamics
Masonry Veneer Prohibited
Over Siding Prohibited
ATTACHING TO:
Notes: Say
Using the AWC National Design Specification (NDS) for Wood Construction assumes connected members are in direct contact with each other, not over structural sheathing or other material. Adding structural or non-structural sheathing between the ledger and rim board may change the dynamics.

## Slide 32: Deck Ledger to Rim Joist Connection
Single Shear Connection Between Ledger and Rim Board
Attaching to Masonry Veneer is Prohibited
Masonry veneer shall not support any vertical load other than the dead load of the veneer above
Deck ledgers shall not be supported on stone or masonry veneer
12 IRC R507.2.2, 15 IRC R507.2.1, 18 IRC R507.9.1.1 12 IRC R703.7.3, 15-18 IRC R703.8.3
For a code-compliant connection:
Remove veneer just below ledger, install a single or double 2x ledger, install a steel angle per code above the deck, and start the veneer again.
Notes: Say
Attaching the ledger directly to masonry veneer is prohibited. Masonry veneer shall not support any vertical load other than the dead load of the veneer above. For a code-compliant connection, remove the brick or masonry veneer just below the ledger, install a single or double 2x ledger, install a steel angle per code above the deck, and start the veneer again.
Note: A ledger connection over masonry veneer may be possible in the near future when a connector for this application is released.

## Slide 33: Deck Ledger to Rim Joist Connection
Rim Board Identification
If you cannot gain access to both sides of the deck ledger to rim joist connection, the deck shall be self-supporting
Or, as an inspector, you must identify and document that you did not provide a complete ledger inspection
12-15 IRC R507.1, 18 IRC R507.8
Notes: Say
If you cannot gain access to both sides of the deck ledger to rim joist connection, the deck shall be self-supporting. Or, as an inspector, you must identify and document that you did not provide a complete ledger inspection.
---
Picture: One week old deck. Parallel chord truss and the ledger was nailed to house siding.

## Slide 34: Part 2: Guard Post to Deck Connection
2
Guard Post to Deck
Connection
When a Guard is Required
Fastening Guard Posts to the Deck
Permissible Deflection Limits of Guard Rails
Tested Guardrail Post Connections
We’ll review the following topics:
Notes: Part 2: Guard Post to Deck Connection.
We’ll review the following topics:
When a Guard is Required
Fastening Guard Posts to the Deck
Permissible Deflection Limits of Guard Rails
Tested Guardrail Post Connections

## Slide 35: Guard Post to Deck Connection
When is a Guard Required?
A guard is required for only those portions (2018) along open-sided walking surfaces, including porches, balconies and ramps, that are located more than 30" to the floor or grade below
If a guard is built on a deck that is not at least 30" above the finish grade, it still must meet the load and deflection requirements because there is an expectation of safety
12-18 IRC R312.1.1 12 IBC 1013.1, 15-18 IBC 1015.2
Notes: Say
A guard is a building component or system of building components that minimizes the possibility of a fall from the walking surface to a lower level. A guard is required along open-sided walking surfaces, including porches, balconies and ramps, that are located more than 30 inches to the floor or grade below. In the 2018 IRC, they added that the guard is required for only those portions that are located more than 30 inches to the floor or below.
If a guard is built on a deck that is not at least 30 inches above the finish grade, it still must meet the load and deflection requirements because there is an expectation of safety.

## Slide 36: Guard Post to Deck Connection
Fastening Guard Posts to the Deck
The guardrail system shall be able to resist 200 lb. applied in any direction at any point along the top
A 200 lb. load at the top of a 36" post results in a load greater than 1,700 lb. at the connection
When using holdowns to resist the load, it is recommended that the holdown anchor capacity exceeds 1,800 lb. for a 36" tall guard height
12-18 IRC Table R301.5 12-18 IBC 1607.8.1.1
Note: A post a 42" would have higher forces at the connection.
Let’s Review the Method to Determine Resisting Force
Notes: Say
The guardrail system shall be able to resist 200 pounds applied in any direction at any point along the top. A 200-pound load at the top of a 36-inch post results in a load greater than 1,700 pounds at the connection. Thus, when using holdowns to resist the load, it is recommended that the holdown anchor capacity exceeds 1,800 pounds for a 36-inch tall guard height.

## Slide 37: Guard Post to Deck Connection
Fastening Guard Posts to the Deck
Method to Determine Resisting Force
Resisting Moment = Applied Moment
Applied Moment = Applied Force x Post Height
Resisting Moment = 200 lb. x 44.75 in. = 8,950 inch-pounds at base of post
Resisting Force = Resisting Moment / Resisting Moment Arm
Resisting Force = 8,950 inch-pounds / 5.25 in. = 1,705 lb.
Notes: Do
Review equations with the class.

## Slide 38: Guard Post to Deck Connection
Permissible Deflection Limits
The code requires that structural members limit the amount of deflection
When utilizing the current code required loads, the “standard railing” as specified in the 1913 Universal Safety Standards resulted in railing deflections between 3/8" and 3/4"
This is very similar to what is in the code for deflection of structural members today
12-18 IRC Table R301.7 12-18 IBC Table 1604.3
These deflections are nearly impossible to design.
IRC
0.30"
IBC
0.60"
Universal Safety Standards 1913
3/8" – 3/4"
Notes: Say
The code requires that structural members limit the amount of deflection.
When utilizing the current code required loads, the “standard railing” as specified in the 1913 Universal Safety Standards resulted in railing deflections between 3/8" and 3/4" (h/56 – h/111). This is very similar to what is in the code for deflection of structural members today.
IRC Table R301.7 displays the allowable deflection of any structural member under the live load listed in Section R301.5. In this table, guardrails fall under the category of “all other structural members.” The deflection limit is L (or H)/240 and the footnotes allow L (or H) to be taken as twice the length of the cantilever. Typical railings are classified as a cantilevered member since they extend above the deck surface. Therefore, assuming a 36-inch tall guard post with H/240, the allowable deflection is 0.30" (<3/8").
In the IBC, Table 1604.3 displays the permitted deflection of structural members. Guardrails were determined to fall under the “Exterior walls with flexible finishes” category, which is the closest to a deck railing. The deflection limit is L (or H)/120. The footnotes allow L (or H) to be taken as twice the length of the cantilever. Therefore, assuming a 36-inch tall guard post with H/120, the allowable deflection is 0.60” (<5/8").
While these deflections are nearly impossible to design, their stiffness provides a confident perception of safety for the user.

## Slide 39: Guard Post to Deck Connection
Tested Guardrail Post Connections
The four most common methods of attachment were tested in a Virginia Tech study conducted by Dr. Frank Woeste, P.E., Dr. Joseph Loferski and Dustin Albright. It was published by Wood Design Focus in 2006.
Connections were tested to a load of 500 lb.
Given a 200 lb. design load and a factor of safety of 2.5
200 lb. x 2.5 = 500 lb. test load resistance
To pass the test, the connection must survive the 500 lb. load and have a deflection less than or equal to 3-1/3" when 200 lb. is applied at 36".
12 IBC 1710.3.1, 15-18 IBC 1709.3.1 Test Procedure
Next: Connections that Failed and Passed
Notes: Say
The four most common methods of attachment were tested in a Virginia Tech study conducted by Dr. Frank Woeste, P.E., Dr. Joseph Loferski and Dustin Albright. It was published by Wood Design Focus in 2006. Connections were tested to a load of 500 lb.
Given a 200 lb design load and a factor of safety of 2.5, the test load resistance is 500 lb.
To pass the test, the connection must survive the 500 lb load and have a deflection less than or equal to 3-1/3" when 200 lb is applied at 36".
---
A note about design loads: The AC273 now requires a load of 600 pounds or 3x factor of safety for wood components, only. It is important to note that many companies tested their connectors to 500 pounds and stopped the test. Their tests do not meet the new criteria.

## Slide 40: Guard Post to Deck Connection
Tested Guardrail Post Connections
Post Connections that Failed
a Must be 500 lb. = 100% to be considered code conforming.
1/2" lag screws didn’t even reach 200 lb.: FAILED
1/2" bolts didn’t reach 500 lb. and didn’t reach deflection criteria: FAILED
1/2" lag screws failed
1/2" bolts failed
NOTE: New test criteria is 600 lb.
Notes: Do
Review tested connections that failed.

## Slide 41: Guard Post to Deck Connection
Tested Guardrail Post Connections
Post Connections that Passed
a Must be 500 lb. = 100% to be considered code conforming.
HD2A anchor (4x4 post inside band): PASSED
HD2A anchor (4x4 post outside band): PASSED
Connector bypasses rim joist to connect with a deck joist or blocking in such a manner as to create a shear connection.
Plan View
Side View
NOTE: New test criteria is 600 lb.
Notes: Do
Review tested connections that passed.

## Slide 42: Part 3: Post-base to Foundation Connection
3
Post-base to Foundation
Connection
Minimum Footing Dimensions
Support of Live and Dead Loads
Resisting Lateral and Uplift Forces
We’ll review the following topics:
Notes: Part 3: Post-base to Foundation Connection.
We’ll review the following topics:
Minimum Footing Dimensions
Support of Live and Dead Loads
Resisting Lateral and Uplift Forces

## Slide 43: Post-base to Foundation Connection
Minimum Footing Dimensions
The length and width of a footing shall be a minimum 12" x 12" or equivalent
The thickness of a footing shall not be less than 6"
A pier or stem without a footing must be at least 12" x 12" or equivalent
12 IRC R403.1, 15-18 IRC R403.1.1 12-18 IBC 1809.4 12-18 IBC 1809.7 15 IRC R507.8.1, 18 IRC R507.3
2015 IRC Figure R507.8.1 Typical Deck Posts to Deck Footings
SIDE VIEW
PLAN VIEW
Length
Thickness
Width
Notes: Say
The length and width of a footing shall be a minimum 12" x 12" or equivalent. The thickness of a footing shall not be less than 6".
A pier or stem without a footing must be at least 12" x 12" or equivalent.

## Slide 44: Post-base to Foundation Connection
Deck Footings in 2018
2018 IRC R507.3 …Posts shall bear on footings in accordance with Section R403 and Figure R507.3.
2018 IRC Figure R507.3 Typical Deck Posts to Deck Footings
2018 IRC added ½" through-bolts, more detailing, premanufactured post base connector, and gravel below footing for embedded post.

## Slide 45: Post-base to Foundation Connection
Support of Live and Dead Loads
Decks shall be able to support the dead and live loads properly. See Figure 12 and Table 4 in the AWC DCA 6 for footing size, footing thickness, and post attachment options and requirements.
Notes: Say
Decks shall be able to support the dead and live loads properly. See Figure 12 and Table 4 in the AWC DCA 6 for footing size, footing thickness, and post attachment options and requirements.

## Slide 46: Post-base to Foundation Connection
Support of Live and Dead Loads
2018 IRC Table R507.3.1 Minimum Footing Size for Decks
Live or ground snow load (psf) | Tributary area (sq. ft.) | Load bearing value of soils (psf) |  |  |  |  | 
 |  | 1500 |  |  | 2000 |  | 
 |  | Side of a square footing (in.) | Diameter of a round footing (in.) | Thickness (in.) | Side of a square footing (in.) | Diameter of a round footing (in.) | Thickness (in.)
40 | 20 | 12 | 14 | 6 | 12 | 14 | 6
 | 40 | 14 | 16 | 6 | 12 | 14 | 6
 | 60 | 17 | 19 | 6 | 15 | 17 | 6
 | 80 | 20 | 22 | 7 | 17 | 19 | 6
 | 100 | 22 | 25 | 8 | 19 | 21 | 6
 | 120 | 24 | 27 | 9 | 21 | 23 | 7
 | 140 | 26 | 29 | 10 | 22 | 25 | 8
 | 160 | 28 | 31 | 11 | 24 | 27 | 9
Notes: Say
It is important to note that the 2018 IRC has added a useful “Minimum Footing Size for Decks” table.
2018 IRC Table R507.3.1 Minimum Footing Size for Decks – Full version available at https://codes.iccsafe.org/public/document/IRC2018/chapter-5-floors

## Slide 47: Post-base to Foundation Connection
Resisting Lateral and Uplift Forces
Posts must be restrained to prevent lateral displacement at the bottom support
A positive connection shall be made to resist lateral and uplift forces
12-18 IRC R407.3 12-18 IRC R502.9 12 IBC 2304.9.7, 15-18 IBC 2304.10.7 15 IRC R507.8.1, 18 IRC 507.4
Where is the positive connection?
Notes: Say
Posts must be restrained to prevent lateral displacement at the bottom support. A positive connection shall be made to resist lateral and uplift forces.

## Slide 48: Post-base to Foundation Connection
Resisting Lateral and Uplift Forces
Pre-Manufactured Post Base with 1" Standoff Highly Recommended
As shown in Figure 507.3 of the 2018 IRC, it is recommended to use a code-listed pre-manufactured post base to connect the footer to the post. Otherwise, moisture may collect at the bottom of the post causing wood posts to rot and steel posts to corrode.
1" Standoff
Corroded steel post
Rotted wood post
Notes: Say
Pre-Manufactured Post Base with 1" Standoff Highly Recommended: As shown in Figure R507.3 of the 2018 IRC, it is recommended to use a code-listed pre-manufactured post base to positively connect the footer to the post. Otherwise, moisture may collect at the bottom of the post causing wood posts to rot and steels posts to corrode.

## Slide 49: Post-base to Foundation Connection
Resisting Lateral and Uplift Forces
Spread or Pad Footing Must Be Connected to the Pier or Concrete Stem
Provisions shall be made for the transfer of shear and other forces through construction joints. 08 ACI 318 6.4.3
Forces and moments at the base of the column shall be transferred to supporting pedestal by bearing on concrete and by reinforcement, dowels, and mechanical connectors. 08 ACI 318 15.8.1
Notes: Say
Spread or Pad Footing Must Be Connected to the Pier or Concrete Stem: Provisions shall be made for the transfer of shear and other forces through construction joints. Forces and moments at the base of the column shall be transferred to supporting pedestal by bearing on concrete and by reinforcement, dowels, and mechanical connectors.

## Slide 50: Lesson Two Complete
Now that we’ve completed this lesson, you should be able to:
Summarize the common code violations found during an inspection of new deck construction
Let’s Continue to
Lesson Three
Notes: Do
Review the lesson objective summary.

## Slide 51: INSPECTION OF EXISTING CONSTRUCTION
After completing this lesson, you will be able to:
Detect if an existing deck has developed a potentially unsafe issue and is no longer code-compliant
Notes: Do
Review the lesson title and objective.

## Slide 52: Five Things to Look for on an Existing Deck
It is recommended that you annually inspect your deck for issues that need to be addressed. It’s best to do this prior to seasons when you use your deck most. A deck should also be inspected prior to the purchase or sale of a home.
When inspecting a deck to determine overall safety and compliance with building codes, look at these five areas:
Improper connections
Loose connections
Corrosion
Decay
Splitting
1.
2.
3.
4.
5.
Notes: Say
It is recommended that you annually inspect your deck for issues that need to be addressed. It’s best to do this prior to seasons when you use your deck most.
A deck should also be inspected prior to the purchase or sale of a home.
When inspecting a deck to determine overall safety and compliance with building codes, look at these five areas:
Improper connections,
Loose connections,
Corrosion,
Decay, and
Splitting.

## Slide 53: Part 1: Improper Connections
1
What are Improper Connections?
Missing a Positive Connection
Fractured Connections by Bending Steel
Improper Connections
We’ll review the following topics:
Notes: Part 1: Improper Connections.
We’ll review the following topics:
What are Improper Connections?
Missing a Positive Connection
Fractured Connections by Bending Steel

## Slide 54: Improper Connections
What are Improper Connections?
Any connections that do not meet the requirements discussed in the codes can compromise the safety of the deck
In many cases, toenailing does not constitute a proper connection
Connectors must be installed with the correct fastener
Notes: Say
Any connections that do not meet the requirements discussed in the codes can compromise the safety of the deck. In many cases, toenailing (such as, joining two wood members with angled nailing) does not constitute a proper connection.
Connectors must be installed with the correct fastener.

## Slide 55: Improper Connections
Missing a Positive Connection
Nails, screws and spikes loaded in withdrawal from the end grain of the wood has been prohibited since the 1944 NDS
05 AWC NDS 11.2.3.2, 12 AWC NDS 11.2.3.5, 15 AWC NDS 12.2.3.5
Where is the positive connection to resist lateral and uplift forces?
Notes: Say
Nails, screws and spikes loaded in withdrawal from the end grain of the wood has been prohibited since the 1944 edition of the NDS.

## Slide 56: Improper Connections
Fractured Connections by Bending Steel
Bending steel in the field may cause fractures at the bend line
Fractured steel will not carry the load and must be replaced
Connectors shall be load-tested and code-listed to ensure a safe and strong deck
Field-bent steel in the field used for a girder-over-post connection may fracture and will not be able to carry the load.
Notes: Say
Bending steel in the field may cause fractures at the bend line.
Fractured steel will not carry the load and must be replaced.
Connectors shall be load-tested and code-listed to ensure a safe and strong deck.

## Slide 57: Part 2: Loose Connections
2
Loose Connections
What are Loose Connections?
Examples of Loose Connections
We’ll review the following topics:
Notes: Part 2: Loose Connections.
We’ll review the following topics:
What are Loose Connections?
Examples of Loose Connections

## Slide 58: Loose Connections
What are Loose Connections?
Vital connections may have degraded over time
Wobbly railings, loose stairs and ledgers that appear to be pulling away from the adjacent structure are all causes for concern
Notes: Say
Vital connections may have degraded over time. Wobbly railings, loose stairs and ledgers that appear to be pulling away from the adjacent structure are all causes for concern.

## Slide 59: Loose Connections
Notes: Do
Discuss the loose connection in each photo.
Left image: Rim joist’s connection into the end grain is very weak.
Middle image: Wood cleat on deck stairs is showing how the nails are withdrawing.
Right image: Stringer on deck stairs showing how the nails are withdrawing.

## Slide 60: Part 3: Corrosion
3
Corrosion
What is Corrosion?
Coating Recommendations
Dissimilar Metals in Contact with Each Other
We’ll review the following topics:
Notes: Part 3: Corrosion.
We’ll review the following topics:
What is Corrosion?
Coating Recommendations
Dissimilar Metals in Contact with Each Other

## Slide 61: Corrosion
What is Corrosion?
Ocean salt air, fire-retardants, fumes, fertilizers, preservative-treated wood, de-icing salts, dissimilar metals and more can cause corrosion
Metal connectors, fasteners, and anchors may lose load-carrying capacity if they corrode
It is impossible to predict when corrosion will begin or reach a critical level; this uncertainty makes it crucial to select a product suitable for the intended use
Common to see some corrosion in outdoor applications; even stainless steel can corrode
The presence of some corrosion does not mean that load capacity has been affected or that failure is imminent
Notes: Say
Corrosion is the deterioration of a metal as a result of chemical reactions between it and the surrounding environment.
Many environments and materials can cause corrosion including ocean salt air, fire-retardants, fumes, fertilizers, preservative-treated wood, de-icing salts, dissimilar metals and more. Metal connectors, fasteners, and anchors could corrode and lose load-carrying capacity when installed in corrosive environments or when installed in contact with corrosive materials.
The many variables present in a building environment make it impossible to accurately predict if, or when, corrosion will begin or reach a critical level. This relative uncertainty makes it crucial that specifiers and users are knowledgeable of the potential risks and select a product suitable for the intended use. It is also important that regular maintenance and periodic inspections are performed especially for outdoor applications.
It is common to see some corrosion in outdoor applications. Even stainless steel can corrode. The presence of some corrosion does not mean that load capacity has been affected or that failure is imminent. If significant corrosion is apparent or suspected, then the wood, fasteners, anchors, and connectors should be inspected by a qualified engineer or inspector. Replacement of affected components may be appropriate.
Do
Show students how to find the “General Corrosion Risks” webpage for more information. https://www.strongtie.com/products/product-use-information/corrosion-information/general-corrosion-risks

## Slide 62: Corrosion
Coating Recommendations
Connectors, anchors and fasteners feature a wide range of materials and coatings designed to meet specific performance criteria
It is important to select a material and/or coating that is suitable for the intended application and environment
Manufacturer recommendations for coatings shall govern unless the code or standard is more restrictive
Notes: Say
Connectors, anchors and fasteners feature a wide range of materials and coatings designed to meet specific performance criteria. It is important to select a material and/or coating that is suitable for the intended application and environment based upon factors such as corrosion resistance and mechanical properties of the material.
Manufacturer recommendations for coatings shall govern unless the code or standard is more restrictive.
Do
Show students how to find the “Guidelines for Selecting the Proper Materials and Coatings” webpage for more information. https://www.strongtie.com/products/product-use-information/corrosion-information/guidelines-for-selecting-proper-materials-and-coatings

## Slide 63: Corrosion
Coating Recommendations
Corrosion Resistance Recommendations
Low | Medium | High | Severe
Fasteners and Anchors |  |  | 
Phosphate (gray, black), Clear (bright) zinc (ASTM F1941), Heavy electro-galvanized (ASTM A641-Class 1), Yellow zinc (ASTM F1941), Electrocoat (E-coat), Type 410 stainless steel | Mechanically galvanized (AS 3566.2-C3, N2000, ASTM B695-Class 55), Quik Guard coating, Hot-dip galvanized (ASTM A153-Class D), Double-barrier coating, Type 410 stainless steel with protective top coat | Type 304 stainless steel, Type 305 stainless steel | Type 316 stainless steel, Hot-dip galvanized (ASTM A153-Class C), Silicon bronze, Copper
Connectors |  |  | 
SST gray paint, Powder coating, Standard G90 zinc coating | ZMAX (G185) Hot-dip galvanized (ASTM A653) | Type 316L stainless steel | Type 316L stainless steel
Notes: Do
Review table.
---
Low Corrosion Resistance: Primarily dry, interior, non-corrosive environments and applications.
Medium Corrosion Resistance: Primarily when stainless steel nor a “Low” level are recommended.
High Corrosion Resistance: When stainless steel is recommended; primarily wet service and uncertain environments.
Severe Corrosion Resistance: Primarily ocean and waterfront environments that include airborne chlorides and some splash.

## Slide 64: Corrosion
Coating Recommendations
Corrosion Resistance Classifications
Environment | Material to be Fastened |  |  |  |  |  | 
 | Untreated Wood or Other Material | Preservative-treated Wood |  |  |  |  | FRT Wood
 |  | SBX-DOT Zinc Borate | Chemical Retention ≤ AWPA, UC4A | Chemical Retention > AWPA, UC4A | ACZA | Other or Uncertain | 
Dry Service | Low | Low | Low | High | Med | High | Med
Wet Service | Med | N/A | Med | High | High | High | High
Elevated Service | High | N/A | Severe | Severe | High | Severe | N/A
Uncertain | High | High | High | Severe | High | Severe | Severe
Waterfront | Severe | N/A | Severe | Severe | Severe | Severe | N/A
Notes: Do
Review table.

## Slide 65: Corrosion
Dissimilar Metals in Contact with Each Other
When dissimilar metals are in contact with each other, the anode provides corrosion protection to the cathode by sacrificing itself.
To help reduce the possibility of galvanic corrosion of fasteners:
Use fasteners and metals with similar electrochemical properties
Separate dissimilar metals with insulating materials
Ensure that the fastener is the cathode when dissimilar metals are present
Prevent exposure to and pooling of electrolytes
Corroded End (Anode)
Magnesium, Magnesium alloys, Zinc
Aluminum 1100, Cadmium, Aluminum 2024-T4, Iron and Steel
Lead, Tin, Nickel (active), Inconel Ni-Cr alloy (active), Hastelloy alloy C (active)
Brasses, Copper, Cu-Ni alloys, Monel
Nickel (passive)
304 stainless steel (passive), 316 stainless steel (passive), Hasteloy alloy C (passive)
Silver, Titanium, Graphite, Gold, Platinum
Protected End (Cathode)
Notes: Say
When dissimilar metals are in contact with each other, the anode provides corrosion protection to the cathode by sacrificing itself.
The greater the separation between the two metals used, the greater the corrosion potential. For example, if zinc (galvanized steel) and stainless steel were in direct contact and in the presence of an electrolyte (water), galvanic corrosion will probably occur.
Good detailing practice, including the following, can help reduce the possibility of galvanic corrosion of fasteners:
Use fasteners and metals with similar electrochemical properties
Separate dissimilar metals with insulating materials
Ensure that the fastener is the cathode when dissimilar metals are present
Prevent exposure to and pooling of electrolytes

## Slide 66: Part 4: Decay
4
What is Decay?
Examples of Decay in Embedded Posts
Decay in Field-cut PPT Wood
Strength Loss as Wood Decays
Decay
We’ll review the following topics:
Notes: Part 4: Decay.
We’ll review the following topics:
What is Decay?
Examples of Decay in Embedded Posts
Decay in Field-cut PPT Wood
Strength Loss as Wood Decays

## Slide 67: Decay
What is Decay?
Wood can rot and degrade over time with exposure to the elements
Deck framing members that have rotted may no longer be able to perform the function for which they were installed
Notes: Say
Wood can rot and degrade over time with exposure to the elements. Deck framing members that have rotted may no longer be able to perform the function for which they were installed.

## Slide 68: Decay
Notes: Do
Review photos.
---
Left image: Here is a deck footing with embedded post in concrete. When the wood dries out, it shrinks and water (rain) gets into the opening causing the post to rot.
Right image: Here is a deck footing with embedded post in the ground. Posts in the ground may rot at the surface-to-ground interface, just below the surface.

## Slide 69: Decay
Decay in Field-cut PPT Wood
The code states that field-cut ends, notches and drilled holes of preservative pressure treated wood shall be treated in the field. Otherwise, the untreated field cuts will lead to decay and rot.
12-18 IRC R317.1.1
12 IBC 2303.1.8, 15-18 IBC 2303.1.9
Notes: Say
Wood can rot and degrade over time with exposure to the elements. Deck framing members that have rotted may no longer be able to perform the function for which they were installed.

## Slide 70: Decay
Strength Loss as Wood Decays
Dr. Al DeBonis stated that decay is visible to the eye starting at approximately 10%
A mere 5% weight loss—which is only detectable by a microscope—produces a 47% loss of bending strength
106 lb
5%
5% wood decayed
200 lb
0% wood decayed
To illustrate this concept, let’s say we have a wood guard post that has the capacity to resist 200 lb.
If 5% of the wood has decayed, the guard would only have the capacity to resist 106 lb.
Notes: Say
In an AWC webinar, Dr. Al DeBonis discussed the impact of early decay. He stated that decay is visible to the eye starting at approximately 10%. However, a mere 5% weight loss—which is only detectable by a microscope—produces a 47% loss of bending strength.
To illustrate this concept, let’s say we have a wood guard post that has the capacity to resist 200 pounds. If 5% of the wood has decayed, the guard would only have the capacity to resist 106 pounds.
Note: Instructions for how to do a pick test to detect decay can be found in “Manual for the Inspection of Residential Wood Decks and Balconies” by Cheryl Anderson, Dr. Frank Woeste, P.E., and Dr. Joseph Loferski (Forest Products Society, 2003).

## Slide 71: Part 5: Splitting
5
Splitting
What is Splitting?
Why Not Notch?
We’ll review the following topics:
Notes: Part 5: Splitting.
We’ll review the following topics:
What is Splitting?
Why Not Notch?

## Slide 72: Decay
What is Splitting?
As wood ages, it is common for splitting to develop
Large cracks or excessive splitting can weaken deck framing members
Notes: Say
As wood ages, it is common for splitting to develop. Large cracks or excessive splitting can weaken deck framing members.

## Slide 73: Decay
Why Not Notch?
Many years of observation have proved that moisture cycles (freezing & thawing, drying & wetting) will typically cause cracks to develop and propagate, parallel to the grain, from the corner of the notch. As a crack develops a steep “slope of grain” can critically reduce the section. This split or crack will continue to develop as the post is laterally loaded in service, which can lead to a failure.
- Dr. Frank Woeste, P.E., Virginia Tech
Notes: Say
Dr. Frank Woeste has this to say about notching: Many years of observation have proved that moisture cycles (freezing & thawing, drying & wetting) will typically cause cracks to develop and propagate, parallel to the grain, from the corner of the notch. As a crack develops a steep “slope of grain” can critically reduce the section. This split or crack will continue to develop as the post is laterally loaded in service, which can lead to a failure.

## Slide 74: Lesson Three Complete
Now that we’ve completed this lesson, you should be able to:
Detect if an existing deck has developed a potentially unsafe issue and is no longer code-compliant
Let’s Continue to the
Conclusion
Notes: Do
Review the lesson objective summary.

## Slide 75: Deck Evaluation Checklist
Deck Evaluation Checklist Overview
NADRA has produced a valuable resource to assist with the inspection of a new or existing deck. The checklist has been designed to be used as a streamlined, walk-up evaluation tool to check and note the various structural and safety components.
Notes: Say
NADRA has produced a valuable resource to assist with the inspection of a new or existing deck. The checklist has been designed to be used as a streamlined, walk-up evaluation tool to check and note the various structural and safety components.
The walk-up evaluation process is as follows:
Stairs
Footings/Deck Support and Posts/Columns
Beams and Joists
Ledger
Deck Boards/Deck Surface
Handrail Assemblies and Guards
Miscellaneous items such as hot tubs, grills, and lighting
Do
Pass out the Deck Evaluation Checklist and accompanying Code References handout to the class.

## Slide 76: COURSE COMPLETION
Questions?
NADRA Checklist and Course Materials
training.strongtie.com/deck
Notes: Do
Ask students if they have any questions regarding deck inspections or information presented in this course.
Let them know that the NADRA Deck Evaluation Checklist, accompanying code references, and course resources can be downloaded at training.strongtie.com/deck.

## Slide 77: Course Completion
Simpson Strong-Tie
This concludes the continuing education course
For a library of Simpson Strong-Tie courses,
visit strongtie.com/workshops
Notes: Do
Draw the meeting to a close. Hand out literature and business cards.
Say
If you have ongoing projects that you would be interested in reviewing together, please let me know.

## Slide 78: Next Steps!
AIA: For those seeking AIA LU/HSW: You will receive an email with a link allowing access to print your Certificate. Congratulations, you will have earned 1 LU/HSW credit. If your AIA member number has been inserted into your profile, Simpson Strong-Tie will report your credits on your behalf to the AIA. No test is required in order to receive HSW credits.
IACET: For those seeking IACET CEUs: You will receive an email with a link allowing access to print your Certificate of Attendance and instructions directing you to the Simpson Student Center to take the exam before credits can be awarded. Once the exam is taken and passed, you will have earned 0.1 CEUs (1 hour of credit). You can then access your Certificate of Completion from the Course Content tab. You must self-report your credits to your certifying organization or agency.
If you have questions or need assistance, please contact training@strongtie.com.
Notes: Presenter Notes:
Review the email and notification process as outlined in this slide.
AIA LUs:
For those that want AIA HSW credit, be sure to provide your AIA number on the sign-in sheet and Simpson will report your credits to the AIA on your behalf.
No test is required for AIA credit.
CEUs:
For those seeking CEUs, watch for an email with instructions to access the online test. After you have passed the test, you may access your Certification of Completion from the course content tab.
You must self-report your credits to your certifying organization or agency.

## Slide 79: Next Steps!
ICC: For those seeking ICC CEUs: You will receive an email with a link allowing access to print your Certificate. Congratulations, you will have earned 0.1 ICC CEUs (1 hour of credit). Please make sure your ICC member number has been inserted into your profile. It is your responsibility to self-report your credits to the ICC. Please retain your Completion Certificate for your records.
IACET: For those seeking IACET CEUs: You will receive an email with a link allowing access to print your Certificate of Attendance and instructions directing you to the Simpson Student Center to take the exam before credits can be awarded. Once the exam is taken and passed, you will have earned 0.1 CEUs (1 hour of credit). You can then access your Certificate of Completion from the Course Content tab. You must self-report your credits to your certifying organization or agency.
If you have questions or need assistance, please contact training@strongtie.com.
Notes: Presenter Notes:
Review the email and notification process as outlined in this slide.
Watch for an email directing you to the Student Center to print your certificate.
No test is required for ICC credit. You must self-report your credits to ICC.
For those seeking general IACET CEUs after you have passed the online test, you may access your Certification of Completion from the course content tab. You must self-report your credits to your certifying organization or agency.