## Slide 1
PLEASE READ
Dear Instructor,
This presentation is available in both AIA and ICC versions.
For AIA: Right click and un-hide slides 5 and 131
For ICC: Right click and un-hide slides 6 and 132
Slide 2 is an optional slide

## Slide 2: Welcome!
We will begin in a few minutes.
Please be sure to sign the registration form to receive credit for attending today’s learning event.
Notes: Do
Meet and greet participants as they arrive. Start learning names, make them feel comfortable and settled in the training environment.
Make sure your opening has PUNCH:
Promotes interest and enthusiasm for the session
Understands participants’ needs
Notes ground rules and administrative/housekeeping needs
Clarifies expectations
Helps everyone get to know each other
State your expectations around participation: Make it known and expected that you will be encouraging and inviting participation.
Tips to facilitate connections:
Thank participants for their contribution (ideally with their name)
Praise participation (especially the first person to speak)
Express confidence in the participants
Restate what someone said earlier (“As John mentioned earlier….”)
Encourage participants to share what others were saying in their small groups (without naming names)
Invite someone you heard speaking in a small group to share with the entire group
Encourage the group to respond to an individual’s comment/question
Physical Room / Training Venue Setup:
If using a table arrangement, consider grouping 4 to 6 students at each station. This will help encourage conversation and discussion during activities.
Get people standing at regular intervals during your training session. Research shows that people learn up to 15% more when standing up!

## Slide 3: Understanding Moment Frames
Instructor Name | Title
AIA Provider: 50119826 | AIA Course: AIA-UMF10217 | ICC Provider: 1025 | ICC Course: 10788
Notes: Do
Be sure to mention the AIA/ICC provider and course number for those requiring AIA/ICC credit. Ask the attendees to write down this information for reference. For AIA members, we will submit this information for them.

## Slide 4: Credit Information
IACET Accreditation Information
Simpson Strong-Tie® has been accredited as an Authorized Provider by the International Association for Continuing Education and Training (IACET). As a result of their Authorized Provider accreditation status, Simpson Strong-Tie® is authorized to offer IACET CEUs for its programs that qualify under the ANSI/IACET Standard.
This course offers 0.2 CEU (2 hours of credit).
Notes: Review the submission process for audiences requiring IACET CEU credits.
For those seeking IACET credit, they must take and pass the online test. They must self-report CEU credits to their certifying organization or agency.
Explain the credits awarded: IACET: 0.2 (Equivalent to 2 hours) CEUs.

## Slide 5: Credit Information
AIA Member Information
This course is registered with AIA CES for continuing professional education. As such, it does not include content that may be deemed or construed to be an approval or endorsement by the AIA of any material of construction or any method or manner of handling, using, distributing, or dealing in any material or product. Upon completion of this course, Credit(s) earned will be reported to AIA CES for AIA members who pass the course and have entered their AIA member number on their Simpson profile page. A link to the Certificate of Completion will be available upon completion of this course. Only AIA LU/HSW will be reported.
This course offers 2 LU/HSW credits.
AIA Course Number: AIA-UMF10217
Notes: Presenter Information
NOTE: Please be sure each attendee LEGIBLY signs the event sign-in sheet.
Say
All questions concerning proprietary products will be addressed after the conclusion of the AIA portion of the presentation. The meeting format is 110 minutes of content, followed by 10 minutes of Q & A.
Do
Explain the credits awarded for:
AIA: 2LU/HSW credits.
IACET: 0.2 (Equivalent to 2 hours) CEU credits.
Review the submission process for audiences requiring either AIA LU/HSW (health, safety and welfare) credits or CEU credits:
For those seeking AIA HSW credit, there is no test required. AIA members must be sure to provide their AIA member number on the sign-in sheet. Please make sure name, email and AIA member number are clearly printed so Simpson can report credits to the AIA on their behalf.
For those seeking IACET credit, they must take and pass the test. They must self-report CEU credits to their certifying organization or agency.

## Slide 6: Credit Information, cont.
ICC Member Information
This course has been approved by the International Code Council (ICC) for continuing professional education. For learners that complete this course, it is your responsibility to self-report your credits to the ICC. Please retain your Completion Certificate for your records.
Be sure that your ICC ID number is provided on the sign-in sheet or in your Simpson profile in order to have it displayed on your certificate.
This course offers 0.2 CEU (2 hour of credit).
ICC Course Number: 10788
Notes: Review the submission process for audiences requiring ICC CEU credits.
For those seeking ICC credit, there is no test required. ICC members must provide their ICC ID number on the sign-in sheet or in their Simpson profile in order to have it displayed on their certificate. It is the responsibility of the participant to self-report their credits to the ICC. Ask them to retain their Completion Certificate for their records.
Explain the credits awarded: ICC: 0.2 (Equivalent to 2 hours) CEUs.

## Slide 7: Additional Credit Offerings
Visit
strongtie.com/workshops
for more information
Course Name | CEUs | AIA | ICC
Introduction to Deck Design | 0.1 | ✔ | ✔
Introduction to Wind Design and the Wood Frame Construction Manual | 0.1 | ✔ | ✔
Shear Walls and Lateral Bracing in Light Frame Construction | 0.1 | ✔ | ✔
Understanding Restraint Rod Systems | 0.1 | ✔ | ✔
Cracking the Concrete Anchor Codes | 0.1 | ✔ | ✔
Concrete Deterioration | 0.1 | ✔ | ✔
Moment Frame Design | 0.1 | ✔ | ✔
Introduction to Wind Code Provisions and Meteorological Concepts | 0.1 | ✔ | ✔
Wind Design in Accordance with ASCE 7-10 | 0.1 | ✔ | ✔
Wood Framed Seismic Design 1: Code Provisions, Design Parameters | 0.1 | ✔ | ✔
Notes: Do
Explain that we have additional PK topics available that offer credit for ICC members and HSW credits for AIA members.
Explain that we have a library of online courses available in our Simpson Student Center that also offer ICC and AIA HSW credits. They can access our online courses at strongtie.com/workshops.

## Slide 8: Course Description
This is a technical course intended primarily for structural engineers and designers interested in understanding and designing steel moment frames. This course reviews the types and applications of steel moment frames and walks through a design solution for pre-fabricated moment frame solutions.
Course Contents
Introduction / Learning Objectives
Lesson 1: Moment Frame Design Background
Lesson 2: Code Limitations and Requirements
Lesson 3: Moment Frame Applications
Lesson 4: Moment Frame Design Solutions
Lesson 5: Design Example

## Slide 9: Learning Objectives
Upon completion of this seminar, you will be able to:
Describe the differences between the types of steel moment frames
Summarize how steel moment frames are used in the field for new and existing construction
Articulate the code limitations and requirements for steel moment frames

## Slide 10: Learning Objectives, cont.
Upon completion of this seminar, you will be able to:
Explain the proper application of ordinary moment frames and special moment frames
Explain the advantages of using a predesigned and manufactured steel moment frame
Demonstrate how to determine the necessary specifications for an ordinary moment frame application

## Slide 11: LESSON 1
Moment Frame Design Background
After completing this lesson, you will be able to:
Describe the differences between the types of steel moment frames
Summarize how steel moment frames are used in the field for new and existing construction
Notes: After completing this lesson, you will be able to:
Describe the differences between the types of steel moment frames
Summarize how steel moment frames are used in the field for new and existing construction

## Slide 12: What is a Moment Frame?
Moment frames…
Resist forces primarily through bending of beams and columns
Have welded or bolted connections
Are designed to carry vertical loads and lateral wind or seismic loads
Can be used for engineered designs as well as prescriptive code requirements
Notes: Say
Moment frames consist of beams and columns, typically connected by a combination of bolts and welds to form rigid joints. The frames resist lateral loads caused by wind or seismic forces primarily through bending in the beams and columns.
Moment frames:
Resist forces primarily through bending of beams and columns
Have connections that are either welded or bolted
Are designed to carry vertical gravity loads as well as lateral wind or seismic loads
Can be used for engineered designs as well as prescriptive code requirements

## Slide 13: Introduction to Moment Frames
Why steel?
Steel-frame structures were developed in response to the limitations of masonry-bearing wall structures.
Notes: Say
Steel-frame structures were developed during the 19th century in response to the limitations of masonry-bearing wall structures, which were the common method of commercial construction at the time. These masonry-bearing wall structures were limited to about 10 stories high and allowed for only small openings because of the limited strength of masonry materials.

## Slide 14: Introduction to Moment Frames, cont.
New solutions were explored
Property owners want the maximum amount of rentable space on their land and plenty of natural light let in by large openings.
Notes: Say
Since property owners back then wanted the same things that developers and architects want today—the maximum amount of rentable space on their land and plenty of natural light let in by large openings—new solutions were explored.

## Slide 15: Introduction to Moment Frames, cont.
Steel moment frames were the answer to these demands
Originally intended for use in high-rise construction, steel moment frames have evolved to encompass a large number of residential and mixed-use projects because of the flexibility they give designers.
Notes: Say
Steel-frame building construction using rigid frames, or moment frames, was the answer to these demands.
While originally intended for use in high-rise construction, the use of steel moment frames has evolved to encompass a large number of residential and light-framed, mixed-use projects because of the flexibility they give designers (such as larger openings with smaller structural members).
Quiz Note
This slide features information that will be found on the post-course knowledge assessment.
True or false: Moment frames were originally constructed for use in high-rise construction and evolved to residential applications.
True
False

## Slide 16: Brief History of Moment Frames
The conception of early moment frames
Early steel moment frames used riveted connections with angles or T-sections connecting the beam flanges to the columns to create moment connections.
New welding technologies and high-strength bolts ended the use of riveting.
The Welded Flange Connection became one of the most common moment frame joints.
❶
❷
❸
❹
❶ Complete joint penetration weld top and bottom flanges
❷ Weld backing left in place (Pre-Northridge)
❸ Weld access hole
❹ Shear tab with high-strength bolts
Notes: Say
The earliest steel moment frame buildings used riveted connections with angles or T-sections connecting the beam flanges to the columns to create moment connections. The development of new welding technologies throughout the 20th Century and the introduction of high-strength bolts in the 1950s ended the use of riveting in building and bridge construction in the United States.
The Welded Flange connection became one of the most common moment frame joints, using either a bolted or welded shear tab for vertical loads, and complete joint penetration welds for the beam flange-to-column flange moment connection (see image to the right).

## Slide 17: Brief History of Moment Frames, cont.
Expected failure points
Steel moment frames are expected to achieve ductility through yielding beams or columns.
Connections must be capable of remaining intact through several cycles of inelastic rotation due to seismic loading.
During 1994 Northridge Earthquake, standard connection at the time fractured at low levels of plastic deformation.
Notes: Say
Steel moment frames are expected to achieve ductility, the ability for a material to deform under tensile stress, through yielding beams or columns, and the connections must be capable of remaining intact through several cycles of inelastic rotation due to seismic loading. In other words, the steel is expected to fail by bending and deforming and not by a sudden, brittle failure.
The 1994 Northridge Earthquake demonstrated that the standard connection at the time did not perform as expected, in many cases fracturing or breaking at low levels of plastic deformation. Failures in the moment frame connections were attributed to multiple causes and are well documented.

## Slide 18: Brief History of Moment Frames, cont.
Perceived Shaking | Not Felt | Weak | Light | Mod. | Strong | Very Strong | Severe | Violent | Extreme
Potential Damage | None | None | None | Very Light | Light | Mod. | Mod. / Heavy | Heavy | Very Heavy
Peak Acc. (%g) | <0.17 | 0.17-1.4 | 1.4-3.9 | 3.9-9.2 | 9.2-18 | 18-34 | 34-65 | 65-124 | >124
Peak Vel. (cm/s) | <0.1 | 0.1-1.1 | 1.1-3.4 | 3.4-8.1 | 8.1-16 | 16-31 | 31-60 | 60-116 | >116
Instrumental Intensity | I | II-III | IV | V | VI | VII | VIII | IX | X+
1994 Northridge Earthquake
Game changer for seismic design: The performance of welded steel moment frames during that time did not live up to expectations.
A large number of steel buildings with welded moment frame connections failed.
Notes: Say
The Northridge earthquake was a game changer for seismic design. It was the first major earthquake that put a large number of moment frame designs to the test. The performance of welded steel moment frames during that time did not live up to expectations. The large number of failed steel buildings with welded moment frame connections shed light on the overlooked issues surrounding field welding procedures.

## Slide 19: Brief History of Moment Frames, cont.
Results of Northridge
Magnitude of 6.7
$57 billion in damages
New regulations adapted:
AISC adopts prequalification standards
All moment frames in seismic areas have to be prequalified or otherwise tested and accepted
Failures need to be calculated and controlled
Notes: Say
The 1994 Northridge Earthquake had a magnitude of 6.7 with the highest recording ground acceleration, causing $57 billion in damages.
Due to the devastating structural damage of the earthquake, a number of new regulations were adapted. The AISC adopted prequalification standards for moment frames. All steel moment frames in seismic areas would now have to be tested and accepted by the ICC or local jurisdictions.

## Slide 20: Brief History of Moment Frames, cont.
Damage caused by Northridge
Most damage occurred in buildings identified as those with low seismic resistance and high risk of damage.
There were unpredicted failures in moment-frame buildings, such as brittle fractures of the frame at the welded beam-column connection. This was generally isolated to Welded Steel Moment Frames.
Notes: Say
Most of the damage occurred in buildings identified as those with low seismic resistance and high risk of damage—such as old masonry and concrete buildings.
There were unpredicted failures in moment-frame buildings, such as brittle fractures of the frame at the welded beam-column connection. This was generally isolated to Welded Steel Moment Frames (WSMF).
Most damaged structures revealed no visible signs of failures making detection difficult and expensive.

## Slide 21: Brief History of Moment Frames, cont.
The Los Angeles Ordinance
The results of the damage inspection included:
Imperfections in original construction work
A third of the buildings inspected had damage resulting from the earthquake
90% of the total damage occurred in approximately 30 buildings
Notes: Say
The City of Los Angeles enacted an ordinance following the Northridge earthquake to requiring inspection of the damage.
200 buildings inspected in the area where ground motion was most severe. Initial reports indicated nearly all buildings saw signs of damage but this was later found to be incorrect.
The results of the damage inspection included:
Imperfections in original construction work
33% of those inspected had damage resulting from the earthquake
90% of the total damage occurred in approximately 30 buildings

## Slide 22: Brief History of Moment Frames, cont.
The SAC Joint Venture
In mid-1994, the SAC Joint Venture was established.
It was tasked with developing new design recommendations for welded steel moment frames.
Documents addressed the design of moment frames in new structures, repair and evaluation of existing structures, and quality control guidelines.
Notes: Say
In mid-1994, the SAC Joint Venture was established, bringing together the Structural Engineers Association of California (SEAOC), Applied Technology Council (ATC), and Consortium of Universities for Research in Earthquake Engineering (CUREE).
Funded by Federal Emergency Management Agency (FEMA), SAC was tasked with developing new design recommendations for welded steel moment frames.
Several documents were published to address the design of moment frames in new structures, repair and evaluation of existing structures, and quality control guidelines.

## Slide 23: Brief History of Moment Frames, cont.
New design requirements
New design requirements were developed in a relatively short time frame.
They were not uniformly adopted by building jurisdictions.
Recommendations for design and quality control contained in FEMA publications have been incorporated into the AISC Seismic Provisions for Structural Steel Buildings.
Notes: Say
The period after the 1994 Northridge Earthquake held some uncertainty for structural engineers. Many new design requirements were developed in a relatively short time frame and were not uniformly adopted by building jurisdictions. Fortunately, the recommendations for design and quality control contained in the numerous FEMA publications have been incorporated into the American Institute of Steel Construction Seismic Provisions for Structural Steel Buildings.

## Slide 24: Types of Moment Frames
Ordinary Moment Frame (OMF)
OMFs are expected to withstand limited inelastic deformations in their members and connections as a result of lateral forces.
They are typically used in non- or low- seismic regions.
Richard, Dylan. “Steel Moment Frames 101: What to consider when creating wide-open spaces.” Structural Engineer, 2008.
Ordinary Moment Frames
Intermediate Moment Frames
Special Moment Frames
Notes: Say
Ordinary Moment Frames are expected to withstand limited inelastic deformations in their members and connections as a result of lateral forces.

## Slide 25: Types of Moment Frames, cont.
Intermediate Moment Frame (IMF)
IMFs are expected to withstand limited inelastic deformations in their members and connections as a result of lateral forces and require the use of prequalified connections per the American Institute of Steel Construction (AISC) or connections that have undergone and passed a qualifying cyclic test.
They must sustain an inter-story drift angle of up to 0.02 radians, and are typically used in low- to mid- seismic regions.
Richard, Dylan. “Steel Moment Frames 101: What to consider when creating wide-open spaces.” Structural Engineer, 2008.
Ordinary Moment Frames
Intermediate Moment Frames
Special Moment Frames
Notes: Say
Intermediate Moment Frames are expected to withstand limited inelastic deformations in their members and connections as a result of lateral forces and require the use of pre-qualified connections.

## Slide 26: Types of Moment Frames, cont.
Special Moment Frame (SMF)
SMFs are expected to withstand significant inelastic deformation in their members and connections as a result of lateral forces and require the use of prequalified connections per AISC or connections that have undergone and passed a qualifying cyclic test.
They must sustain an inter-story drift angle of up to 0.04 radians, and are typically used in mid- to high- seismic regions.
Richard, Dylan. “Steel Moment Frames 101: What to consider when creating wide-open spaces.” Structural Engineer, 2008.
Ordinary Moment Frames
Intermediate Moment Frames
Special Moment Frames
Notes: Say
Special Moment Frames are expected to withstand significant inelastic deformation in their members and connections as a result of lateral forces and require the use of pre-qualified connections.

## Slide 27: Moment Frame Uses
Larger openings for a variety of applications
Moment frames allow larger openings and smaller wall sections while still providing the loads structural designers need.
Applications:
Garage Fronts
Large Entryways
Walls with Large Openings
Tuck-under Parking
Great Rooms
Notes: Say
Moment frames allow larger openings and smaller wall sections while still providing the loads structural designers need.
Moment frames are commonly used in applications such as garage fronts, large entryways, walls with large, numerous windows, tuck-under parking and great rooms.

## Slide 28: Overview of Connection Types
1
2
3
Welded
Welded Moment Connections
Bolted
Bolted Moment Connections
Proprietary
Proprietary Moment Connections
Next, we’ll review each of these connection types
Notes: Say
There are three connection types that are commonly available for moment frames.
The available connection types are: Welded Moment Connections, Bolted Moment Connections, and Proprietary Moment Connections.
Quiz Note
This slide features information that will be found on the post-course knowledge assessment.
Which of the following is not a moment frame connection type?
Bending moment connection
Welded moment connection
Bolted moment connection
Proprietary moment connection

## Slide 29: Connection Type: Welded
RBS (Dog Bone)
Free Flange
WUF-W
WFP
Welded Connection
RBS (Dog Bone)
Notes: Do
Review the types of welded connections.

## Slide 30: Connection Type: Welded, cont.
RBS (Dog Bone)
Free Flange
WUF-W
WFP
Welded Connection
Free Flange
Notes: Do
Review the types of welded connections.

## Slide 31: Connection Type: Welded, cont.
RBS (Dog Bone)
Free Flange
WUF-W
WFP
Welded Connection
Welded Unreinforced Flange-Welded Web
Notes: Do
Review the types of welded connections.

## Slide 32: Connection Type: Welded, cont.
RBS (Dog Bone)
Free Flange
WUF-W
WFP
Welded Connection
Welded Flange Plate
Notes: Do
Review the types of welded connections.

## Slide 33: Connection Type: Bolted
BFP
DST
BUEP
BSEP
Bolted Connection
Bolted Flange Plate
Notes: Do
Review the types of bolted connections.

## Slide 34: Connection Type: Bolted, cont.
BFP
DST
BUEP
BSEP
Bolted Connection
Double Split T
Notes: Do
Review the types of bolted connections.

## Slide 35: Connection Type: Bolted, cont.
BFP
DST
BUEP
BSEP
Bolted Connection
Bolted Unstiffened End Plate
Notes: Do
Review the types of bolted connections.

## Slide 36: Connection Type: Bolted, cont.
BFP
DST
BUEP
BSEP
Bolted Connection
Bolted Stiffened End Plate
Notes: Do
Review the types of bolted connections.

## Slide 37: Connection Type: Proprietary
Proprietary Side Plate
Proprietary Slotted Web
Kaiser Bolted Bracket
Proprietary Connection
Proprietary Side Plate Connection
Notes: Do
Review the types of proprietary connections.

## Slide 38: Connection Type: Proprietary, cont.
Proprietary Side Plate
Proprietary Slotted Web
Kaiser Bolted Bracket
Proprietary Connection
Proprietary Slotted Web Connection
Notes: Do
Review the types of proprietary connections.

## Slide 39: Connection Type: Proprietary, cont.
Proprietary Side Plate
Proprietary Slotted Web
Kaiser Bolted Bracket
Proprietary Connection
Kaiser Bolted Bracket Connection
Notes: Do
Review the types of proprietary connections.

## Slide 40: Inelastic Deformation
What happens when the force is removed?
Inelastic deformation is the deformation of a structural element where the element does not return to the original shape after the force is removed.
This may be the result of large forces during an earthquake that are far in excess of normal structural loading conditions.
INELASTIC DEFORMATION
Notes: Say
Inelastic deformation is the deformation of a structural element where the element does not return to the original shape after the force is removed.
This may be the result of large forces during an earthquake that are far in excess of normal structural loading conditions.
Quiz Note
This slide features information that will be found on the post-course knowledge assessment.
This image is an example of which of the following? [Image on this slide will be shown on the test]
Inelastic deformation
Elasticity
Racking
None of the above

## Slide 41: The Importance of Ductility
What is ductility?
Ductility is the ability to sustain large inelastic deformations without significant loss in strength.
Why is ductility important?
Permits redistribution of internal stresses and forces
Results in more robust structures
Provides warning of failure
Permits structure to survive severe earthquake loading
Ductility = inelastic deformation capacity
Notes: Say
Ductility is the ability to sustain large inelastic deformations without significant loss in strength.
Ductility is important because it:
Permits redistribution of internal stresses and forces
Results in more robust structures
Provides a warning of failure
Permits the structure to survive severe earthquake loading

## Slide 42: Ductility Comparison
SMF is among the most ductile lateral-force resisting systems
M
ϴ
OMF
SMF
IMF
Minimal Ductility
Moderate Ductility
High Ductility
Notes: Say
The steel moment frame is among the most ductile lateral-force resisting.

## Slide 43: Response Modification Coefficients (R-Values)
What is an R-Value?
R represents the ratio of forces that would develop under the specified ground motion if the structure had an entirely linearly elastic response, and is the measure of the ability of the system to absorb energy and sustain cyclic inelastic deformations without collapse.
The higher the R-Value, the more ductile a system is, and as such, the lower the force.
The lower the R-Value, the more brittle the system is.
Notes: Say
R represents the ratio of forces that would develop under the specified ground motion if the structure had an entirely linearly elastic response, and is the measure of the ability of the system to absorb energy and sustain cyclic inelastic deformations without collapse.
The higher the R-Value, the more ductile a system is, and as such, the lower the force. The lower the R-Value, the more brittle the system is.

## Slide 44: Response Modification Coefficients (R-Values), cont.
Comparison of R-Values
Here are some examples of R-Values for different structural systems from the 2012 International Building Code (IBC).
Special Moment Frames (SMF) R = 8.0
Plywood Shear Walls R = 6.5
Special Reinforced Concrete Shear Walls R = 5.0
Intermediate Moment Frame (IMF) R = 4.5
Ordinary Moment Frame (OMF) R = 3.5
Cantilevered Steel Columns R = 2.5
Notes: Say
Here are some examples of R-values for different structural systems from the International Building Code. Note that the higher the R-Value, the more ductile the structural system.
Quiz Note
This slide features information that will be found on the post-course knowledge assessment.
Which of the following has the highest R-Value?
Special Moment Frame
Pre-Engineered Shear Wall
Ordinary Moment Frame
Braced Wall

## Slide 45: Moment Frame Requirements Comparison
 | OMF | IMF | SMF
Expected to withstand… | Limited inelastic deformations | Limited inelastic deformations | Significant inelastic deformations
Prequalified connections | Not required | Required (per AISC) | Required (per AISC)
Testing requirements | Not required | Must sustain inter-story drift angle of up to 0.02 radians | Must sustain inter-story drift angle of up to 0.04 radians
Region use | Non/low seismic regions | Typically used in low/mid seismic regions | Typically used in mid/high seismic regions
Notes: Say
The differences between types of moment frames revolve around ability to withstand inelastic deformations, the use of prequalified connections, testing requirements, and what level of seismic activity they can handle.
Do
Review the table.

## Slide 46: Lesson One Complete
Now that you’ve completed this lesson, you should be able to:
Describe the differences between the types of steel moment frames
Summarize how steel moment frames are used in the field for new and existing construction
Notes: Do
Review the slide.

## Slide 47: LESSON 2
Code Limitations and Requirements
After completing this lesson, you will be able to:
Articulate the code limitations and requirements for steel moment frames
Notes: After completing this lesson, you will be able to:
Articulate the code limitations and requirements for steel moment frames

## Slide 48: Moment Frames and Building Codes
Moment Frame
Frames are covered under the following:
2012 IBC, 2015 IBC
ASCE/SEI 7-10
AISC Steel Construction Manual, 14th Edition (AISC 360-10)
AISC Seismic Provisions for Steel Buildings (AISC 341-10)
Moment Frame
Beam-Column Connection
Base Plate Connection
Wood Beam Nailer Attachment
Anchorage
Notes: Say
Moment frames are covered in many of the present day building codes.

## Slide 49: Moment Frames and Building Codes, cont.
Beam-Column Connection
Beam column connections (bolted unstiffened end plate) are covered under the following:
ASCE Design Guide #4 and #16
2009 RCSC Specification for Structural Joists using ASTM A325 or A490 bolts
Moment Frame
Beam-Column Connection
Base Plate Connection
Wood Beam Nailer Attachment
Anchorage
Notes: Moment frames are covered in many of the present day building codes.

## Slide 50: Moment Frames and Building Codes, cont.
Base Plate Connection
Base plate connections are covered under the following:
AISC Design Guide #1
Moment Frame
Beam-Column Connection
Base Plate Connection
Wood Beam Nailer Attachment
Anchorage
Notes: Moment frames are covered in many of the present day building codes.

## Slide 51: Moment Frames and Building Codes, cont.
Wood Beam Nailer Attachment
Wood beam nailer attachments are covered under the following:
ASCE/SEI 7-10
2015 NDS
Moment Frame
Beam-Column Connection
Base Plate Connection
Wood Beam Nailer Attachment
Anchorage
Notes: Moment frames are covered in many of the present day building codes.

## Slide 52: Moment Frames and Building Codes, cont.
Anchorage
The following anchor types are covered as shown here:
Anchor rod strength: ACI 318-14, 17.5.1
Anchor breakout strength in tension: ACI 318-14, 17.5.2
Anchor pullout strength in tension: ACI 318-14, 17.5.3
Embedded plate bending strength: AISC Chapter F
Concrete shear strength – shear lug: AISC Design Guide 1
Concrete shear strength – tied anchorage: ACI 318-14, Ch. 9
Moment Frame
Beam-Column Connection
Base Plate Connection
Wood Beam Nailer Attachment
Anchorage
Notes: Moment frames are covered in many of the present day building codes.

## Slide 53: Introduction to Moment Frame Limitations
Codes have the following moment frame limitations
Weight and height limitations based on the moment frame type and seismic design category
Use of OMFs in combination with other lateral systems:
  In different directions
  In the same direction
Notes: Say
Codes have weight and height limitations based on the type of moment frame and the seismic design category. There are also limitations on the use of ordinary moment frames in combinations with other lateral systems.

## Slide 54: Limitations in High Seismic Areas
Are ordinary moment frames allowed in high seismic areas (SDC D, E and F)?
ASCE 7-10: Minimum Loads for Buildings and Other Structures Table 12.2-1 says NP for Not Permitted
Exceptions in footnotes h and i
h. See section 12.2.5.7 for limitations of Steel IMFs in SDC D, E or F
i. See section 12.2.5.6 for limitations of Steel OMFs in SDC D or E
Notes: Say
Ordinary moment frames are Not Permitted in high seismic areas (SDC D, E, F), according to ASCE 7-10 Table 12.2-1.
However, there are exceptions in footnotes h and i. Let’s review those in the next few slides.

## Slide 55: Limitations in High Seismic Areas, cont.
ASCE 7-10 §12.2.5.6 Steel Ordinary Moment Frames
Under ASCE 7-10 Section 12.2.5.6.1, steel ordinary moment frames are permitted in Seismic Design Categories D or E under the following limitations:
Section A | Section B (if Section A limitations cannot be met)
Single story limitation up to 65 ft | Single story limitation up to 35 ft
20 psf roof weight limit | 35 psf roof weight limit
20 psf exterior wall limit over 35 ft | 20 psf exterior wall limit
Notes: Say
Under ASCE 12.2.5.6.1, in Seismic Design Categories D or E, steel ordinary moment frames are permitted with limitations.
Do
Review limitations listed on slide.
Quiz Note
This slide features information that will be found on the post-course knowledge assessment.
Under ASCE 12.2.5.6, in Seismic Categories D or E, ordinary moment frames are:
Not permitted
Permitted with limitations
Permitted with the same limitations as Seismic Category F

## Slide 56: Limitations in High Seismic Areas, cont.
ASCE 7-10 §12.2.5.7 Steel Intermediate Moment Frames
Under ASCE 7-10 Section 12.2.5.7.1, steel intermediate moment frames are permitted in Seismic Design Category D under the following limitations:
Section A | Section B (if Section A limitations cannot be met)
Single story limitation up to 65 ft | Single story limitation up to 35 ft
20 psf roof weight limit | --
20 psf exterior wall limit over 35 ft | --
Notes: Say
Under ASCE 12.2.5.7.1, in Seismic Design Category D, steel intermediate moment frames are permitted with limitations.
Do
Review limitations listed on slide.

## Slide 57: Limitations in High Seismic Areas, cont.
ASCE 7-10 §12.2.5.7 Steel Intermediate Moment Frames, cont.
Under ASCE 7-10 Sections 12.2.5.7.2 and 12.2.5.7.3, steel intermediate moment frames are permitted in Seismic Design Categories E or F under the following limitations:
Section A | Section B (if Section A limitations cannot be met)
Single story limitation up to 65 ft | Single story limitation up to 35 ft
20 psf roof weight limit | 35 psf roof weight limit
20 psf exterior wall limit over 35 ft | 20 psf exterior wall limit
Notes: Say
Under ASCE 12.2.5.7.2, in Seismic Design Categories E or F, steel intermediate moment frames are permitted with limitations.
Do
Review limitations listed on slide.

## Slide 58: Additional Limitations
ASCE 7-10 Section 12.2.2 Combinations of Framing Systems in Different Directions
Use the more stringent height and SDC limits
Use respective R, Cd and Ω in each direction
Example: Steel OMF and Wood Shear Walls
Limited to 35-ft and SDC E
R (OMF) = 3.5
R (Shear Walls) = 6.5
Notes: Say
There is an additional design limitation for using an ordinary moment frame is if the design used different lateral systems in the building. One example of this is a combination of a steel ordinary moment frame and wood shear walls. Wood shear walls are designed with R = 6.5 and can be used in structures taller than 35 feet, but when used in combination with a steel OMF, you would be limited to the restrictions of the steel OMF for the entire structure.

## Slide 59: Additional Limitations, cont.
ASCE 7-10 Section 12.2.3 Combinations of Framing Systems in the Same Direction
Use the more stringent height and SDC limits
ASCE 7-10 Section 12.2.3.1 Vertical Combinations
R for design at any story shall not exceed the lowest. R-Value that is used in the same direction at any story above that story. Each line may be designed for the lowest R-Value along that line provided the following are met:
Occupancy Category I or II Building
Two stories or less in height
Use of light-frame construction or flexible diaphragms
ASCE 7-10 Section 12.2.3.3 Horizontal Combinations
Diaphragms: R = lowest R of any system in that direction
Notes: Say
The additional limitation for combining lateral systems applies for both horizontal combinations (different lateral systems for the same floor level) and vertical combinations (different lateral systems for different floor levels). The diaphragms would also be affected by having to use the lower R design value as well.

## Slide 60: Additional Limitations, cont.
Ordinary Moment Frames for Wind Design
No drift requirements for wind
No R-Values for wind design
2015 International Building Code
1604.10 Wind and seismic detailing.
Lateral force-resisting systems shall meet seismic detailing requirements and limitations prescribed in this code and ASCE 7-10, excluding Chapter 14 (Material Specific Design and Detailing) and Appendix 11A (Quality Assurance Provisions), even when wind load effects are greater than seismic load effects.
Notes: Say
It should be noted that the additional limitations mentioned in the previous slides apply to seismic design only. There are no drift requirements or R-values that are applied to wind designs. The 2015 International Building code has a new provision regarding wind and seismic detailing that does note that lateral force resisting systems must meet seismic requirements even when the wind load effects are greater than the seismic load effects.

## Slide 61: Lesson Two Complete
Now that you’ve completed this lesson, you should be able to:
Articulate the code limitations and requirements for steel moment frames
Notes: Do
Review the slide.

## Slide 62: LESSON 3
Moment Frame Applications
After completing this lesson, you will be able to:
Explain the proper application of ordinary moment frames and special moment frames
Notes: After completing this lesson, you will be able to:
Explain the proper application of ordinary moment frames and special moment frames

## Slide 63: Challenges with Modern Design
Application Challenges and Issues
The following slides demonstrate some of these applications and the challenges faced with modern designs. The issues include:
Generally much larger structures
Many windows leave little opportunity for conventional bracing
Heavy finishes combined with open floor plans (large spans) result in higher design loads on lateral elements
Notes: Say
The following slides demonstrate some of these applications and the challenges faced with modern designs. The issues include:
Generally much larger structures
Many windows leave little opportunity for conventional bracing
Heavy finishes combined with open floor plans (large spans) result in higher design loads on lateral elements
Quiz Note
This slide features information that will be found on the post-course knowledge assessment.
Which of the following structural design issues are caused by modern home designs? (Check all that apply)
Larger structures
Energy efficiency
Open floor plans
Heavy finishes

## Slide 64: Two-Story Applications
Simple to specify
Limited load capacity
Prefabricated shear wall panels typically only available with a 12” minimum width
No anchorage solutions on masonry foundations
Shear Wall
Site-Built Moment Frame
Pre-Fabricated Moment Frame
Notes: Say
While shear walls are simple to specify, they have a limited load capacity. Pre-fabricated shear wall panels are typically only available with a 12-inch minimum width. No anchorage solutions are available on masonry foundations.

## Slide 65: Two-Story Applications, cont.
Designed by Specifier
Custom fabricated
Installed by Iron Workers
Field welded ($$$)
Shear Wall
Site-Built Moment Frame
Pre-Fabricated Moment Frame
Notes: Say
Site-built moment frames are designer by the specifier and allow for custom fabrication. However, they must be installed by iron workers and they must be field welded.

## Slide 66: Two-Story Applications, cont.
Simply to specify
Field-bolted connections
Can be installed by Framers
High load capacity
Solutions using 5.5” columns
Shear Wall
Site-Built Moment Frame
Pre-Fabricated Moment Frame
Notes: Say
Pre-fabricated moment frames are simple to specify, have field-bolted connections and can be installed by framers. They feature a high load capacity and offer solutions using five-and-a-half-inch columns.
Quiz Note
This slide features information that will be found on the post-course knowledge assessment.
True or false: Prefabricated moment frames can be installed by framers.
True
False

## Slide 67: Application Installation Photos: Garage Fronts
Notes: Say
Garage fronts: Prefabricated steel moment frames have been used for garage front applications where large openings are needed with very little room for walls.

## Slide 68: Application Installation Photos: Grand Entryways
Notes: Say
Grand entryways: Prefabricated moment frames have also proven to be a useful solution for grand entryways in residential construction where tall ceiling heights are combined with large window and door openings and very minimal wall space.

## Slide 69: Application Installation Photos: Interior
Notes: Say
Interior: Prefabricated moment frames that utilize a bolted connection instead of welds have shown to be an ideal solution for interior applications where the floor system is already in place. By being able to lift the beam into place and secure with bolts, no cutting of the floor above is necessary in order to achieve a proper installation.

## Slide 70: Application Installation Photos: Multi-Family
Notes: Say
Multi-family: Multi-family residential units can also benefit from the use of prefabricated moment frames, due to their ease of installation and high seismic load capacity.

## Slide 71: Application Installation Photos: Residential Seismic Upgrades
Notes: Say
Residential seismic upgrades: Along with being a great solution for new light-frame construction, retrofit projects are another building type than can benefit from using a prefabricated moment frame. Older wood buildings that exhibit a construction type known as having a “soft-story”, or a large opening on the first floor with insufficient lateral capacity, can greatly reduce the risk of collapse by being retrofit with a prefabricated moment frame.

## Slide 72: Application Installation Photos: Retail and Fast Food
Notes: Say
Retail and fast food: Along with the myriad of residential projects, commercial projects such as retail and fast food buildings can use the advantages of a prefabricated steel moment frame.

## Slide 73: Application Installation Photos: RV Garage
Notes: Say
RV garage: Any building that has a large opening and limited wall space can benefit from using a prefabricated moment frame, such as this RV garage, which has a tall ceiling height as well as a wide opening.

## Slide 74: Application Installation Photos: Soft Story Retrofit
Notes: Say
Soft story retrofit: Here is a photo of tuck-under parking typical in multi-family construction completed before 1980. Large openings at the first level are typical in mixed use developments, such as housing over retail.

## Slide 75: Results of Lacking First Story Strength
Notes: Say
Apartments and condominiums with parking or commercial space on the first floor are prone to collapse if ground floor walls and columns are not strong enough to hold up the building during earthquakes. The figure above depicts a weak ground level with extensive damage and a relatively rigid upper level that remains intact.

## Slide 76: Cost Effectiveness
Are moment frames cost effective?
Engineer will need to: design the foundation anchorage, produce steel and welding specifications, and review steel shop drawings and welding procedure specifications
Steel sub-contractor will need to: install the frame
General contractor will need to: coordinate between the iron workers, the framers, and the special inspectors to ensure fitment
Notes: Say
The application of moment frame design requirements remains a time-consuming task.
This can be especially true for engineers who specialize in light-frame construction, where structural steel is sometimes required to resist high lateral loads in a small space.
While the actual design and detailing of a moment frame may only take a few hours to a day’s work, this is only the first stage of the process.
In addition to designing the foundation anchorage, the engineer will need to produce steel and welding specifications, and also review steel shop drawings and welding procedure specifications.
A steel sub-contractor will need to install the frame, and the general contractor will need to coordinate between the iron workers, the framers, and the special inspectors to make sure everything fits together.

## Slide 77: Prefabricated Moment Frames
Benefits of prefabricated frames
To save all this additional design work for the engineer and coordination effort for the general contractor, several manufacturers are now selling prefabricated moment frames.
The specification of premanufactured moment frames can be simplified to selecting a frame model from a catalog that meets the vertical and lateral loading requirements.
Notes: Say
To save all this additional design work for the engineer and coordination effort for the general contractor, several manufacturers are now selling prefabricated moment frames that are geared specifically toward light-frame construction.
The use of prefabricated, load-rated components in building designs has been evolving for the past decade, primarily with narrow shear panels that are tested and code-listed to exceed code height-to-width ratios.
The introduction of moment frames to resist higher loads in light-framed structures is the logical progression for premanufactured products.
The specification of premanufactured moment frames can be simplified to selecting a frame model from a catalog that meets the vertical and lateral loading requirements. This is a tremendous benefit for engineers who do not have the time or budget to design a custom frame.
However, there are still important design considerations that engineers must be aware of when using a moment frame (premanufactured or not) in light-frame construction, such as R-Values, Deflection Amplification Factors (Cd), System Overstrength Factors (Ω0), and requirements for mixing different lateral-force resisting systems.

## Slide 78: Lesson Three Complete
Now that you’ve completed this lesson, you should be able to:
Explain the proper application of ordinary moment frames and special moment frames
Notes: Do
Review the slide.

## Slide 79: LESSON 4
Moment Frame Design Solutions
After completing this lesson, you will be able to:
Explain the advantages of using a predesigned and manufactured steel moment frame
Notes: Say
After completing this lesson, you will be able to:
Explain the advantages of using a predesigned and manufactured steel moment frame

## Slide 80: Pros and Cons of Traditional Moment Frames
Most flexible in detailing and shape
Maximize load capacity with AISC shapes
Open bidding to multiple shops
Labor and time intensive
Additional subtrade involved
Inconsistent quality
Additional inspection costs
Labor intensive to install
Pros
Cons
Notes: Say
Some of the positives of a traditional moment frame include:
They are the most flexible option in detailing and shape,
They can maximize load capacity with AISC shapes, and
They allow for open bidding to multiple shops.
Some of the drawbacks of a traditional moment frame include:
An engineered design is labor and time intensive,
Additional subtrade may be involved,
Quality can be inconsistent,
There are additional costs for inspection, and
They are labor intensive to install.
Quiz Note
This slide features information that will be found on the post-course knowledge assessment.
True or false: Prefabricated moment frames are more flexible in detailing and shape than traditional moment frames.
True
False

## Slide 81: Predesigned and Manufactured Moment Frames
A cost effective alternative
Predesigned and manufactured moment frames are a cost-effective alternative to traditional moment frames. They are available in columns from 6’ to 35’ tall, and beams from 6’ to 35’ wide.
Some manufacturers offer a multi-story and/or multi-bay moment frames, which can accommodate wider openings and up to four stories in light-frame construction.
Notes: Say
Predesigned and manufactured moment frames are a cost-effective alternative to traditional moment frames. They are available in columns from 6 feet to 35 feet tall, and beams from 6 feet to 35 feet wide.
Some manufacturers offer a multi-story and/or multi-bay moment frames, which can accommodate wider openings and up to four stories in light-frame construction. Multiple story and multi-bay frames are an ideal solution for projects featuring tall ceilings, expansive windows and other customized designs with space constraints or load requirements that exceed other lateral-force-resisting options for traditional light-frame construction.

## Slide 82: Installation of Predesigned and Manufactured Moment Frames
Many of the predesigned and manufactured moment frames are bolted connection allowing for easy and efficient installation
Notes: Say
Many of the predesigned and manufactured moment frames are bolted connection allowing for easy and efficient installation.

## Slide 83: Advantages of Predesigned and Manufactured Moment Frames
Time saver in design
New code requirements are tedious and time consuming:
Design and detailing required
Production of steel and welding specifications
Review of steel shop drawings and welding procedure specifications
Widely used
Ease of construction
Architectural and functional versatility
Open spaces without interruption
Used where space is limited
Notes: Say
Some of the advantages of predesigned and manufactured moment frames include:
Architectural and functional versatility – which allow for open spaces without interruption. Predesigned moment frames may be used where space is limited.
Predesigned and manufactured moment frames are widely used and are simple to construct.
They are also a time saver in design. Traditional moment frames may be tedious or time consuming to the engineer due to the extensive design and detailing requirements.

## Slide 84: Predesigned and Manufactured vs. Traditional Moment Frame
Prefabricated | Site-built | Attribute
X |  | Design and detailing (frame and anchors)
 | X | Flexibility in shape and configuration
X |  | Ease and speed of construction
X |  | Field inspection
X |  | Attaching to light-framed structure
X |  | Handling on jobsite
 | X | Cost of materials
X |  | Installation cost
X |  | Quality assurance
Notes: Say
Attributes associated with predesigned and manufactured moment frames:
Design and detailing (frame and anchors)
Ease and speed of installation
Field inspection
Attaching to light-framed structures
Handling on jobsite
Installation cost
Quality assurance
Attributes associated with traditional moment frames:
Flexibility in shape and configuration
Cost of materials
Quiz Note
This slide features information that will be found on the post-course knowledge assessment.
Which of the following is not an advantage of prefabricated frames as compared to site built?
Ease of construction
Time saving
Installation cost
Cost of materials

## Slide 85: When to Use What?
Type | Cost | Strength | Anchorage | Aspect Ratio
Shear Walls | Low | Low | Low | Low
Prefabricated Wood or Steel Shear Walls | Medium | Medium | High | High
Steel Moment Frames | High | High | Low | Highest
Notes: Say
This table displays the cost, strength, anchorage and aspect ratio amounts for site-built shear walls, prefabricated shear walls, and steel moment frames.
Do
Review tabulated information.
Quiz Note
This slide features information that will be found on the post-course knowledge assessment.
Compared to a shear wall, steel moment frames are:
Stronger but less costly
Weaker but less costly
Stronger but more costly
Weaker but more costly

## Slide 86: Moment Frame Software
Helps select frame for a project’s given geometry and loading
Only minimum input geometries are required for the software to select frame for available space
Narrows down available stock frames based on input geometry
Provides possible custom solutions
Notes: Some manufacturers provide moment frame design software to help Designers select an appropriate frame for a project's given geometry and loading. The advantage of using a manufacturer’s software is that only minimum input geometries are required for the software to select an appropriate frame for the available space.
Based on input geometry, the software can narrow down available stock frames to a handful of possible solutions. If opening dimensions are outside stock frame sizes, Designers can enter the specific opening dimensions, and the software will provide possible customized solutions.

## Slide 87: Moment Frame Software
Key features and benefits
Requires only minimal input to help Designers quickly select an appropriate ordinary moment frame |  | Accommodates uniform, partial uniform, and point loads placed anywhere along span of beam
Design frames with custom opening dimensions |  | Provides output in concise format (option for detailed output)
Input screen makes it easy to key in design information and loads |  | Provides anchorage design for selected frame
Notes: Say
The key features and benefits of using moment frame software include:
Requires only minimal input to help Designers quickly select an appropriate ordinary moment frame
In addition to standard frame sizes, the software can analyze and design frames with custom opening dimensions
Input screen with drop-down buttons makes it easy to key in design information and loads
Software can accommodate uniform, partial uniform, and point loads placed anywhere along the span of the beam
Provides output in a concise format, as well as an option for detailed output
Provides anchorage design for the selected frame

## Slide 88: Lesson Four Complete
Now that you’ve completed this lesson, you should be able to:
Explain the advantages of using a predesigned and manufactured steel moment frame
Notes: Do
Review the slide.

## Slide 89: LESSON 5
Design Example
After completing this lesson, you will be able to:
Demonstrate how to determine the necessary specifications for an ordinary moment frame application
Notes: Say
After completing this lesson, you will be able to:
Demonstrate how to determine the necessary specifications for an ordinary moment frame application
To achieve this lesson’s objective, we’ll go through a moment frame design example for a garage-front low-seismic application. This example will reference ASCE 7-10, the International Building Code and the Simpson Strong-Tie Catalog for Strong Frame Moment Frames.

## Slide 90: Garage-Front Low-Seismic Application: Scenario
Based on the following scenario:
2012 or 2015 IBC, Low-Seismic Design, 2,500 psi concrete
Seismic Design Category A, R = 3
20’-0” Floor and 30’-0” Roof Span Tributary to Frame
Vertical Roof Loads = 20 psf Dead, 20 psf Live
Vertical Floor Loads = 15 psf Dead, 40 psf Live
Wall Weight = 12 psf
Nominal Top Plate Height = 8’-0”
Garage Opening = 16’-0” wide x 7’-0” tall
Total ASD Force to Frame (seismic load, wind does not control), Vframe = 3,000 + 5,000 = 8,000 lb.
10” Wide x 6” Tall Curb with 12” Tall Step (height above footing)
Notes: Say
The garage-front low-seismic application design example is based off of the following scenario:
Do
Review the slide.

## Slide 91: Garage-Front Low-Seismic Application: Goals
Determining the following:
Moment Frame Model
End-Plate Bolts
Top-Plate Fasteners
Anchorage Assembly
Outside End Distance
Inside End Distance
Minimum Footing Size for Anchorage
Notes: Say
Using this scenario, we will determine the following:
Moment Frame Model
End-Plate Bolts
Top-Plate Fasteners
Anchorage Assembly
Outside End Distance
Inside End Distance
Minimum Footing Size for Anchorage

## Slide 92: Frame Selection, Step One
❶ Check if an ordinary frame is permitted
Ordinary steel moment frames may be used in Seismic Design Categories A, B and C without limitations
Ordinary steel moment frames may be used in Seismic Design Categories D, E and F subject to limitations set forth in Sections 12.2.5.6, 12.2.5.7 and 12.2.5.8
In our example…
Seismic Design Category A – no limit on use of an Ordinary Moment Frame, OK ✓
Notes: Say
The first step for the frame selection is to determine if an ordinary steel moment frame is permitted for your structure. For structures designed in accordance with ASCE 7-10, ordinary steel moment frames may be used in Seismic Design Categories A, B and C without limitations. However, ordinary steel moment frames may be used in Seismic Design Categories D, E and F are subject to limitations set forth in Sections 12.2.5.6, 12.2.5.7 and 12.2.5.8.
In our example, the structure is located in Seismic Design Category A. Therefore, there is no limit on the use of an Ordinary Moment Frame.

## Slide 93: Frame Selection, Step Two
❷ Check R-Value
If seismic loads are calculated using R > 3.5, convert loads by multiplying by the R used in design and dividing by 3.5.
In our example…
Seismic shear forces were determined using R = 3 – Loads do not need to be converted
when selecting the OMF, OK ✓
Notes: Say
The second step is to check the Response Modification Coefficient. If seismic loads are calculated using an R-Value greater than 3.5, then convert loads by multiplying by the R-Value used in design and dividing by 3.5.
In our example, the seismic shear forces were determined using an R-Factor of 3.0, so loads do not need to be converted when selecting the OMF.

## Slide 94: Frame Selection, Step Three
❸ Select nominal height and width
Select the nominal height for your structure where the frame will be installed and find the corresponding allowable load table (8’, 9’, 10’, 12’, 14’, 16’, 18’, or 19’). Next, select the frame clear-opening width that will accommodate the required wall penetration (8’-2”, 10’-2”, 12’-4”, 14’-4”, 16’-4”, 18’-4”, or 20’-4”).
In our example…
Nominal frame height: 8 ft.
Nominal frame width: 16 ft.
Notes: Say
The third step is to select nominal height and width.
Select the nominal height for your structure where the frame will be installed and find the corresponding allowable load table (8’, 9’, 10’, 12’, 14’, 16’, 18’, or 19’). Next, select the frame clear-opening width that will accommodate the required wall penetration (8’-2”, 10’-2”, 12’-4”, 14’-4”, 16’-4”, 18’-4”, or 20’-4”).
In our example, the nominal frame height is 8-feet and the nominal frame width is 16-feet.

## Slide 95: Frame Selection, Step Four
❹ Check vertical loading
If the beam is loaded with only uniformly distributed vertical loads and the allowable stress design (ASD) uniform loads are all less than the limits listed in footnote 2, use “Maximum Shear” values. If SDS > 1.0, check if uniform dead load must include additional vertical seismic load effects (see allowable load tables, footnote 2).
If the beam is loaded with uniform vertical loads that exceed the limits, a single vertical point load at mid-span, or multiple point loads applied symmetrically about mid-span, use “Minimum Shear”.
Notes: Say
The fourth step is to compare vertical loads on your frame with the limits listed in footnotes 2 and 3 of the allowable load tables (Table: Strong Frame Ordinary Moment Frame - 8 ft. Nominal Heights, Strong-Tie Catalog C-SF13, page 65):
Use maximum shear values if the beam is loaded with only uniformly distributed vertical loads and the allowable stress design uniform loads are all less than the limits listed in footnote 2. If SDS is greater than 1, check if the uniform dead load must include additional vertical seismic load effects.
Use minimum shear values if the beam is loaded with uniform vertical loads that exceed the limits, or if there is a single vertical point load at mid-span, or there are multiple point loads applied symmetrically about mid-span.
If your vertical loading does not meet these criteria, use the Simpson Strong-Tie Frame Selector Software or contact Simpson Strong-Tie to perform a design for custom loading or complete alternate loading worksheet.

## Slide 96: Frame Selection, Step Four
❹ Check vertical loading, cont.
In our example…
WDL = 20 psf x 30’ / 2 + 15 psf x 20’ / 2 + 12 psf x 8’ = 546 plf | | < 800 plf, OK ✓
WRLL = 20 psf x 30’ / 2 = 300 plf | | < 400 plf, OK ✓
WFLL = 40 psf x 20’ / 2 = 400 plf | | = 400 plf, OK ✓
Vertical loads are less than frame design uniform load.
Therefore, use Maximum Shear values.
Notes: Say
In our example, vertical loads are less than frame design uniform load. Therefore, we will use Maximum Shear values.

## Slide 97: Frame Selection, Step Five
❺ Select Ordinary Moment Frame model
Using allowable load table for 8’ nominal height frames on catalog pages 64 to 65, select 16’ wide frame with a Maximum Shear greater than applied shear.
OMF 8 ft. Nominal Heights: Allowable Loads
C-SF13,
page 64
Notes: Say
The fifth step is to select the ordinary moment frame model. Using the allowable load table for 8-foot nominal height frames [Table: Strong Frame Ordinary Moment Frame - 8 ft. Nominal Heights], select a 16-foot wide frame with a maximum shear greater than the applied shear. [8,000 lb.]

## Slide 98: Frame Selection, Step Five
❺ Select Ordinary Moment Frame model, cont.
In our example…
For OMF912-16X8: Allowable ASD shear = 11,045 lb. | | > 8,000 lb., Shear OK ✓
OMF 8 ft. Nominal Heights: Allowable Loads
C-SF13,
page 64
Notes: Say
In our example, we will choose an OMF912-16x8, Its allowable ASD shear is 11,045 pounds, which is greater than the applied shear of 8,000 pounds.

## Slide 99: Frame Selection, Step Six
❻ Check Wmax
For frames selected using Minimum Shear values, check that the maximum total vertical load based on ASD load combinations is less than the tabulated value of Wmax.
If not, select a different frame and re-check.
In our example…
Check of Wmax is not required when the frame is selected using Maximum Shear, OK ✓
Notes: Say
The sixth step is to check the maximum total vertical load, Wmax.
If we had selected a frame using minimum shear values, then we would check that the maximum total vertical load based on ASD load combinations is less than the tabulated value of Wmax. If it were not, then we would select a different frame and re-check.
In our example, the check of Wmax is not required because the frame has been selected using maximum shear.

## Slide 100: Frame Selection, Step Seven
❼ Check Ordinary Moment Frame dimensions
Check that the clear-opening width (W1) is equal to or greater than the wall opening width
Check that the outside frame width (W2) fits within the available wall space
Check that the frame’s clear-opening height (H3) is equal to or greater than that required (remember to add the curb / stemwell height to H3 for installations with the frame base above the floor level)
Notes: Say
The seventh step is to check the dimensions of the ordinary moment frame. Using nominal height and width tables above the allowable load tables in C-SF13, verify that the predesigned and manufactured moment frame selected will accommodate the required wall opening. This requires three steps:
Check that the clear-opening width (W1) is equal to or greater than the wall opening width,
Check that the outside frame width (W2) fits within the available wall space, and
Check that the frame’s clear-opening height (H3) is equal to or greater than that required (remember to add the curb or stemwell height to H3 for installations with the frame base above the floor level)

## Slide 101: Frame Selection, Step Seven
❼ Check Ordinary Moment Frame dimensions, cont.
In our example…
Clear-opening width: W1 = 16'-4" > 16'- 0", OK ✓
Outside frame width: W2 = 18'-4" < 20’-0”, OK ✓
Clear-opening height: H3 + curb height above slab = 6'-6 3/4" + 6" = 7'-0 3/4" > 7'- 0", OK ✓
OMF 8 ft. Nominal Heights: Dimensions
C-SF13, page 64
Notes: Say
In our example:
The clear-opening width, W1, is greater than the wall opening width,
The outside frame width, W2, fits within the available wall space, and
The clear-opening height is greater than required.

## Slide 102: Frame Selection, Step Eight
❽ Select bolt tightening requirements
Determine if snug-tight or pretensioned bolts are required for the end plate:
In SDC D, E, or F: pretensioned bolts are required.
In SDC A, B, or C: snug-tight bolts may be used when seismic design is based on R ≤ 3, otherwise pretensioned bolts are required.
In our example…
For Seismic Design Category A with R = 3 – Specify snug-tight bolts for end plate connection.
Notes: Say
The eighth step is to determine if snug-tight or pretensioned bolts are required for the end plate connections:
In Seismic Design Categories D, E, or F, pretensioned bolts are required.
In Seismic Design Category A, B, or C, snug-tight bolts may be used when seismic design is based on an R-Value less than or equal to 3, otherwise pretensioned bolts are required.
In our example, specify snug-tight bolts for the end plate connection since the structure is in Seismic Design Category A with an R-Value of 3.

## Slide 103: Frame Selection, Step Nine
❾ Select top plate fasteners
In the allowable loads table for Ordinary Moment Frames (C-SF13 Catalog, page 64), select between the nail (16d commons) and screw (1/4"x3-1/2" SDS) options for attaching a field installed top plate to the frame nailers.
For seismic design, quantity of fasteners must be increased if the connection is required to be designed as a collector for load combinations with overstrength (see ASCE 7-10, Section 12.10.2.1).
Notes: Say
The final step is to select the top plate fasteners. In the allowable load tables [Table: Strong Frame Ordinary Moment Frame - 8 ft. Nominal Heights], select between the nail (16d commons) and screw (1/4”x3-1/2” SDS) options for attaching a field installed top plate to the frame nailers.
For seismic design, quantity of fasteners must be increased if the connection is required to be designed as a collector for load combinations with overstrength.

## Slide 104: Frame Selection, Step Nine
❾ Select top plate fasteners, cont.
In our example…
Select (21) - 1/4" x 3-1/2" SDS screws. Design for load combinations with overstrength not required in Seismic Design Category A.
OMF 8 ft. Nominal Heights: Allowable Loads
C-SF13,
page 65
Notes: Say
In our example, select twenty-one 1/4" x 3-1/2" SDS screws. Design for load combinations with overstrength is not required in Seismic Design Category A.

## Slide 105: Tension Anchorage Design, Step One
❶ Determine concrete condition
Determine whether uncracked or cracked concrete is applicable for anchorage design. Assuming cracked concrete is conservative.
Note that the designer must determine whether cracked or uncracked concrete is applicable based on the project conditions in accordance with ACI 318 Appendix D.
In our example…
Concrete is uncracked.
Notes: Say
The first step is to determine the conditions of the concrete. A designer must determine whether cracked or uncracked concrete is applicable for anchorage design based on the project conditions in accordance with ACI 318 Appendix D. Assuming cracked concrete is conservative.
In our example, the concrete is uncracked.

## Slide 106: Tension Anchorage Design, Step Two
❷ Select anchorage design method
Simplified: Requires only column size and frame height to select anchorage. Not for seismic designs that use R = 3.5.
Detailed: Uses column reactions and anchorage assembly capacities to select a solution. Maximum column reactions in allowable load tables may be used.
In our example…
Use Simplified design method.
Notes: Say
The second step is to select the anchorage design method to use for selecting anchorage solutions:
The simplified method is the quickest and easiest method, requiring only the column size and frame height to select the anchorage. This method can result in a conservative design for some frames and loading conditions. The Simplified method is not applicable for seismic designs that use an R-Value of 3.5.
The detailed method uses column reactions and anchorage assembly capacities to select a solution. The maximum column reactions tabulated in the allowable load tables may be used, or for further economy, the reactions calculated for the project-specific design loads can be used (see footnotes 4 and 5 of the allowable load tables).
In our example, we’ll use the simplified design method.

## Slide 107: Tension Anchorage Design, Step Three
❸ Determine tension reaction
Simplified: No calculation of reactions required. Solutions in Tension Anchorage Table 1.1 consider max tension reaction for each frame group.
Detailed: Use max tension reaction in allowable load table for the frame selected, or calculate reaction based on design loads.
In our example…
No calculation of reactions required for Simplified design method.
Notes: Say
The third step is to determine the maximum tension reaction for tension anchorage design:
For simplified anchorage design, no calculation of reactions is required. Solutions presented in Tension Anchorage Table 1.1 [Table 1.1: Simplified Tension Anchorage Solutions – Footing Width and Embedment Depth, C-SF13, p. 85] consider maximum tension reaction for each group of frames.
For detailed anchorage design, use the maximum tension reaction tabulated in the allowable load table for the frame selected, or calculate tension reaction based on design loads in accordance with footnote 5 of the allowable load tables [Table: Strong Frame® 8 ft. Nominal Heights: Allowable Loads, C-SF13, p. 65].
In our example, no calculations of reactions are required since we are using the simplified design method.

## Slide 108: Tension Anchorage Design, Step Four
❹ Select minimum footing size for tension
Simplified: Select embedment and footing width from the Tension Anchorage Table 1.1 based on column size and nominal frame height.
Detailed: Use the Tension Anchorage Allowable Loads Table 1.2 to select embedment and footing width with a capacity that exceeds the tension reaction.
Notes: Say
The fourth step is to determine the minimum embedment and footing size for tension anchorage:
For simplified anchorage design, select the embedment and footing width from the Tension Anchorage Table 1.1 [Table 1.1: Simplified Tension Anchorage Solutions – Footing Width and Embedment Depth, C-SF13, p. 85] based on column size and nominal frame height.
For detailed anchorage design, use the Tension Anchorage Allowable Loads Table 1.2 [Table 1.2: Detailed Tension Anchorage – Allowable Loads, C-SF13, p. 85] to select embedment and footing width with a capacity that exceeds the tension reaction.

## Slide 109: Tension Anchorage Design, Step Four
❹ Select minimum footing size for tension, cont.
In our example…
C9 column 8-ft tall, seismic loading, uncracked concrete: W = 40”, de = 13”
Table 1.1: Simplified Tension Anchorage Solutions –
Footing Width and Embedment Depth
C-SF13, page 85
Notes: Say
In our example, an 8-foot tall C9 column with seismic loading and uncracked concrete gives W equal to 40-inches and de equal to 13-inches.

## Slide 110: Tension Anchorage Design, Step Five
❺ Determine anchorage assembly strength
Simplified: installations requiring high strength anchorage are determined as a part of shear anchorage design (see footnote 3 of Tension Anchorage Table 1.1)
Detailed: installations requiring high strength anchorage are designated in footnote 6 of Tension Anchorage Allowable Loads Table 1.2.
In our example…
From Table 1.1, footnote 3, anchorage strength for Simplified design is determined based on shear anchorage.
Notes: Say
The fifth step is to determine the strength of the anchorage assembly. Standard strength anchorage assemblies are adequate for tension, except where shown in the anchorage tables:
For simplified anchorage design, installations requiring high strength anchorage are determined as a part of shear anchorage design (see footnote 3 of Tension Anchorage Table 1.1).
For detailed anchorage design, installations requiring high strength anchorage are designated in footnote 6 of Tension Anchorage Allowable Loads Table 1.2.
In our example, anchorage strength for Simplified design is determined based on shear anchorage from Table 1.1, footnote 3.

## Slide 111: Tension Anchorage Design, Step Six
❻ Determine rod length and footing size
Add the step height to the minimum required embedment, de, and select an anchorage assembly model number with an embedded rod length, le, that is equal or greater. If this value exceeds the maximum embedded rod length for the anchorage assembly, select an extension kit to achieve the necessary rod length.
In our example…
For 12” tall step (above footing): Required le = de + 12” = 25”
Select MFSL-36-5-KT, le = 30-1/2” OK ✓
Minimum footing depth = 30-1/2” - 12” (step) + 4” = 22-1/2”
Notes: Say
The final step is to determine the rod length and footing size.
Add the step height (height of concrete above the top of footing) to the minimum required embedment, de, and then select an anchorage assembly model number with an embedded rod length, le, that is equal or greater.
If this value exceeds the maximum embedded rod length for the anchorage assembly, select an extension kit to achieve the necessary rod length. Note that the embedded rod length is different for OMFSL and OMFAB anchorage assemblies with the same total rod length. See Step 1 of General Shear Anchorage Design for selection of anchorage assembly type.
In our example, for a 12-inch tall step above footing, the required embedded rod length is the minimum required embedment plus 12-inches, equal to 25-inches. We will select the MFSL-36-5-KT, since the embedded rod length is 30-and-a-half-inches. Minimum footing depth is equal to 22-and-a-half-inches.

## Slide 112: Shear Anchorage Design, Step One
❶ Select anchorage assembly type
OMFSL: Easier to install and allows the frame to be installed flush with edge of concrete, but may require additional end distance.
OMFAB: Offers higher shear capacities without increasing concrete strength or end distance, but requires an increased edge distance and additional tie or hairpin reinforcement.
In our example…
Select OMFSL anchorage assembly for ease of installation and to allow installation flush with edge of concrete curb.
Notes: Say
The first step is to select the anchorage assembly type.
The OMFSL anchorage assembly is easier to install and allows the frame to be installed flush with the edge of concrete, but may require additional end distance.
The OMFAB anchorage assembly offers higher shear capacities without increasing concrete strength or end distance, but requires an increased edge distance and additional tie or hairpin reinforcement.
In our example, we’ll select OMFSL anchorage assembly for ease of installation and to allow installation flush with edge of concrete curb.

## Slide 113: Shear Anchorage Design, Step Two
❷ Select anchorage design method
Simplified: Quick and easy, requires only column size and frame height to select anchorage. Not applicable for seismic designs that use R = 3.5.
Detailed: Uses column reactions and anchorage assembly capacities to select a solution. The maximum column reactions tabulated in allowable load tables may be used.
In our example…
Use Simplified design method.
Notes: Say
The second step is to select the anchorage design method.
The simplified method is the quickest and easiest, requiring only the column size and frame height to select the anchorage. This method can result in a conservative design for some frames and loading conditions. The Simplified method is not applicable for seismic designs that use R = 3.5.
The detailed method uses column reactions and anchorage assembly capacities to select a solution. The maximum column reactions tabulated in the allowable load tables may be used, or for further economy, the reactions calculated for the project-specific design loads can be used. See footnotes 4 and 5 of the allowable load tables.
In our example, we’ll use the simplified design method.

## Slide 114: Shear Anchorage Design, Step Three
❸ Determine shear reaction
Simplified: No calculation of reactions required. Solutions presented in Table 2.1 (OMFSL) and Table 3.1 (OMFAB) consider maximum shear reactions.
Detailed: Use maximum column shear reaction in allowable load table, or shear reaction calculated using footnote 4 of the allowable load tables.
In our example…
No calculations of reactions required for Simplified design method.
Notes: Say
The third step is to determine the maximum shear reaction for shear anchorage design.
For simplified anchorage design, no calculation of reactions is required. Solutions presented in Table 2.1 (for OMFSL) and Table 3.1 (for OMFAB) consider the maximum shear reaction for each group of frames.
For detailed anchorage design, use the maximum column shear reaction tabulated in the allowable load table for the frame selected, or use the shear reaction calculated using footnote 4 of the allowable load tables. For OMFSL, determine the shear reaction at both tension and compression columns. For OMFAB, only the shear reaction at the compression column is required.
In our example, no calculations of reactions are required for the simplified design method.

## Slide 115: Shear Anchorage Design, Step Four
❹ Determine inside and outside distance
Simplified anchorage design: Determine directly from Table 2.1.
Detailed anchorage design: Use the shear reactions from Step 3 and the OMFSL shear capacities in Table 2.2 or 2.3. Select an inside end distance with a capacity that exceeds the tension column shear reaction, and an outside end distance with a capacity that exceeds the compression column shear reaction.
Notes: Say
The fourth step is to determine the minimum inside and outside end distance in concrete.
For simplified anchorage design, determine end distances directly from Table 2.1.
For detailed anchorage design, use the shear reactions from the previous step and the OMFSL shear capacities in Table 2.2 or 2.3. Select an inside end distance with a capacity that exceeds the tension column shear reaction, and an outside end distance with a capacity that exceeds the compression column shear reaction.

## Slide 116: Shear Anchorage Design, Step Four
❹ Determine inside and outside distance, cont.
In our example…
C9 column 8-ft tall, Max Shear with uniform load, 10" curb: Min inside end distance = 6“
C9 column 8-ft tall, Max Shear with uniform load, 10" curb: Min outside end distance = 7-1/2"
Table 2.1: Simplified MFSL Shear Anchorage – Min Required End Distance
C-SF13,
page 86
Notes: Say
In our example, using OMFSL Table 2.1, the minimum inside end distance is 6-inches and the minimum outside end distance is 7-and-a-half-inches.

## Slide 117: Shear Anchorage Design, Step Five
❺ Determine anchorage assembly strength
If high strength anchorage is required for tension, specify a high strength OMFSL anchorage assembly.
Otherwise, standard strength anchorage assemblies are adequate for OMFSL except for shaded regions of the anchorage tables.
Notes: Say
The fifth step is to determine the strength of the anchorage assembly.
If high strength anchorage is required for tension, specify a high strength OMFSL anchorage assembly.
Otherwise, standard strength anchorage assemblies are adequate for OMFSL except for shaded regions of the anchorage tables.

## Slide 118: Shear Anchorage Design, Step Five
❺ Determine anchorage assembly strength, cont.
In our example…
C9 column 8-ft tall, Maximum Shear with uniform load, 10" curb: Standard strength OMFSL (value not shaded).
Table 2.1: Simplified MFSL Shear Anchorage – Min Required End Distance
C-SF13,
page 86
Notes: Say
Using OMFSL Table 2.1 on catalog page 86:
In our example: C9 column 8-ft tall, Maximum Shear with uniform load, 10" curb: Standard strength OMFSL (value not shaded).

## Slide 119: Shear Anchorage Design, Step Six
❻ Verify Ordinary Moment Frame dimensions
If inside end distance exceeds that corresponding to the pre-installed nailer installed flush with inside end of curb, subtract the thickness of additional studs required at each column from the clear-opening width, W1, and check that this still exceeds the required opening width.
If outside end distance exceeds that corresponding to the pre-installed nailer installed flush with outside end of curb, add the thickness of additional studs required at each column to the outside frame width, W2, and check that this still fits within the available wall space.
Notes: Say
If inside end distance exceeds that corresponding to the pre-installed nailer installed flush with inside end of curb, subtract the thickness of additional studs required at each column from the clear-opening width, W1, and check that this still exceeds the required opening width.
If outside end distance exceeds that corresponding to the pre-installed nailer installed flush with outside end of curb, add the thickness of additional studs required at each column to the outside frame width, W2, and check that this still fits within the available wall space.

## Slide 120: Shear Anchorage Design, Step Six
❻ Verify Ordinary Moment Frame dimensions, cont.
In our example…
W1 = 16'-4“ and W2 = 18'-4"
Clear-opening width = W1 - 2[(inside end) - (4½")] = (16'-4") - 2[(6") - (4½")] = 16'-1" | | > 16'- 0", OK ✓
Outside frame width = W2 + 2[(outside end) - (4½")] = (18'-4") + 2[(7½") - (4½")] = 18'-10" | | < 20'-0", OK ✓
OMF – 8 ft. Nominal Heights: Dimensions
Notes: Say
In our example, since inside end distances exceed the minimum with nailer flush with concrete, we’ll check the overall frame width.
Using tables at the top of page 64 in the catalog, we find W1 is 16-feet-4-inches and W2 is 18-feet-4-inches. This gives a clear-opening width of 16-feet-1-inch, which is greater than the minimum 16-feet required. This also gives an outside frame width of 18-feet-10-inches, which is less than the maximum allowed 20-feet.

## Slide 121: Design Summary
Design Summary
From the previous example we determined:
Strong-Frame Model
End-Plate Bolts
Top-Plate Fasteners
Anchorage Assembly
Outside End Distance
Inside End Distance
Minimum Footing Size for Anchorage
OMF912-16x8
Snug-Tight
(21) – ¼” x 3-½” SDS Screws
MFSL-36-5-KT
7-½”
6”
19” x 19” x 22-½”
Notes: Say
Here is the design summary for our Garage-Front Low-Seismic Application design example.

## Slide 122: Design Summary, cont.
Notes for Design Example
Some key points of interest include:
Design of anchorage using Simplified design is simplest. Detailed design may result in more economical anchorage designs.
Footing size shown is based on anchorage design only. Actual footing/grade beam size and reinforcing must be based on project geometry and allowable soil bearing pressures.
Overturning load on steel beam from shear wall above is not shown for simplicity.
Wind roof uplift load on ordinary moment frame not shown.
Out-of-plane load on ordinary moment frame not shown.
Notes: Say
Here is the design summary for our Garage-Front Low-Seismic Application design example.

## Slide 123: Lesson Five Complete
Now that you’ve completed this lesson, you should be able to:
Demonstrate how to determine the necessary specifications for an ordinary moment frame application
Notes: Do
Review the slide.

## Slide 124: Course Summary: Lesson 1
Moment frames allow larger openings and smaller wall sections while still providing the loads structural designers need. Moment frames are commonly used in applications such as garage fronts, large entry ways, walls with large, numerous windows, tuck-under parking and great-rooms.
OMFs and IMFs are expected to withstand limited inelastic deformations, while SMFs are expected to withstand significant inelastic deformations. OMF are typically used in non/low-seismic regions; IMF in low/mid-seismic regions; and SMF in mid/high-seismic regions.
The higher the R value, the more ductile a system is, and as such, the lower the force. The lower the R value, the more brittle the system is.
OMF: R = 3.5. IMF: R = 4.5. SMF: R = 8.0.
L
1
Moment Frame Design Background
Notes: Do
Review the course summary for Lesson 1.

## Slide 125: Course Summary: Lesson 2
Frames are covered under the following: 2012 IBC, 2015 IBC, ASCE/SEI 7-10, AISC Steel Construction Manual 14th Edition (AISC 360-10), AISC Seismic Provisions for Steel Buildings (AISC 341-10)
Codes have the following moment frame limitations: (1) Weight and height limitations based on the moment frame type and seismic design category (2) Use of OMFs in combination with other lateral systems (in different directions; in the same direction)
Are ordinary moment frames allowed in high seismic areas (SDC D, E and F)? ASCE 7-10: Minimum Loads for Building and Other Structures Table 12.2-1 says NP for Not Permitted. However, there are notable exceptions in footnotes h and i.
L
2
Code Limitations and Requirements
Notes: Do
Review the course summary for Lesson 2.

## Slide 126: Course Summary: Lesson 3
Moment frames address challenges faced with modern designs: (1) Generally much larger structures, (2) Many windows leave little opportunity for conventional bracing, (3) Heavy finishes combined with open floor plans (large spans) result in higher design loads on lateral elements
Soft Story Retrofit Applications: Apartments and condominiums with parking or commercial space on the first floor are prone to collapse if ground floor walls and columns are not strong enough to hold up the building during earthquakes.
The introduction of moment frames to resist higher loads in light-framed structures is the logical progression for pre-manufactured products. This is a tremendous benefit for engineers who do not have the time or budget to design a custom frame.
L
3
Moment Frame Applications
Notes: Do
Review the course summary for Lesson 3.

## Slide 127: Course Summary: Lesson 4
Traditional Moment Frame Pros: (1) Most flexible in detailing and shape (2) Can maximize load capacity with AISC shapes (3) Open bidding to multiple shops. Cons: (1) Design is labor and time intensive (2) Additional subtrade involved (3) Inconsistent quality (4) Additional inspection costs (5) Labor intensive to install
Predesigned and manufactured moment frames are a cost-effective alternative. Multiple story and multi-bay frames are an ideal solution for projects featuring tall ceilings and expansive windows with space constraints or load requirements that exceed other lateral-force-resisting options for traditional light-frame construction.
Advantages of Predesigned Moment Frames: (1) Architectural and functional versatility (2) Widely used (3) Ease of construction (4) Time saver in design
L
4
Moment Frame Design Solutions
Notes: Do
Review the course summary for Lesson 4.

## Slide 128: Course Summary: Lesson 5
Some manufacturers provide moment frame design software to help Designers select an appropriate frame for a project's given geometry and loading. The advantage of using a manufacturer’s software is that only minimum input geometries are required for the software to select an appropriate frame for the available space.
A design example for a garage-front low-seismic application is available in Strong-Tie Catalog C-SF13. This process gives a detailed overview of frame selection, tension anchorage design, and shear anchorage design.
L
5
Design Example
Notes: Do
Review the course summary for Lesson 5.

## Slide 129: Course Completion
Questions?

## Slide 130: Course Completion
Simpson Strong-Tie
This concludes the continuing education course.
For a library of Simpson Strong-Tie courses,
visit strongtie.com/workshops
Notes: Do
Draw the meeting to a close. Hand out literature and business cards.
Say
If you have ongoing projects that you would be interested in reviewing together, please let me know.

## Slide 131: Next Steps!
AIA: For those seeking AIA LU/HSW: You will receive an email with a link allowing access to print your Certificate. Congratulations, you will have earned 2 LU/HSW credits. If your AIA member number has been inserted into your profile, Simpson Strong-Tie will report your credits on your behalf to the AIA. No test is required in order to receive HSW credits.
IACET: For those seeking IACET CEUs: You will receive an email with a link allowing access to print your Certificate of Attendance and instructions directing you to the Simpson Student Center to take the exam before credits can be awarded. Once the exam is taken and passed, you will have earned 0.2 CEUs (2 hours of credit). You can then access your Certificate of Completion from the Course Content tab. You must self-report your credits to your certifying organization or agency.
If you have questions or need assistance, please contact training@strongtie.com.
Notes: Presenter Notes:
Review the email and notification process as outlined in this slide.
AIA LUs:
For those that want AIA HSW credit, be sure to provide your AIA number on the sign-in sheet and Simpson will report your credits to the AIA on your behalf.
No test is required for AIA credit.
CEUs:
For those seeking CEUs, watch for an email with instructions to access the online test. After you have passed the test, you may access your Certification of Completion from the course content tab.
You must self-report your credits to your certifying organization or agency.

## Slide 132: Next Steps!
ICC: For those seeking ICC CEUs: You will receive an email with a link allowing access to print your Certificate. Congratulations, you will have earned 0.2 ICC CEU (2 hours of credit). Please make sure your ICC member number has been inserted into your profile. It is your responsibility to self-report your credits to the ICC. Please retain your Completion Certificate for your records.
IACET: For those seeking IACET CEUs: You will receive an email with a link allowing access to print your Certificate of Attendance and instructions directing you to the Simpson Student Center to take the exam before credits can be awarded. Once the exam is taken and passed, you will have earned 0.2 CEUs (2 hours of credit). You can then access your Certificate of Completion from the Course Content tab. You must self-report your credits to your certifying organization or agency.
If you have questions or need assistance, please contact training@strongtie.com.
Notes: Presenter Notes:
Review the email and notification process as outlined in this slide.
Watch for an email directing you to the Student Center to print your certificate.
No test is required for ICC credit. You must self-report your credits to ICC.
For those seeking general IACET CEUs after you have passed the online test, you may access your Certification of Completion from the course content tab. You must self-report your credits to your certifying organization or agency.