## Slide 1: BUILDER TRAINING SERIES
Continuous Load Path Systems for Lateral Resistance
Notes: Welcome
Welcome to this course on Continuous Load Path Systems for Lateral Resistance
Presented by Simpson Strong-Tie
No Change 1

## Slide 2: Credit Information
Professional Development Hours
Simpson Strong-Tie® offers Professional Development Hours for completing this course. No other continuing education or accredited credits are available for this course.
This course offers 0.5 PDH (1/2 hour of PDH credit)
Notes: Credit Information – Professional Development Hours
Simpson Strong-Tie offers Professional Development Hours for completing this course. No other continuing education or accredited credits are available for this course.
No Change 2

## Slide 3: Course Requirements
Pass the Course and Earn Professional Development Hours
READ & LISTEN
Read and listen to all course material in sequence
PASS ASSESSMENT
Pass the Final Assessment at the end of the course
EXERCISES
Complete the Knowledge Checks in the course
Notes: Course Requirements
To pass the course and earn Professional Development Hours, read and listen to all course material in sequence, complete the Knowledge Checks in the course, and pass the final assessment at the end of the course.
No Change 3

## Slide 4: About this Course
Course Description
The Continuous Load path course contains two parts. Part 1 focused on methods to resist uplift forces, while Part 2 focuses on resisting horizontal or lateral forces. This course introduces installers and supervisors to the concepts and methods for lateral restraint systems including braced walls and portal frames.
Course Learning Objectives
When you have completed this course, you should be able to:
  Define Brace Wall Line, Brace Wall panel, and Bracing Methods
  Explain the basic rules for wall bracing including braced wall line spacing and off-sets as well as bracing methods, brace wall panel locations and maximum spacing
  Recall basic requirements for Portal Frames
Notes: About this Course
Course Description
The Continuous Load path course contains two parts. Part 1 focused on methods to resist uplift forces, while Part 2 focuses on resisting horizontal or lateral forces. This course introduces installers and supervisors to the concepts and methods for lateral restraint systems including braced walls and portal frames.
Learning Objectives
When you have completed this course, you should be able to:
Define Brace Wall Line, Brace Wall panel, and Bracing Methods.
Explain the basic rules for wall bracing including braced wall line spacing and off-sets as well as bracing methods, brace wall panel locations and maximum spacing.
Recall basic requirements for Portal Frames
No Change 4

## Slide 5: Course Agenda
LESSON 1 Structural Basics
LESSON 2 Braced Wall Construction
Notes: Course Agenda
The topics covered in this course include the following:
LESSON 1 Structural Basics
LESSON 2 Braced Wall Construction
No Change 5

## Slide 6
Continuous Load Path Systems for Lateral Resistance
LESSON 1
Structural Basics
Notes: LESSON 1: Structural Basics
This lesson discusses the various forces and loads that act on a building with a review of the continuous load path, discussed in Part 1 of this course. It also introduces the continuous load path specific to lateral resistance.
No Change 6

## Slide 7: Wind Loads on a Structure
Wind pressures challenges.
Load transfer connections (CLP).
WIND
Notes: Wind Loads on a Structure
Wind pressures challenge the integrity of a structure when the different types of forces simultaneously apply loads in multiple directions.
The structure must transfer the loads through resisting elements, which requires a series of connections from the roof and walls to the foundation creating a continuous load path.

## Slide 8: Wind Forces
Vertical Forces
Horizontal Forces
Vertical wind pressure can create uplift forces strong enough to lift the roof off the structure or lift the entire structure from its foundation.
Horizontal wind pressure can cause lateral overturning, racking, and sliding failures.
Notes: Wind Forces
Wind forces act on a structure with vertical force and horizontal force. The building stability depends on the capability of the structure to resist wind forces, and carry the loads created by forces without moving or breaking.
Vertical Forces
Vertical wind pressure can create uplift forces strong enough to lift the roof off the structure, or lift the entire structure from its foundation. Part 1 of this course focused on resisting uplift forces.
Horizontal Forces
Horizontal wind pressure can cause lateral overturning, racking, and sliding failures. Part 2 of this course focuses on resisting horizontal or lateral forces.
No Change 7
Student Handbook Material

## Slide 9: Effects of Lateral Forces
Types of events.
Resisting these elements.
Notes: Effects of Lateral Forces
The effects of lateral forces are evident after a hurricane, tornado, or seismic event. These situations apply forces to homes from a wide range of directions.
It is the responsibility of the building designer to determine the magnitude of the wind pressures and define a continuous load path of connections to resist these elements.

## Slide 10: Continuous Load Path in the Code
IRC R301.1 Application
“The construction of buildings and structures in accordance with the provisions of this code shall result in a system that provides a complete load path that meets the requirements for the transfer of loads from their point of origin through the load-resisting elements to the foundation.”
IBC 1604.4 Analysis
"…Any system or method of construction to be used shall be based on a rational analysis in accordance with well-established principles of mechanics. Such analysis shall result in a system that provides a complete load path capable of transferring loads from their point of origin to the load-resisting elements.”
Apply to wind, seismic, and gravity loads.
Notes: Continuous Load Path in the Code
Studies show that homes can significantly resist forces with a strong Continuous Load Path. These excerpts from the IRC and IBC represent a summary of the intent of building codes. Both codes stress the necessity of a continuous or complete load path. These code sections apply to wind, seismic, and gravity loads. Take a moment to read each code section before proceeding.
No Change 8

## Slide 11: Wall Framing
Notes: Wall Framing
This image illustrates the wall framing studs spaced 16“ on center. The bottom connection is where the studs attach to the bottom plate. The top connection is where the studs attach to the top of the wall. When a lateral load such as wind is applied, studs with a weak connection at the top and bottom easily result in racking or tilting. As a result, sheathing or other bracing material is required to resist racking.
No Change 9

## Slide 12: Shear Walls
Resisting lateral loads.
Racking forces.
Sliding forces.
Overturning.
Shear Wall
Brace Wall Panel
System Stiffness
Dead Load
Holdowns
Notes: Shear Walls
Both shear walls and brace wall panels provide resistance to lateral loads. The sheathing nailing resists the racking forces. The sill anchorage resists the sliding forces. On a shear wall, hold downs prevent overturning and on a brace wall panel the dead load from above as well as the system stiffness prevents overturning.

## Slide 13: Wind Forces Acting on a Building
The wind load pushes against the end wall.
The force pushes the entire roof system in the same direction.
The force pulls the end wall in the same direction.
To resist the wind force, the side walls must resist racking.
Notes: Wind Forces Acting on a Building
This illustration shows how wind forces act on a building. The wind load pushes against the end wall and the aerodynamic force channels the air around the wall and pushes the entire roof system in the same direction as the wind force. This creates a force that pulls the end wall in the same direction, attempting to suck the back wall off the building. To resist the wind force, the side walls must resist racking.
No Change 10
Student Handbook Material

## Slide 14: Seismic Forces Acting on a Building
The ground moves towards the wall.
The forces push the roof in the opposite direction.
Forces of inertia act against the roof and walls.
The walls move in the direction of the force.
))
))
To resist seismic forces, the side walls must transfer loads from the foundation up into the roof.
Notes: Seismic Forces Acting on a Building
This illustration shows how seismic forces act on a building. In this case, the ground moves towards the wall, the walls move in the direction of the force, while the forces push the roof in the opposite direction. The forces of inertia act against the roof and walls, pushing in the opposite direction as the seismic ground motion. To resist seismic forces, the side walls must transfer loads from the foundation up into the roof to keep the building together.
No Change 11
Student Handbook Material

## Slide 15: Lateral Load Path Requirements
Uplift/lateral Connectors
Prefabricated Shearwalls
Holdown Anchor
Mudsill Anchor
Site-Built Shearwall
Roof Boundary Clip
Notes: Lateral Load Path Requirements
A strong lateral load path helps the structure resist horizontal forces. This diagram illustrates wall connection points that require the addition of bracing, connectors, and shear walls. In addition, large window and door openings along wall lines and especially garage fronts may require the use of prefabricated panels to meet load requirements.

## Slide 16: Check Your Knowledge
What is the primary reason
For using braced walls?
To provide additional insulation in walls
To resist racking
To support walls with window and door openings
To resist uplift forces
Notes: Check Your Knowledge
No Change 12

## Slide 17
Braced Wall Construction
Continuous Load Path Systems for Lateral Resistance
LESSON 2
Notes: Lesson 2: Braced Wall Construction
This lesson discusses wall reinforcement and construction requirements that integrate wall bracing used for creating a lateral continuous load path.
No Change 12 (deleted line on slide)

## Slide 18: Wall Bracing Building Plan
Typical Building Plan
Included in Plan
Key and Notes
Notes: Wall Bracing Building Plan
This is an example of a typical building plan that contains wall bracing information. The plan includes brace wall lines, specified methods of bracing, and panel locations. The plan also contains a legend key with notes that further define the plan elements.

## Slide 19: Nails
Length The length of the nail also affects the shear capacity. Nails must have enough penetration into wood to achieve full shear capacity.
Diameter The diameter, or gauge of the nail, affects the shear capacity of the nail. The thicker the nail, the more shear resistance provided. Smaller nails have less load capacity and may not be code compliant when substituted for code listed fasteners.
Choose the Correct Fastener
Type
Diameter
Length
Quantity
Notes: Wall Construction Nails
When constructing walls it is important to use the proper type, diameter, length and quantity of fasteners to comply with the code, even though some of the specified nails are less common to builders and installers.
The diameter, or gauge of the nail, affects the shear capacity of the nail. The thicker the nail, the more shear resistance provided. Smaller nails have less load capacity and may not be code compliant when substituted for code listed fasteners.
The length of the nail also affects the shear capacity. Nails must have enough penetration into wood to achieve full shear capacity.

## Slide 20: Fastening Schedule
This code table provides the fastening schedule for installing different joints in the building.
Table R602.3(1)
Notes: Fastening Schedule
This code table provides the fastening schedule for installing different joints within the building. The table references the correct type, quantity, and size of nail or fastener for specific joints. As an example, the blocking between ceiling joists or rafters to the top plate connection specifies four different allowable toe-nails. The code table also includes the specific length and diameter for each type of nail allowed. Some items, such as the Rafter or roof truss to plate connection, also includes the spacing and location of the nail pattern, shown in the far right column.
No Change 13

## Slide 21: Fastening Schedule
Table R602.3(1) for Interior Lateral applications
(see Table R602.3(3) for wood structural panel exterior wall sheathing to wall framing
Notes: Fastening Schedule
This is a continuation of the fastening schedule table. The table indicates the difference in the allowable fastener if used at a regular section of the wall as shown in Row 14, versus the same connection used at a braced wall panel segment shown in Row 15. As this example indicates the braced wall panel requires three times as many 16 penny common nails for the same connection.
Row 30 specifies the fastener schedule for wood structural panels and wall sheathing. This table reflects the fastening schedule for interior wall applications and Table R602.3(3) is the fastening schedule for exterior applications.
No Change 14

## Slide 22: Braced Wall Plan
602.10.1 Brace wall lines
602.10.1.1 Length of a brace wall line The length of a braced wall line is the distance between the two ends.
602.10.1.2 Offsets along a brace wall line Exterior walls parallel to braced wall lines and all interior walls used as bracing, should not be offset more than 4 feet from a braced wall line.
602.10.1.3 Spacing of brace wall lines Brace wall lines can be no more than 60 feet on center when designing for wind and 35 feet when designing for seismic applications.
Brace wall lines are the walls that require bracing in order to provide resistance to wind or seismic loads. All exterior walls are part of the braced wall lines. Some interior walls may be braced walls, depending on the building shape, spacing, and other factors.
Notes: Slide 23 – Braced Wall Plan
This is a typical braced wall plan. Brace wall lines are the walls that require bracing in order to provide resistance to wind or seismic loads. All exterior walls are part of the braced wall lines. Some interior walls may be braced walls, depending on the building shape, spacing, and other factors.
The code specifies three characteristics of a brace wall line.
Length of a Brace Wall Line
The length of a braced wall line is the distance between the two ends.
Offsets along a Brace Wall Line
Exterior walls parallel to braced wall lines and all interior walls used as bracing, should not be offset more than 4 feet from a braced wall line.
Spacing of Brace Wall Lines
Brace wall lines can be no more than 60 feet on center when designing for wind and 35 feet when designing for seismic applications.
No Change 15
Student Handout Material

## Slide 23: Braced Wall Panels
Braced wall lines consist of braced wall panels. Each braced wall panel contains the wall panel material, the framing and the fasteners.
Braced Wall Panel
602.10.2 Brace wall panels
Full height sections of wall.
No vertical or horizontal offsets.
Bracing methods per section R602.10.4.
602.10.1 Brace wall lines
Braced wall panels must start within 10’ of the end of the brace wall line.
Braced wall panels must be no more than 20’ edge to edge.
Minimum amount of braced wall panels in each braced wall line.
Braced Wall Panel
Framing
Fasteners
Notes: Braced Wall Panels
Braced wall lines consist of braced wall panels. Each braced wall panel contains the wall panel material, the framing, and the fasteners.
The code states that braced wall panels must start within 10 feet of the end of the brace wall line and must be no more than 20 feet edge to edge.
It also states that each panel must be full height sections of the wall. The panel must not contain vertical or horizontal offsets. The code defines a variety of acceptable bracing methods in section R602.10.4.
No Change 16
Student Handout Material

## Slide 24: Braced Wall Spacing
A
B
C
D
x
x
x
x
x
x
x
x
x
x
Braced wall line
x
Braced wall spacing
Notes: Braced Wall Spacing
However, braced wall lines do not need to extend all the way through the building. Diagram A contains the distance x between two braced wall lines. Diagram B contains three braced wall lines with half the braced wall spacing as Diagram A, even though the center wall does not go all the way through the building, but the braced wall spacing is still calculated as the distance from one brace wall line to the next closest brace wall line.
No Change 17

## Slide 25: Braced Wall Line Offsets
Code states that braced wall panels must not contain vertical or horizontal offsets.
Horizontal Offset
Vertical Offset
Notes: Braced Wall Panel Offsets
Code states that braced wall panels must not contain vertical or horizontal offsets. This illustration demonstrates a vertical offset where the garage is lower than the section of home constructed on a raised floor system. The front wall section would not qualify for a braced wall panel since it contains a vertical offset.
Similarly, the plan view at the bottom illustrates a horizontal offset where the wall of the garage is bumped out. This wall section would not qualify for a braced wall panel since it contains a horizontal offset.
No Change 18

## Slide 26: Bracing Methods
The code defines many different bracing methods in this table.
Notes: Braced Wall Panel Methods
The code defines many different bracing methods in this table. Each method defines the material, minimum thickness, and connector fasteners and spacing. Bracing method preferences tend to be regional, so they will change throughout the country.
No Change 19

## Slide 27: Braced Wall Panel Length
Notes: Braced Wall Panel Length
The code defines the minimum horizontal length for different types of braced wall panels in this table. The most common panels are 48 inches. However, builders should reference this table for lengths when using other materials.

## Slide 28: Locations for Braced Wall Panels
R602.10.2.2 Locations of braced wall panels
Shall begin no more than 10’ from end of braced wall line.
Shall be no more than 20’ edge to edge.
Notes: Locations for Braced Wall Panels
Braced wall panels must begin no more than 10 feet from the end of a braced wall line and no more than 20 feet from edge to edge. The figure shows code approved designs with the use of windows on the top and bottom.
No Change 20
Student Handout Material

## Slide 29: Required Length of Bracing
R602.10.3 Required length of bracing
Along each braced wall line shall be per Table 602.10.3(1).
Adjustment factors Table 602.10.3(2).
Notes: Required Length of Bracing
Two tables specify the length of bracing required for braced wall lines. The first table specifies the length of bracing and the second table provides adjustment factors.

## Slide 30: Continuous Sheathing
Notes: Continuous Sheathing
This figure shows the use of braced wall panels when used with continuous sheathing. The panel width in this application benefits by the use of sheathing above the window and door openings, allowing the use of smaller panels.

## Slide 31: Continuous Sheathing Table R602.10.5
This table lists the minimum length of braced wall panels when used with continuous sheathing.
Notes: Continuous Sheathing Table R602.10.5
This table lists the minimum length of braced wall panels when used with continuous sheathing. In this example of an 8 foot wall next to an 82 inch door clear opening, the minimum panel length should be between 32-35 inches.
No Change 21

## Slide 32: Continuous Sheathing End Conditions: Adding holdowns
If a braced wall panel is at the end of the braced wall line but there is no return panel on the adjacent wall, a holdown is required to keep the thin panel from over turning.
END CONDITION 2
If a braced wall panel is at the end of the braced wall line and on the adjacent wall, no holdown is required.
END CONDITION 1
If a minimum of 48 inch braced wall panel is at the end of the braced wall line, no holdown is required.
END CONDITION 3
If there is a return panel in the corner of at least 2 feet, no holdown is required.
END CONDITION 4
If there is a window in the corner of the braced wall line, the first braced wall panel needs to be less than 10 feet from the end. However, if there is no return panel in the corner, a holdown device is required on the leading edge of the first braced wall panel.
END CONDITION 5
These five end conditions indicate where to install a holdown device.
Notes: End Conditions for Braced Wall Lines with Continuous Sheathing
There are 5 end conditions shown here that indicate where to install a holdown device, based on what element is in the corner of the braced wall line.
End Condition 1 – If a braced wall panel is at the end of the braced wall line and on the adjacent wall, no holdown is required.
End Condition 2 – If a braced wall panel is at the end of the braced wall line but there is no return panel on the adjacent wall, a holdown is required to keep the thin panel from over turning.
End Condition 3 – If a minimum of 48 inch braced wall panel is at the end of the braced wall line, no holdown is required.
End Condition 4 – If there is a return panel in the corner of at least 2 feet, no holdown is required.
End Condition 5 – If there is a window in the corner of the braced wall line, the first braced wall panel needs to be less than 10 feet from the end. However, if there is no return panel in the corner a holdown device is required on the leading edge of the first braced wall panel.
Please take a moment to read the additional requirements shown here before proceeding.
No Change 21

## Slide 33: Check Your Knowledge
Brace wall panels include
Which of the following?
Select all that apply
Roof Rafters
Sheathing
Foundation
Fasteners
Framing
Notes: Check Your Knowledge
No Change 22

## Slide 34: Portal Frame Panel with Holdowns
A portal frame is a type of braced wall panel used when there is a large opening, usually a garage door. This section is taken directly from the code and specifies the requirements for construction of a portal frame with holdowns.
It is important for builders to follow the code precisely as it is drawn and specified. Making substitutions and changes drastically reduce the portal frame capacity.
Notes: Portal Frame Panel with Holdowns
A portal frame is a type of braced wall panel used when there is a large opening, usually a garage door. This section is taken directly from the code and specifies the requirements for construction of a portal frame with holdowns.
It is important for builders to follow the code precisely as it is drawn and specified. Making substitutions and changes drastically reduce the portal frame capacity.

## Slide 35: Continuous Sheathed Portal Frame Panel
This code section specifies the requirements for construction of a portal frame for use with continuous sheathing applications.
Notes: Continuous Sheathed Portal Frame Panel
This code section specifies the requirements for construction of a portal frame for use with continuous sheathing applications.
This panel is very similar to the portal frame in the previous slide without the holdown devices and with just a single plate at the bottom. In addition, this panel accommodates a raised wood floor system.

## Slide 36: Header Strap Table
Both of the previous portal frame designs specified a header to jack-stud strap on both sides of the opening on the opposite side of the sheathing. This table specifies the tension strap capacity.
Notes: Header Strap Table
Both of the previous portal frame designs specified a header to jack-stud strap on both sides of the opening on the opposite side of the sheathing. This table specifies the tension strap capacity.
The highlighted example assumes a 10 foot high wall with a 2 foot pony wall, and a 9 foot door opening. A specified wind speed of 130 miles per hour results in the need for a 1475 pound strap.

## Slide 37: Installation Fail
Notes: Installation Fail
This portal frame installation does not contain the proper holdown devices. Each section should contain two holdown devices per panel. However, this builder only installed one in the center, and one on each side. This significantly reduces the portal frame capacity.

## Slide 38: Installation Fail
Notes: Installation Fail
This portal frame installation has an incorrect header that extends over the doorway opening, but does not extend across any of the walls.

## Slide 39: Proper Header Installation
Header Misconception
Portal Frame
“In a house design where some main walls may have many openings, portal frames can be the key to providing code-compliant wall bracing. The example above illustrates a portal frame solution with two reinforced corners flanking a double garage door. The two garage door assembly could also have a portal frame in the center, but either way, the header should not be continuous.”
Portal Frame
Foundation
Header
Notes: Proper Header Installation
A common misconception of portal frames is that the header should be continuous in double garage applications. This illustration shows the correct method of construction with two reinforced corner panels flanking a double garage door.
Excerpt from JLC Magazine.
Student Handout Material

## Slide 40: Double and Single Portal Frame
Header
King Stud
Extent of
Single Portal Frame
Extent of
Double Portal Frame
Notes: Double and Single Portal Frame
This graphic illustrates a double and single portal frame. As shown in the code, the builder should install the header in two pieces. This allows a king stud to be used in the center wall segment to handle the loads perpendicular to the wall.

## Slide 41: Mixing Methods
Mixing different bracing methods.
Mixing Gypsum Board on the interior of a braced wall line.
Continuous sheathing on the exterior portion.
R602.10.4.1 Mixing methods
Mixing CS-WSP with PF-H shall be permitted.
Mixing intermittent methods (GB) on the interior section of a BWL with CS-WSP on the exterior portions shall be permitted.
The length of bracing required shall be of the weakest method.
Notes: Mixing Methods
The newest code now allows mixing different bracing methods. This applies to the continuous sheathing method with the portal frame with holdown method. In addition, mixing Gypsum Board on the interior of a braced wall line and continuous sheathing on the exterior portion is now code-permitted.

## Slide 42: Interior Finishes
The code now allows Gypsum wall board to be omitted, provided the bracing length is multiplied by the adjustment factor in the factor table shown here.
R602.10.4.3 Interior finishes
Gypsum wall board is permitted to be omitted provided the bracing length is multiplied by the adjustment factor in Table R602.10.3(3)/(4)
  Factor 1.4
Notes: Interior Finishes
The code now allows Gypsum wall board to be omitted, provided the bracing length is multiplied by the adjustment factor in the factor table shown here.

## Slide 43: Braced Wall Panel Connections
Notes: Braced Wall Panel Connections
It is essential to secure the roof, ceiling, and floor diaphragms to the brace wall panels below, as well as securing the brace wall panels to the diaphragm below to form a complete load path. Add a joist above or below the wall, or add blocking every 16" between the joists.

## Slide 44: Connections to Roof Framing
Notes: Connections to Roof Framing
Blocking is mandatory at brace wall panels. Builders must secure the roof diaphragm to the brace wall panel below. The code provides several methods for this connection. If the heel height is less than 15 inches, add solid blocking between the rafters. If the heel height is up to 4 feet, add solid blocking at the end and add solid sheathing at the bottom. A solid frame is allowed with an air gap at the top for ventilation.

## Slide 45: Panel Joints
All horizontal joints are to be blocked in order to secure the panel. There are several exceptions:
R602.10.10 Panel joints
Vertical joints of panel sheathing shall occur over, and be fastened to, common studs. Horizontal joints in braced wall panels shall occur over, and be fastened to, common blocking of a minimum 1½″ (38 mm) thickness.
Exceptions:
- Not required in wall segments that are not counted as brace wall panels.
- Not required where twice the required length is provided. with Method WSP or CS-WSP.
- Not required with method GB*.
- Unless 4” O/C nailing is used.
Notes: Panel Joints
All horizontal joints are to be blocked in order to secure the panel. There are several exceptions:
  Not required in wall segments that are not counted as brace wall panels
  Not required where twice the required length is provided with Method WSP or CS-WSP
  Not required with method GB, unless 4 inch on center nailing is used

## Slide 46: Cripple Wall Bracing
R602.10.11 Cripple wall bracing
Cripple walls shall be braced with the length and method of the wall above.
Multiply length be a factor of 1.15.
Where gypsum is not used multiply by a factor of 1.4 (cumulative).
Where any cripple wall segment in a braced wall line exceeds 48” in height, the entire cripple wall shall be counted as an additional story.
Notes: Cripple Wall Bracing
There are several requirements that apply to bracing for cripple walls that enclose a crawl space under the first floor. Please review them before proceeding.

## Slide 47: Check Your Knowledge
When designing for wind, braced wall lines shall be spaced
No more than ___________.
4 feet
35 feet
60 feet
80 feet
Notes: Check Your Knowledge
No Change 23

## Slide 48: Summary
Continuous load paths for lateral resistance.
Lesson 1 Structural basics for residential wood frame construction. The effects of lateral wind and seismic forces on a building. The importance of establishing a continuous load path.
Lesson 2 Wall construction and wall reinforcement for a lateral continuous load path. Fastening schedules; the importance of using the correct code-listed fastener. Braced wall panels and braced wall lines, and code requirements for spacing, lengths, and methods of bracing. Portal frame panels used with garage door openings.
Notes: Summary
This training covered many different topics on continuous load paths for lateral resistance.
The first lesson discussed structural basics for residential wood frame construction. The lesson discussed the effects of lateral wind and seismic forces on a building and provided information on the importance of establishing a continuous load path.
Lesson 2 provided information on wall construction and wall reinforcement used for creating a lateral continuous load path. The lesson included fastening schedules and the importance of using the correct code-listed fastener. The lesson discussed braced wall panels and braced wall lines, providing code requirements for spacing, lengths, and methods of bracing. The lesson also discussed portal frame panels used with garage door openings.
No Change 24

## Slide 49
Continuous Load Path Systems for Lateral Resistance
ASSESSMENT
Final Assessment
There are 10 questions. You must pass with a score of at least 70%.
Notes: Final Assessment
There are 10 questions in the final assessment and you must pass with a score of at least 70%.
No Change 25

## Slide 50: Congratulations!
You have completed this course. Use the Exit button to close the training.
SST-198-03-P02_Continuous Load Path for Lateral Resistance_v001 Copyright © 2020 Simpson Strong-Tie. All rights reserved.
Notes: Congratulations!
You have completed this course. Use the Exit button to close the training.
No Change 26