## Slide 1: BUILDER TRAINING SERIES
Residential Construction Plans 101
Notes: Welcome
Welcome to this course on Residential Construction Plans 101
Presented by Simpson Strong-Tie

## Slide 2: Credit Information
Professional Development Hours
Simpson Strong-Tie® offers Professional Development Hours for completing this course. No other continuing education or accredited credits are available for this course.
This course offers .5 PDH (1/2 hour of PDH credit)
Notes: Credit Information – Professional Development Hours
Simpson Strong-Tie offers Professional Development Hours for completing this course. No other continuing education or accredited credits are available for this course.

## Slide 3: Course Requirements
Pass the Class to Earn Personal Development Hours
EXERCISES
Complete the Knowledge Checks in the course
PASS ASSESSMENT
Pass the Final Assessment at the end of the course
READ & LISTEN
Read and listen to all course material in sequence
Notes: Course Requirements
To pass the class and earn Professional Development Hours, read and listen to all course material in sequence, complete the Knowledge Checks in the course, and pass the final assessment at the end of the course.

## Slide 4: About this Course
Overview of residential and multi-family construction plans with a focus on the structural aspects of the documents.
Different types of construction documents
Sample plans for review.
Course Learning Objectives When you have completed this course, you should be able to:
  Describe the types of construction plans
  Recall basic elements on construction plans
  Identify specified structural elements on construction documents
Notes: About this Course
This course provides an overview of residential and multi-family construction plans with a focus on the structural aspects of the documents. The course introduces different types of construction documents, explains the information they contain, and provides many sample plans for review.
When you have completed this course, you should be able to:
Describe the types of construction plans
Recall the basic elements contained on construction plans
Identify specified structural elements on construction documents

## Slide 5: Course Agenda
LESSON 1 Overview of Construction Plans
LESSON 2 Types of Construction Plans
LESSON 3 Parts of the Construction Plan Documents
LESSON 4 Identify Specified Products
Notes: Course Agenda
The topics covered in this course include the following:
Lesson 1
Overview of Construction Plans
Lesson 2
Types of Construction Plans
Lesson 3
Parts of the Construction Plan Documents
Lesson 4
Identify Specified Products

## Slide 6
Residential Construction Plans 101
LESSON 1
Overview of Construction Plans
Notes: Lesson 1: Overview of Construction Plans
This lesson introduces the basic components of construction plans including what they are, who creates them, and the information they include.

## Slide 7: Major Market Segments
Infrastructure & Heavy Construction
Residential construction consists of single family and multi-family homes, large residential builders, and custom homes.
Residential
Institutional and commercial construction includes schools, healthcare centers, sports stadiums, shopping centers, warehouses, and other facilities that serve the public.
Institutional & Commercial
Specialized industrial segment includes more technologically complex projects such as oil refineries, steel mills, chemical processing plants, and nuclear power plants.
Specialized Industrial
The infrastructure and heavy construction market includes projects such as highways, mass transit systems, bridges, and sewage treatment plants.
Notes: Major Market Segments
Click: There are four major market segments within the construction industry.
Click: Residential construction consists of single family and multi-family homes, large residential builders, and custom homes.
Click: Institutional and commercial construction includes schools, healthcare centers, sports stadiums, shopping centers, warehouses, and other facilities that serve the public.
Click: Specialized industrial segment includes more technologically complex projects such as oil refineries, steel mills, chemical processing plants, and nuclear power plants.
Click: The infrastructure and heavy construction market includes projects such as highways, mass transit systems, bridges, and sewage treatment plants.
Each of these four market segments use construction documents with variations, specifications, and configurations that address the unique aspects of their specific project requirements.
This training only focuses on the residential and multi-family construction market segment.
Student Handout Material

## Slide 8: Construction Plans
Includes: Cautions, a parts list, required tools, numbered illustrations, and a sequenced set of instructions.
Basic Assembly Instructions
Notes: Construction Plans
Basic Assembly Instructions
Many people have attempted to assemble items that require a construction plan. This could include swing sets, treehouses, furniture, bicycles, or toys. The plan can include cautions, a parts list, required tools, numbered illustrations, and a sequenced set of instructions. The assembly task becomes much easier when the plans are clear and concise.

## Slide 9: Residential Construction Plans
A complete set of construction documents includes:
  Plans
  Specifications
  Drawings
  Mechanical systems
  Finishes
  Installation notes
  Items agreed upon between Owner and Contractor
They reflect the understanding that each party has regarding project construction.
Home Building Instructions
Notes: Residential Construction Plans
Home Building Instructions
Residential construction plans are essentially assembly plans on a much larger and complex scale. The complete set of construction documents include plans, specifications, drawings, mechanical systems, finishes, and installation notes. Construction plans contain items agreed upon between the Owner and the Contractor and reflect the understanding that each party has with regard to constructing the project.

## Slide 10: Construction Plan Development
The team may include a designer or Architect and specialty subcontractors (engineering, grading, electrical, and plumbing).
Individual or Team Preparation
Notes: Construction Plan Development
Individual or Team Preparation
An individual or team of professionals prepare and develop construction plans. Depending on the complexity of the project, the team may include a designer or Architect, and specialty subcontractors from fields such as engineering, grading, electrical, and plumbing.

## Slide 11: Full Sets of Construction Documents
Construction documents are required for city and state officials to understand, permit, and monitor the proposed building based on the jurisdictions current adopted codes.
The Building Code identifies construction document requirements for a building permit.
Code Book Definition
CONSTRUCTION DOCUMENTS
“Written, graphic and pictorial documents prepared or assembled for describing the design, location, and physical characteristics of the elements of a project necessary for obtaining a building permit. Construction drawings shall be drawn to an appropriate scale.”
Notes: Full Sets of Construction Documents
Code Book Definition
Construction documents are required for city and state officials to understand, permit, and monitor the proposed building based on the jurisdictions current adopted codes. This excerpt from the Building Code is quite clear on the aspects of construction documents required in order to obtain a building permit.
CONSTRUCTION DOCUMENTS
Written, graphic and pictorial documents prepared or assembled for describing the design, location, and physical characteristics of the elements of a project necessary for obtaining a building permit. Construction drawings shall be drawn to an appropriate scale.

## Slide 12: Code Guidelines for Construction Documents
Material, Clarity, and Detail Defined
R106.1.1 Information on construction documents.
Construction documents shall be drawn upon suitable materials.
Electronic media documents are permitted to be submitted where approved by the building official. Construction documents shall be of sufficient clarity to indicate the location, nature and extent of the work proposed and show in detail that it will conform to the provisions of this code and relevant laws, ordinances, rules and regulations, as determined by the building official.
Notes: Code Guidelines for Construction Documents
Material, Clarity, and Detail Defined
This segment from the building code indicates that construction documents be drawn on suitable material, and be clear enough to indicate the location, nature, and extent of the proposed work.

## Slide 13: Code Guidelines for Specific Drawings
Braced Wall Design Lines
R106.1.3 Information on braced wall design.
For buildings and structures utilizing braced wall design, and where required by the building official, braced wall lines shall be identified on the construction documents. Pertinent information including, but not limited to, bracing methods, location and length of braced wall panels and foundation requirements of braced wall panels at top and bottom shall be provided.
Notes: Code Guidelines for Specific Drawings
Braced Wall Design Lines
This segment from the building code is for buildings using braced wall designs and the elements that are required to include on the construction documents.

## Slide 14: Construction Document Timeline
Project
Completed
Construction
Drawings
Construction documents issued to the builder should include all aspects of building and installation requirements
Revisions
and RFI’s
Revisions to the documents are submitted throughout the construction process
Preliminary Drawings
The architect or designer supplies preliminary drawings to the design team or project owner
Bid
Documents
The team uses bid documents to obtain material and labor bids for the project, and may not be fully complete at this point
Permit
Documents
Permit Documents are plans submitted to obtain a permit and should be a full and exact plan of the proposed building
From Initial Drawing to Project Completion
Process
Begins
Notes: Construction Document Timeline
From Initial Drawing to Project Completion
This timeline shows the generalized flow of the construction documents, from the creation of the preliminary drawings through project completion. Many times, residential construction project have shorter timelines with consolidated steps.
Preliminary Drawings
The architect or designer supplies preliminary drawings to the design team or project owner.
Bid Documents
The team uses bid documents to obtain material and labor bids for the project, and may not be fully complete at this point.
Permit Documents
Permit Documents are plans submitted to obtain a permit and should be a full and exact plan of the proposed building.
Construction Documents
Construction documents are issued to the contractor or builder and should include all aspects of building and installation requirements.
Revisions and RFI’s
Revisions to the construction documents are submitted throughout the construction process to clarify items that may be unclear.
Student Handout Material

## Slide 15: Request for Information (RFI) Process
RFI is a formal documentation process used to resolve gaps, conflicts, and subtle ambiguities in the construction documents.
RFIs are submitted to the owner, project owner, engineer on record, or other individual.
Revisions to Construction Plans
Notes: Request for Information (RFI) Process
Revisions to Construction Plans
Construction plans and documents change during the course of the project. Request for Information, or RFI, is a formal documentation process used to resolve gaps, conflicts, and subtle ambiguities within the construction documents. RFI’s can occur at any stage of the construction process and usually indicate a situation where feedback is required for a task to proceed to the next step. Some firms have special forms and methods to submit an RFI, that is then submitted to the owner, project owner, engineer on record, or other individual.
Student Handout Material

## Slide 16: Check Your Knowledge
When a contractor or builder is unclear on an element contained in the construction plan, what is the recommended action?
Call the architect, engineer on record, or project owner.
Contact the city building inspector for information.
Submit an RFI to the architect, engineer on record, or project owner.
Contact the manufacturer of the product being installed.
Notes: Check Your Knowledge

## Slide 17
Types of Construction Plans
Residential Construction Plans 101
LESSON 2
Notes: Lesson 2: Types of Construction Plans
This lesson discusses the three main levels of construction plans; basic, detailed, and professional construction plans.

## Slide 18: Basic Plans
Contain elevations and dimensions.
The plans are usually incomplete.
Basic drawings may only contain dimensions with an outline and still receive a permit, depending on the code enforcement jurisdiction.
Minimum Detail and Specifications
Example of a basic plan. It contains dimensions, overall size, fixture locations, window and door indications. This sample contains the minimal construction information.
Notes: Basic Plans
Minimum Detail and Specification
Basic plans contain very little detail beyond elevations and dimensions. The plans may contain some detail on specifications but are usually incomplete. Basic drawings may only contain dimensions with an outline and still receive a permit, depending on the code enforcement jurisdiction.
Basic Plan Example
This is an example of a Basic plan. It contains dimensions, overall size, fixture locations, window and door indications. This sample contains minimal construction information.
Student Handout Material

## Slide 19: Designed Plans
Can include the dimensions and elevations, plus include specifications and call-outs for structural members.
Contain greater detail for structural call-outs such as walls, framing members, foundations, and roofs.
May also include specifications for cabinets, windows, doors, wall coverings, roof coverings, and may also specify structural connections.
Most of these plans are designed prescriptively to the IRC. Approximately 65% or more of residential construction plans fall into the designed plan category.
Prescriptive Specifications
Example of a designed plan. It contains many details that include dimensions, window callouts, vaulted ceiling, and call outs for framing information. This sample does not contain any specifications for structural connections.
Notes: Designed Plans
Prescriptive Specifications
Designed plans can include the dimensions and elevations, plus include specifications and call-outs for structural members. These plans would contain greater detail for structural call-outs such as walls, framing members, foundations, and roofs. These plans may also include specifications for cabinets, windows, doors, wall coverings, roof coverings, and may also specify structural connections. Most of these plans are designed prescriptively to the IRC. Approximately 65% or more of residential construction plans fall into the designed plan category.
Designed Plan Example
This is an example of a designed plan. It contains many details that include dimensions, window callouts, vaulted ceiling, and call outs for framing information. This sample does not contain any specifications for structural connections.
Student Handout Material

## Slide 20: Professional Plans
Contain basic and design plans, plus the design criteria, most or all structural connections, assemblies, structural and non-structural members, and a fully engineered foundation.
May include many pages, with highly detailed and technical notes, installation instructions, call-outs and drawings.
Engineered and Sealed
Example of a professional plan that contains the design parameters to clarify code, hazards, wind and seismic factors, and loads used for the specific project.
Notes: Professional Plan
Engineered and Sealed
Professional plans contain all the elements of the basic and design plans, plus plus the design criteria, most or all structural connections, assemblies, structural and non-structural members, and a fully engineered foundation. Professional Plans may includemany pages, each with highly detailed and technical notes, installation instructions, call-outs, and drawings.
Professional Plan Example
This is an example of a professional plan that contains the design parameters to clarify code, hazards, wind and seismic factors, and loads used for the specific project.
Student Handout Material

## Slide 21: Engineered Plan Example
Structure Design Criteria Sheet accompany a sealed engineered plan:
  Structure design for wind
  Components and cladding pressures
  List of Sheets included
  IRC 2006 General Notes
  Wood frame construction check list
Structure Design Criteria Sheet
Notes: Engineered Plan Example
Structure Design Criteria Sheet
This is an example of a Structure Design Criteria sheet that is one of the documents to accompany a sealed engineered plan.
The notes contain information on the structure design for wind, a chart for components and cladding pressures, an index of the different sheets included with this plan, general notes from the IRC 2006 code, and a wood frame construction check list.

## Slide 22: Prescriptive Design vs Engineered Design
Engineered
Usually project-specific design
Licensed Engineer and/or architect takes legal responsibility and seals plans
All changes are submitted to EOR for approval
Follow the IBC code standards
Prescriptive
General design of plan
American Institute of Building Design (AIBD) or home plan designer
Follow the IRC code standards
Notes: Prescriptive Design vs Engineered Design
There are two methods available for construction design: Prescriptive Design and Engineered Design.
Prescriptive Designs provide a general design of the plan that proposes a set method for the work, specifying both the material and installation. An AIBD, home plan designer, or other design professional can create Prescriptive designs and plans following the IRC code standards.
Engineered designs are usually a project-specific design created by a licensed engineer or architect. Once completed, the design professional signs and seals the plans, indicating that they vouche for the accuracy and accepts legal responsibility for the sealed plans. All changes and revisions to an Engineered design must be submitted to the Engineer on Record (EOR) for approval. Engineered designs and plans usually follow the IBC code standards.
Student Handout Material

## Slide 23: Check Your Knowledge
Which type of construction plan contains a seal that indicates the engineer accepts legal responsibility for the plans?
Basic Plan
Designed Plan
Engineered Plan
Notes: Check Your Knowledge

## Slide 24
Parts of the Construction Plan Documents
Residential Construction Plans 101
LESSON 3
Notes: Lesson 3: Parts of the Construction Plan Documents
This lesson reviews sample construction plans to identify products that require installation.

## Slide 25: Cover Sheet
Most plans include a Cover Sheet that contains an overview of the general project information.
Project Name and Location
Map
Title Block Section
Design Firm
Client
Contractors
Index of Individual Sheets
Legend or Key
Notes: Cover Sheet
Most plans include a Cover Sheet that contains an overview of the general project information.
Click: They have many different layouts and designs, and should always include the project name and project location.
Click: Sometimes cover sheets include a map.
Click: Plan sheets contain a title block section that should always contain the architect or design firm, and usually the client, and specialty contractors.
Click: The cover sheet also includes an index of the individual sheets, including sheet number, issue dates, and revision information.
Click: The sheet also contains a legend or key on how to interpret symbols used throughout the plans. The title block will also include the official seal for engineered plans.
Click:
Student Handout Material

## Slide 26: Standardized Drawing Sizes
Uniform Size and Consistency
Notes: Standardized Drawing Sizes
The charts shown here reference the standardized sizes for architectural and engineering construction drawings. The uniform size requirements assist in the uniform clarity and consistent dimensionality of the project documents. The highlighted section contains the most common sizes used in the field.

## Slide 27: Basic Symbols
Different styles of document symbols are used to highlight, detail, reference, and clarify items on construction document drawings. The drawings may contain a legend to interpret the document symbols. The document symbols reference other drawings within the set in order to enlarge an area and provide more detail.
Identification for Secondary sheets
Notes: Basic Symbols
There are many different methods and styles of document symbols used to highlight, detail, reference, and clarify items on construction document drawings. The drawings may contain a legend to identify how to interpret the document symbols. One of the main functions of the document symbols is to reference other drawings within the set in order to enlarge an area and provide more detail. In this document, the designer highlights an area and then uses a circle that contains the detail number on top and the sheet number on the bottom. The sample on the right uses this type of reference to call-out detail number 88 located on sheet S5.04, which would contain an enlargement of the area and provide instructions that are more detailed for item number 88.

## Slide 28: Floor or Ceiling Framing Symbols
2x6 framing at 16” on center.
Bottom of joists are 12 feet high.
Wood framed plans include framing instructions, shown here.
Identification for Secondary sheets
Notes: Floor or Ceiling Framing Symbols
Wood framed plans include framing instructions such as the one shown here. The symbol indicates 2x6 framing at 16 inches on center. The height is at 12 feet, which indicates the bottom of the joists are 12 feet high.

## Slide 29: Location Grid Lines
Describing Locations on Plans
Notes: Location Grid Lines
Describing Locations on Plans
Construction lines, column lines, or grid lines denote a method for locating and describing a section on the construction drawings. These location grids become invaluable when speaking with an engineer or architect on the phone. The grid pattern usually uses uniform spacing, but may have sub-sets in areas where the building layout changes.

## Slide 30: Construction Document Sheets
Architectural Sheets
While residential projects require a smaller set of construction documents that accompany the drawings and plans, larger commercial projects require a greater set of construction document sheets.
Details for Each Aspect of Construction
CIVIL SHEET containing information on the soil, water flow, street and parking lot information
Civil or Site Sheets
Electrical Sheets
Fire Sheets
Landscape Sheets
Structural Sheets
Plumbing Sheets
Mechanical Sheets
COVER SHEET contains information on the project details and includes the contractors or individuals responsible for each aspect of the project
ARCHITECTURAL SHEETS that contain structural details, dimensions, assembly, and a visual representation of the project
ELECTRICAL SHEETS provide information on the electrical layout including power circuits and voltages
FIRE SHEETS contain egress, fire exits, and other fire requirements
LANDSCAPE SHEETS contain the types and location of trees, plants, and landscaping
PLUMBING SHEETS provide water and sewage pipe layout and locations
STRUCTURAL SHEETS contain detailed information on how the building live loads and dead loads are physically supported
MECHANICAL SHEETS contain all the specifications for heating and air conditioning
Notes: Construction Document Sheets
Details for Each Aspect of Construction
While residential projects require a smaller set of construction documents that accompany the drawings and plans, larger commercial projects require a greater set of construction document sheets. Following are some of the more common document sheets included with large projects:
The Cover Sheet contains information on the project details and includes the contractors or individuals responsible for each aspect of the project
Click: Architectural sheets that contain structural details, dimensions, assembly, and a visual representation of the project
Click: Civil or Site Sheets containing information on the soil, water flow, street and parking lot information
Click: Electrical Sheets provide information on the electrical layout including power circuits and voltages
Click: Fire Sheets contain egress, fire exits, and other fire requirements
Click: Landscape Sheets contain the types and location of trees, plants, and landscaping
Click: Plumbing Sheets provide water and sewage pipe layout and locations
Click: Structural Sheets contain detailed information on how the building live loads and dead loads are physically supported
Click: Mechanical Sheets contain all the specifications for heating and air conditioning

## Slide 31: Check Your Knowledge
Which of the following items should always be included on the cover sheet?
Select All That Apply
Call-outs for Specialty Framing
Project Name
Notes on Specified Foundation Materials
Project Address
Architect of Design Firm
Notes: Check Your Knowledge

## Slide 32
Identify Specified Products
Residential Construction Plans 101
LESSON 4
Notes: Lesson 4: Identify Specified Products
This lesson reviews sample construction plans to identify products that require installation.

## Slide 33: Primary Residential Construction Plans
The Main Sheets Within a Set
Structural Sheets
General Notes
Loading Information
Material Properties
Load Supporting Elements
Connections
Architectural Sheets
Cover Sheet
  Contracted Parties
  Building Occupancy and Size
Elevations of Finished Building
Building & Room Dimensions
Wall Heights and Roof Pitches
Residential builders and installers usually encounter two types of Professional Design Plans; Architectural Sheets and Structural Sheets.
Other sheets may be included with the construction documents. However, these two contain most of the products, connectors, and elements required for installation by builders.
Notes: Primary Residential Construction Plans
Residential builders and installers usually encounter two types of Professional Design Plans; Architectural Sheets and Structural Sheets. Other sheets may be included with the construction documents. However these two contain most of the products, connectors, and elements required for installation by builders.
Architectural Sheets
Architectural sheets contain a cover sheet. This document identifies the contracted parties and the various companies and contractors who are working on the project. The cover sheet also contains general information such as the expected building occupancy and building size. This information helps to identify the scope of the project.
The elevation sheet for each story in the building contains dimensions for walls and floors along with the general appearance of the building.
The building and room dimension sheets are helpful in calculating the square footage for estimates and material requirements.
Architectural sheets also include wall heights and roof pitches to help determine hanger specifications.
Structural Sheets
Structural sheets provide general structural notes that contain the building code, loading information, and critical material properties such as concrete strength.
Load supporting elements are specified on the structural sheets that indicate the types of materials and sizes of structural elements. These include support load materials such as joists, beams, headers, studs, trusses, and plates.
Another necessary specification on structural sheets is connections. Simpson Strong-Tie product requirements are primarily going to be included within the structural documents.
Student Handout Material

## Slide 34: Elevations
Prescriptive Plan
Structure’s appearance and style.
May include below grade line items (foundation walls, footers, and window wells).
Notes: Elevations
This is a typical basic design residential elevation sheet. It indicates the appearance and style of the home from a front and back view. The reference point for most elevations is the grade line. Some elevations include items below the grade line such as foundation walls, footers, and window wells. The elevation provides external dimensions, height, roof slopes and roof features, garages, windows and doors, porches, decks and patios. The elevation also provides information on wall coverings such as brick, siding, or stucco.

## Slide 35: First Floor General Sheet
Prescriptive Plan
Basic design floor drawing.
Legend box may include additional details
Notes: First Floor General Sheet
This is a typical basic design floor drawing.
The plan drawing indicates rooms and room divisions, doors, windows, closets, stairways, dimensions, rough plumbing fixtures, cabinetry, garage, and porch areas.
Many floor plans contain a legend box or area that includes square footage, heated and non-heated area footage, and other overall details of the floor plan.

## Slide 36: First Floor Framing Sheet
Prescriptive Plan
Notes: First Floor Framing Sheet
This is a typical basic design floor framing plan. The drawing shows the same floor plan as the previous page, except this drawing contains framing specifications for the first floor area. Many of the non-structural elements are removed and the drawing now contains detailed information on the walls, sizes, and dimensions.

## Slide 37: Second Floor Framing Sheet
Prescriptive Plan
Lighter areas show first floor rooms for reference.
May contains future expansion areas.
Notes: Second Floor Framing
This drawing shows the upstairs rooms and features. The plan contains lighter areas to indicate the location of first floor rooms for reference orientation only. Many times this sheet also contains future expansion areas for the building.

## Slide 38: Braced Wall Call-Outs
WSW18x12
WSW18x12
WSW18x12
WSW18x12
Plan enlargement with structural element call-outs.
A-1 and 3-1 lines represents brace wall lines.
Brace Wall Line Indications
WSW18x12
WSW18x12
WSW18x12
Notes: Braced Wall Call-Outs
Brace Wall Line Indications
This structural plan enlargement contains typical call-outs for structural elements.
Click: The A-1 horizontal red line represents the brace wall line and 3-1 vertical green line that represents a second brace wall line. The WSW18x12 call-outs are for the Simpson Strong-Wall Wood Shearwall. There are a total of three walls, each 18 inches wide by 12 foot tall.

## Slide 39: Engineered Wiring Sheet
Floor plan sheet with electrical wiring details.
Overhead Fan Electrical
Notes: Engineered Wiring Sheet
Overhead Fan Electrical
This is an example of a floor plan sheet from an engineered floor plan. The legend indicates the various symbols that are used throughout the drawing.
Click: The sheet contains drawings and notes on the electrical wiring for the ceiling fans and overhead lights.

## Slide 40: Roof Elevation Details
Elevation and first floor drawings.
Vertical siding break detail.
Roof trusses, roof ridges.
Roof Truss Notes
Notes: Roof Elevation Details
Roof Truss Notes
This engineered plan example shows multiple items on a single page. It contains the elevation drawing and the floor drawing. The bottom right section contains specific information for the vertical siding break detail.
Click: The notes section contains extensive details for the roof trusses along with a drawing of the roof from the top down, indicating the roof ridges and valleys.

## Slide 41: Foundation Engineered Plan
Dimensions, footings, gas lines, plumbing lines, and water access.
Drainage and foundation notes.
Anchor Bolt Detail
Notes: Foundation Engineered Plan
Anchor Bolt Detail
This engineered plan is for the foundation. The drawing contains indications for dimensions, footings, gas lines, plumbing lines, and water access. The first note includes specifications for drainage and the second note contains foundation notes.
Click: The call-out illustration demonstrates the anchor bolt installation.

## Slide 42: Structural Detail Engineered Plan
Type of materials, sizes, connection types.
Details indicate how to build structural connections and framing areas.
Details for Item Assembly
Notes: Structural Detail Engineered Plan
Details for Specific Item Assembly
Engineered plans often include detail sheets for individual specifications and clarity. These details may include the type of materials, sizes, connection type, and clarity for installation required.
Click: This is another engineered plan that contains details indicating how to build or assemble certain structural connections and framing areas. Always check the main plan before referring to detail pages.

## Slide 43: Structural Anchorage
Details for the structural continuous load path anchorage.
Include step-by-step assembly for the floor-to-floor connection.
Floor to Floor Connection Plan
Notes: Structural Anchorage
Floor to Floor Connection Plan
This particular engineered plan contains details for the structural continuous load path anchorage on the plan view sheet. The plan details how the roof, walls, and floors are connected through to the foundation.
Click: The drawings at the bottom of the page illustrate the step-by-step assembly for the floor-to-floor connection plan.

## Slide 44: Wall Connection Details
Wall connectors details.
Plan for high wind area shown here.
High Wind Engineered Plan
Notes: Wall Connector Call-Outs
High Wind Engineered Plan
This engineered plan contains the connection details for the wall connectors.
Click: This specific plan is for a high wind area that is required to resist 140 miles per hour wind.

## Slide 45: Roof and Truss Details
Includes blocking details.
Nailing and Screw Patterns
Notes: Roof and Truss Call-Out Details
Nailing and Screw Patterns
This engineered plan contains details on roof connections.
Click: The plan contains blocking details, as well as nailing and screw patterns for blocking and other roof elements.

## Slide 46: Hybrid Seismic Wall Brace Plan
This plan is partially prescriptive based on IRC.
Includes wall bracing required for seismic and wind plan specifications.
Wall Brace Charts
Notes: Hybrid Seismic Plan
Wall Brace Charts
This plan is an engineered plan that is partially prescriptive.
Click: The charts at the bottom contain wall bracing information required for seismic and wind plan specifications. This plan type can be engineered or prescriptive based on the IRC.

## Slide 47: Lateral System Shear Walls
Includes a schedule for different shear wall configurations.
Multi-family Plan
Notes: Lateral System Shear Wall Panels
Multi-Family Plan
Click: This engineered multi-family plan includes a shear wall schedule with details and a legend for clarity. In addition, the plan contains a Shear Wall schedule that indicates different symbols for different shear wall configurations.

## Slide 48: Shear Wall Holdowns into Foundation
Holdown anchorage and embedment information.
Multi-family Plan
Notes: Shear Wall Holdowns into Foundation
Multi-Family Plan
Click: This engineered multi-family plan includes a detailed call-out for shear wall holddowns into the building foundation. The chart indicates holddown anchorage and embedment information. The illustration indicates the installation required.

## Slide 49: Check Your Knowledge
Which of the following call-outs may be included on an engineered construction plan?
Wiring and electrical setup
Shear wall specifications
Foundation CLP details
All of the above
Notes: Check Your Knowledge

## Slide 50: Summary
This training covered construction plans.
Lesson 1 Basic components of construction documents Importance of the RFI process in the revision of construction plans.
Lesson 2 Types of construction plans Difference between Prescriptive Design & Engineered Design plans.
Lesson 3 Common elements in plans Construction document sheets for large construction projects.
Lesson 4 Construction plans and typical products that require installation.
Notes: Summary
This training covered many different topics on construction plans. Lesson One introduced the basic components of construction documents including what they are, who creates them, and the information contained within a set of sheets. It also discussed the importance of the RFI process in the revision of construction plans.
Lesson Two discussed the types of construction plans and difference between Prescriptive Design and Engineered Design plans.
Lesson Three discussed the most common elements contained in plans such as cover sheets, symbols, and location grid lines. The lesson also included they many types of construction document sheets that are typical with large construction projects.
The final Lesson Four showed a variety of construction plans and identified typical products that require installation.

## Slide 51
Residential Construction Plans 101
ASSESSMENT
Final Assessment
There are 10 questions. You must pass with a score of at least 70%.
Notes: Assessment: Final Assessment
There are 10 questions in the final assessment and you must pass with a score of at least 70%.

## Slide 52: Congratulations!
You have completed this course.
SST-198-04_ResidentialConstructionPlans101_v001 Copyright © 2020 Simpson Strong-Tie. All rights reserved.
Notes: Congratulations!
You have completed this course.