## Slide 1: BUILDER TRAINING SERIES
Wood-Frame Construction 101
Notes: Title Slide Welcome
Welcome to this course on Wood-Frame Design 101
Presented by Simpson Strong-Tie

## Slide 2: Credit Information
Professional Development Hours
Simpson Strong-Tie® offers Professional Development Hours for completing this course. No other continuing education or accredited credits are available for this course.
This course offers .5 PDH (1/2 hour of PDH credit)
Notes: Credit Information — Professional Development Hours
Simpson Strong-Tie offers Professional Development Hours for completing this course. No other continuing education or accredited credits are available for this course.

## Slide 3: Course Requirements
Pass the Class to Earn Professional Development Hours
READ & LISTEN
Read and listen to all course material in sequence
PASS ASSESSMENT
Pass the Final Assessment at the end of the course
EXERCISES
Complete the Knowledge Checks in the course
Notes: Course Requirements
To pass the class and earn Professional Development Hours, read and listen to all course material in sequence, complete the Knowledge Checks in the course, and pass the final assessment at the end of the course.

## Slide 4: About this Course
Introduction to wood-frame construction for installers and supervisors in residential building construction.
Course Learning Objectives
When you have completed this course, you should be able to:
Understand basic terminology for wood-frame design.
Identify the common usage and benefits of wood-frame construction.
Understand basic framing concepts.
Notes: Course Description and Learning Objectives
This course provides an introduction to wood-frame construction for installers and supervisors in residential building construction.
When you have completed this course, you should be able to:
Understand basic terminology for wood-frame design
Identify the common usage and benefits of wood-frame construction
Understand basic framing concepts

## Slide 5: Course Agenda
Topics Covered in this Course
LESSON 1 Wood-Frame Construction Overview
LESSON 2 Construction Components
LESSON 3 Basic Construction Materials
Notes: Course Agenda
The topics covered in this course include the following:
Lesson 1: Wood-Frame Construction Overview
Lesson 2: Construction Components
Lesson 3: Basic Construction Materials

## Slide 6
Wood-Frame Construction 101
LESSON 1
Wood-Frame Construction Overview
Notes: Lesson 1: Wood-Frame Construction Overview
This lesson identifies the common usage and benefits of wood-frame construction.

## Slide 7: Common Usage
Wood frame construction is typically used in Northern America.
2x4 or 2x6 lumber is common.
Notes: Common Usage
Wood-frame construction is a very typical type of construction within Northern America. Many residential builders use 2”x4” or 2”x6” lumber for framing structures such as homes, apartments, motels, and light commercial projects.

## Slide 8: Benefits of Wood
Low Energy to Produce
Most Renewable
Abundant Resource
Sustainable
Strong Foundational Base
Minimal Construction Skills
Structurally Forgiving
Low-Cost Building Material
1
2
3
4
5
6
7
8
Notes: Benefits of Wood
Wood offers many advantages over other building materials. Wood requires the least amount of energy to produce and is by far the most renewable building material. Wood also is an abundant resource in the United States and harvesting methods provide a sustainable supply well into the future.
Wood provides a strong foundational base for residential construction and is highly adaptable to many different geometric shapes. Wood construction requires a minimal level of construction skills, and requires no heavy tools or equipment while at the same time remaining structurally forgiving. In addition, it is one of the lowest-cost building materials available in the market today.
(Student Handout Material)

## Slide 9: Framing Types
Platform Framing
First floor is built first.
Shorter lumber lengths are used.
Joints may be more complex with connectors between floors.
Fast and efficient construction process.
Balloon Framing
Uses long framing members that run from foundation to the top of the second story suspending the floor in the middle of the extended wall.
Reduces the complexity of creating joints; relies heavily on nail fasteners.
Required where two-story walls are not supported by a floor.
Notes: Framing Types
Typical construction in North America uses what is known as “platform” framing. In this process, the first floor is built first, and the next story is built on top of the previous. Platform framing uses shorter lumber lengths and may require more complex joints and connectors between floors. Platform framing is the most common form of framing and results in a faster and more efficient construction process.
Balloon framing utilizes long framing members that run from the foundation of the structure to the top of the second story, suspending the floor in the middle of the extended wall. Balloon framing reduces the complexity of creating joints and relies heavily on nail fasteners. Balloon framing is required in building design where two-story walls are not supported by a floor. An example of this would be a two-story entryway where the space is open to the upstairs floor. In this situation, the wall studs should be continuous (balloon framed) to the ceiling.

## Slide 10: Check Your Knowledge
Which of the following are benefits of wood
for residential construction?
SELECT ALL THAT APPLY
Low cost building material
Provides a fireproof structure
Abundant resource
Requires minimal construction skills to use
Highly resistant to deterioration and rotting
Notes: Check Your Knowledge

## Slide 11
Construction Components
Wood-Frame Construction 101
LESSON 2
Notes: Lesson 2: Construction Components
This lesson introduces the primary construction components used in residential wood-frame construction.

## Slide 12: Four Main Construction Components
Foundation
Wall
Floors
Roof
Platform Framing
Notes: Four Main Construction Components
The illustration on this slide is an example of platform framing and contains the four main construction components in typical residential buildings.
Click: The first component is the foundation that provides a sound structural base to the building.
Click: The second component is the walls and in some areas of the country may include wall sheathing.
Click: The third component is the floors that include the first level floor and any subsequent floor levels in the building.
Click: The final fourth component is the roof system.
The next section of this lesson reviews each construction component in more detail.
(Student Handout Material)

## Slide 13: Foundation
Anchors the structure to the ground.
Keeps the building level.
Minimizes settling.
Prevents uplift.
Resists horizontal forces.
Keeps wooden parts away from ground elements (organisms, soil moisture).
Notes: Foundation — Structural Function
The foundation is essential in providing stability to the building and anchors the building structure to the ground. The foundation keeps the building level and minimizes settling of the structure into the ground. The heavy mass of the foundation prevents uplift and helps resist horizontal forces applied by nature. Foundations also keep wooden portions of the structure from contacting ground elements such as organisms, soil, and moisture.

## Slide 14: Foundation Types
FOUNDATION TYPES
Slab on Grade
Stem Wall
Pier and Beam
Piling
Basement
Stem Wall / Raised Floor
Used where the structures’ elevation varies. Maintain a sound structural footing; are required to go below grade.
Basement
Constructed with concrete floors and walls. Common where deep footings are required; provide usable space.
Slab on Grade
Poured concrete at ground level; sometimes reinforced with steel rebar or tension bars.
Pier and Beam
Includes a crawl space beneath the living space; concrete footings support the foundation.
Piling
May be concrete, wood or steel driven deep into the ground to act as a support for structures.
Notes: Foundation Types
The main type of residential foundation is slab on grade, where the poured concrete is at ground level. Slab-on-grade foundations consist of a shallow footing, about two feet deep as a code minimum. The ground floor concrete slab is about 5"–12" thick depending on the type.
Conventional slab on grade uses rebar embedded in the concrete in a grid pattern. Rebar provides structural strength to the concrete slab. Another type of slab on grade is post tension slab that uses patterned steel cables embedded in the concrete. Once the concrete is poured, the cables are hydraulically pulled tight to lock it into place, creating a tension member within the concrete mass. This method works well for concrete foundations in unstable soil conditions.
Another foundation type is stem wall, also known as raised floor foundations. Stem walls are popular in the south and other geographical areas where the elevation around the structure varies. These concrete foundations maintain a sound structural footing and are required to go below grade.
Pier and beam foundations are also popular in the south. This foundation type includes a crawl space beneath the living space with concrete footings to support the foundation.
Piling foundations may be concrete, wood or steel driven deep into the ground to act as a steady support for structures.
Basements are another type of foundation constructed with concrete floors and walls. Basement foundations are common where deep footings are required and provide the added benefit of usable space when completed. Codes require concrete slab foundations to rest on stable soil, based on being below the frost line. Extensive depths are required to reach the frost line in colder climates, which naturally creates the option of adding a basement foundation at no additional expense.

## Slide 15: Wall — Structural Function
Non-Load Bearing Walls
Act as a partition that divides rooms.
Provides no structural support.
Load-Bearing Walls
Provide vertical structure that supports upper floors and roof.
Provide lateral structure to stiffen building.
Notes: Wall — Component
Walls in residential buildings are an important element in the structural framework. There are two main types of walls, non-load bearing and load bearing. Non-load-bearing walls act as a partition that divides rooms in the building and provide no structural support. Load-bearing walls provide vertical structure that supports the upper floors and roof, as well as providing lateral structure to stiffen the building. Load-bearing walls are important to counteract wind, seismic, water and other natural forces.
(Student Handout Material)

## Slide 16: Wall — Components
Bottom plate/mudsill
Studs
Header and components
Top plate(s)
Sheathing
Notes: Wall – Component
There are several typical components included in a wood-framed wall.
Click: Bottom Plate / Mudsill
The lumber directly on the concrete foundation is a bottom plate, or mudsill, depending on the geographical area. The bottom plate lumber is treated to reduce deterioration caused by moisture wicking from the concrete and to deter destructive insects, such as termites.
Click: Studs
Studs are 2x4 or 2x6 vertical members used to form walls. Lumber studs are most commonly spaced 16" apart on center, and in certain conditions 12" or 24" on center.
Click: Header and Components
When an opening is required in the wall for a door or window, a header will be included at the top of the opening and carries the load of the members that terminate at the opening. Headers are twice the size of surrounding framing members built from two 2x10, two 2x12, or a solid 4x material.
Click: Top Plate
Top Plates are located across the top of the wall. Typically, two top plates are used in order to transfer loads across splices by staggering the lumber members.
Click: Sheathing
Sheathing boards or panels, constructed of plywood, Oriented Strand Board (OSB) or structural board, are rated to provide a shear element into the wall. This provides rigidity and strength to the wall plane.

## Slide 17: Floor — Structural Function
Live Loads
Moveable and not a permanent part of the structure.
Dead Loads
Weight of the floor structure and other items permanently attached to the floor.
The floor must support weight loads from above.
Transfers the loads from one wall to the other by creating a diaphragm that makes the building rigid.
Notes: Floor — Structural Function
The floor must support weight loads from above. There are two different types of weight loads: live loads and dead loads. Live loads are moveable and not a permanent part of the structure. Live loads include items such as furniture, people, storage, and appliances. Dead loads are the weight of the floor structure and any other items permanently attached to the floor. Dead loads include building materials such as lumber, carpets, drywall, windows, and doors.
To calculate the floor load requirements both live loads and dead loads are added together, along with additional factors such as the joist span, spacing, and lumber grade etc.
The floor also transfers the loads from one wall to the other wall by creating a diaphragm that makes the building rigid. It is important that the floor is properly attached to the top of the walls in order to transfer all the load factors and decrease the chance of the walls moving in or out from the floor.

## Slide 18: Floor — Components
Joists and I-Joists
Beams
Solid sawn lumber
Blocking
Rim or band
Floor-trusses
Bracing
Notes: Floor — Components
Floors contain certain components that assist in providing a solid structure.
Click: I-Joist
One of the most common floor components is an I-joist. This engineered wood member is actually shaped like an I. The top and bottom flanges resist bending and provide outstanding shear resistance. I-joists can extend across the top of the wall, and are ideal for long spans. They are lightweight and easy to install in residential and light commercial projects.
Click: Beams
Beams support greater loads than any one individual joist. They also can support a series of joists. When beams support the second floor of a residential building, they may remain exposed at the bottom and visible on the first floor ceiling.
Click: Solid Sawn Lumber
Solid Sawn lumber is a member cut from a single log and available in 2x10 or 2x12 sizes. Solid sawn lumber was a standard building material in the past. However, the poor availability and consistency of the product, along with increased efficiencies in farming and harvesting, has led to increased use of engineered wood products.
There is also inconsistency in the dimensions of solid sawn lumber. A 2x12 rough cut, or rough sawn, piece of lumber measures about 2x12, whereas a 2x12 dimensional piece of lumber can vary in measurement from 1½" to 1⅝" by 11 1/8" to 11 ½", depending on if it is dried.
Click: Blocking
Solid sawn lumber requires blocking mid-span. The process of cutting and placing the small blocks of lumber is labor intensive. Blocking is not required with the use of I-joists.
Click: Rim or Band Joist
Around the entire perimeter of the floor is a rim or band joist used to attach the floor to the top of the wall and to the end of each individual floor joist. Rim joists are required for both I-joist and solid sawn lumber floor systems.
Click: Floor Trusses
Floor trusses are another type of manufactured flooring system built from small pieces of lumber and attached with metal truss plates to make a strong longer member. Floor trusses have higher capacities resulting in larger widths and more extended spacing. Floor trusses also offer an advantage of chase openings providing easy installation to channel heating, air conditioning, and electrical conduits.
Click: Bracing
Floor trusses require bracing, similar to a band joist. However, the bracing is not required to extend the full depth of the truss system.

## Slide 19: Roof — Structural Function
Keeps building together
Holds walls in place
Resists lateral forces
Provide protection from the elements and has structural functions.
Notes: Roof — Structural Function
The roof is the top of the building with the basic function to provide protection from the elements; yet, the roof also has structural functions, as well. The roof keeps the building together, holds the walls in place, and resists the lateral forces applied to a building, including wind, seismic, water, and earth pressure loads.

## Slide 20: Roof — Components
Ridge board
Rafter
Collar tie
Ridge beam
Truss
Blocking
Bracing
Sheathing
Notes: Roof — Components
There are many different types of roof components used in a wide variety of roof design combinations.
Click: Ridge Board
A ridge board is a non-structural member located at the roof ridge.
Click: Rafters
Rafters are bevel cut and span from the ridge board attaching to the top of the wall. Ceiling joists run across of the plates and connect to the rafters and the top of the wall, preventing the roof from collapsing inward.
Click: Collar Tie
This type of roof requires a collar tie attached to the top 1/3 of the roof span.
Click: Ridge Beam
A ridge beam is a structural member used to support the ends of the rafters at the ridge. A ridge beam transfers loads to posts or columns from the roof all the way down through the structure. Ridge beams are very common with vaulted ceilings.
Click: Truss
Roof trusses are a replacement for conventional framing. Trusses have many small members of lumber attached with metal truss plates offering an efficient use of materials. The use of technology and computers for the roof truss attachments and design enables engineers to create strong members. Since each truss is engineered for the specific conditions where it will be used, the geographic area, and the building load factors, it is critical that none of the truss structural members get cut or altered on the job site.
Click: Blocking
Blocking is the use of short pieces of dimensional lumber to provide filling, spacing, joining or reinforcement of wood frame members. The addition of blocking to roof trusses and rafters at the top plate line is an absolute necessity. In roof systems, blocking provides a surface to nail sheathing to the structure boundary, transferring loads from the roof to the walls. Roof blocking is available with holes to accommodate the application of ventilation screens at the top plate line.
Blocking is a common practice in the western United States although many other areas have removed blocking for ventilation.
Click: Bracing
Diagonal, or X bracing, should be used with roof truss members. Temporary bracing is available during the erection process. This prevents trusses from falling over before installing permanent sheathing bracing.
Click: Sheathing
Roof sheathing is a thin covering to keep the roof trusses and rafters properly spaced, and adds strength and rigidity to the entire roof system. Oriented Strand Board (OSB) or plywood is material often used for roof sheathing.

## Slide 21: Roof — Design Elements
Valley
Hip
Ridge
Gable
Overhang/Eave
Notes: Roof — Design Elements
The vast array of roof types and materials provide a method for customizing and stylizing the exterior look and profile of the building. The most common types of roofing styles include those listed on this slide.
Click: Valley
Roof valleys are the v-shaped channels created by two intersecting roof planes. Since water naturally runs down the valleys, roof valleys are particularly vulnerable to leakage. There are options available for either open or closed roof valleys depending on the location, application, and design style required
Click: Hip
A hip roof is the outward diagonal joint created by the junction of two roof slopes that slope downward toward the wall forming a triangle shape. In addition to the roof style, the wood framing elements that create the hip roof are hip trusses and hip jack trusses.
Click: Ridge
The ridge is the uppermost peak created by the junction of two roof slopes facing opposite directions.
Click: Gable
Gables are the triangle portion of a wall between the edges of intersecting roof planes. Gabled roofs create a structurally weaker roof system for wind and seismic resistance than the hip style roof.
Click: Overhang/Eave
Overhang and eaves are the edges of the roof that hangs over the wall. In the United States, the overhang is typically about two feet long. In some parts of the country, the overhang is finished and in other areas, the overhang remains open.
(Student Handout Material)

## Slide 22: Check Your Knowledge
Which definition best describes an I-joist?
Vertical members used to form walls
One of the most common floor components with top and bottom flanges that resist bending and provide outstanding shear resistance
Short pieces of dimensional lumber that provide filling, spacing, joining, or reinforcement of wood frame members
Notes: Check Your Knowledge

## Slide 23
Wood-Frame Construction 101
LESSON 3
Basic Construction Materials
Notes: Lesson 3: Structural Basics
This lesson introduces the various forces that act on a building and the methods used to resist the forces.

## Slide 24: Wood Size
Rough sawn lumber = unfinished timber cut from a single log; rarely used in modern framing.
Dimensional lumber is timber cut to standardized width and depth and milled to a smooth finish, losing about one quarter inch from each side.
Cross-section of a tree trunk
Characteristic shrinkage.
Distortion of flat, square, and round members influenced by the direction of annual rings.
Notes: Wood Size
It is important to understand some of the basic aspects of wood products in order to understand wood frame construction concepts.
Size
Rough sawn lumber is unfinished timber cut from a single log and rarely used in modern framing. Dimensional lumber is timber cut to standardized width and depth members, such as 2x4 and 2x6, and then milled to have a smooth finish, losing about 1/4" from each side. In addition, lumber experiences shrinkage while drying. The illustrated cross-section of a tree trunk shows characteristic shrinkage and distortion of flat, square and round members, influenced by the direction of annual rings.

## Slide 25: Wood Species
Different species have different strength.
Douglas fir, hem-fir, southern yellow pine, and spruce-pine fir (SPF) are commonly used for U.S. residential construction.
Notes: Wood Species
Species
The wood from each species, or type of tree, has different wood fiber and strength characteristics. The most typical light structural lumber species used for residential construction in the United States are Douglas fir, hem-fir, southern yellow pine and SPF, which is an acronym for spruce-pine-fir.

## Slide 26: Wood Grade
Lumber can be machine stress graded or visually graded.
Grading is based on the number of defects in the board.
Does not reflect color or grain pattern.
The mill stamps the board with a grading mark.
Notes: Wood Grade
Grade
Softwood dimensional lumber can be machine stress graded or visually graded. Structural lumber is usually machine stress graded while non-structural lumber is usually visually graded. The machine stress grading system is based on the strength and number of defects in the individual board, and does not reflect color or grain pattern, while visual inspection focuses mostly on appearance. Once graded, the mill commonly stamps the board with a mark similar to the one shown here. The mark includes the mill’s number, agency providing quality control, the grade, moisture content and the species. In this example, the mill is 000, graded by TP, grade 2 lumber, dried, and the species is southern yellow pine.
Since the lumber strength and compression are very important aspects in the building structural integrity, designers specify to the minimum common grade, with a number two being very common. They may also specify a stud grade, which is a compressive grade stud.

## Slide 27: Wood Moisture Content
Wood contains moisture and shrinks as it dries.
Some lumber species are dried before construction.
Green lumber (undried wood) will dry after construction; it will shrink significantly.
Notes: Wood Moisture Content
Moisture Content
Wood naturally contains a lot of moisture resulting in shrinkage as it dries. Some lumber species are dried before being used in construction. Green lumber is undried wood that will dry after construction, and it will shrink significantly. This is why a green lumber 2x4, used on the West Coast, is only 1 5/8" thick and will dry to become 1 1/2" thick.
For a single-story building that has three plates, a bottom plate, a stud and two top plates, a precut stud is used to give the height to the end wall. The eight-foot wall uses a 92 1/4" precut stud, with the three plates each being 1 5/8" thick that will shrink 3/8" when finally dried.
Other parts of the country use dried lumber where the plates are 1 1/2" thick with a bottom plate, a stud and two top plates. However, because the plates are already dried, the precut studs used in this eight-foot wall are 92 5/8" and will have little or no shrinkage after construction.
Also, when constructing with green lumber, consideration must be given to how and when to install the attachments and other materials that don't shrink. If installed before shrinkage, it will result in cracks and problems at the doors, windows and sheet rock areas. In a two-story building, shrinkage is a primary consideration when planning how to tie material together in a continuous load path.

## Slide 28: Treated Lumber
PRECAUTIONS
CORROSIVE
RESISTS ROT
Treated lumber is used for the portions of a structure that are likely to be in contact with soil and water. While treated lumber does not soak up less water, it is designed to resist rot from frequent contact with water.
Some forms of treated lumber can be very corrosive to steel including nails, screws, bolts, and connectors, causing them to rust prematurely.
Because of the chemicals in the wood fibers, precaution is required when handling treated lumber.
Wood is infused with chemicals through a pressure process to reduce damage from wood rot or insects. Different chemical combinations are available for different applications and marked for use in “above ground” or “ground contact” applications.
Notes: About Wood — Treated Lumber
Treated lumber is a wood product infused with chemicals through a pressure process, to reduce damage from wood rot or insects. Different chemical combinations are available for different applications and marked for use in “above ground” or “ground contact” applications.
Treated lumber is used for the portions of a structure that are likely to be in contact with soil and water. While treated lumber does not soak up less water, it is designed to resist rot from frequent contact with water.
Some forms of treated lumber can be very corrosive to steel including nails, screws, bolts and connectors, causing them to rust prematurely. Use appropriate corrosion-resistant fasteners in treated lumber applications.
Because of the chemicals in the wood fibers, precaution is required when handling treated lumber. Gloves are required when handling treated lumber. Safety goggles and a dust mask are required when cutting, drilling or sanding treated lumber, and personal safety requires that site workers wash their hands thoroughly before ingesting food or drinks.
(Student Handout Material)

## Slide 29: Engineered Wood Products
Manufactured wood product built from bonding wood strands, veneers or lumbers.
Produces a structural product with low variability.
Uses faster-growing and often under-utilized wood species from managed forests and tree farms.
EWP
Notes: About Wood — Engineered Wood
Engineered wood is a manufactured wood product built from bonding wood strands, veneers, or lumbers to produce a structural product with low variability. The fabrication process uses faster-growing and often under-utilized wood species from managed forest and tree farms.
Engineered wood products provide many benefits to residential construction. They are environmentally friendly and enable the use of species and parts of the tree not normally used in construction. There is a lot less waste of wood, a lesser likelihood of warping, and they allow for the use of newer growth materials. In many cases, such as the I-joist, the member is lighter and easier to use, yet stronger than solid lumber.
The following section outlines the different types of engineered wood products.
(Student Handout Material)

## Slide 30
There are several types: OSB (oriented strand board) and plywood.
Panel Products
Notes: Panel Products
EWP panel products are structural panels such as OSB (oriented strand board) and plywood. Manufacturers use panel products in other EWP products such as I-joists.

## Slide 31: Oriented Strand Board
Common building material.
Used where C-D grade plywood would be used.
OSB
Notes: OSB
OSB is a structural board that is a common building material. OSB is manufactured by cross-orienting wood flakes in different directions and then gluing together under heat and pressure. OSB is used in all applications where C-D grade plywood would be used.

## Slide 32
Produced in large standard sized sheets.
Manufactured by laminating several veneers of wood in perpendicular layers.
Plywood
Notes: Plywood
Plywood is produced in large standard sized sheets and is manufactured by laminating several veneers of wood in perpendicular layers.

## Slide 33: Structural Composite Lumber
Man-made engineered wood products created by gluing dried and graded wood veneers or strands together.
Different types of finished products (LVL, PSL and LSL).
Solid, highly predictable uniform members; less likely to warp or shrink compared with solid sawn lumber.
Manufactured by several companies with specific name brands.
SCL
Notes: Structural Composite Lumber (SCL)
SCL is a family of man-made engineered wood products created by gluing dried and graded wood veneers or strands together. SCL encompasses different types of finished products such as LVL, PSL and LSL These products are solid, highly predictable, uniform members in which designers can specify for their plans. SCL is manufactured by several companies with specific name brands, and are less likely to warp or shrink compared with solid sawn lumber.

## Slide 34: Laminated Veneer Lumber
Engineered wood product made from graded veneers of structural wood species.
All wood grain is aligned parallel to the length of the beam; pressed with heat and exterior grade adhesive for strength in the bending orientation.
Several LVL manufacturers in North America.
LVL
Notes: Laminated Veneer Lumber (LVL)
LVL is an engineered wood product made from graded veneers of structural wood species. All wood grain is aligned parallel to the length of the beam and pressed with heat and exterior grade adhesive for strength in the bending orientation. There are several manufacturers of LVL in North America.

## Slide 35: Parallel Strand Lumber
PSL uses long strands of wood lumber glued together in one direction.
Dense material used for studs, beams, headers, and load-bearing columns.
PSL
Notes: Parallel Strand Lumber (PSL)
Parallel Strand Lumber (PSL) uses long strands of wood lumber glued together in a certain direction. PSL is a dense material used to produce studs, beams, headers, and load-bearing columns.

## Slide 36: Laminated Strand Lumber
LSL uses strand fibers instead of veneers; strands are smaller individual pieces of fiber compared to veneers which are peeled off of a log in a continuous thin ribbon.
LSL is made from non-structural wood such as aspen and yellow poplar.
Commonly used for band or rim joist applications; thicker members can be used for beams and headers around doors and windows.
LSL
Notes: Laminated Strand Lumber (LSL)
LSL stands for Laminated Strand Lumber and uses strand fibers instead of veneers for its construction. Strands are smaller individual pieces of fiber compared to veneers which are peeled off of a log in a continuous thin ribbon. LSL is typically made from wood species which are not traditionally considered structural, such as aspen and yellow poplar. LSL is most commonly used for band or rim joist applications, but thicker members can be used for beams and headers around doors and windows.

## Slide 37: Wood I-Joists
Strong, lightweight manufactured wood members that efficiently use raw lumber materials.
Comprise a top and bottom flange using either solid lumber or LVL material, and then glued onto a plywood or OSB web.
Used extensively in floor and roof framing, ideal for long spans, straight and true, easy to install.
I-Joists
Notes: Wood I-Joists
Wood I-joists are strong, lightweight manufactured wood members that efficiently use raw lumber materials. I-joists are comprised of a top and bottom flange using either solid lumber or LVL material, and then glued onto a plywood or OSB web. I-joists are used extensively in residential floor and roof framing, ideal for long spans, straight and true, and easy to install.

## Slide 38: Glue Laminated Beams
Large beams constructed from small pieces of lumber.
Strong and stiff, available in simple straight beams or complex curved members.
Some glulam beams are slightly arched; the member will lie flat once it is used in a span – a stamp showing “top” or “bottom” assists with correct installation.
Glulam Beams
Notes: Glulam Beams
Glue laminated beams have been available for a long time, offering large beams constructed from small pieces of lumber. Glulam is strong and stiff and is available in simple straight beams or complex curved members used in striking, exposed applications. Some glulam beams are slightly arched to enable the member to lie flat once it is used in a span. In this case, the member will have a stamp indicating the top or bottom to assist with installation.

## Slide 39: Check Your Knowledge
Which of the following are examples of Engineered Wood Products (EWP)?
SELECT ALL THAT APPLY
Solid Sawn Board
Laminated Veneer Lumber
Rough Sawn Beams
Glulam Beams
Oriented Strand Board
Notes: Check Your Knowledge

## Slide 40: Fasteners
SCREWS
NAILS
BOLTS
Notes: Fasteners
Wood-frame construction uses many types of fasteners. The most common fasteners are nails, bolts, and screws.

## Slide 41: Nails
Available in many different shapes and sizes.
The longer the nail, the more resistance it has from being pulled out.
The thicker the nail, the greater its shear capacity.
Notes: Fastener Types — Nails
Nails create a mechanical connection between two or more structural components. Nails are available in many different shapes and sizes. The two main characteristics of nails are length and diameter. The longer the nail, the more resistance it has from pulling out, and the thicker the nail, the greater its shear capacity. A common nail is a 16d or 16 penny nail that has a diameter of 0.162" and a length of 3½". The building code is very specific about what nail to use for every attached component in a building, including what nail type, how many nails and what size of nail to use. Connectors are also specific about what nail to use to get full load capacity based on the product testing.

## Slide 42: Bolts
Offer greater strength or when the work requires frequent disassembly.
Require the use of nuts and washers.
Requires drilling a hole through the wood; the washer installs on the wood side of the bolt.
Notes: Fastener Types — Bolts
Bolts are used when greater strength is required or when the work under construction requires frequent disassembly. Bolts require the use of nuts and washers. A bolt requires drilling a hole through the wood and the use of a washer on the wood side of the bolt. The hole is very critical and code requires the hole to be 1/16" larger than the diameter of the bolt. While meeting this requirement is sometimes challenging in the field, it is not acceptable to drill a hole from both sides that meet in the middle, or drill a larger-diameter hole than specified.

## Slide 43: Screws
Used where higher withdrawal capacity is needed.
Provide strong clamping forces to the members being attached.
Provide capacity in sheer and tension that indicates how strong the threads bite in the wood and the overall strength of the steel.
Often can be used for the same fastening applications as bolts, while providing a faster installation.
Notes: Fastener Types — Screws
Screws are used in applications requiring higher withdrawal capacity and provide strong clamping forces to the members being attached.
Screw technology has drastically changed in the last 10 years. There are numerous types of structural screws with a self-drilling mechanism. These screws no longer require a predrilled hole with a pilot drill bit.
Additionally, structural screws have known strength characteristics in both sheer and tension that indicates how strong the threads bite in the wood and the overall strength of the steel. In many cases, structural screws can be used for the same fastening applications as bolts, while providing a much faster installation.
Lag screws are not a viable option for structural applications. Lag screw installation also requires predrilling with two different diameter bits.

## Slide 44: Summary
Basic concepts of wood-frame construction.
Lesson 1 Overview of wood-frame construction Common usage, benefits and types
Lesson 2 Main construction components Foundation, the walls, the floor, and roof Structural function of each component type
Lesson 3 Materials used Wood, treated lumber, engineered wood, and fasteners
Notes: Summary
This training covered the basic concepts of wood frame construction.
Lesson 1 provided an overview of wood frame construction including the common usage in residential building, the benefits and the two main types.
Lesson 2 introduced the main construction components that exist on most every building project. This section included the foundation, the walls, the floor and the roof. The lesson defined the structural function and provided examples for each component type.
Lesson 3 provided details on the basic materials used in wood frame construction. This included wood, treated lumber, engineered wood and fasteners such as nails, screws and bolts.

## Slide 45
Wood-Frame Construction 101
ASSESSMENT
Final Assessment
There are 10 questions. You must pass with a score of at least 70%.
Notes: Assessment: Final Assessment
There are 10 questions in the final assessment and you must pass with a score of at least 70%.

## Slide 46: Congratulations!
You have completed this course. Use the Exit button to close the training.
SST-198-02_WoodFramingConstruction101_v001 Copyright © 2020 Simpson Strong-Tie. All rights reserved.
Notes: Congratulations!
You have completed this course. Use the Exit button to close the training.